## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 2.15
Arm Assembly – Part 4

## Slide 2: Function Calls
Branch with Link (function call) instruction
bl label
Function call to the instruction with the address label (no local labels for functions)
  imm24 number of instructions from pc+8 (24-bits)
  label any function label in the current ﬁle, any function label that is deﬁned as .global in any ﬁle that it is linked to, any C function that is not static
Branch with Link Indirect (function call) instruction
blx Rm
Function call to the instruction whose address is stored in Rm (Rm is a function pointer)
bl and blx both save the address of the instruction immediately following the bl or blx instruction in register lr (link register is also known as r14)
The contents of the link register is the return address in the calling function
bl
imm24
x
main:
●
bl f1 f1:
● ●
(1) Branch to the instruction with the label f1
(2) copies the address of the instruction AFTER the bl in lr
blx
Rm

## Slide 3: Function Call Return
Branch & exchange (function return) instruction
bx lr // we will always use lr
Causes a branch to the instruction whose address is stored in register <lr>
  It copies lr to the PC
This is often used to implement a return from a function call (exactly like a C return) when the function is called using either bl label, or blx Rm
bx
Rn
main:
●
●
bl f1 f1: ●
● ●
● bx lr
●
Branch to the instruction whose address is stored in lr
x
Stores this address in lr
this is the address to resume at in the caller

## Slide 4: Understanding bl and bx - 1
int a(void)
{
return 0;
}
int main(void)
{
a();
a();
// not shown
x
But there is a problem we must address here – next slide
a:
103f4: mov r0, 0
103f8: bx lr
main:
103fc: bl 103f4 //a
10400: bl 103f4 //a
10404: mov r0, 0
lr:
10400
lr:
10404
lr:
10400
lr:
10404
Address in memory

## Slide 5: Understanding bl and bx - 2
int b(void)
{
return 0;
}
int a(void)
{
b();
return 0;
}
int main(void)
{
a();
a();
// not shown
x
b:
103f4: mov r0, 0
103f8: bx lr
a:
103fc: bl 103f4 <b>
10400: mov r0, 0
10404: bx lr
main:
10408: bl 103fc <a>
1040c: bl 103fc <a>
10410: mov r0, 0
lr:
1040c
lr:
10400
lr:
10400
lr:
10400
Uh No
Infinite loop!!!
Modifies the link register (lr), writing over main's return address Cannot return to main()
We need to preserve the lr!

## Slide 6: Understanding bl and blx - 3
int a(void)
{
return 0;
}
int (*func)() = a;
int main(void)
{
(*func)();
// not shown
.data
func:.word a // func initialized with address of a()
.text
.global a
.type a, %function
.equ FP_OFF, 4
a:
mov r0, 0
bx lr
.size a, (. - a)
.global main
.type main, %function
.equ FP_OFF, 4
main:
ldr r4, =func // load address of func in r4
ldr r4, [r4] // load contents of func in r4
blx r4 // we lose the lr for main!
// not shown
bx lr // infinite loop!
But this has the same infinite loop problem when main() returns!
x

## Slide 7: Preserving and Restoring Registers on the stack - 1
high memory
low memory
before
stack pointer
push{ }
after
stack pointer
pop{ }
after stack pointer
before stack
pointer
high memory
low memory
x
registers
registers
registers
registers
registers
registers
push (multiple register str to memory operation)
push (multiple register ldr from memory operation)
Operation | Pseudo Instruction |  | Operation
Push registers Function Entry | push | {reg list} | sp = sp – 4 × #registers Copy registers to mem[sp]
Pop registers Function Exit | pop | {reg list} | Copy mem[sp] to registers, sp = sp + 4 × #registers

## Slide 8: Preserving and Restoring Registers on the Stack - 2
{reg list} is a list of registers in numerically increasing order, left to right
push {r4-r10, fp, lr} // fp is r11, lr is r14
Registers cannot be:
  duplicated in the list
  listed out of increasing numeric order (left to right)
Register ranges can be specified {r4, r5, r8-r10, fp, lr}
Never! push/pop r12, r13, or r15
  the top two registers on the stack must always be fp, lr // ARM function spec – later slides
Operation | Pseudo Instruction |  | Operation
Push registers Function Entry | push | {reg list} | sp = sp – 4 × #registers Copy registers to mem[sp]
Pop registers Function Exit | pop | {reg list} | Copy mem[sp] to registers, sp = sp + 4 × #registers
x

## Slide 9: push: Multiple Register Save to the stack
push copies the contents of the {reg list} to stack segment memory
push subtracts (# of registers saved) * (4 bytes) from the sp to allocate space on the stack
  sp = sp – (# registers_saved * 4)
this must always be true: sp % 8 == 0
saved lr
saved fp
saved r8
saved r6
saved r4
saved r5
save registers
push {r4-r6, r8, fp, lr}
r8
r4
r5
lr
fp
r6
CPU registers to Save
copy
Registers are pushed on to the stack in order
right (high memory) to left (low memory)
If you have no stack variables (later slides) then always push an EVEN number of registers!
sp after push
allocated space
(# registers) * (4 bytes)
stack segment low memory
stack segment high memory
x
sp before push

## Slide 10: pop: Multiple Register Restore from the stack
pop copies the contents of stack segment memory to the {reg list}
pop adds: (# of registers restored) * (4 bytes) to sp to deallocate space on the stack
  sp = sp + (# registers restored * 4)
Remember: {reg list} must be the same in both the push and the corresponding pop
stack segment high memory
r8
r4
r5
saved lr
saved fp
saved r8
saved r6
saved r4
saved r5
lr
fp
r6
stack segment low memory
CPU registers
copy
Restored register contents
Registers are pop’d from the stack in order
left (low memory) to right (high memory)
restore registers
pop {r4-r6, r8, fp, lr}
sp after pop
deallocated space
(# registers) * (4 bytes)
x
sp before pop

## Slide 11: Consequences of inconsistent push and pop operands
lr gets contents of saved r8, likely causing a segmentation fault when the bx lr is executed at function exit
saved lr
saved fp
saved r8
saved r6
r8
lr
fp
r6
CPU registers to Save
copy
sp
stack segment low memory
stack segment high memory
push {r6, r8, fp, lr}
stack segment high memory
copy
sp
saved lr
saved fp
saved r8
saved r6
lr
fp
stack segment low memory
CPU registers
x
pop {fp, lr}

## Slide 12: Registers: Rules For Use
Register | Function Call Use | Function Body Use | Save before use Restore before return
r0 | arg1 and return value | scratch registers | No
r1-r3 | arg2 to arg4 | scratch registers | No
r4-r10 | preserved registers | contents preserved across function calls | Yes
r11 / fp | stack frame pointer | Use to locate variables on the stack | Yes
r12 / ip | may used by assembler with large text file | can be used as a scratch if really needed | No
r13 / sp | stack pointer | stack space allocation | Yes
r14 / lr | link register | contains return address for function calls | Yes
r15 | Do not use | Do not use | No
x

## Slide 13: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
Each parameter and return value is limited to data that can fit in 4 bytes or less
Calling function:
  copy up to the first four parameters into these four registers before calling a function
  MUST assume that the called function will alter the contents of all four registers: r0-r3
  In terms of C runtime support, these registers contain the copies given to the called function
  C allows the copies to be changed in any way by the called function
Called function:
  you receive the first four parameters in these four registers (r0 – r3)
x
Register | Function Call Use | Function Body Use | Save before use Restore before return
r0 | arg1 and return value | scratch registers | No
r1-r3 | arg2 to arg4 | scratch registers | No

## Slide 14: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
For parameters, whose size is larger than 4 bytes, pass a pointer to the parameter (we will cover this later)
One arg value per register! – NO arrays across multiple registers
  chars, shorts and ints are directly stored
  Structs (not always), and arrays (always) are passed via a pointer
  Pointers passed as output parameters contain an address that points at the stack, BSS, data, or heap
x
Register | Function Call Use | Function Body Use | Save before use Restore before return
r0 | arg1 and return value | scratch registers | No
r1-r3 | arg2 to arg4 | scratch registers | No

## Slide 15: Register Arguments and Return Values
When passing or returning values from a function you must do the following:
Make sure that the values in the registers r0-r3 are in their properly aligned position in the register based on data type
Upper bytes in byte and halfword values in registers r0-r3 when passing arguments and returning values are
  zero filled for unsigned values
  sign extended for signed values
0x00
0x00
0x00
0xe1
0
31
Single Byte (unsigned char)
r0
0x00
0x00
0xe3
0xe1
0
31
r0
Single Halfword (unsigned short)
0x87
0x65
0xe3
0xe1
0
31
r0
Full Word (int or pointer)
observe the zero fill
observe the zero fill
x

## Slide 16: What it means to be a Temporary/argument register
  // main()
  // code not shown
  mov r0, 0
  mov r1, 1
  mov r2, 2
  mov r3, 3
  bl a
  // r0 = return value
  // r1-r3 values are unknown as a() has right to change them as it wants
int a(void)
{
// not shown
}
int main(void)
{
int r0 = 0;
int r1 = 1;
int r2 = 2;
int r3 = 3;
r0 = a();
// in C r1 and r3 would have the same values
// after the call

## Slide 17: Preserved Registers
Any value you have in a preserved register before a function call will still be there after the function returns (Contents are “preserved” across function calls)
If the function wants to use a preserved register it must:
  Save the value contained in the register at function entry
  Use the register in the body of the function
  Restore the original saved value to the register at function exit (before returning to the caller)
You use a preserved register when a function makes calls another function and you have:
  Local variables allocated to be in registers
  Parameters passed to you (in r0-r3) that you need to continue to use after calling another function
x
Register | Function Call Use | Function Body Use | Save before use Restore before return
r4-r10 | preserved registers | contents preserved across function calls | Yes
r11/fp | stack frame pointer | Use to locate variables on the stack | Yes
r13/sp | stack pointer | stack space allocation | Yes
r14/lr | link register | contains return address for function calls | Yes

## Slide 18: Minimum Stack Frame (Arm Arch32 Procedure Call Standards)
Minimal frame: allocating at function entry: push {fp, lr}
sp always points at top element in the stack (lowest byte address)
fp always points at the bottom element in the stack
  Bottom element is always the saved lr (contains the return address of caller)
  A saved copy of callers fp is always the next element below the lr
  fp will be used later when referencing stack variables
Minimal frame: deallocating at function exit: pop {fp, lr}
On function entry: sp must be 8-byte aligned (sp % 8 == 0)
x
low address
saved lr
callers fp
sp
fp
Minimum stack frame

## Slide 19: FIrst Look: A typical Stack Frame
Saved lr and fp of the caller (so function calls work)
Save values for any preserved registers this function will change
Space (FRMADD) for local variables is allocated on the stack right below the lowest pushed register
sp
saved lr
saved fp
fp
local
variables
FP_OFF
x
saved register
saved register
FRMADD=
Local Space (bytes)
Total size % 8 == 0
grows down

## Slide 20: Function Prologue and Epilogue
Only one prologue right after the function label (name)
Only one epilogue at the bottom of the function right above the .size directive
.global myfunc
.type myfunc, %function
.equ FP_OFF, 4 // fp distance to sp after push
.equ FRAMDD, 8 // number of bytes for local stack vars
myfunc:
push {fp, lr} // push (save) fp and lr on stack
add fp, sp, FP_OFF // set fp at bottom of stack
add sp, sp, -FRMADD // allocate FRMADD bytes for local vars
    // by moving sp
    // your code here
sub sp, fp, FP_OFF // deallocate local variables by moving sp
pop {fp, lr} // pop (restore) fp and lr from stack
bx lr // return to caller
.size myfunc, (. - myfunc)
Function Prologue
creates stack frame
Function Epilogue
removes stack frame
x

## Slide 21: Minimum Stack Frame (Arm Arch32 Procedure Call Standards)
main() calls funcA()
Function entry (Function Prologue):
  save lr and fp registers (push)
  set fp to top entry in stack
  allocate space for local vars – later slides
Function return (Function Epilogue):
  deallocate space for locals -later
  restores lr and fp registers (pop)
  Return To Caller
x
allocate stack space
SP = SP – "space"
grows "down"
lr to main()
main() fp
sp
fp
saved lr
callers fp
funcA()
main()
deallocate stack space
SP = SP + "space"
shrinks "up"
saved lr
callers fp
sp
fp
main()

## Slide 22: Using Minimal Stack Frames
int b(void)
{
return 0;
}
int a(void)
{
b();
return 0;
}
int main(void)
{
a();
a();
x
b:
103f4: push {fp, lr}
103f8: add fp, sp, 4
103fc: mov r0, 0
10400: sub sp, fp, 4
10404: pop {fp, lr}
10408: bx lr
a:
1040c: push {fp, lr}
10410: add fp, sp, 4
10414: bl 103f4 <b>
10418: mov r0, 0
1041c: sub sp, fp, 4
10420: pop {fp, lr}
10424: bx lr
main:
10428: push {fp, lr}
1042c: add fp, sp, 4
10430: bl 1040c <a>
10434: bl 1040c <a>
// not shown
10480 (lr)
main()
Stack address
90300
902fc
90308 fp
fp
sp
Memory address

## Slide 23: Using Minimal Stack Frames
b:
103f4: push {fp, lr}
103f8: add fp, sp, 4
103fc: mov r0, 0
10400: sub sp, fp, 4
10404: pop {fp, lr}
10408: bx lr
a:
1040c: push {fp, lr}
10410: add fp, sp, 4
10414: bl 103f4 <b>
10418: mov r0, 0
1041c: sub sp, fp, 4
10420: pop {fp, lr}
10424: bx lr
main:
10428: push {fp, lr}
1042c: add fp, sp, 4
10430: bl 1040c <a>
10434: bl 1040c <a>
// not shown
int b(void)
{
return 0;
}
int a(void)
{
b();
return 0;
}
int main(void)
{
a();
a();
x
lr:
10434
10480 (lr)
main()
Stack address
90300
902fc
90308 fp
10434 lr
90300 fp
a()
902f8
902f4
fp
sp

## Slide 24: Using Minimal Stack Frames
b:
103f4: push {fp, lr}
103f8: add fp, sp, 4
103fc: mov r0, 0
10400: sub sp, fp, 4
10404: pop {fp, lr}
10408: bx lr
a:
1040c: push {fp, lr}
10410: add fp, sp, 4
10414: bl 103f4 <b>
10418: mov r0, 0
1041c: sub sp, fp, 4
10420: pop {fp, lr}
10424: bx lr
main:
10428: push {fp, lr}
1042c: add fp, sp, 4
10430: bl 1040c <a>
10434: bl 1040c <a>
// not shown
int b(void)
{
return 0;
}
int a(void)
{
b();
return 0;
}
int main(void)
{
a();
a();
x
lr:
10434
lr:
10418
fp
sp
10480 (lr)
main()
Stack address
90300
902fc
90308 fp
10434 lr
90300 fp
a()
902f8
902f4
10418 lr
902f8 fp
b()
902f0
902ec

## Slide 25: Using Minimal Stack Frames
b:
103f4: push {fp, lr}
103f8: add fp, sp, 4
103fc: mov r0, 0
10400: sub sp, fp, 4
10404: pop {fp, lr}
10408: bx lr
a:
1040c: push {fp, lr}
10410: add fp, sp, 4
10414: bl 103f4 <b>
10418: mov r0, 0
1041c: sub sp, fp, 4
10420: pop {fp, lr}
10424: bx lr
main:
10428: push {fp, lr}
1042c: add fp, sp, 4
10430: bl 1040c <a>
10434: bl 1040c <a>
// not shown
int b(void)
{
return 0;
}
int a(void)
{
b();
return 0;
}
int main(void)
{
a();
a();
x
lr:
10434
lr:
10418
lr:
10418
fp
sp
10480 (lr)
main()
Stack address
90300
902fc
90308 fp
10434 lr
90300 fp
a()
902f8
902f4
10418 lr
902f8 fp
b()
902f0
902ec

## Slide 26: Using Minimal Stack Frames
b:
103f4: push {fp, lr}
103f8: add fp, sp, 4
103fc: mov r0, 0
10400: sub sp, fp, 4
10404: pop {fp, lr}
10408: bx lr
a:
1040c: push {fp, lr}
10410: add fp, sp, 4
10414: bl 103f4 <b>
10418: mov r0, 0
1041c: sub sp, fp, 4
10420: pop {fp, lr}
10424: bx lr
main:
10428: push {fp, lr}
1042c: add fp, sp, 4
10430: bl 1040c <a>
10434: bl 1040c <a>
// not shown
int b(void)
{
return 0;
}
int a(void)
{
b();
return 0;
}
int main(void)
{
a();
a();
x
lr:
10434
lr:
10418
lr:
10418
lr:
10418
lr:
10434
10480 (lr)
main()
Stack address
90300
902fc
90308 fp
10434 lr
90300 fp
a()
902f8
902f4
fp
sp

## Slide 27: Using Minimal Stack Frames
b:
103f4: push {fp, lr}
103f8: add fp, sp, 4
103fc: mov r0, 0
10400: sub sp, fp, 4
10404: pop {fp, lr}
10408: bx lr
a:
1040c: push {fp, lr}
10410: add fp, sp, 4
10414: bl 103f4 <b>
10418: mov r0, 0
1041c: sub sp, fp, 4
10420: pop {fp, lr}
10424: bx lr
main:
10428: push {fp, lr}
1042c: add fp, sp, 4
10430: bl 1040c <a>
10434: bl 1040c <a>
// not shown
int b(void)
{
return 0;
}
int a(void)
{
b();
return 0;
}
int main(void)
{
a();
a();
x
lr:
10434
lr:
10434
lr:
10418
lr:
10418
lr:
10418
lr:
10434
10480 (lr)
main()
Stack address
90300
902fc
90308 fp
fp
sp
We are saving the lr on the stack on each function call and restoring it before returning.
Result: NO infinite loop and we return to the correct instruction in the caller no matter how many functions we call.
Even recursion will work!

## Slide 28: Function Prologue: Allocating the Stack Frame -1
callers fp
low memory
lr to caller
at function entry
x
fp
Function was just called this how the stack looks
The orange blocks are part of the caller's stack frame
Callers
Stack Frame
callers fp
low memory
lr to caller
sp
saved lr
callers fp
saved r5
saved r4
after
push {r4,r5,fp,lr}
sp
fp
using a push, save lr, fp and those preserved registers it wants to use on the stack
Called function
Stack Frame
Callers
Stack Frame
Prologue Step 1 of 3
callers fp
low memory
lr to caller
sp
saved lr
callers fp
saved r5
saved r4
Set FP
add fp, sp, FP_OFF
fp
move the fp to point at the saved lr as required by the Aarch32 spec
FP_OFF
Called function
Stack Frame
Callers
Stack Frame
Prologue Step 2 of 3
myfunc:
push {fp, lr} // push (save) fp and lr on stack
add fp, sp, FP_OFF // set fp for this function
add sp, sp, -FRMADD // allocate FRMADD bytes for local vars
    // by moving sp
Function Prologue

## Slide 29: Function Prologue: Allocating the Stack Frame - 2
callers fp
low memory
lr to caller
sp
Local Variables
Allocate Space for locals
add sp, sp, -FRMADD
saved lr
callers fp
saved r5
saved r4
FRMADD
x
Allocate Space for Local Variables
fp
FP_OFF
Space for local variables is allocated on the stack right below the lowest pushed register
Add memory to the stack frame for local variables by moving the sp towards low memory
The amount moved is the total size of all local variables in bytes plus memory alignment padding
FRMADD = total local var space (bytes) + padding
Allocate the space after the register push by
  add sp, sp, -FRMADD
fp (frame pointer) is used as a pointer (base register) to access all stack variables – later slides
Called function
Stack Frame
Callers
Stack Frame
Prologue Step 3 of 3
myfunc:
push {fp, lr} // push (save) fp and lr on stack
add fp, sp, FP_OFF // set fp for this function
add sp, sp, -FRMADD // allocate FRMADD bytes for local vars
    // by moving sp
Function Prologue

## Slide 30: Function Epilogue: Deallocating the Stack Frame - 1
callers fp
low memory
lr to caller
sp
Local Variables
Stack frame while during function body execution
saved lr
callers fp
saved r5
saved r4
FRMADD
fp
FP_OFF
Use fp as a pointer to find local variables on the stack
x
Stack Frame
callers fp
low memory
lr to caller
sp
Local Variables
Deallocate Space for locals
Put SP back so pop works
sub sp, fp, FP_OFF
saved lr
callers fp
saved r5
saved r4
Deallocated
stack space
Move SP back to where it was after the push in the prologue.
So, pop works properly (this also deallocates the local variables)
fp
FP_OFF
Stack Frame
Step 1
sub sp, fp, FP_OFF // deallocate local variables by moving sp
pop {fp, lr} // pop (restore) fp and lr from stack
bx lr // return to caller
function Epilogue

## Slide 31: Why You must move SP before POP in the Epilogue
callers fp
low memory
lr to caller
sp
Local Variables
Allocate Space for locals
add sp, sp, -FRMADD
saved lr
callers fp
saved r5
saved r4
FRMADD
fp
FP_OFF
callers fp
low memory
lr to caller
sp
saved lr
callers fp
saved r5
saved r4
after
push {r4,r5,fp,lr}
fp
callers fp
low memory
lr to caller
sp
Local Variables
If you do not move sp back!
You get a total mess
pop {r4, r5, fp, lr)
saved lr
callers fp
saved r5
saved r4
FRMADD
fp
FP_OFF
lr
fp
r5
r4
CPU registers
sub sp, fp, FP_OFF // deallocate local variables by moving sp
pop {fp, lr} // pop (restore) fp and lr from stack
bx lr // return to caller
function Epilogue
x

## Slide 32: Function Epilogue: Deallocating the Stack Frame
callers fp
low memory
lr to caller
sp
Local Variables
At function exit after
pop {r4,r5,fp,lr}
saved lr
callers fp
saved r5
saved r4
Deallocated
Eligible for reuse
out of scope
Use pop to restore the registers to the values they had at function entry
fp
x
Stack Frame
callers fp
low memory
lr to caller
sp
Local Variables
Deallocate Space for locals
Put SP back so pop works
sub sp, fp, FP_OFF
saved lr
callers fp
saved r5
saved r4
Deallocated
stack space
Move SP back to where it was after the push in the prologue.
So, pop works properly (this also deallocates the local variables)
fp
FP_OFF
Stack Frame
Step 1
Step 2
sub sp, fp, FP_OFF // deallocate local variables by moving sp
pop {fp, lr} // pop (restore) fp and lr from stack
bx lr // return to caller
function Epilogue

## Slide 33: How to Set FP
FP_OFF = (#regs saved - 1) * 4
low memory
4-byte words
sp
lr to caller
callers fp
saved r5
saved r4
after push {r4-r7,fp,lr}
add fp, sp, FP_OFF
fp = sp + 20 bytes
saved r7
saved r6
// other code etc .equ FP_OFF, 20
main:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF …….
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
# regs saved | FP_OFF in Bytes Distance from lr to lowest saved register
2 | 4
3 | 8
4 | 12
5 | 16
6 | 20
7 | 24
8 | 28
9 | 32
Function Prologue
always at top of function saves regs and sets fp
Function Epilogue
always at bottom of function restores regs including the sp
Function Stack Frame
FP_OFF:
Distance from lr to lowest saved register
Means Caution, odd number of saved regs!
If odd number pushed, make sure frame is 8-byte aligned (later)
this must always be true: sp % 8 == 0
x
grows down

## Slide 34: Reference Table: Global Variable access
.data
x: .data y //x = &y
.bss // from libc
stderr:.space 4 // FILE *
var | global variable address into r0 (lside) | global variable contents into r0 (rside) | contents of r0 into global variable
x | ldr r0, =x | ldr r0, =x ldr r0, [r0] | ldr r1, =x str r0, [r1]
*x | ldr r0, =x ldr r0, [r0] | ldr r0, =x ldr r0, [r0] ldr r0, [r0] | ldr r1, =x ldr r1, [r1] str r0, [r1]
**x | ldr r0, =x ldr r0, [r0] ldr r0, [r0] | ldr r0, =x ldr r0, [r0] ldr r0, [r0] ldr r0, [r0] | ldr r1, =x ldr r1, [r1] ldr r1, [r1] str r0, [r1]
stderr | ldr r0, =stderr | ldr r0, =stderr ldr r0, [r0] | <do not write unless you really know what you are doing>
.Lstr | ldr r0, =.Lstr | ldr r0, =.Lstr ldrb r0, [r0] | <read only>
.section .rodata
.Lstr: .string "HI\n"
stdin, stdout and stderr are global variables
x

## Slide 35: Assembler Directives: Label Scope Control (Normal Labels only)
.extern <label>
  Imports label (function name, symbol or a static variable name);
  An address associated with the label from another file can be used by code in this file
.global <label>
  Exports label (or symbol) to be visible outside the source file boundary (other assembly or c source)
  label is either a function name or a global variable name
  Only use with function names or static variables
Without .global, labels are usually (depends on the assembler) local to the file
.extern printf
.extern fgets
.extern strcpy
.global fbuf
x

## Slide 36: Passing global variables as a parameter: fprintf()
r0 = function(r0, r1, r2, r3)
fprintf(stderr, "arg2", arg3, arg4)
create a literal string for arg2 which tells fprintf() how to interpret the remaining arguments
stdin, stdout, stderr are all global variable and are part of libc
  these names are their lside (label names)
  get their contents and pass that to fprintf(), fread(), fwrite()
.extern fprintf //declare fprintf
.section .rodata // note the dots "."
.Lfst: .string "c=%d\n"
// part of the text segment below
mov r2, 2 // int a = 2;
mov r3, 3 // int b = 3;
add r2, r2, r3 // arg 3: int c = a + b;
ldr r0, =stderr // get stderr address
ldr r0, [r0] // arg 1: get stderr contents
ldr r1, =.Lfst // arg 2: =literal address
bl fprintf
#include <stdio.h>
#include <stdlib.h>
int
main(void)
{
int a = 2;
int b = 3;
int c;
c = a + b;
fprintf(stderr,"c=%d\n", c);
return EXIT_SUCCESS;
}
three passed args in this use of fprintf
x
We are going to put these variables in temporary registers
r0, r1, r2

## Slide 37: Example: using preserved registers for local variables
.extern getchar
.extern putchar
.section .rodata
.Lst: .string "Echo count: %d\n"
.text
.type main, %function
.global main
.equ EOF, -1 .equ FP_OFF, 12
.equ EXIT_SUCCESS, 0
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
mov r4, 0 //r4 = count
/* while loop code will go here */
mov r0, EXIT_SUCCESS
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size main, (. – main)
#include <stdio.h>
#include <stdlib.h>
int
main(void)
{
int c; // use r0
int count = 0; // use r4
while ((c = getchar()) != EOF) {
putchar(c);
count++;
}
printf("Echo count: %d\n", count);
return EXIT_SUCCESS;
}
r0 r1
x
You must assume that
both getchar() and
putchar() alter r0-r3
r0
r0
Push two registers to keep stack 8-byte aligned (sp % 8 == 0)

## Slide 38: Putchar/getchar: The while loop
mov r4, 0 //count
bl getchar
cmp r0, EOF
beq .Ldone
.Lloop:
bl putchar
bl getchar
add r4, r4, 1
cmp r0, EOF
bne .Lloop
.Ldone:
mov r1, r4 //arg2
ldr r0, =.Lst //arg1
bl printf
#include <stdio.h>
#include <stdlib.h>
int
main(void)
{
int c;
int count = 0;
while ((c = getchar()) != EOF) {
putchar(c);
count++;
}
printf("Echo count: %d\n", count);
return EXIT_SUCCESS;
}
pre loop test with a call to getchar()
if it returns EOF in r0 we are done
File header and footers are not shown
echo the character read with getchar and then read another and increment count
initialize count
did getchar() return EOF if not loop
saw EOF, print count
x
address of string literal variable
.Lst: .string "Echo count: %d\n"

## Slide 39: Accessing Pointers (argv) in ARM assembly
.extern printf
.extern stderr
.section .rodata
.Lstr: .string "argv[%d] = %s\n"
.text
.global main // main(r0=argc, r1=argv)
.type main, %function
.equ FP_OFF, 20
main:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF
mov r7, r1 // save argv!
ldr r4, =stderr // get the address of stderr
ldr r4, [r4] // get the contents of stderr
ldr r5, =.Lstr // get the address of .Lstr
mov r6, 0 // set indx = 0;
// see next slide
.Ldone:
mov r0, 0
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
argc
**argv
Registers
argv[0]
./cipher
in/book
-b
-e
r7
r6
r5
r4
r3
r2
r1
r0
% ./cipher -e -b in/BOOK
argv[0] = ./cipher
argv[1] = -e
argv[2] = -b
argv[3] = in/BOOK
file * stderr
indx
"argv[%d] = %s\n"
fprintf(stderr, "argv[%d] = %s\n", indx, *argv);
argv[1]
argv[2]
argv[3]
NULL
need to save r1 as we are calling a function - fprintf
r0-r3 lost due to fprintf call
x

## Slide 40: Accessing Pointers (argv) in ARM assembly
.Lloop:
// fprintf(stderr, "argv[%d] = %s\n", indx, *argv)
ldr r3, [r7] // arg 4: *argv
cmp r3, 0 // check *argv == NULL
beq .Ldone // if so done
mov r2, r6 // arg 3: indx
mov r1, r5 // arg 2: "argv[%d] = %s\n"
mov r0, r4 // arg 1: stderr
bl fprintf
add r6, r6, 1 // indx++ for printing
add r7, r7, 4 // argv++ pointer
b .Lloop
.Ldone:
argc
**argv
Registers
argv[0]
./cipher
in/book
-b
-e
r7
r6
r5
r4
r3
r2
r1
r0
% ./cipher -e -b in/BOOK
argv[0] = ./cipher
argv[1] = -e
argv[2] = -b
argv[3] = in/BOOK
file * stderr
indx
"argv[%d] = %s\n"
argv[1]
argv[2]
argv[3]
NULL
observe the different increment sizes
r0-r3 lost due to fprintf call
x

## Slide 41: Allocating Space For Locals on the Stack
Space for local variables is allocated on the stack right below the lowest pushed register
  Move the sp towards low memory by the total size of all local variables in bytes plus padding
FRMADD = total local var space (bytes) + padding
Allocate the space after the register push by
  add sp, sp, -FRMADD
Requirement: on function entry, sp is always 8-byte aligned
  sp % 8 == 0
Padding (as required):
  Additional space between variables on the stack to meet memory alignment requirements
  Additional space so the frame size is evenly divisible by 8
fp (frame pointer) is used as a pointer (base register) to access all stack variables – later slides
sp
lr to caller
callers fp
fp
local
variables
sp = sp - local space
FP_OFF
x
saved register
saved register
FRMADD=
Local Space (bytes)
Total size % 8 == 0
grows down

## Slide 42: Review Variables: Size
Integer types
  char (unspecified default)
  int (signed default)
Floating Point
  float, double
Optional Modifiers for each base type
  short [int]
  long [int, double]
  signed [char, int]
  unsigned [char, int]
  const: variable read only
char type
  One byte in a byte addressable memory
  Be careful char is unsigned on arm and signed on other HW like intel
C Data Type | AArch-32 contiguous Bytes | printf specification
unsigned char | 1 | %c
signed char | 1 | %c
short int | 2 | %hd
unsigned short int | 2 | %hu
int | 4 | %d / %i
unsigned int | 4 | %u
long int | 4 | %ld
long long int | 8 | %lld
float | 4 | %f
double | 8 | %lf
long double | 8 | %Lf
pointer * | 4 | %p
x

## Slide 43: Local Variables on the stack
Add space on the stack for each local
  we will allocate space in same order the locals are listed the C function shown from high to low stack address
  gcc compiler allocates from low to high stack addresses
  Order does not matter for our use
int main(void)
{
int c;
int count = 0;
// rest of code
}
lr to caller
callers fp
saved r5
saved r4
after push {r4-r5,fp,lr}
add fp, sp, FP_OFF
fp
FRMADD = 8
count
sp after push
c
sp after
allocating locals
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 8
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
In this example we are allocating two variables on the stack
When writing assembly functions, in many situations you may choose allocate these to registers instead
x
// when FRMADD values fail to assemble
ldr r3, =-FRMADD
add sp, sp, r3

## Slide 44: Accessing Stack Variables: Introduction
To Access data stored in the stack
  use the ldr/str instructions
Use register fp with offset (distance in bytes) addressing (use either register offset or immediate offset)
No matter what address the stack frame is at, fp always points at saved lr, so you can find a local stack variable by using an offset address from the contents of fp
x
Variable | distance from fp | Read variable | Write Variable
int c | -16 | ldr r0, [fp, -16] | str r0, [fp, -16]
int count | -20 | ldr r0, [fp, -20] | str r0, [fp, -20]
low memory 4-byte words
lr to caller
callers fp
saved r5
saved r4
fp
count
c
sp
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 8
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
4
4
fp - 16
fp - 20
int main(void)
{
int c;
int count = 0;
// rest of code
}
Total frame size
24 bytes
8-byte aligned
FRMADD
FP_OFF
12
4

## Slide 45: Stack Frame Design – Local Variables
When writing an ARM equivalent for a C program, for CSE30 we will not re-arrange the order of the variables to optimize space (covered in the compiler course)
Arrays start at a 4-byte boundary (even arrays with only 1 element)
  Exception: double arrays [ ] start at an 8-byte boundary
  struct arrays are aligned to the requirements of largest member
Single chars (and shorts) can be grouped together in same 4-byte word (following the alignment for the short)
Padding may be required (see next slide)
x
A
B
C
D
E
0
pointer
int
a[0]
a[1]
1
2 bytes
pointers and integers
short
char
4 bytes
4
Rule: When the function is entered the stack is already 8-byte aligned
4
4
4
4

## Slide 46: Stack Variables: Padding
Variable padding – start arrays at 4-byte boundary and leave unused space at end (high side address) before the variable higher on the stack
Frame padding – add space below the last local variable to keep 8-byte alignment
x
lr to caller
callers fp
saved r5
saved r4
fp
sp
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 16
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
4
4
fp - 16
fp - 20
int main(void)
{
int c;
int count = 0;
char buf[] = "hi";
// rest of code
}
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
buf[2]
buf[1]
buf[0]
var pad
count
sp
buf
var pad
frame pad
count
c

## Slide 47: Accessing Stack Variables, the hard way
Calculating offsets is a lot of work to get it correct
It is also hard to debug
There is a better way!
x
Variable | distance from fp | Read variable | Write Variable
int c | 16 | ldr r0, [fp, -16] | str r0, [fp, -16]
int count | 20 | ldr r0, [fp, -20] | str r0, [fp, -20]
char buf[0] | 24 | ldrb r0, [fp, -24] | strb r0, [fp, -24]
char buf[1] | 23 | ldrb r0, [fp, -23] | strb r0, [fp, -23]
char buf[2] | 22 | ldrb r0, [fp, -22] | strb r0, [fp, -22]
lr to caller
callers fp
saved r5
saved r4
fp
sp
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 16
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
4
4
fp - 16
fp - 20
int main(void)
{
int c;
int count = 0;
char buf[] = "hi";
// rest of code
}
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
char buf[ ] by usage with ASCII chars we will use strb (or make it unsigned char)
count
c
buf[2]
buf[1]
buf[0]
var pad
fp - 24
fp - 23
fp - 22
fp - 21
increasing address

## Slide 48: Best Practice: Assembler Generated FP Distance Table
For each stack variable create a .equ symbol whose value is the distance in bytes from the FP after the prologue
After the last variable add a name PAD for the size of the frame padding (if any). if no padding, PAD will be set to the same value as the variable above it
The value of the symbol is an expression that calculates the distance from the FP based on the distance of the variable above it on the stack. The first variable will use SP_OFF as the starting distance
  .equ VAR, size_of var + variable_padding + previous_var_symbol // previous_var_symbol distance of the var above
Calculate the size of the local variable area that needs to be added to the sp in bytes
  FRMADD = distance PAD minus distance of the SP to the FP (FP_OFF) after the prologue push
x
lr to caller
callers fp
saved r5
saved r4
fp
sp
4
4
fp - 16
fp - 20
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
count
c
.type main, %function
.global main
.equ FP_OFF, 12
.equ C, 4 + FP_OFF
.equ COUNT, 4 + C
.equ BUF, 4 + COUNT
.equ PAD, 4 + BUF
.equ FRMADD, PAD – FP_OFF
// FRMADD = 28 - 12 = 16
variable size in bytes
Prior allocation distance
pushed reg fp distance
FP Distance Table one For each function

## Slide 49: Best Practice: Assembler Generated FP Distance Table
x
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int c | C | add r0, fp, -C | ldr r0, [fp, -C] | str r0, [fp, -C]
int count | COUNT | add r0, fp, -COUNT | ldr r0, [fp, -COUNT] | str r0, [fp, -COUNT]
char buf[0] | BUF | add r0, fp, -BUF | ldrb r0, [fp, -BUF] | strb r0, [fp, -BUF]
char buf[1] | BUF-1 | add r0, fp, -BUF+1 | ldrb r0, [fp, -BUF+1] | strb r0, [fp, -BUF+1]
char buf[2] | BUF-2 | add r0, fp, -BUF+2 | ldrb r0, [fp, -BUF+2] | strb r0, [fp, -BUF+2]
lr to caller
callers fp
saved r5
saved r4
fp
sp
.type main, %function
.global main
.equ FP_OFF, 12
.equ C, 4 + FP_OFF
.equ COUNT, 4 + C
.equ BUF, 4 + COUNT
.equ PAD, 4 + BUF
.equ FRMADD, PAD – FP_OFF
// FRMADD = 28 - 12 = 16
4
4
fp - 16
fp - 20
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
buf[2]
buf[1]
buf[0]
var pad
fp -BUF
fp –BUF+1
fp –BUF+2
fp –BUF+3
count
c
increasing address
FP Distance Table For each function

## Slide 50: Initializing and Accessing Stack variables
x
lr to caller
callers fp
saved r5
saved r4
fp
count
c
sp
4
4
fp - 16
fp - 20
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
./a.out
-136572160 0 hi
int main(int argc, char **argv)
{
int c;
int count = 0;
char buf[] = "hi";
printf("%d %d %s\n", c, count, buf);
// rest of code
pass stack address
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// nothing to do for C
mov r2, 0
str r2, [fp, -COUNT]
strb r2, [fp, -BUF+2]
mov r2, 'h'
strb r2, [fp, -BUF]
mov r2, 'i'
strb r2, [fp, -BUF+1]
ldr r0, =.Lmess // arg1
ldr r1, [fp, -C] // arg2
ldr r2, [fp, -COUNT] // arg3
add r3, fp, -BUF // arg4
bl printf
passes address of a stack variable buf
passes contents of stack var C and COUNT
.section .rodata
.Lmess: .string "%d %d %s\n"
.extern printf
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int c | C | add r0, fp, -C | ldr r0, [fp, -C] | str r0, [fp, -C]
int count | COUNT | add r0, fp, -COUNT | ldr r0, [fp, -COUNT] | str r0, [fp, -COUNT]
char buf[0] | BUF | add r0, fp, -BUF | ldrb r0, [fp, -BUF] | strb r0, [fp, -BUF]
char buf[1] | BUF-1 | add r0, fp, -BUF+1 | ldrb r0, [fp, -BUF+1] | strb r0, [fp, -BUF+1]
char buf[2] | BUF-2 | add r0, fp, -BUF+2 | ldrb r0, [fp, -BUF+2] | strb r0, [fp, -BUF+2]

## Slide 51: Stack Frame Design Practice
Write the variables in C
Draw a picture of the stack frame
Write the code to generate the offsets
create the distance table to the variables
.equ FP_OFF, 12
.equ C, 1 + FP_OFF
.equ S, 3 + C
.equ B, 8 + S
.equ PTR, 4 + B
.equ PAD, 0 + PTR
.equ FRMADD, PAD – FP_OFF
// FRMADD = 28 - 12 = 16
void func(void)
{
signed char c;
signed short s;
unsigned char b[] = "Stack";
unsigned char *ptr = &b;
// rest of code
}
lr to caller
callers fp
saved r5
saved r4
12
4
s
var pad
C
1, 1+2
var pad
var pad
b[5]
b[4]
b[3]
b[2]
b[1]
b[0]
2 + 6
x
Variable | distance from fp | Address on Stack | Read variable | Write Variable
signed char c | C | add r0, fp, -C | ldrsb r0, [fp, -C] | strsb r0, [fp, -C]
signed short s | S | add r0, fp, -S | ldrsh r0, [fp, -S] | strsh r0, [fp, -S]
unsigned char b[0] | B | add r0, fp, -B | ldrb r0, [fp, -B] | strb r0, [fp, -B]
unsigned char *ptr | PTR | add r0, fp, -PTR | ldr r0, [fp, -PTR] | str r0, [fp, -PTR]
fp
*ptr
4
FRMADD = 16
fame PAD
0
sp
Total frame size
8-byte aligned
Alternative design
s
var pad
C
1+1,2
.equ FP_OFF, 12
.equ C, 2 + FP_OFF
.equ S, 2 + C
…

## Slide 52: Working with Pointers on the stack
int sum(int j, int k)
{
return j + k;
}
void testp(int j, int k, int (*func)(int, int), int *i)
{
*i = func(j,k);
return;
}
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
Output Parameters (like i) you pass a pointer to them, must be on the stack!

## Slide 53: Working with Pointers on the stack
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
.section .rodata
.Lmess: .string "%d\n"
.extern printf
.text
.global main
.type main, %function
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ FRMADD, PAD-FP_OFF
// FRMADD = 12 - 4 = 8
x
lr to caller
callers fp
4
4
i
4
(*pf)()
4
fp
sp
frame pad
0
FRMADD
Total frame size
8-byte aligned

## Slide 54: Working with Pointers on the stack
int main()
{
int i;
int (*pf)(int, int) = sum;
testp(1, 2, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
main:
push {fp, lr}
add fp, sp, FP_OFF
add sp, sp,-FRMADD
ldr r2, =sum // func address
add r1, fp, -PF // PF address
str r2, [r1] // store in pf
mov r0, 1 // arg 1: 1
mov r1, 2 // arg 2: 2
ldr r2, [fp, -PF] // arg 3: (*pf)()
add r3, fp, -I // arg 4: &I
bl testp
ldr r0, =.Lmess // arg 1: "%d\n"
ldr r1, [fp, -I] // arg 2: I
bl printf
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
x
.section .rodata
.Lmess: .string "%d\n"
.extern printf
.text
.global main
.type main, %function
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ FRMADD, PAD-FP_OFF
// FRMADD = 12 - 4 = 8
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
lr to caller
callers fp
4
4
i
4
(*pf)()
4
fp
sp
frame pad
0
FRMADD
I is Output Parameter

## Slide 55: Working with Pointers on the stack
void
testp(int j, int k, int (*func)(int, int), int *i)
{
*i = func(j, k);
return;
}
.global testp
.type testp, %function
.equ FP_OFF, 12
testp:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
mov r4, r3 // save i
blx r2 // r0=func(r0,r1)
str r0, [r4] // *i =r0
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size testp, (. - testp)
r0,r1,r2 already set
x
lr to caller
callers fp
i
(*pf)()
fp
sp
frame pad
lr to main
main's fp
testp()
stack
main()
stack

## Slide 56: Working with Pointers on the stack
int
sum(int j, int k)
{
return j + k;
}
.global sum
.type sum, %function
.equ FP_OFF, 4
sum:
push {fp, lr}
add fp, sp, FP_OFF
add r0, r0, r1
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
.size sum, (. - sum)
x
lr to caller
callers fp
i
(*pf)()
frame pad
lr to main
main's fp
fp
sp
lr to testp
testp fp
testp()
stack
main()
stack
sum()
stack

## Slide 57: Passing More Than Four Arguments – At the point of Call
Approach: Increase stack frame size to include space for args# > 4
  Arg5 and above are in caller's stack frame at the bottom of the stack
Arg5 is always at the bottom (at sp), arg6 and greater are above it
One arg value per slot! – NO arrays across multiple slots
  chars, shorts and ints are directly stored
  Structs (not always), and arrays (always) are passed via a pointer
Output parameters contain an address that points at the stack, BSS, data, or heap
Prior to any function call (and obviously at the start of the called function):
  sp must point at arg5
  sp and therefore arg5 must be at an 8-byte boundary,
  Add padding to force arg5 alignment if needed is placed above the last argument the called function is expecting
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
x
arg 5
sp
lr to caller
callers fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
arg1 – arg4 Registers
fp
….
calling functions stack frame
Stack segment
high memory
saved regs
local
variables
PAD (if needed)
Outgoing arg space part of calling functions frame

## Slide 58: Passing More Than Four Arguments – At the point of Call
Called functions have the right to change stack args just like they can change the register args!
  Caller must always assume all args including ones on the stack are changed by the caller
Calling function prior to making the call you must
  Evaluate first four args: place the resulting values in r0-r3
  Evaluate Arg 5 and greater and place the resulting values on the stack
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
x
arg 5
sp
lr to caller
callers fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
arg1 – arg4 Registers
fp
….
calling functions stack frame
Stack segment
high memory
saved regs
local
variables
PAD (if needed)
Outgoing arg space part of calling functions frame

## Slide 59: Passing More Than Four Arguments – At the point of Call
Approach: Extend the stack frame to include enough space for stack arguments for the called function that has the greatest number of args
  Examine every function call in the body of a function
  Find the function call with greatest arg count, this determines space needed for outgoing args
  Add the greatest arg count space as needed to the frame layout
  Adjust PAD as required to keep the sp 8-byte aligned
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
x
arg 5
sp
lr to caller
callers fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
arg1 – arg4 Registers
fp
….
calling functions stack frame
Stack segment
high memory
saved regs
local
variables
PAD (if needed)
Outgoing arg space part of calling functions frame

## Slide 60: Determining Size of the Passed Parameter Area on The Stack
Find the function called by main with the largest number of parameters
That function determines the size of the Passed Parameter allocation on the stack
int main(void)
{
/* code not shown */
a(g, h);
/* code not shown */
sixsum(a1, a2, a3, a4, a5, a6);
/* code not shown */
b(q, w, e, r);
/* code not shown */
}
largest arg count is 6
allocate space for 6 - 4 = 2 arg slots
x

## Slide 61: Calling Function Stack Frame: Pass ARG 5 and higher
oarg5
sp
oarg6
Frame PAD
lr to caller
callers fp
fp
Rules: At point of call
OARG5 must be pointed at by sp
SP must be 8-byte aligned at function call
x
Previous stack frame
.equ FP_OFF, 4
.equ CNT, 4 + FP_OFF // int cnt
.equ PAD, 4 + CNT // added as needed
.equ OARG6, 4 + PAD // 4 bytes
.equ OARG5, 4 + OARG6 // 4 bytes
.equ FRMADD OARG5 – FP_OFF
// FRMADD = 20 - 4 = 16
int cnt;
r0 = func(r0, r1, r2, r3, OARG5, OARG6);
cnt
4
FRMADD
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int cnt | CNT | add r0, fp, -CNT | ldr r0, [fp, -CNT] | str r0, [fp, -CNT]
int oarg6 | OARG6 | add r0, fp, -OARG6 | ldr r0, [fp, -OARG6] | str r0, [fp, -OARG6]
int oarg5 | OARG5 | add r0, fp, -OARG5 | ldr r0, [fp, -OARG5] | str r0, [fp, -OARG5]
4
4
4
4
4
OARG5
OARG6
CNT
Total frame size
8-byte aligned

## Slide 62: Called Function: Retrieving Args From the Stack
At function start and before the push{} the sp is at an 8-byte boundary
Args > 4 in caller's stack frame and arg 5 always starts at fp+4
  Additional args are higher up the stack, with one “slot” every 4-bytes
This "algorithm" for finding args was designed to enable variable arg count functions like printf("conversion list", arg0, … argn);
No limit to the number of args (except running out of stack space)
r0 = func(r0, r1, r2, r3, ARG5, ARG6);
x
.equ ARGN, (N-4)*4 // where n must be > 4
oarg5
sp
oarg6
Frame PAD
lr to callers
callers fp
cnt
fp
Previous stack frame
lr to caller
callers fp
indx
c
fp-8
fp-12
fp+4
fp+8
Rule:
Called functions always access stack args using a positive offset to the fp
calling functions stack frame
called functions stack frame

## Slide 63: Called Function: Retrieving Args From the Stack
r0 = func(r0, r1, r2, r3, r4, ARG5, ARG6);
x
.equ FP_OFF, 4
.equ C, 4 + FP_OFF
.equ INDX, 4 + C
.equ PAD, 0 + INDX
.equ FRMADD, PAD – FP_OFF
// below are distances into the caller's stack frame
.equ ARG6, 8
.equ ARG5, 4
Variable or Argument | distance from fp | Address on Stack | Read variable | Write Variable
int arg6 | ARG6 | add r0, fp, ARG6 | ldr r0, [fp, ARG6] | str r0, [fp, ARG6]
int arg5 | ARG5 | add r0, fp, ARG5 | ldr r0, [fp, ARG5] | str r0, [fp, ARG5]
int c | C | add r0, fp, -C | ldr r0, [fp, -C] | str r0, [fp, -C]
int count | INDX | add r0, fp, -INDX | ldr r0, [fp, -INDX] | str r0, [fp, -INDX]
oarg5
sp
oarg6
Frame PAD
lr to caller
callers fp
cnt
fp
lr to callers
callers fp
indx
c
Rule:
Called functions always access stack args using a positive offset to the fp
calling functions stack frame
called functions stack frame
Observe the positive offsets
ARG5
ARG6
C
INDX
Frame PAD

## Slide 64: Example: Passing Stack Args, Calling Function
int sum(int j, int k)
{
return j + k;
}
void
testp(int j, int k, int l, int m, int (*func)(int, int), int *i)
{
*i = func(j,k) + func(l, m); // notice two func() calls
return;
}
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, 3, 4, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
arg1 arg2 arg3 arg4 arg5 arg6

## Slide 65: Example: Passing Stack Args, Calling Function
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, 3, 4, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ OARG6, 4 + PAD
.equ OARG5 4 + OARG6
.equ FRMADD, OARG5 - FP_OFF
// FRMADD = 20 - 4 = 16
oarg5
sp
oarg6
fp
FRMADD = 16
4
4
lr to caller
callers fp
i
4
(*pf)()
4
frame pad
0
4
4
Main() stack
Variable or Argument | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
int oarg6 | OARG6 | add r0, fp, -OARG6 | ldr r0, [fp, -OARG6] | str r0, [fp, -OARG6]
int oarg5 | OARG5 | add r0, fp, -OARG5 | ldr r0, [fp, -OARG5] | str r0, [fp, -OARG5]
Total frame size
8-byte aligned

## Slide 66: Example: Passing Stack Args, Calling Function
int main()
{
int i;
int (*pf)(int, int) = sum;
testp(1, 2, 3, 4, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
Variable or Argument | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
int oarg6 | OARG6 | add r0, fp, -OARG6 | ldr r0, [fp, -OARG6] | str r0, [fp, -OARG6]
int oarg5 | OARG5 | add r0, fp, -OARG5 | ldr r0, [fp, -OARG5] | str r0, [fp, -OARG5]
main:
push {fp, lr}
add fp, sp, FP_OFF
add sp, sp,-FRMADD
ldr r0, =sum // get func address
add r1, fp, -PF // PF address on stack
str r0, [r1] // store sum in var pf
add r0, fp, -I // get address of I
add r1, fp, -OARG6 // address of OARG6
str r0, [r1] // arg 6: store address of I
ldr r0, [fp, -PF] // get PF from stack
add r1, fp, -OARG5 // address of OARG5
str r0, [r1] // arg 5: store sum() address
mov r0, 1 // arg 1: 1
mov r1, 2 // arg 2: 2
mov r2, 3 // arg 3: 3
mov r3, 4 // arg 4: 4
bl testp
ldr r0, =.Lmess // arg 1: "%d\n"
ldr r1, [fp, -I] // arg 2: i
bl printf
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ OARG6, 4 + PAD
.equ OARG5 4 + OARG6
.equ FRMADD, OARG5 - FP_OFF
// FRMADD = 20 - 4 = 16
oarg5
sp
oarg6
fp
FRMADD = 16
4
4
lr to caller
callers fp
i
4
(*pf)()
4
frame pad
0
4
4
Total frame size
8-byte aligned

## Slide 67: Example: Passing Stack Args, Called Function
void
testp(int j, int k, int l, int m, int (*func)(int, int), int *i)
{
*i = func(j, k) + func(l, m);
return;
}
x
oarg5
sp
oarg6
fp
4
4
lr to caller
callers fp
i
(*pf)()
frame pad
testp()
stack
lr to main
main's fp
Argument | distance | Address on Stack | Read variable | Write Variable
int *i | ARG6 | add r0, fp, ARG6 | ldr r0, [fp, ARG6] | str r0, [fp, ARG6]
int (*pf)() | ARG5 | add r0, fp, ARG5 | ldr r0, [fp, ARG5] | str r0, [fp, ARG5]
.equ FP_OFF, 20
.equ ARG6, 8
.equ ARG5, 4
testp:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF
mov r4, r2 // save l
mov r5, r3 // save m
ldr r6, [fp, ARG5] // load func
ldr r7, [fp, ARG6] // load i
blx r6 // r0 = func(j, k)
mov r1, r5 // arg 2 saved m
mov r5, r0 // save func return value
mov r0, r4 // arg 1 saved l
blx r6 // r0 = func(l, m)
add r0, r0, r5 // func(l,m) + func(j,k)
str r0, [r7] // store sum to *i
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
main()
stack
arg1 arg2 arg3 arg4 arg5 arg6
short circuit: make this call first

## Slide 68: Extra Slides

## Slide 69: By following the saved fp, you can find each stack frame
How gdb finds stack frames
sp
fp
saved lr
callers fp
main()
sp
fp
saved lr
callers fp
main()
lr to main()
main() fp
funcA()
sp
fp
saved lr
callers fp
main()
lr to funcC()
funcC() fp
funcD()
lr to funcB()
FuncB() fp
funcC()
lr to funcA()
funcA() fp
funcB()
lr to main()
main() fp
funcA()
saved lr
callers fp
main()
lr to funcA()
funcA() fp
funcB()
lr to main()
main() fp
funcA()
sp
fp
sp
fp
saved lr
callers fp
main()
lr to funcB()
FuncB() fp
funcC()
lr to funcA()
funcA() fp
funcB()
lr to main()
main() fp
funcA()
x