## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 2.12
Lecture - 18

## Slide 3: Allocating Space For Locals on the Stack
Space for local variables is allocated on the stack right below the lowest pushed register
  Move the sp towards low memory by the total size of all local variables in bytes plus padding
FRMADD = total local var space (bytes) + padding
Allocate the space after the register push by
  add sp, sp, -FRMADD
Requirement: on function entry, sp is always 8-byte aligned
  sp % 8 == 0
Padding (as required):
  Additional space between variables on the stack to meet memory alignment requirements
  Additional space so the frame size is evenly divisible by 8
fp (frame pointer) is used as a pointer (base register) to access all stack variables – later slides
sp
lr to caller
callers fp
fp
local
variables
sp = sp - local space
FP_OFF
x
saved register
saved register
FRMADD=
Local Space (bytes)
Total size % 8 == 0
grows down

## Slide 4: Review Variables: Size
Integer types
  char (unspecified default)
  int (signed default)
Floating Point
  float, double
Optional Modifiers for each base type
  short [int]
  long [int, double]
  signed [char, int]
  unsigned [char, int]
  const: variable read only
char type
  One byte in a byte addressable memory
  Be careful char is unsigned on arm and signed on other HW like intel
C Data Type | AArch-32 contiguous Bytes | printf specification
unsigned char | 1 | %c
signed char | 1 | %c
short int | 2 | %hd
unsigned short int | 2 | %hu
int | 4 | %d / %i
unsigned int | 4 | %u
long int | 4 | %ld
long long int | 8 | %lld
float | 4 | %f
double | 8 | %lf
long double | 8 | %Lf
pointer * | 4 | %p
x

## Slide 5: Local Variables on the stack
Add space on the stack for each local
  we will allocate space in same order the locals are listed the C function shown from high to low stack address
  gcc compiler allocates from low to high stack addresses
  Order does not matter for our use
int main(void)
{
int c;
int count = 0;
// rest of code
}
lr to caller
callers fp
saved r5
saved r4
after push {r4-r5,fp,lr}
add fp, sp, FP_OFF
fp
FRMADD = 8
count
sp after push
c
sp after
allocating locals
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 8
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
In this example we are allocating two variables on the stack
When writing assembly functions, in many situations you may choose allocate these to registers instead
x
// when FRMADD values fail to assemble
ldr r3, =-FRMADD
add sp, sp, r3

## Slide 6: Accessing Stack Variables: Introduction
To Access data stored in the stack
  use the ldr/str instructions
Use register fp with offset (distance in bytes) addressing (use either register offset or immediate offset)
No matter what address the stack frame is at, fp always points at saved lr, so you can find a local stack variable by using an offset address from the contents of fp
x
Variable | distance from fp | Read variable | Write Variable
int c | -16 | ldr r0, [fp, -16] | str r0, [fp, -16]
int count | -20 | ldr r0, [fp, -20] | str r0, [fp, -20]
low memory 4-byte words
lr to caller
callers fp
saved r5
saved r4
fp
count
c
sp
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 8
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
4
4
fp - 16
fp - 20
int main(void)
{
int c;
int count = 0;
// rest of code
}
Total frame size
24 bytes
8-byte aligned
FRMADD
FP_OFF
12
4

## Slide 7: Stack Frame Design – Local Variables
When writing an ARM equivalent for a C program, for CSE30 we will not re-arrange the order of the variables to optimize space (covered in the compiler course)
Arrays start at a 4-byte boundary (even arrays with only 1 element)
  Exception: double arrays [ ] start at an 8-byte boundary
  struct arrays are aligned to the requirements of largest member
Single chars (and shorts) can be grouped together in same 4-byte word (following the alignment for the short)
Padding may be required (see next slide)
x
A
B
C
D
E
0
pointer
int
a[0]
a[1]
1
2 bytes
pointers and integers
short
char
4 bytes
4
Rule: When the function is entered the stack is already 8-byte aligned
4
4
4
4

## Slide 8: Stack Variables: Padding
Variable padding – start arrays at 4-byte boundary and leave unused space at end (high side address) before the variable higher on the stack
Frame padding – add space below the last local variable to keep 8-byte alignment
x
lr to caller
callers fp
saved r5
saved r4
fp
sp
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 16
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
4
4
fp - 16
fp - 20
int main(void)
{
int c;
int count = 0;
char buf[] = "hi";
// rest of code
}
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
buf[2]
buf[1]
buf[0]
var pad
count
sp
buf
var pad
frame pad
count
c

## Slide 9: Accessing Stack Variables, the hard way
Calculating offsets is a lot of work to get it correct
It is also hard to debug
There is a better way!
x
Variable | distance from fp | Read variable | Write Variable
int c | 16 | ldr r0, [fp, -16] | str r0, [fp, -16]
int count | 20 | ldr r0, [fp, -20] | str r0, [fp, -20]
char buf[0] | 24 | ldrb r0, [fp, -24] | strb r0, [fp, -24]
char buf[1] | 23 | ldrb r0, [fp, -23] | strb r0, [fp, -23]
char buf[2] | 22 | ldrb r0, [fp, -22] | strb r0, [fp, -22]
lr to caller
callers fp
saved r5
saved r4
fp
sp
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 16
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
4
4
fp - 16
fp - 20
int main(void)
{
int c;
int count = 0;
char buf[] = "hi";
// rest of code
}
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
char buf[ ] by usage with ASCII chars we will use strb (or make it unsigned char)
count
c
buf[2]
buf[1]
buf[0]
var pad
fp - 24
fp - 23
fp - 22
fp - 21
increasing address

## Slide 10: Best Practice: Assembler Generated FP Distance Table
For each stack variable create a .equ symbol whose value is the distance in bytes from the FP after the prologue
After the last variable add a name PAD for the size of the frame padding (if any). if no padding, PAD will be set to the same value as the variable above it
The value of the symbol is an expression that calculates the distance from the FP based on the distance of the variable above it on the stack. The first variable will use SP_OFF as the starting distance
  .equ VAR, size_of var + variable_padding + previous_var_symbol // previous_var_symbol distance of the var above
Calculate the size of the local variable area that needs to be added to the sp in bytes
  FRMADD = distance PAD minus distance of the SP to the FP (FP_OFF) after the prologue push
x
lr to caller
callers fp
saved r5
saved r4
fp
sp
4
4
fp - 16
fp - 20
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
count
c
.type main, %function
.global main
.equ FP_OFF, 12
.equ C, 4 + FP_OFF
.equ COUNT, 4 + C
.equ BUF, 4 + COUNT
.equ PAD, 4 + BUF
.equ FRMADD, PAD – FP_OFF
// FRMADD = 28 - 12 = 16
variable size in bytes
Prior allocation distance
pushed reg fp distance
FP Distance Table one For each function

## Slide 11: Best Practice: Assembler Generated FP Distance Table
x
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int c | C | add r0, fp, -C | ldr r0, [fp, -C] | str r0, [fp, -C]
int count | COUNT | add r0, fp, -COUNT | ldr r0, [fp, -COUNT] | str r0, [fp, -COUNT]
char buf[0] | BUF | add r0, fp, -BUF | ldrb r0, [fp, -BUF] | strb r0, [fp, -BUF]
char buf[1] | BUF-1 | add r0, fp, -BUF+1 | ldrb r0, [fp, -BUF+1] | strb r0, [fp, -BUF+1]
char buf[2] | BUF-2 | add r0, fp, -BUF+2 | ldrb r0, [fp, -BUF+2] | strb r0, [fp, -BUF+2]
lr to caller
callers fp
saved r5
saved r4
fp
sp
.type main, %function
.global main
.equ FP_OFF, 12
.equ C, 4 + FP_OFF
.equ COUNT, 4 + C
.equ BUF, 4 + COUNT
.equ PAD, 4 + BUF
.equ FRMADD, PAD – FP_OFF
// FRMADD = 28 - 12 = 16
4
4
fp - 16
fp - 20
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
buf[2]
buf[1]
buf[0]
var pad
fp -BUF
fp –BUF+1
fp –BUF+2
fp –BUF+3
count
c
increasing address
FP Distance Table For each function

## Slide 12: Initializing and Accessing Stack variables
x
lr to caller
callers fp
saved r5
saved r4
fp
count
c
sp
4
4
fp - 16
fp - 20
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
./a.out
-136572160 0 hi
int main(int argc, char **argv)
{
int c;
int count = 0;
char buf[] = "hi";
printf("%d %d %s\n", c, count, buf);
// rest of code
pass stack address
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// nothing to do for C
mov r2, 0
str r2, [fp, -COUNT]
strb r2, [fp, -BUF+2]
mov r2, 'h'
strb r2, [fp, -BUF]
mov r2, 'i'
strb r2, [fp, -BUF+1]
ldr r0, =.Lmess // arg1
ldr r1, [fp, -C] // arg2
ldr r2, [fp, -COUNT] // arg3
add r3, fp, -BUF // arg4
bl printf
passes address of a stack variable buf
passes contents of stack var C and COUNT
.section .rodata
.Lmess: .string "%d %d %s\n"
.extern printf
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int c | C | add r0, fp, -C | ldr r0, [fp, -C] | str r0, [fp, -C]
int count | COUNT | add r0, fp, -COUNT | ldr r0, [fp, -COUNT] | str r0, [fp, -COUNT]
char buf[0] | BUF | add r0, fp, -BUF | ldrb r0, [fp, -BUF] | strb r0, [fp, -BUF]
char buf[1] | BUF-1 | add r0, fp, -BUF+1 | ldrb r0, [fp, -BUF+1] | strb r0, [fp, -BUF+1]
char buf[2] | BUF-2 | add r0, fp, -BUF+2 | ldrb r0, [fp, -BUF+2] | strb r0, [fp, -BUF+2]

## Slide 13: Stack Frame Design Practice
Write the variables in C
Draw a picture of the stack frame
Write the code to generate the offsets
create the distance table to the variables
.equ FP_OFF, 12
.equ C, 2 + FP_OFF
.equ S, 2 + C
.equ B, 8 + S
.equ PTR, 4 + B
.equ PAD, 0 + PTR
.equ FRMADD, PAD – FP_OFF
// FRMADD = 28 - 12 = 16
void func(void)
{
signed char c;
signed short s;
unsigned char b[] = "Stack";
unsigned char *ptr = &b;
// rest of code
}
lr to caller
callers fp
saved r5
saved r4
12
4
s
var pad
C
1+1, 2
var pad
var pad
b[5]
b[4]
b[3]
b[2]
b[1]
b[0]
2 + 6
x
Variable | distance from fp | Address on Stack | Read variable | Write Variable
signed char c | C | add r0, fp, -C | ldrsb r0, [fp, -C] | strsb r0, [fp, -C]
signed short s | S | add r0, fp, -S | ldrsh r0, [fp, -S] | strsh r0, [fp, -S]
unsigned char b[0] | B | add r0, fp, -B | ldrb r0, [fp, -B] | strb r0, [fp, -B]
unsigned char *ptr | PTR | add r0, fp, -PTR | ldr r0, [fp, -PTR] | str r0, [fp, -PTR]
fp
*ptr
4
FRMADD = 16
fame PAD
0
sp

## Slide 14: Working with Pointers on the stack
int sum(int j, int k)
{
return j + k;
}
void testp(int j, int k, int (*func)(int, int), int *i)
{
*i = func(j,k);
return;
}
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
Output Parameters (like i) you pass a pointer to them, must be on the stack!

## Slide 15: Working with Pointers on the stack
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
.section .rodata
.Lmess: .string "%d\n"
.extern printf
.text
.global main
.type main, %function
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ FRMADD, PAD-FP_OFF
// FRMADD = 12 - 4 = 8
x
lr to caller
callers fp
4
4
i
4
(*pf)()
4
fp
sp
frame pad
0
FRMADD

## Slide 16: Working with Pointers on the stack
int main()
{
int i;
int (*pf)(int, int) = sum;
testp(1, 2, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
main:
push {fp, lr}
add fp, sp, FP_OFF
add sp, sp,-FRMADD
ldr r2, =sum // func address
add r1, fp, -PF // PF address
str r2, [r1] // store in pf
mov r0, 1 // arg 1: 1
mov r1, 2 // arg 2: 2
ldr r2, [fp, -PF] // arg 3: (*pf)()
add r3, fp, -I // arg 4: &I
bl testp
ldr r0, =.Lmess // arg 1: "%d\n"
ldr r1, [fp, -I] // arg 2: I
bl printf
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
x
.section .rodata
.Lmess: .string "%d\n"
.extern printf
.text
.global main
.type main, %function
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ FRMADD, PAD-FP_OFF
// FRMADD = 12 - 4 = 8
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
lr to caller
callers fp
4
4
i
4
(*pf)()
4
fp
sp
frame pad
0
FRMADD
I is Output Parameter

## Slide 17: Working with Pointers on the stack
void
testp(int j, int k, int (*func)(int, int), int *i)
{
*i = func(j, k);
return;
}
.global testp
.type testp, %function
.equ FP_OFF, 12
testp:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
mov r4, r3 // save i
blx r2 // r0=func(r0,r1)
str r0, [r4] // *i =r0
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size testp, (. - testp)
r0,r1,r2 already set
x
lr to caller
callers fp
i
(*pf)()
fp
sp
frame pad
lr to main
main's fp
testp()
stack
main()
stack

## Slide 18: Working with Pointers on the stack
int
sum(int j, int k)
{
return j + k;
}
.global sum
.type sum, %function
.equ FP_OFF, 4
sum:
push {fp, lr}
add fp, sp, FP_OFF
add r0, r0, r1
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
.size sum, (. - sum)
x
lr to caller
callers fp
i
(*pf)()
frame pad
lr to main
main's fp
fp
sp
lr to testp
testp fp
testp()
stack
main()
stack
sum()
stack

## Slide 19: Passing More Than Four Arguments – At the point of Call
Approach: Increase stack frame size to include space for args# > 4
  Arg5 and above are in caller's stack frame at the bottom of the stack
Arg5 is always at the bottom (at sp), arg6 and greater are above it
One arg value per slot! – NO arrays across multiple slots
  chars, shorts and ints are directly stored
  Structs (not always), and arrays (always) are passed via a pointer
Output parameters contain an address that points at the stack, BSS, data, or heap
Prior to any function call (and obviously at the start of the called function):
  sp must point at arg5
  sp and therefore arg5 must be at an 8-byte boundary,
  Add padding to force arg5 alignment if needed is placed above the last argument the called function is expecting
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
x
arg 5
sp
lr to caller
callers fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
arg1 – arg4 Registers
fp
….
calling functions stack frame
Stack segment
high memory
saved regs
local
variables
PAD (if needed)
Outgoing arg space part of calling functions frame

## Slide 20: Passing More Than Four Arguments – At the point of Call
Called functions have the right to change stack args just like they can change the register args!
  Caller must always assume all args including ones on the stack are changed by the caller
Calling function prior to making the call you must
  Evaluate first four args: place the resulting values in r0-r3
  Evaluate Arg 5 and greater and place the resulting values on the stack
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
x
arg 5
sp
lr to caller
callers fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
arg1 – arg4 Registers
fp
….
calling functions stack frame
Stack segment
high memory
saved regs
local
variables
PAD (if needed)
Outgoing arg space part of calling functions frame

## Slide 21: Passing More Than Four Arguments – At the point of Call
Approach: Extend the stack frame to include enough space for stack arguments for the called function that has the greatest number of args
  Examine every function call in the body of a function
  Find the function call with greatest arg count, this determines space needed for outgoing args
  Add the greatest arg count space as needed to the frame layout
  Adjust PAD as required to keep the sp 8-byte aligned
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
x
arg 5
sp
lr to caller
callers fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
arg1 – arg4 Registers
fp
….
calling functions stack frame
Stack segment
high memory
saved regs
local
variables
PAD (if needed)
Outgoing arg space part of calling functions frame

## Slide 22: Determining Size of the Passed Parameter Area on The Stack
Find the function called by main with the largest number of parameters
That function determines the size of the Passed Parameter allocation on the stack
int main(void)
{
/* code not shown */
a(g, h);
/* code not shown */
sixsum(a1, a2, a3, a4, a5, a6);
/* code not shown */
b(q, w, e, r);
/* code not shown */
}
largest arg count is 6
allocate space for 6 - 4 = 2 arg slots
x

## Slide 23: Calling Function Stack Frame: Pass ARG 5 and higher
oarg5
sp
oarg6
Frame PAD
lr to caller
callers fp
fp
Rules: At point of call
OARG5 must be pointed at by sp
SP must be 8-byte aligned at function call
x
Previous stack frame
.equ FP_OFF, 4
.equ CNT, 4 + FP_OFF // int cnt
.equ PAD, 4 + CNT // added as needed
.equ OARG6, 4 + PAD // 4 bytes
.equ OARG5, 4 + OARG6 // 4 bytes
.equ FRMADD OARG5 – FP_OFF
// FRMADD = 20 - 4 = 16
int cnt;
r0 = func(r0, r1, r2, r3, OARG5, OARG6);
cnt
4
FRMADD
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int cnt | CNT | add r0, fp, -CNT | ldr r0, [fp, -CNT] | str r0, [fp, -CNT]
int oarg6 | OARG6 | add r0, fp, -OARG6 | ldr r0, [fp, -OARG6] | str r0, [fp, -OARG6]
int oarg5 | OARG5 | add r0, fp, -OARG5 | ldr r0, [fp, -OARG5] | str r0, [fp, -OARG5]
4
4
4
4
4
OARG5
OARG6
CNT

## Slide 24: Called Function: Retrieving Args From the Stack
At function start and before the push{} the sp is at an 8-byte boundary
Args > 4 in caller's stack frame and arg 5 always starts at fp+4
  Additional args are higher up the stack, with one “slot” every 4-bytes
This "algorithm" for finding args was designed to enable variable arg count functions like printf("conversion list", arg0, … argn);
No limit to the number of args (except running out of stack space)
r0 = func(r0, r1, r2, r3, r4, ARG5, ARG6);
x
.equ ARGN, (N-4)*4 // where n must be > 4
oarg5
sp
oarg6
Frame PAD
lr to callers
callers fp
cnt
fp
Previous stack frame
lr to caller
callers fp
indx
c
fp-8
fp-12
fp+4
fp+8
Rule:
Called functions always access stack args using a positive offset to the fp
calling functions stack frame
called functions stack frame

## Slide 25: Called Function: Retrieving Args From the Stack
r0 = func(r0, r1, r2, r3, r4, ARG5, ARG6);
x
.equ FP_OFF, 4
.equ C, 4 + FP_OFF
.equ INDX, 4 + C
.equ PAD, 0 + INDX
.equ FRMADD, PAD – FP_OFF
// below are distances into the caller's stack frame
.equ ARG6, 8
.equ ARG5, 4
Variable or Argument | distance from fp | Address on Stack | Read variable | Write Variable
int arg6 | ARG6 | add r0, fp, ARG6 | ldr r0, [fp, ARG6] | str r0, [fp, ARG6]
int arg5 | ARG5 | add r0, fp, ARG5 | ldr r0, [fp, ARG5] | str r0, [fp, ARG5]
int c | C | add r0, fp, -C | ldr r0, [fp, -C] | str r0, [fp, -C]
int count | INDX | add r0, fp, -INDX | ldr r0, [fp, -INDX] | str r0, [fp, -INDX]
oarg5
sp
oarg6
Frame PAD
lr to caller
callers fp
cnt
fp
lr to callers
callers fp
indx
c
Rule:
Called functions always access stack args using a positive offset to the fp
calling functions stack frame
called functions stack frame
Observe the positive offsets
ARG5
ARG6
C
INDX
Frame PAD

## Slide 26: Example: Passing Stack Args, Calling Function
int sum(int j, int k)
{
return j + k;
}
void
testp(int j, int k, int l, int m, int (*func)(int, int), int *i)
{
*i = func(j,k) + func(l, m); // notice two func() calls
return;
}
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, 3, 4, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
arg1 arg2 arg3 arg4 arg5 arg6

## Slide 27: Example: Passing Stack Args, Calling Function
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, 3, 4, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ OARG6, 4 + PAD
.equ OARG5 4 + OARG6
.equ FRMADD, OARG5 - FP_OFF
// FRMADD = 20 - 4 = 16
oarg5
sp
oarg6
fp
FRMADD = 16
4
4
lr to caller
callers fp
i
4
(*pf)()
4
frame pad
0
4
4
Main() stack
Variable or Argument | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
int oarg6 | OARG6 | add r0, fp, -OARG6 | ldr r0, [fp, -OARG6] | str r0, [fp, -OARG6]
int oarg5 | OARG5 | add r0, fp, -OARG5 | ldr r0, [fp, -OARG5] | str r0, [fp, -OARG5]

## Slide 28: Example: Passing Stack Args, Calling Function
int main()
{
int i;
int (*pf)(int, int) = sum;
testp(1, 2, 3, 4, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
oarg5
sp
oarg6
fp
FRMADD = 16
4
4
lr to caller
callers fp
i
4
(*pf)()
4
frame pad
0
4
4
Variable or Argument | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
int oarg6 | OARG6 | add r0, fp, -OARG6 | ldr r0, [fp, -OARG6] | str r0, [fp, -OARG6]
int oarg5 | OARG5 | add r0, fp, -OARG5 | ldr r0, [fp, -OARG5] | str r0, [fp, -OARG5]
main:
push {fp, lr}
add fp, sp, FP_OFF
add sp, sp,-FRMADD
ldr r0, =sum // get func address
add r1, fp, -PF // PF address on stack
str r0, [r1] // store sum in var pf
add r0, fp, -I // get address of I
add r1, fp, -OARG6 // address of OARG6
str r0, [r1] // arg 6: store address of I
ldr r0, [fp, -PF] // get PF from stack
add r1, fp, -OARG5 // address of OARG5
str r0, [r1] // arg 5: store sum() address
mov r0, 1 // arg 1: 1
mov r1, 2 // arg 2: 2
mov r2, 3 // arg 3: 3
mov r3, 4 // arg 4: 4
bl testp
ldr r0, =.Lmess // arg 1: "%d\n"
ldr r1, [fp, -I] // arg 2: i
bl printf
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ OARG6, 4 + PAD
.equ OARG5 4 + OARG6
.equ FRMADD, OARG5 - FP_OFF
// FRMADD = 20 - 4 = 16

## Slide 29: Example: Passing Stack Args, Called Function
void
testp(int j, int k, int l, int m, int (*func)(int, int), int *i)
{
*i = func(j, k) + func(l, m);
return;
}
x
oarg5
sp
oarg6
fp
4
4
lr to caller
callers fp
i
(*pf)()
frame pad
testp()
stack
lr to main
main's fp
Argument | distance | Address on Stack | Read variable | Write Variable
int *i | ARG6 | add r0, fp, ARG6 | ldr r0, [fp, ARG6] | str r0, [fp, ARG6]
int (*fp)() | ARG5 | add r0, fp, ARG5 | ldr r0, [fp, ARG5] | str r0, [fp, ARG5]
.equ FP_OFF, 20
.equ ARG6, 8
.equ ARG5, 4
testp:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF
mov r4, r2 // save l
mov r5, r3 // save m
ldr r6, [fp, ARG5] // load func
ldr r7, [fp, ARG6] // load i
blx r6 // r0 = func(j, k)
mov r1, r5 // arg 2 saved m
mov r5, r0 // save func return value
mov r0, r4 // arg 1 saved l
blx r6 // r0 = func(l, m)
add r0, r0, r5 // func(l,m) + func(j,k)
str r0, [r7] // store sum to *i
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
main()
stack
arg1 arg2 arg3 arg4 arg5 arg6
short circuit: make this call first

## Slide 30: Extra Slides

## Slide 31: By following the saved fp, you can find each stack frame
How gdb finds stack frames
sp
fp
saved lr
callers fp
main()
sp
fp
saved lr
callers fp
main()
lr to main()
main() fp
funcA()
sp
fp
saved lr
callers fp
main()
lr to funcC()
funcC() fp
funcD()
lr to funcB()
FuncB() fp
funcC()
lr to funcA()
funcA() fp
funcB()
lr to main()
main() fp
funcA()
saved lr
callers fp
main()
lr to funcA()
funcA() fp
funcB()
lr to main()
main() fp
funcA()
sp
fp
sp
fp
saved lr
callers fp
main()
lr to funcB()
FuncB() fp
funcC()
lr to funcA()
funcA() fp
funcB()
lr to main()
main() fp
funcA()
x