## Slide 1
UCSD CSE 30 Section B
Keith Muller
Computer Organization and Systems Programming
Version 2.01
DEC PDP 11/45 - 1973
C Part 1

## Slide 2: CSE30 Section B Spring 2024
Zoom Office Hours
  https://ucsd.zoom.us/j/94331007124
  Friday: 4:00 PM to 4:45 PM
  These office hours can be indivual of for a group if you like
  Additional office times By Appointment
  Send me email to schedule
Instructor: Keith Muller
I highly encourage feedback
  Please bring any issues to my attention, I will promptly address them
How to contact me directly:
  kmuller@ucsd.edu
  Please do not use canvas messages
x
In Person Office Hours: CSE 2109
  Tue, Thu: 2:00 PM to 3:00 PM
  These office hours are group meetings
  Ask questions, review material, or just come to listen
  Students who attend office hours tend to do better in the course

## Slide 3: CSE 30 Spring 2024 – Staff Covers Both Sections A & B
x
TA's
Nitya Agarwal
Mihir Kekkar
Yuchen Jing
Liam Fernandez
Tutors
Ali Alabiad
Bryan Cho
Charlotte Dong
Vivian Liu
Kate Romero
Kevin Shen
Charvi Sukla
Fong Vachirathanusorn
Joseph Edmonston
Thanh-Nhan Lam
Section A (Cao) and B (Muller) share the same pool of TA's and Tutors
Tutors
Christian Lee
Jessie Ouyang
Brandon Reponte
Adrian Rosing
Luffy Saito
Leica Shen
Shijie Wang
Alex Simonyan
Reese Whitlock

## Slide 4: CSE30 Spring 2024 Section B Specific
x
There are two sections: Section A (Cao) and Section B (Muller)
What is the same in the two sections
  study topics (roughly in-sync by the end of each week)
  quizzes
  Programming Assignments
What is different between the two sections
  lecture materials
  midterm questions (from Sect B lecture)
  final questions (from Sect B lecture)
In-person lecture attendance is strongly encouraged (attendance points)
  Lectures are podcast recorded
Discussion section attendance is optional but strongly encouraged
  You may attend either discussion section and still be enrolled in Sect B
  Section B sections are podcast recorded
See the syllabus for grading details

## Slide 5: CSE30 Class Resources
Section B Lecture Slides: https://github.com/cse30-sp24/Muller_Slides
  Located on class github in both pptx and pdf format
  Slides are updated constantly to correct errors and to improve content
    Version is at the upper left on the title slide
    Always check you have the current version the morning before lecture
Class github: https://github.com/cse30-sp24
Piazza: https://piazza.com/ucsd/spring2024/cse30_sp24_a0/home
  First Place to go to for Q/A and important announcements
  Public piazza posts are for: general questions on PA's and lectures
    Do not post publicly any parts of an assignment, quiz or exam solution
  Private posts are for: specific situation relating to just you or you are not sure
Tutor Lab hour schedule: https://autograder.ucsd.edu
  For getting help from the tutors
Canvas: https://canvas.ucsd.edu/courses/54650
  quizzes, textbooks, programming assignments, exams
Gradescope: https://www.gradescope.com
  Submitting programming assignments
x

## Slide 6: Surviving Section B Lectures (In-person)
Make sure you bring your copy of lecture slides to class, it helps
How to get my attention in class
  I never intentionally ignore questions; I just may not see you
  Raise your hand, or just call out if I appear to ignore you by accident
You must SLOW ME DOWN: Otherwise, I tend to speed up
  Please do not be shy, speak up and remind me to slow down
If you have questions, or I went too fast, or the material is not clear, etc.
  Please ask me to go over it again (do this right away, not 5 slides later)
    Just don’t sit there and waste your time
  my responsibility: help you learn the material
  your responsibility: ask questions (I love questions, they also slow me down!)
x

## Slide 7: How to do well in CSE30 - 1
Go to lecture
  Before lecture go over the class slides
  Lecture slides are posted the day before class (last minute updates that morning)
  Keep your lecture slides up to date (I update them to fix errors and address questions)
Go to Discussion Sessions
  ask the TA’s and Tutors for help
Studying for exams
  All the exam question topics are found in my slides and the PA writeups
  Try to write the exam yourself, with practice you will be able to guess the questions
Post to piazza when you have questions
Do the readings on time
Review the material: watch the podcasts and occasional special topic videos
x

## Slide 8: How to do well in CSE30 - 2
Most important: Keep up, do not procrastinate as it is hard to catch up
  The class material starts easy and gets much harder over the quarter
  Do not expect you can do later programming assignments in less than 5 days
  Do not expect to learn the material by binge watching podcasts, this never ends well
Please be careful when using web resources for this class
  a lot of the material you will find is either not correct or does not apply to our programming environment
  this is especially true with assembly language programming topics
Are you struggling?
  Do not wait, ask for help as soon as possible – do not fall behind
  Best advice: Come to my office hours (or schedule a zoom meeting)
    Give me a chance to help you
    I will spend as much time as necessary to help you understand the material
x

## Slide 9: A General-Purpose Computer – Von Neuman Architecture
Since the middle of the 20th century, many architectural approaches to the general-purpose computer have been tried
The architecture which nearly all modern computers are based was proposed by John Von Neuman in the late 1940's
The major components are:
Central Processing Unit (CPU): a device which fetches, interprets, and executes a specified set of operations called instructions
Memory: Storage of N words of W bits, where W is a fixed architectural parameter, and N can can be expanded to meet workload (the programs running on the CPU) and cost requirements
I/O: Devices for communication with the outside world (including external persistent storage)
  External connections (from CPU to memory and I/O) typically use industry "standards"
  Standards enable technologies from different companies to interoperate
x

## Slide 10: What is Computer Architecture?
Instruction Set Architecture (ISA)
Functional behavior of a computer system as viewed by a programmer
  describes how the CPU is controlled by software programs
  specifies both what the processor can do as well as how it gets it done
Architectural Characteristics (partial list):
  supported data types (how data is encoded)
  CPU registers (number, size, use, etc.)
  how the hardware manages main memory
  instructions a microprocessor can execute
    What they "do"
    What is the instruction "format" (bit patterns) in memory
  input/output model
Machine Organization
Physical (design) realization of what is specified by the instruction set architecture
It deals with how the hardware components are linked together to meet the requirements specified by instruction set architecture
  An ISA allows variability in the physical design implementations to match different workload needs (cost, scalability, etc.)
Machine organizational characteristics (partial)
  Hardware component choices
    Expandability
    Configurability
  Physical layout
  Number and type of peripherals (I/O devices)
x

## Slide 11: Von Neuman Architecture
Distinguishing feature: Memory contains both program instructions and data
CPU Instructions are often called machine code and encoded in memory using patterns of ones and zeros (like binary numbers)
Example: three 32-bit instructions (shown in hexadecimal format below)
Instructions operate on data that is stored in a small capacity volatile memory in the CPU
  these are called registers
CPU reads/writes data from memory into these data registers to operate on them
An executable program contains
  series of instructions (the program)
  (maybe some) data to operate on
81 fe 89 32
81 54 22 af
81 22 10 9A
Memory
CPU
registers
instruction register
data
instructions
add
r0
r1
r2
Rn
…
R2
R1
R0
Address
(Register name)
Register
Contents
…
data
data
data
instruction #3
instruction #2
instruction #1
x

## Slide 12: C, Assembly and Machine Code
Machine Language (or code)
  Are encoded in memory using patterns of ones and zeros (like binary numbers)
  Example: arm32 machine code stores just one instruction in 32 bits (4 bytes)
Assembly language is a symbolic version of the machine language
  Instructions describe operations the hardware can perform (e.g., =, +, -, *)
  Unique to a specific ISA: e.g., ARM-32 versus IA-64
  May be stored in a human readable text file
  You can write in assembly language just like C or Java
    Assembly is much easier to program than machine code
A high-level language (like C) is compiled into an assembly language equivalent
  A statement in C is represented by a sequence of one or more assembly language instructions (why a do you think it is a sequence?)
Assembly language program
  assembly language program is translated (assembled) into machine code
x

## Slide 13: Assembly & Machine Code Example: ARM-32 (32-bits)
Consider an addition statement
R0 = R1 + R3;
Assembly Language (human readable)
machine code pattern in memory
List of Different operations for this type of instruction
x

## Slide 14: Machine Organization – Von Neuman
CPU executes a machine code program
  Machine code is specific to a particular CPU Instruction set Architecture (ISA)
Memory contains both data and programs
I/O (input/Output): Connects the CPU and memory to the external world
  An I/O operation is where data (including machine code) is copied between persistent storage (like an SSD) and ram memory
Volatile (non-persistent) memory
  contents lost when power is removed
  Memory dimms (memory bus)
  CPU registers (memory inside the CPU)
Non-volatile (persistent) memory
  contents preserved when power is removed
  SSD (I/O bus attached)
  NVDIMM (memory bus attached)
CPU
+
Registers
Volatile
Memory
(RAM)
Network
USB
I/O HUB
Volatile
Memory
(RAM)
Storage
Non-volatile
Memory
Optional
Video
Adapter
Keyboard + Mouse
I/O
PCI-E
I/O
PCI-E
Memory Bus
DDR5
x

## Slide 15: Memory Triangle: Hardware Cost/Performance/Capacity Tiers
x
DIMM memory Module
PCI-E
ALU & Logic
Address
Data
Registers
Caches
Address
Data
CPU
~300 K Cycles
Largest Capacity
Slowest performance
Lowest Cost $/capacity
Assume each instruction takes 1 clock cycle
Clock cycle =~ time to access; larger is slower
Smallest Capacity
Highest Performance
Highest cost/capacity
Design Goal: best performance at the lowest (or specific) cost
Other goals: performance/energy (operating cost), expandability, high margin (price/cost)

## Slide 16: Memory Organization is in Units of Bytes
One bit (digit) of storage (in memory) has two possible states: 0 or 1
Memory is organized into a fixed unit of 8 bits, called a byte
Conceptually, memory is a single, large array of bytes, where each byte has a unique address (this is a: byte addressable memory)
An address is an unsigned (positive #) fixed-length n-bit binary value
  Range (domain) of possible addresses = address space
Each byte in memory can be individually accessed and operated on given its unique address
..00000000
..00000001
n-bit Memory
Address
..00000010
..00000011
..00000100
..00000101
..00000110
..00000111
Low address
High address
01010101
10101010
01010101
10101010
01010101
10101010
01010101
10101010
1 byte
(8-bits wide)
Memory
contents
Bit position in Byte |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Content of each bit |  |  |  |  |  |  | 
MSB
Most Significant Bit
LSB
(Least Significant Bit)
x
This is one byte

## Slide 17: Variables in Memory: Size and Address
Variable name is associated with a starting address in memory
The number of contiguous bytes required to store a variable is based on the type of the variable
  Different variable types require different amount of contiguous bytes
  ARM 32 has fixed length (32-bit) instructions (stored in 4 contiguous bytes)
Example Below: Variables all starting at address 0, each box is a byte
Aside: we will see later that the starting addresses for a specific data type or instruction has restrictions on what the starting address may be (this is called memory alignment)
x
01010101
memory
char
0
Start
00000000
11111111
10101010
01010101
memory
int
4 bytes
0
2
1
3
Start
Size in bytes
memory
short int
2 bytes
0
10101010
1
01010101
Start
Size in bytes

## Slide 18: Variables in C
Integer types
  char, int
Floating Point
  float, double
Modifiers for each base type
  short [int]
  long [int, double]
  signed [char, int]
  unsigned [char, int]
  const: read only
char type
  One byte in a byte addressable memory
  Signed vs Unsigned implementation dependent
  Be careful char is unsigned on arm and signed on other HW like intel
C Data Type | AArch-32 contiguous Bytes | AArch-64 contiguous Bytes
char (arm unsigned) | 1 | 1
short int | 2 | 2
unsigned short int | 2 | 2
int | 4 | 4
unsigned int | 4 | 4
long int | 4 | 8
long long int | 8 | 8
float | 4 | 4
double | 8 | 8
long double | 8 | 16
pointer * | 4 | 8
x
word size is the size of the address (pointer)

## Slide 19: Machine code execution order
Execution order: Programs execute from instructions located in low address memory to high address memory stepping one machine instruction at a time (called execution order) unless there is a branch (example: loop, if statement etc.)
Memory
data
instructions
data
data
data
instruction #3
instruction #2
instruction #1
low memory address
high memory address
machine code program
instruction #n
instruction #...
Direction of execution
CPU
registers
instruction register
add
r0
r1
r2
Rn
…
R2
R1
R0
Address
(Register name)
Register
Contents
…
x

## Slide 20: From Source to Machine code
The granularity of compilation and assembly is a single text file (called a translation unit)
  .c file is a C source file (file.c)
  .S file (upper case S) is a human written assembly source file (file.S)
  .s file (lower case s) is a compiler generated assemble source file (file.s)
  .o file is a machine code binary (object) file (file.o)
Multiple .o files are combined (linked) into an executable file
C source
Rust source
go source
ARM Assembly
ARM Machine code
High level Language
File (text)
Assembly file
(text)
Object file
(binary)
compiler
assembler
C source
Rust source
go source
intel Assembly
intel Machine code
compiler
assembler
x

## Slide 21: Linker: Combines object files to create an executable file
Each source file (Translation unit) is compiled (or assembled) independently to an object file
  When we modify a single file in a multi-source file program, we want to only recompile the file that changed and combine it with the other already compiled object files
Library file (libXX.a – where XX is the library name) is an aggregation of distinct object (.o) files
Linker combines all the listed object files together plus just those object files in libraries whose contents are referenced
  Example: one.c and two.c call functions contained in func1.o and func3.o (no calls to func2.o or func4.o)
Important: Object files created from C and assembly source can be linked (call each other) into a working executable when certain rules are followed (we will be doing a lot of this later this quarter)
C
one.c
assembly three.S
ARM Machine one.o
C
two.c
ARM Machine two.o
ARM Machine three.o
linker
func1.o
func2.o
func3.o
func4.o
Static
Library file (libsample.a)
func1.o
one.o
two.o
three.o
func3.o
Executable file
(a.out)
x

## Slide 22: From Source to Execution: Different ISA
C source
Rust source
go source
ARM Assembly
ARM Machine code
High level Language
File (text)
Assembly file
(text)
Object file
(binary)
ARM Machine
ARM Machine
ARM Machine
library file
Executable file
(binary)
compiler
assembler
linker
C source
Rust source
go source
intel Assembly
intel Machine code
intel Machine
intel Machine
intel Machine
library file
compiler
assembler
linker
arm executable on linux
intel executable on linux
Pi-cluster system (all CSE30 PA's)
ieng6
x

## Slide 23: From Source code to Execution
$ cat test.c
#include <stdlib.h>
#include <stdio.h>
int main (void)
{
printf("Hello!\n");
return EXIT_SUCCESS;
}
$ gcc -Wall –Wextra –Werror -c -S test.c
$ ls -ls
total 8
4 -rw-r--r-- 1 kmuller kmuller 109 Mar 14 15:57 test.c
4 -rw-r--r-- 1 kmuller kmuller 725 Mar 14 15:58 test.s
$ gcc test.s
$ ls -ls
total 16
8 -rwxr-xr-x 1 kmuller kmuller 7708 Mar 14 15:58 a.out
4 -rw-r--r-- 1 kmuller kmuller 109 Mar 14 15:57 test.c
4 -rw-r--r-- 1 kmuller kmuller 725 Mar 14 15:58 test.s
$ ./a.out
Hello!
loader
disk file
CPU
+
Registers
Volatile
Memory
(RAM)
I/O HUB
Volatile
Memory
(RAM)
Source to Execution Steps
Compile (c source)
Assemble (assembler source)
Link
Load
Execute
compile
assemble and link
gcc automatically calls the assembler with .S or .s files
load and then execute
crt0.o
crt0 is the c runtime startup code
x

## Slide 24: Equivalent Code: C -> Assembly -> Machine
x
00010408 <main>:
10408: e92d4800 push {fp, lr}
1040c: e28db004 add fp, sp, 4
10410: e59f0010 ldr r0, [pc, 16] //10428 <L1>
10414: ebffffb3 bl 102e8 <printf@plt>
10418: e3a00000 mov r0, 0
1041c: e24bd004 sub sp, fp, 4
10420: e8bd4800 pop {fp, lr}
10424: e12fff1e bx lr
00010428 <L1>:
10428: 0001049c
0001049c <mesg>:
1049c: 6c6c6548 // 'l, 'l', 'e', 'h'
104a0: 000a216f // '\0', '\n', '!', 'o'
memory
address contents
corresponding assembly
high low bytes
.section .rodata
mesg: .string "Hello!\n"
.text
.global main
.type main, %function
.equ FP_OFF, 4
.equ EXIT_SUCCESS, 0
main: push {fp, lr}
add fp, sp, FP_OFF
ldr r0, L1
bl printf
mov r0, EXIT_SUCCESS
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
L1: .word mesg
ARM-32 assembly
Data
address of mesg
address of mesg
Code aka TEXT
#include <stdlib.h>
#include <stdio.h>
int main(void)
{
printf("Hello!\n");
return EXIT_SUCCESS;
}
C source
Machine instructions

## Slide 25: Introduction: C Program Structure (Single file)
#include <stdlib.h>
#include <stdio.h>
/*
* This is block comment
*/
// this is a line comment
int main(int argc, char *argv[]) // or int main() or int main(void)
{
char x = '\n';
printf("Hello World!%c", x); // "Hello World!\n"
return EXIT_SUCCESS; // main always returns either
// EXIT_SUCCESS or EXIT_FAILURE
}
x
char literal '\n'
string literal "Hello World!%c"
directives to the preprocessor
main() is the first function to run
Every executable program must have one function called main()
library function for writing to stdout

## Slide 26: What is the preprocessor (cpp)?
Preprocessing is the first phase in the compilation (.c files) or assembly (.S files only) process
The preprocessor (cpp) transforms your source code, then passes it to the compiler (on .c files) or the assembler (on .S files only, not .s files)
  cpp is automatically invoked by gcc
Usually, the input to cpp is a C source file (.c) or an assembly source file (.S only) and output from cpp is still a C file or assembly file
  output from cpp is in a temporary .i file (deleted after use)
  cpp does not modify the input source file
Common use: When a program is divided across multiple source files (including library files), cpp helps you keep consistency among the files (one version of the truth)
  Examples: Consistent values for a constants, correct function definitions, etc.
x
assembly three.S
C
two.c
cpp
cpp
assembly three.i
C
two.i
gcc
gcc(gas)
ARM Machine two.o
ARM Machine three.o
temp files

## Slide 27: Common Preprocessor (cpp) Operations
Comments are replaced with a single space /* */ , //
  You will do a design for this in PA2 and program it in PA3
Continued lines: where the last character in a line is a \ causes the line to be joined with the next line
A preprocessor directive: commands to cpp to perform an operation (these start with a #)
  #include <stdio.h> contents of the include file is to be inserted at that spot in the source file
  #define MAX 8
    Does two things: Defines MAX to be a macro name and assigns it the value 8
      #define MINE just defines MINE to be a macro name with no value
    Convention: MACRO names are in CAPITAL letters
  Macros with values – cpp replaces MAX with 8 everywhere in the source file
x
#define MAX 8
int main(void)
{
int x[MAX]; // histogram array
for (int i = 0; i < MAX; i++) {
…
}
…
}
file ex.i
int main(void)
{
int x[8];
for (int i = 0; i < 8; i++) {
…
}
…
}

## Slide 28: First Look at Header Files (also called .h or "include" files)
Header file: a file whose only purpose is to be #include’d by the preprocessor
  Contains: Exported (public) Interface declarations
    Examples: function prototypes, user defined types, global variable, macros, etc.
  To import the public interface of another C source file
    #include it's header (interface) file
NEVER EVER use cpp to #include a .c file, a .S or a .s file
Convention (strongly enforced): header files use a .h filename extension (example: filename.h)
  Example: Source file src.c exported (public) interface is located in the header file src.h
How to specify the file to be #include’d
  <system-defined> are system header files (typically located under /usr/include/…)
    #include <stdio.h> // located in /usr/include/stdio.h
  "programmer-defined" header files usually in a relative Linux path (see –I flag to gcc)
    #include "else.h" // looks in the current directory first
Convention: #include directives are usually placed at the top of a source file
x

## Slide 29: Compilation Process Operations
#include <stdlib.h>
#include <stdio.h>
// A simple C Program
int
main(void)
{
printf("Hello World!\n");
return EXIT_SUCCESS;
}
compile: gcc –Wall –Wextra –Werror prog.c -o prog
cpp first processes the file (cpp is called by gcc)
Compiler (gcc) compiles main to assembly
Assembler (gas – called by gcc) translates the assembly to machine code
Linker (ld) merges the machine code for printf() (from a library) with your programs machine code to create the executable file prog (machine code)
  -o specifies the name of the executable (default: a.out)
x
preprocessor: removes the Comment, replaces with one blank
preprocessor: inserts and processes the contents of files here. Inserts: Function protype for printf (later in course)
  macro value for EXIT_SUCCESS
File locations: /usr/include/stdio.h & /usr/include/stdlib.h
cpp: replaces EXIT_SUCCESS with 0
on linux
compiler generates assembly code to call the library function printf() and pass the string "Hello World!"

## Slide 30: cpp conditional operation
You can use conditional preprocessor tests (like if-else statements) around blocks of code
  #ifdef MACRO, #ifndef MACRO, #else, #endif
In this use, the MACRO is called the guard MACRO ("guards" entry to the following block)
#ifdef MACRO if MACRO is defined the block is included otherwise #else block (if any) is included
#ifndef MACRO if MACRO is NOT defined the block is included otherwise #else block (if any) is included
#endif is the end of a block
#define MACRO // defines MACRO -- #define MACRO 8 defines macro and assigns a value of 8
#undef MACRO // undefines MACRO
#define VERS1
#define MAX 8
// file ex.c
void func(void)
{
#ifdef VERS1
int x[MAX];
#else
short x[MAX];
#endif
….
return;
}
void func(void)
{
int x[8];
….
return;
}
after the preprocessor runs
void func(void)
{
short x[8];
….
return;
}
// #define VERS1
#define MAX 8
// file ex.c
void func(void)
{
#ifdef VERS1
int x[MAX];
#else
short x[MAX];
#endif
….
return;
}
after the preprocessor runs
x

## Slide 31: cpp conditional tests: header guards
Header guards ensure that only one copy of a .h file is included in a source file
A Convention: header guard (macro) NAME (all capital letters) is created as follows:
  use the filename of header file but in all caps
  replace the period in header file name with an _
  Example: file sum.h header guard macro name is SUM_H
x
#include "sum.h"
// file func.c
int func(void)
{
int z[MAX];
int func(void)
{
int z[8];
func.i
How do you use "header guards" in your code?
#ifndef NAME_H // first line in the file
#define NAME_H
. . .
#endif // last line in the file
#include "sum.h"
// file ex.c
int main(void)
{
int x[MAX];
#ifndef SUM_H
#define SUM_H
#define MAX 8
#endif
int main(void)
{
int x[8];
ex.i
header guards
(two lines)
header guards
(one line)
file sum.h

## Slide 32: Why header guards are needed
x
#include "sum.h"
#include "bar.h"
// file ex.c
int main(void)
{
int x[MAX];
int z = MIN;
int main(void)
{
int x[8];
int z = 1;
#ifndef SUM_H
#define SUM_H
#define MAX 8
#endif
file sum.h
#ifndef BAR_H
#define BAR_H
#include "sum.h"
#define MIN 1
#endif
file bar.h
#ifndef SUM_H
#define SUM_H
#define MAX 8
#endif
#ifndef BAR_H
#define BAR_H
#ifndef SUM_H
#define SUM_H
#define MAX 8
#endif
#define MIN 1
#endif
// file ex.c
int main(void)
{
int x[MAX];
int z = MIN;
SUM_H is already defined here
So
#define MAX 8 is not included
SUM_H is defined here

## Slide 33: Quick Look: Character and String Literals (more later)
Problem: How do you place a non-printable character like a newline in a literal?
  The following are not legal in C as a newline in a source file represents a statement delimiter (white space) in C
  Solution: C has a special line continuation character \
char x = 'a'; // 'a' is a character literal
printf("Hello World!"); // "Hello World!" is a string literal
char a1[] = "xyz"; // char array initialized with contents of a string literal
Usually used to store characters – thus things like file names
char literals: a single (1) character inside a set of single quotes 'a'
string literals: 0 or more characters inside a set of double quotes "string"
char x = 'a
';
x
printf("Hello World!
");

## Slide 34: There are three different uses for \ in C
Line continuation char \ followed by a newline at the end of a source line (comment be careful with these)
How do you put a single ' as a character literal or a single " inside a string literal?
  You use an escape character \: which escapes the special meaning of the next character inside a character or a string literal
x
char sequence | Description
'\\' or "\\" | \ char
'\'' or "\'" | single quote
'\"' or "\"" | double quote
// line comment \
rest of line comment
x = x +\
5;
char a[] = "string: Hello \
World";
char a = '\''; // char: '
char b = '\\'; // char: \
char d[] = "ab\""; // string: ab"
char e[] = "ab\\"; // string: ab\
char c = '"'; // char: "
char f[] = "ab'"; // string: ab'
char a[] = "a "string""; // syntax error ; expected
char a[] = "a \"string\""; // ok

## Slide 35: There are three different uses for \ in C - continued
Embed characters with a special meaning inside a (char or string) literal using a two-character sequence starting with a \ followed by a single character
This is typically used for characters that are "non printable". Here are some examples:
char sequence | Description
'\n' or "\n" | newline char
'\r' or "\r" | carriage return
'\t' or "\t" | tab char
'\b' or "\b" | back space
'\0' or "\0" | null char
x
printf("\n\nHello World!\n\n");
printf("\n\nHello\tWorld!\n\n");

## Slide 36: Characters In C
ASCII Chars are 0-127 (stored in 8 bits)
Many of the values are not "printable"
x
\n in c encodes a linefeed
\b in c encodes a backspace
\t in c encodes a horizontal tab
\0 in c encodes a null
Ascii column: decimal integers

## Slide 37: Understanding Comments in C (Prep for PA2 and PA3)
In PA2 (design) and PA3 (program in C), you are going to write equivalent preprocessor code to replace each comment in an input file with a single space character (a blank space) while writing the rest of the input to output unaltered
IMPORTANT: the preprocessor does NOT perform any syntax checking
/* this is /* one block comment */ text outside comment
// this is // one line comment
text outside comment
/* block comment // part of block comment not a line comment
yet more block comment
*/ text outside comment
// line comment /* part of line comment not a block comment */
// line comment /* part of line comment not the start of a block comment oops! text outside of comment, this is not a comment anymore */
x

## Slide 38: Complexity for programming a preprocessor: Literals may contain what appears to be comments, but are not
char x = 'a'; // 'a' is a character literal
printf("Hello World!"); // "Hello World!" is a string literal
"/* text */" not a comment but a string literal whose contents looks like a block comment
'/* text */' not a comment but a character literal whose contents looks like a block comment
"// text" not a comment but a string literal whose contents looks like a line comment
'// text' not a comment but a character literal whose contents looks like a line comment
x

## Slide 39: PA2/PA3 Design: Using a Finite State Machine
Finite state machine (or Finite State Automaton) is a way of representing (or detecting) a language
  Example: set of string patterns (e.g., HA) accepted or rejected based on an input sequence
Circle (States) and Arc representation
A circle (state) represents (remembers) what has already been seen in the input stream
An arc represents a transition from one state to the next state for a specified input and may specify an optional output (or operation to be performed)
  The next state can be the same state or a different state
At any point in time, one of the states is the current state of the machine
  Current state "remembers" the input sequence seen so far by the machine
x
start
1
2
3
State
State
State
Arc
Arc
Arc
Arc

## Slide 40: Machine States and Transitions
Two Special states
  start state (machine starts "powers up" in this state) required
  end state (done or final state) not required – designed to run forever
Each arc has a label(s) that uses the notation: input1, …, input n / output or action taken
  When the input to the machine matches one of the input labels, it selects that arc to be taken
  The arc taken also specifies the output produced or action taken
    it is ok to have no output, or no operation associated with an arc
Example: FSA machine below recognizes the sequence HA on an input stream, then stops
  Question: what is missing here? – What do we do for inputs NOT specified?
H
H / no
end
A / yes
start
end
start
x
On this input
Output this or perform this action

## Slide 41: Designing a Deterministic Finite State Automaton
Deterministic Finite State Automaton (or deterministic finite state machine)
  For any given state, then for all possible inputs, there is always one next state
Step 1: Define the states (using the recognizer example from the previous slide)
  Start (initial or power up) state: input has not seen an H (or no input so far)
  H state: input has seen at least one H (or more than one H
  end state: input has seen an H immediately followed by an A
Step 2: Define the arcs
  Specify arcs at each state for all possible inputs (an arc can be taken on more than on input)
  Specify output or action (if any) on each arc
  Check: each state transition (arc) is unambiguous (unique – a specific input selects just one arc)
start
H
end
H / no
all other / no
H / no
A / yes
all other / no
x
Special input label: all other
Specifies that this arc is taken for all inputs that are not specified by the other arcs out of that state

## Slide 42: DFA recognizing multiple instances of a pattern
The state machine on the previous slide would stop after seeing the first HA, and does not take any more input, missing later occurrences of HA in the input
Say you want to process the entire contents of a text file to find and count all HA's
  from the top (top of file)
  to the bottom (end of file)
Action: Alter the machine to process input from a text file until the end of the file (EOF) is reached
x
This is a text file with a lot
of HHAA in it.
There is a HA here and a HA
there and a HA everywhere.
There is also HAHA HA.
TOF
EOF

## Slide 43: DFA detecting multiple instances of a pattern - 2
To adjust the DFA to act on continuous input (multiple instances of the pattern)
"redirect" the arc(s) that pointed at the end state to point to the start state
Convert output to counting actions
Add arcs from each state when EOF on input is detected to the eof state
x
H /
all other /
start
H
H /
all other /
A / (count = count + 1)
EOF / print count
eof
EOF / print count
/ count = 0
this is power up

## Slide 44: Merging DFA's: Step one design each sequence
start
S
O
This DFA replaces SOL with a @
S /
end
O /
L / @
EOF / S
all other / all other
all other / S all other
all other / SO all other
EOF / SO
EOF /
S / S
x

## Slide 45: Merging DFA's: Step one design each sequence
This DFA replaces SAM with DAD
x
start
S
A
S /
end
A /
M / DAD
EOF / S
all other / all other
all other / S all other
all other / SA all other
EOF / SA
EOF /
S / S

## Slide 46: Merging DFA's – 3 (Finished)
x
start
S
O
S /
end
O /
L / @
EOF / S
all other / all other
all other / S all other
all other / SO all other
EOF / SO
EOF /
S / S
A
M / DAD
all other / SA all other
EOF / SA
A /
This DFA replaces SOL with a @
and This DFA replaces SAM with DAD

## Slide 47: Data types: C Versus Java
Data Types | Java | C
Character | char // 16-bit unicode | char // 8 bits (varies by hardware)
integers | byte // 8 bits short // 16 bits int // 32 bits long // 64 bits | (unsigned, signed) char // see row above (unsigned, signed) short // unspecified (unsigned, signed) int // unspecified (unsigned, signed) long // unspecified
Floating Point | float // 32 bits double // 64 bits | float // unspecified double // unspecified
Logical type | boolean | #include <stdbool.h> bool conditional tests that evaluate to 0 are false, true for all other values
Constants | final int MAX = 1000; | // two alternatives to do this #define MAX 1000 // C preprocessor const int MAX = 1000;
x

## Slide 48: Caution: Char type can be either signed or unsigned
variable c is being cast promoted to an int
So, what is printed?
  Depends on the hardware
On arm (pi-cluster)
  char default is unsigned
255
On Intel 64-bit (ieng6)
  char default is signed
-1
unsigned char: 8 bits positive values only 0 to 255
signed char: 8 bits negative & positive values (-128 to +127)
char (with no modifier): 8-bit (signed or unsigned: implementation dependent)
#include <stdio.h>
#include <stdlib.h>
int
main(void)
{
char c = 255;
printf("%d\n", (int)c);
return EXIT_SUCCESS;
}
x

## Slide 49: Fixed size types in C (later addition to C)
Sometimes programs need to be written for a particular range of integers or for a particular size of storage, regardless of what machine the program runs on
In the file <stdint.h> the following fixed size types are defined for use in these situations:
x
Signed Data types | Unsigned Data types | Exact Size
int8_t | uint8_t | 8 bits (1 byte)
int16_t | uint16_t | 16 bits (2 bytes)
int32_t | uint32_t | 32 bits (4 bytes)
int64_t | uint64_t | 64 bits (8 bytes)

## Slide 50: C vs Java: Expression Type Promotions, Demotions, Casts
Java: demotions are not automatic C: demotions are automatic
Cast: a unary operator(variable_type) explicitly converts the type the value of an expression to variable_type
To explicitly get the floating-point equivalent of the integer variable a you would use a cast and write (float)a
int i;
char c;
i = c; /* Implicit promotion */
/* OK in Java and C */
c = i; /* Implicit demotion */
/* Java: Compile time error */
/* C: OK; truncation */
c = (char)i; /* Explicit demotion using a cast */
/* Java: OK; truncation */
/* C: OK; truncation */
x

## Slide 51: Java versus C: Mostly Similar Syntax
int x = 42 + (7 * -5);
double pi = 3.14159;
char c = 'Q';
for (int i = 0; i < end; i++) { // variable i is a loop guard
if (i % 2 == 0) {
x += i;
}
}
int i; // i initial value is undefined ... if (i) /* is the same as (i != 0) */
statement1;
else
statement2;
x
Which statement is executed
after the if statement test?
Depends on what value of i,
is i zero or non-zero

## Slide 52: Conditional Statements (if, while, do...while, for)
C conditional test expressions: 0 (NULL) is FALSE, any non-0 value is TRUE
C comparison operators ( ==, !=, >, etc.) evaluate to either 0 (false) or 1 (true)
Legal in Java and in C:
Illegal in Java, but legal in C (often a typo!):
i = 0; if (i == 5) statement1; else statement2;
i = 0; if (i = 5) statement1; else statement2;
Assignment operators evaluate to
the value that is assigned, so….
Which statement is executed
after the if statement test?
Which statement is executed
after the if statement test?
x

## Slide 53: Program Flow – Short Circuit or Minimal Evaluation
In evaluation of conditional guard expressions, C uses what is called short circuit or minimal evaluation
Each expression argument is evaluated in sequence from left to right including any side effects (modified using parenthesis), before (optionally) evaluating the next expression argument
If after evaluating an argument, the value of the entire expression can be determined, then the remaining arguments are NOT evaluated (for performance)
x
if ((x == 5) || (y > 3)) // if x == 5 then y > 3 is not evaluated

## Slide 54: Program Flow – Short Circuit or Minimal Evaluation
x
if ((a != 0) && func(b)) // if a is 0, func(b) is not called
do_something();
// if (((x > 0) && (c == 'Q')) evaluates to non zero (true)
// then (b == 3) is not tested
while (((x > 0) && (c == 'Q')) || (b == 3)) { // c short circuit
x = x / 2;
if (x == 0) {
return 0;
}
}

## Slide 55: Be Careful with the comma , sequence operator
Sequence Operator ,
  expr1,expr2
Evaluates expr1 first and then expr2 evaluates to or returns expr2
Unexpected results with , operator (some compilers will warn)
for (i = 0, j = 0; i < 10; i++, j++)
…
x
i = 64,323; // i = 64 (assigns first)
i = (64, 323); // i = 323 (value of expression)

## Slide 56: Aside: Suppress compiler warnings on fall throughs
When writing switch statements in C it is not uncommon to see a case use a fall through to the next case below it (this is legal to do in C)
  Why do this: First state does extra steps and then the same steps as the "fall through" state
  But compilers often (with extra checking flags, using heuristics) decide to flag this as a potential error
  The Fix: use the comment /* FALL THROUGH */ (a bit of a "hack"  )
int a = 2;
switch (a) {
case 1:
printf("1\n");
break;
case 2:
printf("2\n");
default:
printf("default\n");
break;
}
% gcc -ggdb -Wall -Wextra -Werror switch.c
switch.c: In function ‘main’:
switch.c:11:9: error: this statement may fall through [-Werror=implicit-fallthrough=]
11 | printf("2\n");
| ^~~~~~~~~~~~~
switch.c:12:5: note: here
12 | default:
| ^~~~~~~
cc1: all warnings being treated as errors
int a = 2;
switch (a) {
case 1:
printf("1\n");
break;
case 2:
printf("2\n");
/* FALL THROUGH */
default:
printf("default\n");
break;
}
% gcc -ggdb -Wall -Wextra -Werror switch.c
% ./a.out
2
default
%
x

## Slide 57: C Function Definitions - 1
C Functions are not methods
  no classes, no objects
C function definition
  returns a value of returnType
  zero or more typed parameters
Every program must have initial (start) function: int main()
main() is the first function in your code to run/execute
  main() is not the first function to run in a Linux process, it is the C runtime startup code
    later in course
  You should never make a call to main() from your code
// returns: sum of integers from 1 to max
int
sum(int max) // function definition
{
int i, sum = 0; // variable definition
for (i = 1; i <= max; i++) {
sum += i;
}
return sum;
}
returnType fname(type param1, …, type paramN)
{
// statements
return value;
}
function definition
x

## Slide 58: C Function Definitions - 2
A function of type void does not return a value
A void parameter or an empty parameter list specifies this is a function with no parameters
  A common practice is to use the keyword void to specify an empty or an ignored parameter list
At runtime, function arguments are evaluated, then the resulting value is COPIED to a memory location allocated for the argument (like a local variable)
  So, functions are free to change parameter values in their body without side effect to the calling function
  C Parameter passing is called: call by value
// prints sum of integers 1 to MAX
#define MAX 8
int
sum(void) // or sum()
{
int i, total = 0;
for (i = 1; i <= MAX; i++) {
total += i;
}
return total;
}
remember this is a pre-processor (cpp) macro
it is not a variable, it is a "substitution"
x

## Slide 59: C Function Definitions - 3
In standard C, functions cannot be nested (defined) inside of another function (called local functions in other languages)
int outer(int i)
{
int inner(int j) // do not do this, not in standard c
{
}
}
x
Assignment inside conditional test with a function call (this is very common!)
if ((i = SomeFunction()) != 0) statement1; else statement2;
assignment returns the value that is placed into the variable to the left of the = sign, then the test is made

## Slide 60: Textbook Over-ride: Linux Return Value Convention
In your code, main() is the first function to start to execute and usually the last
Linux uses a convention on signaling errors at process termination to the "shell"
  Remember checking return values in CSE15L scripts?
  It is the value often associated with the return statement from main()
In this class, always use the Linux standard return codes as defined in <stdlib.h> when returning from main() or exiting your program
EXIT_SUCCESS // program completed ok; usually 0
EXIT_FAILURE // program completed with error; non-zero value
return EXIT_SUCCESS;
x

## Slide 61: Setting program termination return (status) values
#include <stdio.h>
#include <stdlib.h>
int
main(void) {
/* Your code here */
/* code was successful */
return EXIT_SUCCESS;
}
#include <stdio.h>
#include <stdlib.h>
int
main(void) {
/* Your code here */
/* a failure occurred */
return EXIT_FAILURE;
}
Indicating your program operated incorrectly/errors
Indicating your program operated correctly

## Slide 62: Linux/Unix Process and Standard I/O (CSE 15L) - Defaults
Linux OS "file descriptor number"
c stdio file handle/pointer (file *)
THIS IS A TEST
THIS IS A TEST
echo input to output
THIS IS A TEST
I/O Is not part of C it is supplied in the runtime environment: standard C library
x

## Slide 63: stdio File I/O – File Position Pointer
Read/write functions advance the file position pointer from TOF towards EOF after each call to a read/write function
  position pointer moves towards EOF by number of bytes read/written
  This is called Sequential I/O (sequential read & sequential write)
EOF condition during a read operation
  After the last byte is read in a file, additional reads results in a function return value of EOF
  EOF is NOT a character in the file, but a condition on the stream
  EOF signals no more data is available to be read
  EOF is usually a #define EOF -1 macro located in the file stdio.h
file
Old file position pointer
x
New file position pointer
read N
bytes/chars
TOF
EOF

## Slide 64: stdio File I/O – Working with a Keyboard
How can you have an EOF when reading from a keyboard?
stdio I/O library functions designed to work primarily on files
  With keyboard devices the semantics of file operations needs to be "simulated"
Example: when a program (or a shell) is reading the keyboard and is blocked waiting for input it is waiting for you to type a line
  This is NOT an EOF condition
To set an EOF condition from the keyboard, type on an input line all by itself:
two key combination (ctrl key and the d key at same time), followed by a return/enter
  ctrl-d often shown in slides etc. as ^d
x
How do I
signal EOF?

## Slide 65: C Library Function: Simple Formatted Printing
#include <stdio.h> // import the public interface
int fprintf(FILE *file, const char *format, ...);
  Write chars to the file identified by file (stdout, stderr are already open)
  Convert values to chars, as directed by format
  Return count of chars successfully written
  Format is the output specifications enclosed in a "string"
  Returns a negative value if an error occurs
int printf(const char *format, ...); // *format - later in course
  Equivalent to fprintf(stdout, format, ...);
Type % man 3 printf for more information on format
Task | Example Function Calls
Write formatted data | int status; status = fprintf(stderr, "%d\n", i); status = printf("%d\n", i); /* Writes to stdout */
x

## Slide 66: Some Formatted Output Conversion Examples
Conversion specifications example
  %d conversion specifier for int variables
  %c conversion specifier for char variables
  many more conversion specifiers (online manual: % man printf and the textbooks)
  Output
int i = 10; char z = 'i';
char a[] = " Hello\n";
printf("%c = %d,%s", z, i, a); // write to stdout
fprintf(stderr, "This is an error message to stderr\n");
i = 10, Hello
This is an error message to stderr
x

## Slide 67: C Library Function API : Simple Character I/O – Used in PA3
#include <stdio.h> // import the public interface
int putchar(int c);
  writes c (demoted to a char) to stdout
  returns either: c on success OR EOF (a macro often defined as -1) on failure
  see % man 3 putchar
int getchar(void);
  returns the next input character (if present) promoted to an int read from stdin
  see % man 3 getchar
Make sure you use int variables with putchar() and putchar()
Both functions return an int because they must be able to return both valid chars and indicate the EOF condition (-1) which is outside the range of valid characters
Operation | Usage Examples
Write a char | int status; int c; status = putchar(c); /* Writes to screen stdout */
Read a char | int c; c = getchar(); /* Reads from keyboard stdin */
x
Why is character I/O using an int?
Answer: Needs to indicate an EOF (-1) condition that is not a valid char

## Slide 68: Character I/O (Also the Primary loop in PA3)
// copy stdin to stdout one char at a time
#include <stdio.h>
#include <stdlib.h>
int main(void)
{
int c;
while ((c = getchar()) != EOF) {
(void)putchar(c); // ignore return value
}
return EXIT_SUCCESS;
}
% ./a.out
thIS is a TeSt
thIS is a TeSt
^d
%
%./a.out < a > b
Always check return code to handle EOF
EOF is a macro integer in stdio.h
Always check return codes unless you do not need it
Sometimes you may see a (void) cast which indicates ignoring the return value is deliberate this is often required by many coding standards
x
Typed on keyboard
Printed by program
Typed on keyboard
Copies file a to file b
Make sure you use int variable with getchar() and putchar()!

## Slide 69: Background: What is a Definition?
Definition: creates an instance of a thing
There must be exactly one definition of each function or variable (no duplicates)
In C you must define a variable or a function before first use in your code
Function definition (compiler actions)
  creates code you wrote in the functions body
  allocates memory to store the code
  binds the function name to the allocated memory
Variable definitions (compiler actions)
  allocates memory: generate code to allocate space for local variables
  initialize memory: generate code to initialize the memory for local variables
  binds (or associates) the variable name to the allocated memory
x

## Slide 70: Background: What is a Declaration?
Declaration: describes a thing – specifies types, does not create an instance
Each declaration has an associated identifier (the name)
Function prototype describes how to write the code to call a function defined elsewhere
  Identifier is the function name
  Describes the type of the function return value
  Describes the types of each of the parameters
Variable declaration describes how to write the code to use a variable in a statement
  Identifier is the variable name
  Describes the type of a variable that is defined elsewhere
Derived and defined type description
  Identifier describes the derived/defined type
  struct, arrays, plus others (covered later)
An identifier may be declared multiple times, but only defined once
A definition is also a declaration in C
x

## Slide 71: Definitions and Declarations Use in C
#include <stdio.h>
#include <stdlib.h>
#define MAX 8
int sumit(int max)
{
int i, sum = 0;
for (i = 1; i <= max; i++) {
sum += i;
}
return sum;
}
int main(void)
{
printf("sum: %d\n", sumit(MAX));
return EXIT_SUCCESS;
}
sumit() is defined and declared here
sumit() is used here
Independent Translation Unit: the granularity (unit) of source which is compiled or assembled
Default Definition and declaration validity:
  Restricted to the file (translation unit) where they are located and
  Start at the point of definition or declaration in the file to the end of the source file (translation unit)
x
You must declare a function or variable before you use it
Warning: Use before declaration will implicitly default to int
Restrictions that we need to relax
sum() must be defined in the same source files
sum() appear before it is used by main()
i, sum, are defined and declared here

## Slide 72: Function Prototypes: Creating a Function Declaration
Function prototype is a function declaration in C
Function prototype is function definition header followed by a single semicolon (;) NO code block
Describes the function from that point in the source file
x
#include <stdlib.h>
#define NUM 100
int sum(int); // function declaration starts here
int main(void)
{
sum(NUM); // rest of code not shown
return EXIT_SUCCESS;
}
int sum(int max) // function definition is here
{
int i, sum = 0;
for (i = 1; i <= max; i++) {
sum += i;
}
return sum;
}
returnType fname(type_1, …, type_n); // function prototype
this is the code block
C requires the function declaration to be seen in the source file before use
A function prototype for sum() enables:
body of sum() to be either after main() in the same source file or
body of sum() to be in a different source file
Common practice: Function prototypes in a .C file are usually placed at the top the file

## Slide 73: C Variable Storage Lifetime
  Static Storage Lifetime: valid while program is executing
    Storage allocated and initialized prior to runtime (implicit default = 0)
  Automatic Storage Lifetime: valid while enclosing block is activated
    Storage allocated and is not implicitly initialized (value = garbage) by executing code when entering scope
  Allocated Storage Lifetime: valid from point of allocation until freed or program termination
    Storage allocated by call to an allocator function (malloc() etc.) at runtime and is not implicitly initialized (value = garbage) - one allocator does initialize to zero at runtime calloc() – later in course
  Thread Storage Lifetime: valid while thread is executing (not CSE 30)
x

## Slide 74: C and Scope
Scope: Range (or the extent) of instructions over which a name/identifier is allowed be referenced by C instructions/statements
  File Scope: Range is within a single source file (also called a translation unit)
  Block Scope: Range is within an enclosing block (for variables only)
int global; // global variable with file scope
void // function foo with file scope
foo(int parm) // parameter parm block scope begins
{ // function body (block) begins int i, j = 5; // variables with block scope
for (int k = 0; k < 10; i++) { // inner block scope
// some code
} } // function body ends
x

## Slide 75: Nested Scope
Nested Scope: When two different variables have the same name are in scope at the same time, the declaration (remember definitions are also declarations) that appears in the inner scope hides the declaration that appears in the outer scope
void funcA(int n) // scope of the function parameter 'n' begins
{ // the body of the function begins
++n; // 'n' is in scope and refers to the function parameter
// int n = 2; // error: cannot redeclare identifier in the same scope
for(int n = 0; n < 10; ++n) { // scope of loop-local 'n' begins
printf("%d\n", n); // prints 0 1 2 3 4 5 6 7 8 9
} // scope of the loop-local 'n' ends
// the function parameter 'n' is back in scope
printf("%d\n", n); // prints the value of the parameter
} // scope of function parameter 'n' ends
x

## Slide 76: Variables in C
Global variables
  Defined at file scope (outside of a block)
  have static storage duration
  global variables defined without an initial value default to 0 (set prior to program execution start)
  global variables defined with an initial value are set at program start
Local (block scope) variables (including function parameter variables)
  Defined at block scope (inside of a block)
  have automatic storage duration
  block scope variables defined without an initial value have an undefined initial value
  block scope variables defined with an initial are set each time the block is entered
  All block scope variables become undefined at block exit
Variable definitions preceded by the keyword static have static storage duration including variables defined with block scope
x
int global; // global with static storage duration
int foo(void)
{
static int s = 0; // "local" with static storage duration
int x; // "local" with automatic storage duration
}

## Slide 77: Example: Block scope (local) static storage duration variables
x
#include <stdio.h>
#include <stdlib.h>
#define MAX 5
int foo(void)
{
static int s = 0; //static storage duration, set to 0 at program start
return s += 1;
}
int main(void)
{
for (int i = 0; i < MAX; i++)
printf("%d ", foo());
return EXIT_SUCCESS;
}
% ./a.out
1 2 3 4 5
%

## Slide 78: Where things are in Memory
When your program is running it has been loaded into memory and is called a process (under the control of the OS)
Stack segment: Local variables: defined in functions
  Allocated/freed at function call entry & exit
Data segment + BSS: Global and static variables
  Allocated/freed when the entire process starts/exits
    BSS - Static variables with an implicit initial value
    Static Data - Initialized with an explicit initial value
Heap segment: dynamically-allocated (during runtime) variables
  Allocated with a function call to a library routine
  Managed by the library routines linked to your code
Read Only Data: immutable Literals
Text: Your code in machine language + non-shared libraries
0xFF…FF
0x00…00
per process address space
OS kernel [protected]
Stack
Heap
BSS
Shared Libraries
Read Only Data
Read Only Text Segment
Data
x
Process memory during execution

## Slide 79: Real programs are distributed across multiple files
Large programs in one source file can be very difficult to manage
  Consider a program with many millions of lines of code
  And there are 100's developers working on it, changing source parts of the code
  The program is being rebuilt (compiled/linked) and tested several times a day
Approach: Break a program into individual translation units (source files)
  Compile them individually and then link them together
  Only need to recompile those source files that have changed
x
file1.c
file2.c
fileN.c
file1.o
file2.o
fileN.o
libraries
executable program
Example: fixing a bug in a existing program
You fix bug in just fileN.c
Only need to recompile fileN.c to FileN.o (all the other .o files are fine)
Relink all .o files and libraries
Test the executable

## Slide 80: Controlling Linkage Across Files in Multi-File C Programs
Linkage determines whether an object (like a variable or a function) can be referenced outside the source file it is defined in
External Linkage: function and variables with external linkage can be referenced anywhere in the entire program
  Global variables and all functions have external linkage by default
  Unless explicitly declared, the default type is int for both functions and global variables
  However, the compiler must know the correct types before the use of a function or a variable, so it is able to generate the correct code
    NEVER DEPEND implicit default typing
  Use function prototypes to declare functions before use
  Use the keyword extern to "extend the visibility", e.g., declare a global variable before use
x
// example here is at file scope
extern int x; // declaration
int x = 10; // definition

## Slide 81: Controlling Linkage Across Files in Multi-File C Programs
Internal Linkage (private): function and global variables with internal linkage can only be referenced in the same source file
  Global variables and functions can be changed to internal linkage by using the keyword static in front of the definition (confusingly another use of the word static)
  Use of the keyword static in front of a global variable definition or function definition changes it to internal linkage and effectively makes it private to the file they are defined in (It cannot be referenced by another file
  Function definitions in different files (translation units) can re-use the same name if at most one has external linkage (all others must be internal linkage)
No Linkage: function parameters, variables defined inside a block (including a functions body)
  Remember: the keyword static in front of a block scope variable changes the variable to static storage duration (it does not change the linkage)
x

## Slide 82: Linkage Examples
int global0 = 1; // external linkage
static int global2; // internal linkage restricted to this file
int funcA(int x) // funcA has external linkage; x has no linkage
{
int y; // no linkage
}
static int funcB(void) // internal linkage restricted to this file
{ }
x

## Slide 83: Creating Public Interface files (header files)
file.h contains any
  public preprocessor macros
  function prototypes for the functions defined in the source file, file.c that you want visible (exported) for use (called) by functions defined in other source files
  global variable declarations (external linkage)
  Do not put any definition statements in a header file
the definitions of functions etc.
file.c
exported information
how to use functions etc. in file.h
file.h
declarations
definitions
x
To enable a source file to use any of the functions, global variables, and MACROS defined in another file (separate translation unit)
  You must create a file that exports all permitted accesses so the compiler can generate the correct code
Convention: For each source file, file.c, the public interface file is file.h
If a file has no external interfaces, then it does not need a .h file
file.c contains
  All function and global variable definitions (internal and external linkage)
  Any private preprocessor macros
  Any private (internal linkage) function prototypes

## Slide 84: Creating Public Interface files (header files)
x
// file.c
#include <stdlib.h>
#include "file.h"
static int P(char );
// above: private function prototype
int global; // initial value is 0
static int private = 1; // private global
int A(int c)
{
// body not shown
}
char B(int x, int y)
{
// body not shown
}
static int P(char z)
{
// body not shown
}
// file.h
#ifndef FILE_H
#define FILE_H
#define MAX 5
extern int global;
int A(int);
char B(int, int);
#endif
Always #include your own declaration files BEFORE any definitions
  compiler will then check that the definition and declarations are consistent
public interface for file.c
// myprog.c
#include <stdlib.h>
#include <stdio.h>
#include "file.h"
// code not shown
int main(void)
{
// body not shown
}
using the public interface

## Slide 85: Compiling Multi-File Programs (assembly steps not shown)
compile each .c file independently to a .o object file (incomplete machine code)
  gcc -Wall –Wextra –Werror –c file.c # creates file.o
  gcc -Wall –Wextra –Werror –c myprog.c # creates myprog.o
link all the .o objects files and library's (aggregation of multiple .o files) to produce an executable file (complete machine code) (gcc calls ld, the linker)
  gcc -Wall –Wextra –Werror myprog.o file.o –o myprog
libraries are a
collection of .o files
(e.g. libc)
"file.h"
file.c
file.o
cpp
gcc –c
myprog
ld – link editor
(called by gcc)
x
<stdio.h>
<stdlib.h>
cpp
myprog.c
myprog.o
cpp
gcc –c

## Slide 86: Extra Slides
Slides in this section are not used in class but contain material that you will find useful
You are not responsible for their contents
x

## Slide 87: C Versus Java
 | Java | C
Overall Program Structure | source file: Hello.java public class Hello { public static void main (String[] args) { System.out.println( "hello world!"); } } | source file: hello.c #include <stdio.h> #include <stdlib.h> int main(void) { printf("hello world!\n"); return EXIT_SUCCESS; }
Access a library | import java.io.File; | #include <stdio.h> // may need to specify library at compile time with -llibname
Building | % javac Hello.java | % gcc –Wall –Wextra -Werror hello.c –o hello
Running (execution) | % java Hello hello world! | % ./hello hello world!
Note: Sorry for the "poor" code indentation; adjusted to fit into the table
x

## Slide 88: C Versus Java
 | Java | C
Strings | String s1 = "Hello"; | char *s1 = "Hello"; // pointer version char s1[] = "Hello"; // array version
String Concatenation | s1 + s2 s1 += s2; | #include <string.h> strcat(s1, s2);
Logical ops | &&, ¦¦, ! | &&, ¦¦, !
Relational ops | ==, !=, <, >, <=, >= | ==, !=, <, >, <=, >=
Arithmetic ops | +, -, *, /, %, unary - | +, -, *, /, %, unary -
Bitwise ops | <<, >>, >>>, &, ^, ¦, ~ | <<, >>, &, ^, ¦, ~
Assignment ops | =, +=, -=, *=, /=, %=, <<=, >>=, >>>=, &=, ^=, ¦= | =, +=, -=, *=, /=, %=, <<=, >>=, &=, ^=, ¦=
x

## Slide 89: C Versus Java
 | Java | C
Arrays | int [] a = new int [10]; float [][] b = new float [5][20]; | int a[10]; float b[5][20];
Array bounds checking | // run time checking | // no run time checks – speed optimized
Pointer type | // Object reference is an // implicit pointer | int *p; char *p;
Record type | class Mine { int x; float y; } | struct Mine { int x; float y; };
x

## Slide 90: C Versus Java
 | Java | C
if, switch, for, do-while, while, continue, break, return | // equivalent | // equivalent
exceptions | throw, try-catch-finally | // no equivalent
labeled break | break somelabel; | // no equivalent
labeled continue | continue somelabel; | // no equivalent
calls: Java method C function | f(x, y, z); someObject.f(x, y, z); SomeClass.f(x, y, z); | f(x, y, z); // other differences, later…
x

## Slide 91: C Programming Toolchain - Basic Tools
gcc
  Is a front end for all the tools and by default will turn C source or assembly source into executable programs
preprocessor
  Insertion into source files during compilation or assembly of files containing macros (expanded), declarations etc.
compiler
  Translates C programs into hardware dependent assembly language text files
assembler
  Converts hardware dependent assembly language source files into machine code object files
Linker (or link editor)
  Combines (links) one or more object files and libraries into executable program files
  this may include modification of the code to resolve uses with definitions and relocate addresses
x

## Slide 92: C Programming Toolchain: The Source files
The C development toolchain uses several different file types (indicated by .suffix in the filename)
filename.h public interface "header or include files" often used as <filename.h> or "filename.h"
  common contents: public (exported) function and variable declarations, and constants and language macros
  Processed by cpp (the C pre-processor) to do inline expansion of the include file contents and insert it into a source file before the compilation starts, enables consistency
filename.c
  a source text file in C language source
  Processed by gcc
filename.S
  a source text file in hardware specific assembly language (programmer created)
  processed by gcc which calls gas (assembler)
filename.s
  machine generated by the compiler from a .c file
  processed by gcc which calls gas (assembler)
x

## Slide 93: C Programming Toolchain: The Generated files
filename.o "relocatable object file"
  Compiled from a single source file in a .c file or assembled from a single .s file into machine code
  A .o file is an incomplete program (not all references to functions or variables are defined) this code will not execute
  The .o and .c, .s, or .S files share the same root name by convention
  created by gcc calling ld (linkage editor)
library.a "static library file"
  aggregation of individual .o files where each can be extracted independently
  during the process of combining .o files into an executable by the linkage editor, the files are extracted as needed to resolve missing definitions
  created by ar, processed by ld (usually invoked via gcc)
a.out "executable program"
  Executable program (may be a combination of one or more .o files and .a files) that was compiled or assembled into machine code and all variables and functions are defined
  processed by ld (usually invoked via gcc)
x

## Slide 94: Basic gcc toolchain usage
Producing an executable file
  gcc –Wall –Wextra -Werror mysrc.c
    creates an executable file a.out
To use a specific version of C use of one the std= option
  gcc –Wall –Wextra –Werror –std=c11 mysrc.c
Producing an object file with gdb debug support add -ggdb
  gcc –Wall -Wextra –Werror –c –ggdb mysrc.c
    creates an object file mysrc.o
  gcc –Wall –Wextra -Werror –c –ggdb mymain.c
    creates an object file mymain.o
Linkage step
  combining a program spread across multiple files
  gcc –Wall -Wextra –Werror –o myprog mymain.o mysrc.o
    creates executable file myprog
Compile and linkage of file(s) in one step
  gcc –Wall –Wextra -Werror -o myprog mysrc.c mymain.c
run the program (refer to cse15l notes)
  % ./myprog
Run gcc with flags
  -Wall -Wextra
    required flag for c programs in cse30
    output all warning messages
  -c
    Optional flag (lower case)
    Compile or assemble to object file only do not call ld to link
    creates a .o file
  -ggdb
    Optional flag
    Compile with debug support (gdb)
    generates code that is easier to debug
    removes many optimizations
  -o <filename>
    specifies filename of executable file
    a.out is the default
  -S
    Optional flag (upper case S)
    Compiles to assembly text file and stops
    creates a .s file
x