## Slide 1
UCSD CSE 30
Keith Muller
Lecture 5
Computer Organization and Systems Programming
Version 2.03

## Slide 3: Compiling Multi-File Programs (assembly steps not shown)
compile each .c file independently to a .o object file this requires you use the –c flag to gcc to only compile and assemble and NOT to call the liner yet
  gcc -Wall –Wextra –Werror –c file.c # creates file.o
  gcc -Wall –Wextra –Werror –c myprog.c # creates myprog.o
link all the .o objects files and libraries (aggregation of multiple .o files) to produce an executable file (gcc calls ld, the linker
  The .o's in the libraries are automatically linked in as needed to produce an executable file
  gcc -Wall –Wextra myprog.o file.o –o myprog
libraries are a
collection of .o files
(e.g. libc)
"file.h"
file.c
file.o
cpp
gcc –c
myprog
ld – link editor
(called by gcc)
x
<stdio.h>
<stdlib.h>
cpp
myprog.c
myprog.o
cpp
gcc –c

## Slide 4: C standard I/O Library (stdio) File I/O File Position Pointer and EOF
Read/write functions in the standard I/O library advances the file position pointer from the top of a file (before the 1st byte if any) towards the end of the file after each call to a read/write function
  Side effect of call: file position pointer moves towards the end of file by number of bytes read/written
standard I/O File position pointer indicates where in the file (byte distance from the top of the file) the next read/write I/O will occur
Performing a sequence of read/write operations (without using any other stdio functions to move the file pointer between the read/write calls) performs what is called Sequential I/O (sequential read & sequential write)
EOF condition state may be set after a read operation
  After the last byte is read in a file, additional reads results in a function return value of EOF
  EOF signals no more data is available to be read
  EOF is NOT a character in the file, but a condition state on the stream
  EOF is usually a #define EOF -1 macro located in the file stdio.h (later in course)
file
Old file position pointer
x
New file position pointer
read N
bytes/chars
TOF
EOF

## Slide 5: C Library Function API : Simple Character I/O – Used in PA3
#include <stdio.h> // import the public interface
int putchar(int c);
  writes c (demoted to a char) to stdout
  returns either: c on success OR EOF (a macro often defined as -1) on failure
  see % man 3 putchar
int getchar(void);
  returns either: next input character promoted to an int read from stdin OR EOF
  see % man 3 getchar)
Make sure you use int variables with putchar() and putchar()
Both functions return an int because they must be able to return both valid chars and indicate the EOF condition (-1) which is outside the range of valid characters
Operation | Usage Examples
Write a char | int status; int c; status = putchar(c); /* Writes to screen stdout */
Read a char | int c; c = getchar(); /* Reads from keyboard stdin */
x

## Slide 6: Character I/O (Also the Primary loop in PA3)
// copy stdin to stdout one char at a time
#include <stdio.h>
#include <stdlib.h>
int main(void)
{
int c;
while ((c = getchar()) != EOF) {
(void)putchar(c); // ignore return value
}
return EXIT_SUCCESS;
}
% ./a.out
thIS is a TeSt
thIS is a TeSt
^d
%
%./a.out < a > b
Always check return code to handle EOF
EOF is a macro integer in stdio.h
Always check return codes unless you do not need it
Sometimes you may see a (void) cast which indicates ignoring the return value is deliberate this is often required by many coding standards (it is optional)
x
Typed on keyboard
Printed by program
Typed on keyboard
Copies file a to file b
Make sure you use int variables with getchar() and putchar()!

## Slide 7: stdio File I/O – Working with a Keyboard
How can you have an EOF when reading from a keyboard?
stdio I/O library functions designed to work primarily on files
  With keyboard devices the semantics of file operations needs to be "simulated"
Example: when a program (or a shell) is reading the keyboard and is blocked waiting for input it is waiting for you to type a line
  This is NOT an EOF condition
To set an EOF condition from the keyboard, type on an input line all by itself:
two key combination (ctrl key and the d key at same time), followed by a return/enter
  ctrl-d often shown in slides etc. as ^d
x
How do I
signal EOF?

## Slide 8: Linux/Unix Process and Standard I/O (CSE 15L)
Linux OS "file descriptor number"
c stdio file handle/pointer (file *)
THIS IS A TEST
THIS IS A TEST
echo input to output
THIS IS A TEST
I/O Is not part of C it is supplied in the runtime environment: standard C library
x

## Slide 9: C Library Function: Simple Formatted Printing
#include <stdio.h> // import the public interface
int fprintf(FILE *file, const char *format, ...);
  Write chars to the file identified by file (stdout, stderr are already open)
  Convert values to chars, as directed by format
  Return count of chars successfully written
  Format is the output specifications enclosed in a "string"
  Returns a negative value if an error occurs
int printf(const char *format, ...); // *format - later in course
  Equivalent to fprintf(stdout, format, ...);
Type % man 3 printf for more information on format
Task | Example Function Calls
Write formatted data | int status; status = fprintf(stderr, "%d\n", i); status = printf("%d\n", i); /* Writes to stdout */
x

## Slide 10: Some Formatted Output Conversion Examples
Conversion specifications example
  %d conversion specifier for int variables
  %c conversion specifier for char variables
  many more conversion specifiers (online manual: % man printf and the textbooks)
  Output
int i = 10; char z = 'i';
char a[] = " Hello\n";
printf("%c = %d,%s", z, i, a); // write to stdout
fprintf(stderr, "This is an error message to stderr\n");
i = 10, Hello
This is an error message to stderr
x

## Slide 11: Conditional Statements (if, while, do...while, for)
C conditional test expressions: 0 (NULL) is FALSE, any non-0 value is TRUE
C comparison operators ( ==, !=, >, etc.) evaluate to either 0 (false) or 1 (true)
Legal in Java and in C:
Illegal in Java, but legal in C (often a typo!):
i = 0; if (i == 5) statement1; else statement2;
i = 0; if (i = 5) statement1; else statement2;
Assignment operators evaluate to
the value that is assigned, so….
Which statement is executed
after the if statement test?
Which statement is executed
after the if statement test?
x

## Slide 12: Program Flow – Short Circuit or Minimal Evaluation
In evaluation of conditional guard expressions, C uses what is called short circuit or minimal evaluation
Each expression argument is evaluated in sequence from left to right including any side effects (modified using parenthesis), before (optionally) evaluating the next expression argument
If after evaluating an argument, the value of the entire expression can be determined, then the remaining arguments are NOT evaluated (for performance)
x
if ((x == 5) || (y > 3)) // if x == 5 then y > 3 is not evaluated

## Slide 13: Program Flow – Short Circuit or Minimal Evaluation
x
if ((a != 0) && func(b)) // if a is 0, func(b) is not called
do_something();
// if (((x > 0) && (c == 'Q')) evaluates to non zero (true)
// then (b == 3) is not tested
while (((x > 0) && (c == 'Q')) || (b == 3)) { // c short circuit
x = x / 2;
if (x == 0) {
return 0;
}
}

## Slide 14: Be Careful with the comma , sequence operator
Sequence Operator ,
  expr1,expr2
Evaluates expr1 first and then expr2 evaluates to or returns expr2
Unexpected results with , operator (some compilers will warn)
for (i = 0, j = 0; i < 10; i++, j++)
…
x
i = 64,323; // i = 64 (assigns first)
i = (64, 323); // i = 323 (value of expression)

## Slide 15: Review: Binary Numbering
Binary is base 2
  adjective: being in a state of one of two mutually exclusive conditions such as on or off, true or false, molten or frozen, presence or absence of a signal
  From Late Latin bīnārius (“consisting of two”)
Two symbols:
  0 1
Numbers in C that start with 0b are binary
Example: What is 0b110 in base 10?
  0b110 = 1102 = (1 22) + (1 21) + (0 20) = 610
A bit is a single binary digit
A byte is an 8-bit value
powers of two
=
x

## Slide 16: Review: Hexadecimal Numbering
hexadecimal is base 16
  From “hexa” (Ancient Greek ἑξα-) ⇒ six
  and from “decem” (Latin) ⇒ ten
Sixteen symbols
  0 1 2 3 4 5 6 7 8 9 a b c d e f
Numbers in C that start with 0x are hexadecimal numbers
  1610 = 0x1016
Example: What is 0xa5 in base 10?
  0xa5 = a516 = (10 161) + (5 160) = 16510
Hexadecimal numbers are very commonly used in programming to express binary values
  Imagine the difficulty in correctly expressing a 64-bit binary value in your code
=
x

## Slide 17: Binary <---> Hexadecimal Equivalences
Hex Binary: = 1 digit hex = 4 digits binary
  Replace hex digits with binary digits
  Drop leading zeros
  Example: 0x2d to binary
    0x2 is 0b0010, 0xd is 0b1101
    Drop two leading zeros, answer is 0b101101
Binary Hex:
  Pad with enough leading zeros until number of digits is a multiple of 4
  Replace each group of 4 with the HEX equivalent
  Example: 0b101101
    Pad on the left to: 0b 0010 1101
    Replace to get: 0x2d
x

## Slide 18: Number Base Overview (as written in C)
Decimal is base 10 and Hexadecimal is base 16,
Hex digits have 16 values 0 - 9 a - f (written in C as 0x0 – 0xf)
No standard prefix in C for binary (most use hex)
  gcc (compiler) allows 0b prefix others might not
Hex digit | 0x0 | 0x1 | 0x2 | 0x3 | 0x4 | 0x5 | 0x6 | 0x7
Decimal value | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Binary value | 0b0000 | 0b0001 | 0b0010 | 0b0011 | 0b0100 | 0b0101 | 0b0110 | 0b0111
Hex digit | 0x8 | 0x9 | 0xa | 0xb | 0xc | 0xd | 0xe | 0xf
Decimal value | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Binary value | 0b1000 | 0b1001 | 0b1010 | 0b1011 | 0b1100 | 0b1101 | 0b1110 | 0b1111
x

## Slide 19: Hex to Binary (group 4 bits per digit from the right)
1111 1010 0101 0011
0x f
a
5
3
0b1111101001010011
binary start with a 0b in C
x
Each Hex digit is 4 bits in base 2 =

## Slide 20: Binary to Hex (group 4 bits per digit from the right)
4 binary bits is one Hex digit
0b 0110 1010 0011 1111
6
a
3
f
0x6a3f
hex start with 0x in C
x

## Slide 21: Address and Pointers
An address refers to a location in memory, the lowest or first byte in a contiguous sequence of bytes
A pointer is a variable whose contents (or value) can be properly used as an address
  The value in a pointer should be a valid address allocated to the process by the operating system
The variable x is at memory address 0x90001008
The variable pt is at memory location 0x90001000
The contents of pt is the address of x 0x90001008
00
00
00
77
(1 Byte)
90
00
01
08
0x90001000
0x90001001
0x90001002
0x90001003
0x90001004
0x90001005
0x90001006
0x90001007
0x90001008
0x90001009
0x9000100A
0x9000100B
0x9000100C
0x9000100D
0x9000100E
0x9000100F
32-bit address
(hex)
int x =
0x77; ------>
pt is a pointer to x------>
x

## Slide 22: Variables in Memory: Size and Address
The number of contiguous bytes a variable uses is based on the type of the variable
  Different variable types require different numbers of contiguous bytes
Variable names map to a starting address in memory
Example Below: Variables all starting at address 0x80, each box is a byte
x
01010101
memory
char
80
Start
00000000
11111111
10101010
01010101
memory
int
4 bytes
80
82
81
83
Start
Size in bytes
memory
short int
2 bytes
80
10101010
81
01010101
Start
Size in bytes

## Slide 23: Variables: Size
Integer types
  char, int
Floating Point
  float, double
Modifiers for each base type
  short [int]
  long [int, double]
  signed [char, int]
  unsigned [char, int]
  const: variable read only
char type
  One byte in a byte addressable memory
  Signed vs Unsigned Char implementations
  Be careful char is unsigned on arm and signed on other HW like intel
C Data Type | AArch-32 contiguous Bytes | AArch-64 contiguous Bytes | printf specification
char (arm unsigned) | 1 | 1 | %c
short int | 2 | 2 | %hd
unsigned short int | 2 | 2 | %hu
int | 4 | 4 | %d / %i
unsigned int | 4 | 4 | %u
long int | 4 | 8 | %ld
long long int | 8 | 8 | %lld
float | 4 | 4 | %f
double | 8 | 8 | %lf
long double | 8 | 16 | %Lf
pointer * | 4 | 8 | %p
x
size of a pointer is the word size

## Slide 24: sizeof(): Variable Size (number of bytes) Operator
sizeof() operator returns a value of type size_t:
the number of bytes used to store a variable or variable type
  size_t size = sizeof(variable_type);
  or
  size_t size = sizeof(variable_name); // preferred!
The argument to sizeof() is often an expression:
size = sizeof(int * 10);
  reads as:
    number of bytes required to store 10 integers (an array of [10])
#include <stddef.h>
/* size_t type may vary by system but is always unsigned */
x

## Slide 25: Memory Addresses & Memory Content
Variable names in a C statement evaluation
x = x + 1; // Lvalue = Rvalue
Lvalue: when on the left side (Lside or Left value) of the = sign
  address where it is stored in memory – a constant
  Address assigned to a variable cannot be changed at runtime
  Does not require a memory read
  Lside Must evaluate to an address
Rvalue: when on the right side (Rside or Right value) of an = sign
  contents or value stored in the variable (at its memory address)
  requires a memory read to obtain contents
x
00
00
00
77
(1 Byte)
00
00
01
08
0x90001000
0x90001001
0x90001002
0x90001003
0x90001004
0x90001005
0x90001006
0x90001007
0x90001008
0x90001009
0x9000100A
0x9000100B
0x9000100C
0x9000100D
0x9000100E
0x9000100F
32-bit address
(hex)
x's
contents (Rvalue)
x's
address (Lvalue)

## Slide 26: Memory Addresses & Memory Content
y = 42;
x = y; // Lvalue = Rvalue
x on left side (Lside) of the assignment operator = evaluates to:
  Address of the memory assigned to the x – this is x's Lvalue
y on right side (Rside) of the assignment operator = evaluates to:
  Contents of the memory assigned to the variable y (type determines length – number of bytes) - this is y’s Rvalue
So, x = y; is:
Read memory at y (Rvalue); write it to memory at x's address (Lvalue)
x
42
y
42
x
copy
One memory read required
One memory write required

## Slide 27: Introduction: Address Operator: &
Unary address operator (&) produces the address of where an identifier is in memory
  Print g's assigned address
Example this might print:
  value of g is: 42
  address of g is: 0x71a0a0
  (the address will vary)
Tip: printf() format specifier to display an address/pointer (in hex) is "%p"
int main(void)
{
int g = 42;
printf("value of g is: %d\n", g);
printf("address of g is: %p\n", &g);
return EXIT_SUCCESS;
}
x

## Slide 28: Introduction: Address Operator: &
Requirement: identifier must have a Lvalue
  Cannot be used with constants (e.g., 12) or expressions (e.g., x + y)
  Example: &12 does not have an Lvalue,
    so, &12 is not a legal expression
How can I get an address for use on the Rside?
  &var (any variable identifier or name)
  function_name (name of a function, not func());
    &funct_name is equivalent
  array_name (name of the array like array_name[5]);
    &array_name is equivalent
x

## Slide 29: Pointer Variables
In C, there is a variable type for storing an address: a pointer
  Contents of a pointer is an unsigned (positive numbers) memory address
A pointer is defined by placing a star (or asterisk) (*) before the identifier (name)
You also must specify the type of variable to which the pointer points
Pointers are typed! Why?
  The compiler needs to know the size (sizeof()) of the data you are pointing at (number of consecutive bytes to access) to use (dereference) the pointer
When the Rside of a variable contains a memory address, (it evaluates to an address) the variable is called a pointer variable
x
type *name; // defines a pointer; name contains address of a variable of type

## Slide 30: Pointer Variables - 2
A pointer cannot point at itself, why?
  p is defined as (int *), a pointer to an int, but
  the type of &p is (int **), a pointer to a pointer to an int
Pointer variables all use the same amount of memory no matter what they point at (in all but very tiny, often old design, cpu's)
Above prints on a 32-raspberry pi
  int *iptr;
  char *cptr;
  printf("iptr(%u) cptr(%u)\n", sizeof(iptr), sizeof(cptr));
x
% ./example
iptr(4) cptr(4)
int *p = &p; /* is not legal – type mismatch */

## Slide 31: Defining Pointer Variables
Assigning a value to a pointer:
int *p = &i; /* p points at i (assign address i to p) */
Is the same as writing the following definition and assignment statements
    int *p; /* p is defined (not initialized) */
    p = &i; /* p points at i (assign address of i to p */
The * is part of the definition of p and is not part of the variable name
  The name of the variable is simply p, not *p
C mostly ignores whitespace, so these three definitions are equivalent
x
int *p = &i; /* Style A */
int * p = &i; /* Style B */
int* p = &i; /* Style C */

## Slide 32: Using Pointer Variables and the Address Operator & - 1
Recommended: be careful when defining multiple pointers on the same line:
  is not the same as:
  Some find this clearer instead:
int i = 42;
int *p; /* p contains the address of an integer */
p = &i; /* p "points at" i (assign address of i to p) */
x
int *p1, p2;
int *p1, *p2;
int *p1;
int *p2;
42
i
p
42
i
0x10000
p = &i
0x8000
0x10000
Memory
contents
4 bytes
Memory
address
4 bytes
Low address

## Slide 33: Using Pointer Variables and the Address Operator & - 2
As with any variable, its value can be changed
    p = &j; /* p now points at j */
p = &i; /* p now points at i */
x
77
j
p
42
i
0x800
Address
0x1000
0x900
0x900
0x800
Address
0x1000
0x900
77
j
p
42
i
0x1000

## Slide 34: Indirection (or dereference) Operator: *
The indirection operator (*) or the dereference operator to a variable is the inverse of the address operator (&)
address operator (&) can be thought of as:
"get the address of this box”"
indirection operator (*) can be thought of as:
"follow the arrow to the next box and get its contents”"
Indirection operator causes an additional read to occur, when on either the Rside or Lside of a statement
x
0x900
0x900
0x800
42
i or (*p)
p = &i

## Slide 35: Rside Indirection (or dereference) Operator: *
Performs the following steps when the * is on the Rside:
read the contents of the variable to get an address
read and return the contents at that address
  (requires two reads of memory on the Rside)
z = *x; // copy the contents of memory pointed at by x to z
x
Rside x
0x0c
z
0x0c
copy
read (address)
read
Two reads here
read to get an address
(2) read the address to get the value

## Slide 36: Rside Indirection (or dereference) Operator: *
Contents of p is the address of i (p points at i)
x
int i = 42;
int *p;
p = &i;
printf("*p is %d\n", *p);
% ./a.out
*p is 42
Two reads here
read to get an address
(2) read the address to get the value
42
i or (*p)
0x10000
p = &i
0x8000
0x10000
Memory
contents
4 bytes
Memory
address
4 bytes
Low address
No reads here

## Slide 37: Lside Indirection Operator
Performs the following steps when the * is on the Lside:
read the contents of the variable to get an address
write the evaluation of the Rside expression to that address
  (requires one read of memory and one write of memory on the Lside)
x
*p = x; // copy the value of x to the memory pointed at by p
int x
0x0c
Lside p
0x0c
copy
write
read (address)