## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 2.03
ARM – Part 1

## Slide 2: Arm Core Floorplan
Control: Specifies the operation of the CPU
Register File: Memory inside the CPU
  Instructions reference these directly
ALU: Arithmetic Logic Unit: Arithmetic and bitwise hardware (on the bits)
Barrel shifter: (shifts bits in a register during instruction execution - Later)
Instruction Decode: Interprets the the bits in an instruction to determine what the instruction means
Register Decode: controls the registers in during instruction execution
Address and Data: Interface to external RAM (like memory dimms)
Single core arm die Floorplan
x

## Slide 3: 32-Bit Arm - Registers
Registers are memory located within the CPU
Registers are the fastest read and write storage
Register is word size in length stores 32-bit values
  Memory is accessed using pointers in registers
In assembly language, register "addresses" are specified using predefined names starting with an r to differentiate them from main memory addresses which are labels (address)
16 registers: from r0 to r15 (encoded: 0x0 – 0xf)
x
Registers
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
1- Byte
32-bit address
External memory
0x00000000
0xFFFFFFFF
Capacity:4 GBytes
CPU
CPU Memory Bus consists of two parts:
Address bus + Data bus
arithmetic Logic Unit

## Slide 4: Using Arm-32 Registers
There are two basic groups of registers, general purpose and special use
General purpose registers can be used to contain up to 32-bits of data, but you must follow the rules for their use
  Rules specify how registers are to be used so software can communicate and share the use of registers (later slides)
Special purpose registers: have a dedicated hardware use (r15 the pc) or special use when used with certain instructions (r13 & r14)
r15/pc is the program counter that contains the address of an instruction being executed (not exactly … later)
r8
r9
r10
r4
r5
r6
r7
Preserved registers
Called functions can't change
r0
r1
r2
r3
Scratch Registers
First 4 Function Parameters
Function return value
Called functions can change
x
r15/pc
r13/sp
r14/lr
r11/fp
r12/ip
Special Use Registers
function call implementation & long branching
Special Use Registers
program counter

## Slide 5: Assembly and Machine Code
Machine Language (or code): Set of instructions the CPU executes are encoded in memory using patterns of ones and zeros (like binary numbers)
Assembly language is a symbolic version of the machine language
Each assembly statement (called an Instruction)
  Executes exactly one from a list of simple commands
  Instructions describe operations (e.g., =, +, -, *)
  Execution proceeds from low to high memory one instruction at a time unless there is a branch
One line of arm32 machine code contains one instruction in one word (32 bits)
x
0xFF…FF
0x00…00
32-bit address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment
1040c: e28db004 add fp, sp, 4
10410: e59f0010 ldr r0, [pc, 16]
10414: ebffffb3 bl 102e8 <printf>
10418: e3a00000 mov r0, 0
1041c: e24bd004 sub sp, fp, 4
Instruction Instruction (4-bytes)
Address contents Assembly Equivalent
Machine Code
high <- low bytes

## Slide 6: Anatomy of an Assembly instruction (3 address instruction)
Assembly language instructions specify an operation and the operands to the instruction (arguments of the operation)
Three basic types of operands
  Destination: where the result will be stored
  Source: where data is read from
  Immediate: an actual value like the 1 in y = x + 1
add r0, r1, r2
add r0, r1, 1
Operands (variables)
Source Operands
Destination Operand
Immediate Operand
x
operation

## Slide 7: Meaning of an Instruction - ARM
Operations are abbreviated int opcodes (1– 5 letters)
Assembly Instructions are specified with a rigid syntax
  Opcodes are followed by arguments
  Usually the destination argument is next, then one or more source arguments (this is not strictly the case, but it is generally true)
Why this order?
Analogy to C or Java
int r0, r1, r2;
r0 = r1 + r2; // c
x
r0 = r1 + r2
add r0, r1, r2 // assembly

## Slide 8: 32-Bit Arm - Registers
Almost all arithmetic, logic operations and data movement operations involve at least one register
As a result, Register addresses are directly encoded into 4-bit fields in machine instructions (see below)
x
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
registers
Arithmetic & Logic Unit (ALU)
All computations (add, subtract, etc.) are performed in the ALU

## Slide 9: Program Execution: A Series of Instructions
Instructions are retrieved sequentially from memory
Each instruction executes to completion before the next instruction is completed
Conceptually the pc (program counter) points at executing instruction
exceptions: loops, function calls, traps,..
add r0, r1, r1
add r0, r0, r0
add r0, r0, r0
sub r1, r0, r1
r0 = 4 r1 = 2
r0 = 1 r1 = 2
r0 = 8 r1 = 2
r0 = 16 r1 = 2
r0 = 16 r1 = 14
x
Memory Content in Text segment
initial values
Low memory
High memory
Register contents inside the CPU

## Slide 10: How to Access Memory?
31 | 0
Address of a location in memory | 
Consider a = b + c are operands are in memory
  Operation code: add Destination: a
  Operand 1: b Operand 2: c
Aarch32 Instructions are always word size: 32 bits wide
  Some bits must be used to specify the operation code
  Some bits must be used to specify the destination
  Some bits must be used to specify the operands
Address space is 32 bits wide so put a POINTER in a register
31 |  |  | 0 | 
Opcode
Destination
NOT ENOUGH BITS for FULL Addresses to be stored in the instruction
32 bits wide
x
Operand 1
Operand 2
0xFF…FF
0x00…00
32-bit Address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment

## Slide 11: 32-Bit Arm is a Load/Store Architecture
x
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
registers
1- Byte
32-bit address
memory
0x00000000
0xFFFFFFFF
Capacity:4 GBytes
Arithmetic & Logic Unit (ALU)
All computations (add, subtract, etc.) are performed in the ALU
Instruction operands and results are only in registers
Load:
(also called a Fill)
Copy the contents of a variable from memory into a register.
Store:
(also called a Spill)
Copy the contents of a register back into a variable in memory.

## Slide 12: Load/Store Concept: Load Operation
x
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
0x1004
0x4321
0x1
0x2
0x3
0x4
External memory
0x00001000
0x00001004
0x00001008
0x0000100c
0x00001010
// load store concept
int r3;
int x[2];
int *r1;
r1 = &x; // r1 contains x's address
r3 = *(r1); // read memory , load register 3
x[0]
x[1]
points at
reads memory
int x[2] = {0x4321, 0x0};
x[1] = x[0];

## Slide 13: Load/Store Concept: Store Operation
x
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
0x1004
0x4321
0x1
0x2
0x3
0x4
External memory
0x00001000
0x00001004
0x00001008
0x0000100c
0x00001010
x[0]
x[1]
r1 + 4
points at
writes memory
0x1
0x2
0x3
0x4
// load store concept
int r3;
int x[2];
int *r1;
r1 = &x; // r1 contains x's address
r3 = *(r1); // read memory , load register 3
r1 = r1 + 1;
*(r1) = r3; // store register 3 to memory
int x[2] = {0x4321, 0x0};
x[1] = x[0];

## Slide 14: Arm Register Summary
16 Named registers r0 – r15
The operands of almost all instructions are registers
To operate on a variable in memory do the following:
  Load the value(s) from memory into a register
  Execute the instruction
  Store the result back into memory (only if needed!)
Going to/from memory is expensive
  4X to 20X+ slower than accessing a register
Strategy: Keep variables in registers as much as possible
x

## Slide 15: AArch32 Instruction Categories
Data movement to/from memory
  Data Transfer Instructions between memory and registers
    Load, Store
Arithmetic and logic
  Data processing Instructions (registers only)
    Add, Subtract, Multiply, Shift, Rotate, …
Control Flow
  Compare, Test, If-then, Branch, function calls
Miscellaneous
  Traps (OS system calls), Breakpoints, wait for events, interrupt enable/disable, data memory barrier, data synchronization barrier
  Many others that we will not cover in the class
Arithmetic and logic
Data Movement
Control Flow
Miscellaneous
x

## Slide 16: First Look: Copying Values Between Registers - MOV
mov r0, r1
// Copies all 32 bits of the // value in register r1 into
// register r0
register r0
register r1
mov r0, 100
// Expands an 8-bit (imm8) value 100
// stored in the instruction
// into the register r0
register r0
100
x
Immediate "addressing"
register direct "addressing"

## Slide 17: mov – Copies Register Content between registers
mov r1, r5 // r1 = r5
mov r1, 1 // r1 = 1
mov r1, -4 // r1 = -4
constant (immediate value)
destination register
mov
Rd
source register
mov
Rd
Rm
destination register
rot4
imm8
mov Rd, constant // Rd = constant
mov Rd, Rm // Rd = Rm
machine code bit fields
x
Immediate "addressing"
register direct "addressing"
imm8 is 8 bits in size!
IMPACT: limited range of values
(-256) <= imm8 <= 255 + values from "rotating" bits - later

## Slide 18: First Look: Add/Sub Registers
add r0, r1, r2
// Adds r1 to r2 and
// stores the result // in r0
register r0
register r1
register r2
+
x
sub r0, r1, 100
// Perform r1 – 100 and
// stores the result in
// r0
register r0
register r1
100
-

## Slide 19: add/sub – Add or Subtract two integers
add r1, r2, r3 // r1 = r2 + r3
sub r1, r1, 1 // r1 = r1 – 1; or r1--
add r1, r2, 234 // r1 = r2 + 234
add Rd, Rn, constant // Rd = Rn + constant
sub Rd, Rn, constant // Rd = Rn - constant
add Rd, Rn, Rm // Rd = Rn + Rm
sub Rd, Rn, Rm // Rd = Rn - Rm
Operand 2 constant
destination
add/sub
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
add/sub
Rd
Rn
operand 1
Rm
x

## Slide 20: Writing a Sequence of Add & Subtract Instructions
You need to perform the following sequence of integer adds/subtracts
a = b + c + d - e;
Since ARM uses a three-operand instruction set, you can only operate on two operands at a time
So, you need to use one register as an accumulator and create a sequence of add instructions to build up the solution
a = b + c + d - e;
r0 = r1 + r2 + r3 – r4;
r0 = ((r1 + r2) + r3) – r4;
r0 = r1 + r2;
r0 = r0 + r3
r0 = r0 – r4
r0  a
r1  b
r2  c
r3  d
r4  e
a = (b + c) – 5;
r0 = (r1 + r2) – 5;
x
add r0, r1, r2
add r0, r0, r3
sub r0, r0, r4
add r0, r1, r2
sub r0, r0, 5

## Slide 21: Line Layout in an Arm Assembly Source
Assembly language source text files are line oriented (each ending in a '\n')
Each line represents a starting address in memory and does one of:
  Specifies the contents of memory for a variable (segments containing data)
  Specifies the contents of memory for an instruction (text segment)
  Assembler directives tell the assembler to do something (for example, change label scope, define a macro, etc.) that does not allocate memory
Each line is organized into up to four columns
  Not every column is used on each line
  Not every line will result in memory being allocated
label: operation operand(s) // comments
tab
white space
white space
x
column 1 column 2 column 3 column 4

## Slide 22: Labels in Arm Assembly - 1
Labels (optional); starts in column 1 (often on a line by itself ABOVE the "operation")
  Only put a label on a line when you need to associate a name (a global variable, a function name, a loop/ branch target, etc.) to that line's location in memory
  You then refer to the address by name in an instruction
Operation type 1: assembler directives (all start with a period e.g. .word )
Operation Type 2: assembly language instructions
Zero or more operands as required by the instruction or assembler directive
Comments: C and C++ style; also @ in the place of a C++ comment //
x
label: operation operand(s) // comment
// assembler directive below
cnt: .word 5 /* define a global int cnt = 5; */
/* instruction example below */
add r1 r2, r3 // add the values

## Slide 23: Labels in Arm Assembly - 2
Remember, a Label associates a name with memory location
Regular Label:
  Used with a Function name (label) or all static variables in any of the data segments
Local Label: Name starts with .L (local label prefix) only usable in the same file
  Targets for
    branches: if switch, goto, break, continue,
    loops: for, while, do-while
  Anonymous variables (the address of literal not the address of foo in the following)
    char *foo = "literal";
x
.Lmesg: .string "Hello CSE30! We Are CountinG UpPpER cASe letters!"
main:
push {fp, lr}
.Lwhile:
add r2, r2, 1 // increment char pointer
local label
Regular label
local label
label main is the starting address of the push instruction
label .Lmesg is the starting address for the ascii string
label .Lwhile is the starting address of the add instruction

## Slide 24: Unconditional Branching – Forces Execution to Continue at a Specified Label (goto)
b .Ldone // goto .Ldone
:
.Ldone:
add r0, EXIT_SUCCESS // set return value
Unconditional Branch instruction (branch to only local labels in CSE30)
b .Llabel
Causes an unconditional branch (aka goto) to the instruction with the address .Llabel
.Llabel is called a branch target label (the "target" of a branch instruction)
Be careful! do not to branch to a function label!
.Llabel: translates into an number offset being imm24 shifted left two bits (+/- 32 MB)
b
imm24
x
imm24 is Relative direction
from the branch instruction (in +/- instructions)

## Slide 25: Examples of of Unconditional Branching
Branches are used to change execution flow using labels as the branch target
In these example, .Lforward and .Lbackward are the branch target labels
Branch target labels are placed at the beginning of the line (or above it)
Caution: Backward branches should only used with loops!
b .Lforward
add r1, r2, 4
add r0, r6, 2
add r3, r7, 4
.Lforward:
sub r1, r2, 4
.Lbackward:
add r1, r2, 4
sub r1, r2, 4
add r4, r6, r7
b .Lbackward
// not reachable unless
// there is a label after the .b above
Backward Branch
(Infinite loop)
Unconditional Branch Forward
x
Not a practical example as this code is unreachable
Branch target (local label)

## Slide 26: Never Branch to the following instruction: It is not needed!
x
mov r2, 0
b .Lnext // do not do this, not needed
.Lnext:
add r1, r2, r3
mov r2, 0
add r1, r2, r3

## Slide 27: Anatomy of a Conditional Branch: If statement
Branch guard: determines when to execute the "condition true block" or the "condition false block"
In C, when the branch guard (condition test) evaluates non-zero you fall through to the condition true block, otherwise you branch to the condition false (else) block
Step 1: evaluate the branch guard(s) (involves one or more compares/tests)
Step 2: If branch guard evaluates to be false
  branch around the true block and execute the else block
  otherwise "fall through" and execute the true block
Block order in C is where the True Block appears above the False block
if (r0 == 5) {
/* condition block #1 */
/* branch to "here" */
} else {
/* condition block #2 */
/ * fall through to "here" */
}
// resume here
Branch condition
Test (branch guard)
r0 == 5
condition true block
condition else block

## Slide 28: cmp/cmm – Making Conditional Tests
cmp r1, 0 // r1 – 0 and sets flags on the result
cmp r1, r2 // r1 – r2 and sets flags on the result
cmp Rn, constant // Rn – constant; then sets condition flags
cmm Rn, constant // Rn + constant; then sets condition flags
cmp Rn, Rm // Rn – Rm; then sets condition flags
cmm Rn, Rm // Rn + Rm; then sets condition flags
Operand 2 constant
cmp/cmm
rot4
imm8
Rn
operand 1
Operand 2
cmp/cmm
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
The values stored in the registers Rn and Rm are not changed
The assembler will automatically substitute cmn for negative immediate values
x

## Slide 29: Quick Overview of the Condition Bits/Flags
The CSPR is a special register (like the other registers) in the CPU
The four bits at the left are called the Condition Code flags
  Summarize the result of a previous instruction
  Not all instruction will change the CC bits
Specifically, Condition Code flags are set by cmm/cmp (and others)
Example: cmp r4, r3
N (Negative) flag: Set to 1 when the result of r4 – r3 is negative, set to 0 otherwise
Z (Zero) flag: Set to 1 when the results of r4 – r3 is 0, set to 0 otherwise
C (Carry bit) flag: Set to 1 when r4 – r3 does not have a borrow, set to 0 otherwise
V flag (oVerflow): Set to 1 when r4 – r3 causes an overflow, set to 0 otherwise
N
Z
C
V
CPSR
31
30
29
28
5 0
Execution Mode
x

## Slide 30: Conditional Tests: Implementing ARM Branch guards
Branch instruction
bsuffix .Llabel
Bits in the condition field specify the conditions when the branch happens
If the condition evaluates to be true, next instruction executed is at .Llabel:
If the condition evaluates to be false, next instruction executed is immediately after the branch
Unconditional branch is when the condition is "always"
bsuffix
imm24
cond
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
BNE | Not equal | Z = 0
BGE | Signed ≥ ("Greater than or Equal") | N = V
BLT | Signed < ("Less Than") | N ≠ V
BGT | Signed > ("Greater Than") | Z = 0 && N = V
BLE | Signed ≤ ("Less than or Equal") | Z = 1 ¦¦ N ≠ V
BMI | Minus/negative | N = 1
BPL | Plus - positive or zero (non-negative) | N = 0
B | Branch Always (unconditional) | 
x
imm24 is Relative direction
from the branch instruction
(in +/- instructions)
Use a local label with branch instructions

## Slide 31: Branch and Loop Guard Strategy
How to implement a branch/loop guard in CSE30
Use a cmp/cmm instruction to set the condition bits
Follow the cmp/cmm with one or more variants of the conditional branch instruction
  Conditional branch instructions if evaluate to true (based on the flags set by the cmp) the next instruction will the one at the branch label
  Otherwise, execution falls through to the instruction that immediately follows the branch
You may have one or more conditional branches after a single cmp/cmm
cmp r0, 10
ble .Lendif
// True Block
.Lendif:
Branch guard
x

## Slide 32: Program Flow: Simple If statement, No Else
Realize that in ARM assembly you can only either "fall through" to the next instruction or branch to a specific instruction
Approach: adjust the conditional test then branch around the true block
Use a conditional test that specifies the inverse of the condition used in C
  This preserves C block order
C source Code | Incorrect Assembly | Correct Assembly
int r0; if (r0 > 10) { // True Block } | cmp r0, 10 bgt .Lendif // True Block .Lendif: | cmp r0, 10 ble .Lendif // True Block .Lendif:
x

## Slide 33: Branch Guard "Adjustment" Table Preserving C Block Order In Assembly
if (r0 compare 5)
/* condition true block */
/* then fall through */
}
Compare in C | "Inverse" Compare in C | Assembly using Inverse Compare
== | != | bne
!= | == | beq
> | <= | ble
>= | < | blt
< | >= | bge
<= | > | bgt
cmp r0, 5
inverse compare .Lelse
// condition true block
// then fall through
.Lendif:
x

## Slide 34: Arm Conditional Branching Simple IF no else
If statements in ARM
Step 1: make a conditional test using a cmp instruction
Step 2: if test evaluates to FALSE, branch around the condition true block with a one of the conditional branch instruction
x
cmp r0, 5
bne .Lendif
/* condition true block */
/* then fall through */
.Lendif:
/* branch around to this code */
If r0 == 5 false
then branch around the true block
int r0;
if (r0 == 5) {
/* condition true block */
/* then fall through */
}
/* branch around to this code */
If r0 == 5 true
then fall through to the true block
C If statement
ARM If statement

## Slide 35: If statement examples – Branch Around the True block!
int r0;
if (r0 == 5) {
r1 = r2++ + r3;
}
r3 = r2;
cmp r0, 5
bne .Lendif
add r1, r2, r3
add r2, r2, 1
.Lendif:
mov r3, r2
x
If r0 == 5 false
then branch around the true block
Fall through
int r0;
if (r0 <= 5) {
r1 = r2++;
}
r3 = r2;
cmp r0, 5
bgt .Lendif
mov r1, r2
add r2, r2, 1
.Lendif:
mov r3, r2
Fall through

## Slide 36: Branching Avoid: Spaghetti Code ("goto structure")
Do not use unnecessary branches
Optimize your use of "fall throughs"
For example: Do not make a conditional branch around an unconditional branch that immediately follows it
Do not do the following:
cmp r0, 0
beq .Lthen
b .Lendif
.Lthen:
add r1, r1, 1
.Lendif:
add r1, r1, 2
x
Do the following:
cmp r0, 0
bne .Lendif
// fall through
add r1, r1, 1
.Lendif:
add r1, r1, 2
Caution!
Two adjacent branches

## Slide 37: Program Flow: If with an Else
Approach:
adjust the conditional test to branch to the False Block
Fall through to the True Block
Bottom of the True Block unconditionally branches around the False block
C source Code | Assembly
int r0; if (r0 > 10) { // true block // branch always around the false block } else { // false block } | cmp r0, 10 ble .Lelse /fall through // true block b .Lendif .Lelse: // false block // fall through .Lendif:
x

## Slide 38: If with an Else Examples
if (r0 == 5) {
/* cond. true block */
/* branch around false */
} else {
/* condition false block */
/* fall through */
}
r1 = 4;
If r0 == 5 false
then branch to false block
x
cmp r0, 5
bne .Lelse
// Fall through
// cond. true block
/*
* Now branch around the
* condition false block
*/
b .Lendif
.Lelse
// condition false block
// fall through
.Lendif:
mov r1, 4
If r0 == 5 false
then branch to false block

## Slide 39: If with an Else Examples
…
if (r0 < r1) {
r2 = 1;
// branch around else
} else {
r2 = 0;
/* fall through */
}
r4 = r2 + r4;
  cmp r0, r1
  bge .Lelse
  mov r2, 1
  b .Lendif
.Lelse:
mov r2, 0
/* fall through */
.Lendif:
add r4, r2, r4
x
If r0 < r1 false
then branch to false block
Branch condition
Test (branch guard)
condition true block
condition false block

## Slide 40: If statement – C Block Reordering
if (r0 != 5) {
/* condition block #2 */
} else {
/* condition block #1 */
/* fall through */
}
Block order: (the order the blocks appear in C code) can be changed by inverting the conditional test, swapping the order of the true and false blocks
if (r0 == 5) {
/* condition block #1 */
} else {
/* condition block #2 */
/ * fall through */
}
x
Branch condition
Test (branch guard)
condition true block
condition false block
condition true block
condition false block
Branch condition
Test (branch guard)

## Slide 41: Preserving the same branch guard test
if (r0 < r1) {
// true block
r2 = 1;
// now branch around else
} else {
// false block
r2 = 0;
/* fall through */
}
r4 = r2 + r4;
x
  cmp r0, r1
  blt .Lelse
  // false block
mov r2, 0
  b .Lendif // around else
.Lelse:
  // true block
  mov r2, 1
/* fall through */
.Lendif:
add r4, r2, r4
Swap the order of true and false blocks
Same branch guard test

## Slide 42: Switch Statement
switch (r0) {
case 1:
// block 1
break;
case 2:
// block 2
break;
default:
// default 3
break;
}
x
cmp r0, 1
beq .Lblk1
cmp r0, 2
beq .Lblk2
// fall through
// default 3
b .Lendsw // break
.Lblk1:
// block 1
b .Lendsw // break
.Lblk2:
// block 2
// fall through
// NO b .Lendsw
.Lendsw:
Branch block

## Slide 43: Bad Style: Branching Upwards (When Not a loop)
Do not Branch "Upwards" unless it is part of a loop (later slides)
If you cannot easily write the equivalent C code for your assembly code, you may have code that is harder to read than it should be
Action: adjust your assembly code to have a similar structure as an equivalent version written in C
  mov r3, r4
  b .Llabel2
.Llabel1:
mov r2, 0
b .Llabel3
.Llabel2:
add r4, r3, r2
b .Llable1
.Llabel3:
add r4, r2, r4
x
Upwards
branch
Do not do this
  mov r3, r4
  add r4, r3, r2
mov r2, 0
add r4, r2, r4
Do this

## Slide 44: Review – Short Circuit or Minimal Evaluation
In evaluation of conditional guard expressions, C uses what is called short circuit or minimal evaluation
Each expression argument is evaluated in sequence from left to right including any side effects (modified using parenthesis), before (optionally) evaluating the next expression argument
If after evaluating an argument, the value of the entire expression can be determined, then the remaining arguments are NOT evaluated (for performance)
x
if ((x == 5) || (y > 3)) // if x == 5 then y > 3 is not evaluated
if ((a != 0) && func(b)) // if a is 0, func(b) is not called
// do something

## Slide 45: Program Flow – If statements && compound tests - 1
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
bne .Lendif
cmp r1, 3
ble .Lendif
mov r2, r5 // true block
// fall through
.Lendif:
mov r4, r3
If r0 == 5 false
then short circuit branch around the true block
x

## Slide 46: Program Flow – If statements && compound tests - 2
cmp r0, 5 // test 1
bne .Lelse
cmp r1, 3 // test 2
ble .Lelse
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse:
mov r5, r2 // false block
// fall through
.Lendif:
mov r4, r3
if r0 == 5 false
then short circuit branch to the false block
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
// branch around else
} else {
r5 = r2; False block */
/* fall through */
}
r4 = r3;
x
if r1 > 3 false
then branch to the false block
test1 test2

## Slide 47: Program Flow – If statements || compound tests - 1
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lendif
// fall through
.Lthen:
mov r2, r5 // true block
/* fall through */
.Lendif:
mov r4, r3
If r0 == 5 true, then branch to true block
if r1 > 3 false then branch around true block
x

## Slide 48: Program Flow – If statements || compound tests - 2
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lelse
// fall through
.Lthen:
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse
mov r5, r2 // false block
// fall through
.Lendif:
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* branch around else */
} else {
r5 = r2; // false block
/* fall through */
}
x
If r0 == 5 true, then branch to the true block
if r1 > 3 false then branch to false block

## Slide 49: Program Flow – Pre-test and Post-test Loop Guards
loop guard: code that must evaluate to true before the next iteration of the loop
If the loop guard test(s) evaluate to true, the body of the loop is executed again
pre-test loop guard is at the top of the loop
  If the test evaluates to true, execution falls through to the loop body
  if the test evaluates to false, execution branches around the loop body
post-test loop guard is at the bottom of the loop
  If the test evaluates to true, execution branches to the top of the loop
  If the test evaluates to false, execution falls through the instruction following the loop
x
while (i < 10) {
/* block */
i++;
}
pre-test
loop guard
loop control variable
zero or more iterations
do {
/* block */
i++;
} while (i < 10);
post-test
loop guard
one or more iterations

## Slide 50: Pre-Test Guards - While Loop
.Lwhile:
cmp r1, 10
bge .Lendw
// block
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
/* block */
r1++;
}
r2 = r1;
x
pre-test
loop guard
loop iteration
inverted test

## Slide 51: Pre-Test Guards - While Loop
x
.Lwhile:
cmp r1, 10
bge .Lendw
cmp r2, r1
beq .Lnext
// block
.Lnext:
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
if (r2 != r1) {
/* block */
}
r1++;
}
r2 = r1;
pre-test
loop guard
loop iteration
if stmt guard

## Slide 52: Post-Test Guards – Do While Loop
.Ldo:
// block
add r1, r1, 1
cmp r1, 10
blt .Ldo
mov r2, r1
do {
/* block */
r1++;
} while (r1 < 10);
r2 = r1;
x
loop iteration
post-test
loop guard
test is not inverted

## Slide 53: Post-Test Guards – Do While Loop
.Ldo:
cmp r2, r1
beq .Lnext
// block
.Lnext
add r1, r1, 1
cmp r1, 10
blt .Ldo
move r2, r1
x
do {
if (r2 != r1) {
/* block */
}
r1++;
} while (r1 < 10);
r2 = r1;
loop iteration
post-test
loop guard

## Slide 54: Program Flow – Counting (For) Loop Version 1
mov r1, 0
.Lfor:
cmp r1, 10
bge .Lendfr
// block code
add r1, r1, 1
b .Lfor
.Lendfr:
A counting loop has three parts:
Pre-loop setup
Pre-test loop guard conditions
Post-loop update
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Post loop update
Pre loop setup
Pre-test loop guard

## Slide 55: Program Flow – Counting (For) Loop – Version 2
Alternative:
move Pre-test loop guard before the loop
Add post-test loop guard
  converts to do while
  removes an unconditional branch
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
mov r1, 0
cmp r1, 10
bge .Lendfr
.Ldo:
// block code
add r1, r1, 1
cmp r1, 10
blt .Ldo
.Lendfr:
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Pre-loop setup
Post loop update
Pre-test loop guard
Post-test loop guard

## Slide 56: Nested loops
Nest loop blocks as you would in C or Java
for (r3 = 0; r3 < 10; r3++) {
r0 = 0;
do {
r0 = r0 + r1++;
} while (r1 < 10);
// fall through
r2 = r2 + r1;
}
r5 = r0;
x
mov r3, 0
.Lfor:
cmp r3, 10 // loop guard
bge .Lendfor
mov r0, 0
.Ldo:
add r0, r0, r1
add r1, r1, 1
cmp r1, 10 // loop guard
blt .Ldo
// fall through
add r2, r2, r1
add r3, r3, 1 // loop iteration
b .Lfor
.Lendfor:
mov r5, r0

## Slide 57: Keep loops Properly Nested: Do not branch into the middle of a loop
It is hard to understand and debug loops when you branch into the middle of a loop
Keep loops proper nested
Do not do the following:
.Lloop1:
add r1, r1, 1
.Lloop2:
add r2, r2, 1
add r2, r1, r3
cmp r1, 10
blt .Lloop1
beq .Lend1
add r3, r3, 1
cmp r2, 20
ble .Lloop2
.Lend1:
x
Bad practice: branch into loop body

## Slide 58: Extra Slides

## Slide 59: CPU Operational Overview: Executing Machine Code
0001042c <inloop>:
1042c: e3530061 cmp r3, 0x61
10430: ba000002 blt 10440 <store>
10434: e353007a cmp r3, 0x7a
10438: ca000000 bgt 10440 <store>
1043c: e2433020 sub r3, r3, #32
00010440 <store>:
10440: e7c13002 strb r3, [r1, r2]
10444: e2822001 add r2, r2, 0x1
10448: e7d03002 ldrb r3, [r0, r2]
1044c: e3530000 cmp r3, 0x0
10450: 1afffff5 bne 1042c <inloop>
Everything has a memory address: instructions & data
  Machine code uses addresses for loops, branches, function calls, variables, etc.
1 Fetch
  read the instruction into memory (fetch)
  program counter is automatically incremented (+4) to contain the address of the next instruction in memory Instructions are 32 bits
2 Decode
  Decodes the instruction and sets up execution
3 Execute
  CPU completes the execution of the instruction
  Execution may alter the pc to take branches, etc.
  Go to fetch
address contents
assembly version
text segment in memory
x
r15/pc
r15/pc
r15/pc
r15/pc
r15/pc
r15/pc
Edited output For output Created by the command
%objdump –d a.out
%objdump –d –S a.out adds source code

## Slide 60: Program Execution: Looping in the Execution Flow
Repeat the series of instructions in a loop means altering the flow of execution
This is used with if statements and loops
Below is an infinite loop (br instruction: unconditional branch: "goto"
.Lloop: add r0, r1, r1
add r0, r0, r0
add r0, r0, r0
sub r1, r0, r1
r0 = 4 r1 = 2
r0 = 1 r1 = 2
r0 = 8 r1 = 2
r0 = 16 r1 = 2
r0 = 16 r1 = 14
x
br .Lloop
branch to the instruction at memory location with the label: .Lloop
the address of this instruction has the name .Lloop
Infinite loop C
do {
r0 = r1 + r1;
r0 = r0 + r0;
r0 = r0 + r0;
r1 = r0 – r1;
} while(1);

## Slide 61: Branch Target Address (BTA): What Is imm24?
Previous slide: phases of execution: (1) fetch, (2) decode, (3) execute
The pc (r15) contains the address of the instruction being fetched, which is two instructions ahead or executing instruction + 8 bytes
Branch target address (or imm24) is the distance measured in the # of instructions (signed, 2's complement) from the fetch address contained in r15 when executing the branch
imm24 | 0x 00 00 02
0001042c <inloop>:
1042c: e3530061 cmp r3, 0x61
10430: ba000002 blt 10440 <store>
10434: e353007a cmp r3, 0x7a
10438: ca000000 bgt 10440 <store>
1043c: e2433020 sub r3, r3, #32
00010440 <store>:
10440: e7c13002 strb r3, [r1, r2]
10444: e2822001 add r2, r2, 0x1
10448: e7d03002 ldrb r3, [r0, r2]
1044c: e3530000 cmp r3, 0x0
10450: 1afffff5 bne 1042c <inloop>
x
executing instruction
decode instruction
fetch instruction
BTA: + 2 instructions
target address = 0x10440
fetch address = 0x10438
distance(bytes) = 0x00008
distance(instructions)= 0x8/(4 bytes/instruction)= 0x2

## Slide 62: Program Flow – multiple branches, one cmp
There are many other ways to do this
if ((r0 > 5) {
/* condition block 1 */
// branch to endif
} else if (r0 < 5){
/* condition block 2 */
// branch to endif
} else {
/* condition block 3 */
// fall through to endif
}
// endif
r1 = 11;
cmp r0, 5
bgt .Lblk1
blt .Lblk2
// fall through
// condition block 3
b .Lendif
.Lblk1:
// condition block 1
b .Lendif
.Lblk2:
// condition block 2
b .Lendif
.Lendif:
mov r1, 5
special case: multiple branches from one cmp
x

## Slide 63: How are I – Type Constants Encoded in the instruction?
Aarch32 provides only 8-bits for specifying an immediate constant value
Without "rotation" immediate values are limited to the range of positive 0-255
Imm8 expands to 32 bits and does a rotate right to achieve additional constant values (YUCK)
positions to
rotate X 2
unsigned value to rotate
rot4 value | 32-bit constant result
0000 | 0000 0000 0000 0000 0000 0000 1111 1111
0001 (2 bits) | 1100 0000 0000 0000 0000 0000 0011 1111
x
two bits rotated right
results are interpreted as a 2's complement number

## Slide 64: Rot4 - Imm8 Values
positions to
rotate X 2
unsigned value to rotate
00000001
x
How would 256 be encoded?
  rotate = 12, imm8 = 1
Bottom line: the assembler will do this for you
If you try and use an immediate value that it cannot generate it will give an error
There is a workaround - later
results are interpreted as a 2's complement number