## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 2.12
Arm – Part 2

## Slide 2: What is a Bitwise Operation?
Bitwise operators are applied independently to each of the corresponding bit positions in each variable
Each bit position of the result depends only on bits in the same bit position within the operands
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0
x

## Slide 3: Bitwise (Bit to Bit) Operators in C
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
output = a | b;
| with 1 to set a bit to 1
| with 0 to let a bit through
a | ~a
0 | 1
1 | 0
output = ~a;
a | b | a ^ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
output = a ^ b; //EOR
^ with 1 will flip the bit
^ with 0 to let a bit through
a | b | a & b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
output = a & b;
& with 1 to let a bit through
& with 0 to set a bit to 0
0110
& 1100
----
0100
Bitwise
AND
0110
| 1100
----
1110
Bitwise
OR
0110
^ 1100
----
1010
Bitwise
EOR
~ 1100
----
0011
Bitwise
NOT
x

## Slide 4: Bitwise Not (vs Boolean Not)
a | ~a
0 | 1
1 | 0
in C
int output = ~a;
x
Boolean operators act on the entire value not the individual bits
Meaning | Operator | Operator | Meaning
Boolean NOT | !b | ~b | Bitwise NOT
 | Bitwise Not
number | 0101 1010 0101 1010 1111 0000 1001 0110
~number | 1010 0101 1010 0101 0000 1111 0110 1001
Type | Operation | result
bitwise | ~0x01 | 1111 1111 1111 1111 1111 1111 1111 1110
Boolean | !0x01 | 0000 0000 0000 0000 0000 0000 0000 0000
~ 1100
----
0011
Bitwise NOT

## Slide 5: MVN (not)
A bitwise NOT operation
mvn r0, r1
// Copies all 32 bits
// of the value held
// in register r1 into
// the register r0
// then does a bitwise NOT
register r0
register r1
mvn r0, 12
// Expands an imm8 value 0x0c
// stored in the instruction
// into a register then does
// a bitwise NOT
0xffff fff3
0x0c
x
~ 1100
----
0011
Bitwise NOT
register r0
0xfffffff3
0x 0c
imm8 expansion
0x0000000c
bitwise not

## Slide 6: mvn – Copies NOT (~)
constant (immediate value)
destination register
mvn
Rd
source register
mvn
Rd
Rm
destination register
bitwise NOT operation. Immediate (constant) version copies to 32-bit register, then does a bitwise NOT
mvn r1, 4 // x = ~4
mvn r1, r5 // x = ~y in C
mvn r1, 0 // x = -1
imm8 | extended imm8 | inverted imm8 | signed base 10
0x00 | 0x00 00 00 00 | 0xff ff ff ff | -1
0xff | 0x00 00 00 ff | 0xff ff ff 00 | -256
0xfffffffb
r1
0x4
invert the bits
0x00000004
copy into 32 bits zero extend
0xaaaaaaaa
0x55555555
r5
r1
rot4
imm8
~ 1100
----
0011
Bitwise NOT
x
mvn Rd, constant // Rd = constant
mvn Rd, Rm // Rd = Rm
0x0
0xffffffff
r1

## Slide 7: Bitwise Instructions
<op> Rd, Rn, constant // Rd = Rn <op> constant
<op> Rd, Rn, Rm // Rd = Rn <op> Rm
Operand 2 constant
destination
<op>
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
<op>
Rd
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
Bitwise <op> description | C Syntax | Arm <op> Syntax Op2: either register or constant value | Operation
Bitwise AND | a & b | and Rd, Rn, Op2 | Rd = Rn & Op2
Bitwise OR | a ¦ b | orr Rd, Rn, Op2 | Rd = Rn ¦ Op2
Exclusive OR | a ^ b | eor Rd, Rn, Op2 | Rd = Rn ^ Op2
Bitwise NOT | a = ~b | mvn Rd, Rn | Rd = ~Rn
x

## Slide 8: Bitwise versus C Boolean Operators
Boolean operators act on the entire value not the individual bits
bitwise & versus Boolean &&
0x10 & 0x01 = 0x00 (bitwise)
0x10 && 0x01 = 0x01 (Boolean)
bitwise ~ versus Boolean !
~0x01 = 0xfffffffe (bitwise)
!0x01 = 0x0 (Boolean)
!0xff = 0x0 (Boolean)
Meaning | Operator |  | Operator | Meaning
Boolean AND | a && b |  | a & b | Bitwise AND
Boolean OR | a ¦¦ b |  | a ¦ b | Bitwise OR
Boolean NOT | !b |  | ~b | Bitwise NOT
x
Boolean Operators
Bitwise Operators

## Slide 9: The act (operation) of Masking
Bit masks access/modify specific bits in memory
Masking act of applying a mask to a value with a specific op:
orr: 0 passes bit unchanged, 1 sets bit to 1 (a = b | c; // in C)
eor: 0 passes bit unchanged, 1 inverts the bit (a = b ^ c; // in C)
and: 0 clears the bit, 1 passes bit unchanged (a = b & c; // in C)
x
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0

## Slide 10: Mask on
force bits to 1 "mask on" operation
  1 to set a bit to 1
  0 to let a bit through unchanged
orr r1, r2, r3
r1 = r2 | r3; // in C
x
Example: force lower 16 bits to 1
DATA: r2 0xab ab ab 77
orr
MASK: r3 0x00 00 ff ff
RSLT: r1 0xab ab ff ff
forces to a 1
unchanged
Example: force lower 8 bits to 1
DATA: r2 0xab ab ab 77
orr r1 r2, 0xff
r1 = r2 | 0xff; // in C
RSLT: r1 0xab ab ab ff

## Slide 11: Mask off
x
force bits to 0 "mask off" operation
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
r1 = r2 & r3; // in C
Example: force lower 8 bits to 0
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff ff ff 00
RSLT: r1 0xab ab ab 00
forces to a 0
unchanged
Example: force lower 8 bits to 0
DATA: r2 0xab ab ab 77
and r1 r2, 0xffffff00
r1 = r2 & 0xffffff00; // in C
RSLT: r1 0xab ab ab 00

## Slide 12: Extracting (Isolate) a Field of Bits with a mask
x
extract top 8 bits of r2 into r1
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff 00 00 00
RSLT: r1 0xab 00 00 00
forces to a 0
unchanged
extract top 8 bits of r2 into r1
DATA: r2 0xab ab ab 77
and r1, r2, 0xff000000
RSLT: r1 0xab 00 00 00
r1 = r2 & 0xff000000; // in C

## Slide 13: Finding if a bit is set
x
query the status of a bit "bit status" operation
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, 0x02
cmp r1, 0
beq .Lendif
// code for is set
.Lendif:
Example is bit 1 set
DATA: r2 0xab ab ab 77
and
MASK: 0x00 00 00 02 is bit 1 set?
RSLT: r1 0x00 00 00 02 != 0 if set
forces to a 0
unchanged
  unsigned int r1, r2;
  // code
  r1 = r2 & 0x02
  if (r1 != 0) {
  // code for is set
  }
  unsigned int r2;
  // code
  if ((r2 & 0x02) != 0) {
  // code for is set
  }

## Slide 14: Even/Odd
Even or odd, check LSB (same as mod %2)
check LSB (bit 0) if set then odd, else even
and r1, r2, 0x01
cmp r1, 0x01
bne .Lendif
// code for handling odd numbers
.Lendif:
x
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 01 (mod 2 even or odd)
RSLT: r1 0x00 00 00 01 (odd)
forces to a 0
unchanged
  unsigned int r2;
  // code
  if ((r2 & 0x01) != 0) {
  // code for handling odd numbers
  }

## Slide 15: MOD %<power of 2>
remainder (mod): num % d where num ≥ 0 and d = 2k
mask = 2k -1 so for mod 16, mask = 16 -1 = 15
and r1, r2, r3
x
Example: %2
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 01 (mod 2 even or odd)
RSLT: r1 0x00 00 00 01 (odd)
forces to a 0
unchanged
Example: Mod 16
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 0f (mod 16)
RSLT: r1 0x00 00 00 07
forces to a 0
unchanged

## Slide 16: Flipping bits: bit toggle Used in PA7/PA8
x
invert (flip) bits "bit toggle" operation
  1 will flip the bit
  0 to let a bit through
eor r1, r2, r3
Observation: When applied twice, it returns the original value (symmetric encoding)
With a mask of all 1's is a 1's compliment
Example: invert (flip) the lower 8-bits
DATA: r2 0xab ab ab 77
eor
MASK: r3 0x00 00 00 ff
RSLT: r1 0xab ab ab 88
inverts (flips)
unchanged
88: 1000 1000
DATA: r1 0xab ab ab 88
eor
MASK: r3 0x00 00 00 ff apply a 2nd time
RSLT: r1 0xab ab ab 77 original value!
inverts (flips)
77: 0111 0111
Example: flip the lower 8-bits
eor r1, r2, 0xff
unsigned int r1, r2;
r1 = r2 ^ 0xff;

## Slide 17: Unsigned Integers (positive numbers) with Fixed # of Bits
4 bits is = ONLY 16 distinct values
Modular (C operator: %) or clock math
  Numbers start at 0 and “wrap around” after 15 and go back to 0
Keep adding 1
wraps (clockwise)
  0000 -> 0001 … -> 1111 -> 0000
Keep subtracting 1
wraps (counter-clockwise)
  1111 -> 1110 … -> 0000 -> 1111
Addition and subtraction use normal "carry" and "borrow" rules, just operate in binary
x

## Slide 18: Problem: How to Encode Both Positive and Negative Integers
How do we represent the negative numbers within a fixed number of bits?
  Allocate some bit patterns to negative and others to positive numbers (and zero)
distinct bit patterns to encode positive and negative values
Unsigned values: 0 ... –1
Signed values: … –1 (dividing the range in ~ half including 0)
On a number line (below): 8-bit integers – signed and unsigned (e.g., char in C)
-
+
-1
Same “width” (same number of encodings), just shifted in value
-1
Unsigned
Signed
x
-1 comes from counting 0 as a "positive" number

## Slide 19: Two’s Complement: The MSB Has a Negative Weight
4-bit (w = 4) weight = = -23 = -8
  10102 unsigned: 1x23 + 0x22 + 1x21 + 0x20 = 10
  10102 two’s complement: -1x23 + 0x22 + 1x21 + 0x20 = -8 + 2 = –6
  -8 in two’s complement: 10002 = -23 + 0 = -8
  -1 in two’s complement: 11112 = -23 + (23 – 1) = -8 + 7 = -1
weight is ), all other bits: have positive weights )
. . .
b0
bn-1
bn-2
x

## Slide 20: 2's Complement Signed Integer Method
Positive numbers encoded same as unsigned numbers
All negative values have a one in the leftmost bit
All positive values have a zero in the leftmost bit
  This implies that 0 is a positive value
Only one zero
For n bits, Number range is) to - 1)
  Negative values “go 1 further” than the positive values
Example: the range for 8 bits: -128, -127, .. 0, .. 126, +127
Example the range for 32 bits: -2147483648 .. 0, .. +2147483647
Arithmetic is the same as with unsigned binary!
x

## Slide 21: Sign Extension (how type promotion works)
Sometimes you need to work with integers encoded with different number of bits
8 bits (char) -> (16 bits) short -> (32 bits) int
Sign extension increases the number of bits: -bit wide signed integer , EXPANDS to a wider n + -bit signed integer where both have the same value
Unsigned
Just add leading zeroes to the left side
Two’s Complement Signed:
If positive, add leading zeroes on the left
  Observe: Positive stay positive
If negative, add leading ones on the left
  Observe: Negative stays negative
• • •
• • •
• • •
• • •
n
original
copies of MSB
x

## Slide 22: Example: Two’s Complement Sign or bit Extension - 1
Adding 0's in front of a positive numbers does not change its value
7 = 0111
extend to
8 bits
00000111
Number is still 7
x
1 = 0001
extend to
8 bits
00000001
Number is still 1

## Slide 23: Example: Two’s Complement Sign or bit Extension -2
Adding 1's if front of a negative number does not change its value
7 = 0111
invert = 1000
add 1 + 1
-7 1001
7 = 00000111
invert = 11111000
add 1 + 1
-7 11111001
-7 = 1001
extend to
8 bits
11111001
x
1001 = -8 + 1 = -7
11111001 =
(-128 + 64 + 32 + 16 + 8) + 1 = -8 + 1 = -7

## Slide 24: Sign Extension in C: Type casts
Convert from smaller to larger integral data types
C and Java automatically performs sign extension
Example (on pi-cluster with 32-bit int)
x
#include <stdlib.h>
#include <stdio.h>
int main(void)
{
signed char c = -1;
signed int i = c;
unsigned char d = 1;
unsigned int j = d;
printf("c decimal = %hd\n", c);
printf("c = 0x%hhx\n", c);
printf("i decimal = %d\n", i);
printf("i = 0x%x\n", i);
printf("\nd decimal = %hd\n", d);
printf("d = 0x%hhx\n", d);
printf("j decimal = %d\n", j);
printf("j = 0x%x\n", j);
return EXIT_SUCCESS;
}
%./a.out
c decimal = -1
c = 0xff
i decimal = -1
i = 0xffffffff
d decimal = 1
d = 0x1
j decimal = 1
j = 0x1

## Slide 25: Different Type of Numbers each have a Fixed # of Bits Spanning one or more contiguous bytes of memory
x
C Data Type | AArch-32 contiguous Bytes
char (arm unsigned) | 1
short int | 2
unsigned short int | 2
int | 4
unsigned int | 4
long int | 4
long long int | 8
float | 4
double | 8
long double | 8
pointer * | 4
0
31
00000000
00000001
00000010
00000011
Word 32-bit integer uses 4 bytes
0
7
15
00000000
000000001
Half Word 16-bit integer uses 2 bytes
0
7
00000000
Byte 8-bit integer uses 1 byte
most significant bit (largest power of 2)
least significant bit (smallest power of 2)
most significant byte
least significant byte

## Slide 26: Byte Ordering of Numbers In Memory: Endianness
Two different ways to place multi-byte integers in a byte addressable memory
Big-endian: Most Significant Byte (“big end”) starts at the lowest (starting) address
Little-endian: Least Significant Byte (“little end”) starts at the lowest (starting) address
Example: 32-bit integer with 4-byte data
a1
b2
c3
d4
0x100
0x101
0x102
0x103
01
23
a1
b2
c3
d4
01
23
d4
c3
b2
a1
Big-Endian
Little-Endian
MSB
Most significant byte
LSB
Least significant byte
x
0x100
0x101
0x102
0x103

## Slide 27: Byte Ordering Example
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
int x = 12345;
// or x = 0x00003039; // show all 32 bits
39
30
00
00
IA32, ARM32 (little-endian)
30
39
00
00
(big-endian)
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
x

## Slide 28: Byte Addressable Memory Shown as 32-bit words
Observation
32-bit aligned addresses
rightmost 2 bits of the address are always 0
0x12345680
0x12345682
0x12345681
0x12345683
0x00
0x01
0x02
0x03
1 32-bit
(4 byte) word
0x12345684
0x12345686
0x12345687
0x12345685
0x04
0x05
0x06
0x07
1 byte Memory Content
One byte per row
Byte
Memory
Address
1 32-bit
(4 byte) word
Word Aligned address
Word Aligned address
x
0x04
0x05
0x06
0x07
0x00
0x01
0x02
0x03
LSByte
MSByte
0x12345680
0x12345681
0x12345682
0x12345683
Contents of Memory
One 32-bit (4 byte) word per row
0x12345680
0x12345684
Byte address
0x12345688
0x1234568c
Word
Memory
Address

## Slide 29: Using pointers to examine byte order (on pi-cluster)
#include <stdio.h>
#include <stdlib.h>
#define SZ 2
int main()
{
unsigned int foo[SZ] = {0x11223344, 0xaabbccdd};
unsigned char *chptr = (unsigned char *)foo;
// print from MSB to LSB – high to low memory)
for (int i = sizeof(foo)-1; i >= 0; i--)
printf("byte %d: %x\n", i, *(chptr + i));
return EXIT_SUCCESS;
}
$ ./a.out
byte 7: aa
byte 6: bb
byte 5: cc
byte 4: dd
byte 3: 11
byte 2: 22
byte 1: 33
byte 0: 44
0x12345680
0x12345682
0x12345681
0x12345683
0x44
0x33
0x22
0x11
0x12345684
0x12345686
0x12345687
0x12345685
0xdd
0xcc
0xbb
0xaa
x
a1
b2
c3
d4
01
23
d4
c3
b2
a1
Little-Endian
MSB
Most significant byte
LSB
Least significant byte
0x100
0x101
0x102
0x103

## Slide 30: Bit Shifting ARM and C Equivalents
Instruction | ARM | C | Diagram
Logical Shift Left 0 fills on right 0 <= n <= 32 bits | lsl Rd, Rm, n lsl Rd, Rm, Rs | int x; or unsigned int x x << n; | 
Logical Shift Right 0 fills on left 0 <= n <= 32 bits | lsr Rd, Rm, n lsr Rd, Rm, Rs | unsigned int x; x >> n; | 
Arithmetic Shift Right Sign extends on left 0 <= n <= 32 bits | asr Rd, Rm, n asr Rd, Rm, Rs | int x; x >> n; | 
Rotate Right 0 <= n <= 32 bits | ror Rd, Rm, n ror Rd, Rm, Rs | ror n in a 32-bit registers unsigned int x; x = (x >> n) ¦ (x << (32 - n)); | 
x
operand 2 constant
destination
<inst>
Rd
const5
Rm
operand 1
Number of bit to shift or rotate: const 5 bits
operand 2
destination
<inst>
Rd
Rm
operand 1
Rs
Number of bit to shift or rotate: Rs

## Slide 31: Shift Operations in C
n is number of bits to shift a variable x of width w bits
Shifts by n < 0 or n ≥ w are undefined
Left shift (x << N) – Multiplies by
  Shift N bits left, Fill with 0s on right
In C: behavior of >> is determined by compiler
  gcc: it depends on data type of x (signed/unsigned)
Right shift (x >> N) - Divides by
  Logical shift (for unsigned variables)
    Shift N bits right, Fill with 0s on left
  Arithmetic shift (for signed variables) – Sign Extension
    Shift N bits right while Replicating the most significant bit on left
    Maintains sign of x
In Java: logical shift is >>> and arithmetic shift is >>
Left Shift
Right logical Shift
Right Arithmetic Shift
x

## Slide 32: Arithmetic Shift Right Example: Testing Sign
asr r2, r0, 31
r0 0xab ab ab 77 // bit 31 is a one
r2 0xff ff ff ff // see the sign extend
asr r2, r0, 31
cmp r2, -1
bne .Lendif
//code neg #
.Lendif:
Test for sign
-1 if r0 negative
x
int i;
//code
if ((i>>31) == -1) {
// code neg #
}

## Slide 33: Arithmetic Shift Right Example: Testing SIgn
asr r2, r0, 31
r0 0x7b ab ab 77 // bit 31 is a zero
r2 0x00 00 00 00 // see the sign extend
asr r2, r0, 31
cmp r2, 0
bne .Lendif
//code positive #
.Lendif:
Test for sign
0 if r0 positive
x
int i;
//code
if ((i>>31) == 0) {
// code pos #
}

## Slide 34: Logical Shift & Rotate Operations
lsr r2, r0, 8
r0 0xab ab ab 77
r2 0x00 ab ab ab
lsl r2, r0, 8
r0 0xab ab ab 77
r2 0xab ab 77 00
ror r2, r0, 8
r0 0xab ab ab 77
r2 0x77 ab ab ab
x

## Slide 35: Extracting/Isolating Unsigned Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsr r1, r1, 24
r1 = r1 >> 24;
unsigned zero-extension (all 0’s)
Extracted bit-field
r1
byte 0
byte 1
byte 3
byte 2
lsl r1, r0, 8
unsigned int r0,r1;
r1 = r0 << 8;
Next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
pushed bits to far right
Hint: Useful for PA7

## Slide 36: Extracting Signed Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsl r1, r0, 8
int r0,r1;
r1 = r0 << 8;
next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
asr r1, r1, 24
r1 = r1 >> 24;
signed extend (all 1’s)
Extracted
bit-field
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far right

## Slide 37: Inserting Bitfields – Inserting Source Field into Destination Field
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
r1
r0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Task: Insert source into destination
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
results in
orr r1, r1, r2
r1 = r1 | r2;
r1
r2
Approach
(1) isolate source field
(2) clear destination field
(3) Bitwise or together
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 38: Inserting Bitfields – Isolating the Source Field
r2
r0
x
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
isolate source field
lsl r2, r0, 24
lsr r2, r2, 8
r2 = r0 << 24;
r2 = r2 >> 8;
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r0
r2

## Slide 39: Inserting Bitfields – Clearing the Destination Field
x
lsl r1, r1, 8
r1 = r1 << 8;
r1
r3
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
r1
r1
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
clear the destination field
ror r1, r1, 24
r1=(r1>>24)|(r1<<8);
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ror r1, r1, 16
r1= (r1>>16)|(r1<<16);

## Slide 40: Inserting Bitfields – Combining Isolated Source and Cleared Destination
x
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
inserted field
orr r1, r1, r0
r1 = r1 | r0;
r1
r2
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
isolated source
r1
r1
field cleared in destination

## Slide 41: Example: Swapping bits7,6 with bits 1,0
x
r0
r1
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
r0
source
r1
r2
and r1, r0, 0x3
(optional bits 31-8 == 0)
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
r0
r0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
lsl r1, r1, 6
lsr r2, r0, 6
and r0, r0, 0x3c
orr r0, r0, r2
orr r0, r0, r1

## Slide 42: Masking Summary - 1
Isolate a field: Use lsr, lsl to get a field surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Select a field: Use and with a mask of one's surrounded by zeros to select the bits that have a 1 in the mask, all other bits will be set to zero
Clear a field: Use and with a mask of zero's surrounded by ones to select the bits that have a 1 in the mask, all other bits will be set to zero
x
0 0 0 0 0 0 0 0 | 0 0 0 0 0 0 0 0 | 0 0 0 0 0 0 0 0 | 0 0 1 1 1 1 0 0
selects this field when used with and
selection mask 0x3c
clear a field mask 0xffffffc3
clears this field when used with and
lsl this edge to bit 31 (left edge)
then lsr to move back
lsr this edge to bit 0 (right edge)
then lsl to move back
1 1 1 1 1 1 1 1 | 1 1 1 1 1 1 1 1 | 1 1 1 1 1 1 1 1 | 1 1 0 0 0 0 1 1

## Slide 43: Masking Summary - 2
Isolate a field: Use and to get a field surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 | 0 0 0 0 0 0 0 0
x
Insert a field: Use orr with fields surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Keep these bits | 0 0 0 0 0 0 0 0 | Keep these bits
selection mask 0x00ff0000
rotate a field: Use ror to move a field without changing other bits
Keep these bits | source | Keep these bits
Keep these bits | Keep these bits | source