## Slide 1
UCSD CSE 30
Keith Muller
Lecture - 11
Computer Organization and Systems Programming
Version 2.01
Cray XMP-1982

## Slide 3: Creating a Node & Inserting it at the Front of the List
struct node {
int year;
char *name;
struct node *next;
};
// create node; insert at front when passed head
struct node *
creatNode(int year, char *name, struct node *link)
{
struct node *ptr = malloc(sizeof(*ptr));
if (ptr != NULL) {
if ((ptr->name = strdup(name)) == NULL) {
free(ptr);
return NULL;
}
ptr->year = year;
ptr->next = link;
}
return ptr;
}
// calling function body
struct node *head = NULL; // insert at front
struct node *ptr;
if ((ptr = creatNode(2020, "Joe", head)) != NULL) {
head = ptr; // error handling not shown
}
if ((ptr = creatNode(1955, "Sam", head)) != NULL) {
head = ptr; // error handling not shown
}
head
x
head
2020
"Joe"
NULL
head
2020
"Joe"
NULL
1955
"Sam"
Never use head here!
you can lose your linked list
if creatNode() fails!

## Slide 4: Creating a Node & Inserting it at the End of the List
// create a node and insert at the end of the list
struct node *
insertEnd(int year, char *name, struct node *head)
{
struct node *ptr = head;
struct node *prev = NULL; // base case
struct node *new;
if ((new = creatNode(year, name, NULL)) == NULL)
return NULL;
while (ptr != NULL) {
prev = ptr;
ptr = ptr->next;
}
if (prev == NULL)
return new;
prev->next = new;
return head;
}
struct node *head = NULL; // insert at end
struct node *ptr;
if ((ptr = insertEnd(2020, "Joe", head)) != NULL)
head = ptr;
if ((ptr = insertEnd(1955, "Sam", head)) != NULL)
head = ptr;
x
head
head
2020
"Joe"
NULL
head
1955
"Sam"
NULL
2020
"Joe"

## Slide 5: "Dumping" the Linked List "walk the list from head to tail"
struct node *head;
struct node *ptr;
…
printf("\nDumping All Data\n");
ptr = head;
while (ptr != NULL) {
printf("year: %d name: %s\n", ptr->year, ptr->name);
ptr = ptr->next;
}
x
Dumping All Data
year: 1955 name: Sam
year: 2020 name: Joe
ptr
ptr
ptr
head
2020
"Joe"
NULL
1955
"Sam"
struct node {
int year;
char *name;
struct node *next;
};

## Slide 6: Finding A Node Containing a Specific Payload Value
x
struct node *findNode(char *name, struct node *ptr)
{
while (ptr != NULL) {
if (strcmp(name, ptr->name) == 0)
break;
ptr = ptr->next;
}
return ptr;
}
struct node *found;
if ((found = findNode("Joe", head)) != NULL)
printf("year: %d name: %s\n", found->year, found->name);
ptr
ptr
head
2020
"Joe"
NULL
1955
"Sam"
struct node {
int year;
char *name;
struct node *next;
};
Returns pointer if found
NULL otherwise

## Slide 7: Deleting a Node in a Linked List
// returns head pointer; may have changed…
struct node *deleteNode(int name, struct node *head)
{
struct node *ptr = head;
struct node *prev = NULL;
while (ptr != NULL) {
if (strcmp(name, ptr->name) == 0)
break;
prev = ptr;
ptr = ptr->next;
}
if (ptr == NULL) // not found return head
return head;
if (ptr == head) // remove first node new head
head = ptr->next;
else
prev->next = ptr->next; // remove not head
free(ptr->name); // free strdup() space
free(ptr);
return head;
}
struct node *head = NULL;
head = deleteNode("Joe", head);
head = deleteNode("Sam", head);
x
ptr
ptr
head
2020
"Joe"
NULL
1955
"Sam"
head
NULL
1955
"Sam"
ptr
NULL
head

## Slide 8: Improving On Linked List Performance
When linked lists get long, the cost of finding an entry continues to increase O(n)
How to improve search time?
Break the single linked list into multiple shorter length linked lists
  Shorter lists are faster to search
Requires a function that takes a lookup key and selects just one of the shortened lists
x
2020
head
1955
1933
…
…
…
…
…
…
…
Joe
2020
Sam
1955
Pat
1933
…
…
…
…
…
…
…
…
How do you determine on which linked list an entry is stored?
?
Pat
Sam
Joe
…
…
…
…
Pat
1933
same as 
Pat
1933

## Slide 9: Hashing
Hash table is an array of pointers to the head of different linked lists (called hash chains)
Each data item must have a unique key that identifies it (e.g., auto license plate)
  h(k) is the hash value of key k to encode the key k into an integer
Use the Hash value to map to one entry in the hash table T[ ] of size TABLESIZE
  Index = h(k) % TABLESIZE (mod operator % maps a keys hash value to table index)
Keys that hash to the same array index (collide) are put on a linked list
After hashing a key, you then traverse the selected linked list to find the entry
x
9
3
5
7
8
Nodes with keys to be put into the table
1
Using a Simple hash
h(k) = k // this is has value
index = k % size // map to a chain
5
index = h(5) % 3 = 2 -> T+2
7
index = h(7) % 3 = 1 -> T+1
Hash Table T[3] of linked list head pointers
TABLESIZE = 3
*(T+2) 
*(T+1) 
*T 
5
7
1
3
8
9

## Slide 10: Hash Table With Collision Chaining (multiple linked lists)
Calculate index i = hash(key) % TABLESIZE
Go to array element i, i.e., T+i that contains the head pointer for collision chain
Walk the linked list for element, add element, remove element, etc. from the linked list
New items added to the hash table are typically added at the front or at the end of the collision chain linked list (when multiple keys hash to same index .. they collide)
Hash arrays need an index number to select a chain, so if we have a string, we must first convert to a number
Make TABLESIZE prime as keys are typically not randomly distributed, and have a pattern
  Mostly even, mostly multiples of 10, etc.
  In general: mostly multiples of some k
If k is a factor of TABLESIZE, then only (TABLESIZE/k) slots will ever be used!
x
Hash Table T[3]
TABLESIZE = 3
T+2
T+1
T
5
7
1
3
8
9

## Slide 11: Simple 32-bit String Hash Function in C (djb2)
Many different algorithms for string hash function (Dan Berman's djb2 above)
  << is the left bit shift operator (later in course)
Fast to compute, has a reasonable key distribution for short 8-bit ASCII strings into 32-bit unsigned ints
uint32_t hash(char *str)
{
uint32_t hash = 0U;
uint32_t c;
while ((c = (unsigned char)*str++) != '\0’)
hash = c + (hash << 6) + (hash << 16) - hash;
return hash;
}
x
c | s | e | 3 | 0 | '\0'
ptr
ptr
ptr
ptr
ptr
ptr
Signed Data types | Unsigned Data types | Exact Size
int32_t | uint32_t | 32 bits (4 bytes)

## Slide 12: Allocating the Hash Table (collision chain head pointers) Good use for calloc()
#define TBSZ 3
int main(void)
{
struct node *ptr;
struct node **tab; // pointer to hashtable
uint32_t index;
if ((tab = calloc(TBSZ, sizeof(*tab))) == NULL) {
fprintf(stderr,"Cannot allocate hash table\n");
return EXIT_FAILURE;
}
// continued on next slide
x
TABLESIZE = 3
tab[2]
tab[1]
tab[0]
tab

## Slide 13: Inserting Nodes into the Hash Table (at the end)
#define TBSZ 3
unit32_t index;
index = hash("Pat") % TBSZ;
if ((ptr = insertEnd(1933, "Pat", *(tab + index))) != NULL)
*(tab + index) = ptr;
index = hash("Sam") % TBSZ;
if ((ptr = insertEnd(1955, "Sam", *(tab + index))) != NULL)
*(tab + index) = ptr;
index = hash("Sally") % TBSZ;
if ((ptr = insertEnd(2020, "Sally", *(tab + index))) != NULL)
*(tab + index) = ptr; index = hash("Zoe") % TBSZ;
if ((ptr = insertEnd(2022, "Zoe", *(tab + index))) != NULL)
*(tab + index) = ptr;
x
tab+2
tab+1
tab
Notice
Substitute createNode() for insertEnd() to insert nodes at the front of the collision chain instead of at the end of the collision chain
Sally
2020
Sam
1955
Zoe
2022
Pat
1933
struct node {
int year;
char *name;
struct node *next;
};

## Slide 14: "Dumping" the Hash Table (traversing all Nodes)
tab+2
tab+1
tab
Sally
2020
Sam
1955
Zoe
2022
Pat
1933
printf("\nDumping All Data\n");
for (index = 0U; index < TBSZ; index++) {
ptr = *(tab + index);
printf("chain: %d\n", index);
while (ptr != NULL) {
printf("Year: %d Name: %s\n", ptr->year, ptr->name);
ptr = ptr->next;
}
}
x
Dumping All Data
chain: 0
Year: 1933 Name: Pat
chain: 1
Year: 2020 Name: Sally
chain: 2
Year: 1955 Name: Sam
Year: 2022 Name: Zoe
ptr
ptr
ptr
ptr

## Slide 15: Finding a Node with a Specific Payload Value
x
index = hash("Zoe") % TBSZ;
if ((ptr = findNode("Zoe", *(tab + index))) != NULL)
printf("Found Year: %d name: %s\n", ptr->year, ptr->name);
else
printf("Not Found Zoe\n");
ptr
ptr
tab+2
tab+1
tab
Sally
2020
Sam
1955
Zoe
2022
Pat
1933
// same routine as shown in a previous slide
struct node *findNode(char *name, struct node *ptr)
{
while (ptr != NULL) {
if (strcmp(name, ptr->name) == 0)
break;
ptr = ptr->next;
}
return ptr;
}

## Slide 16: Arm Core Floorplan
Control: Specifies the operation of the CPU
Register File: Memory inside the CPU
  Instructions reference these directly
ALU: Arithmetic Logic Unit: Arithmetic and bitwise hardware (on the bits)
Barrel shifter: (shifts bits in a register during instruction execution - Later)
Instruction Decode: Interprets the the bits in an instruction to determine what the instruction means
Register Decode: controls the registers in during instruction execution
Address and Data: Interface to external RAM (like memory dimms)
Single core arm die Floorplan
x

## Slide 17: 32-Bit Arm - Registers
Registers are memory located within the CPU
Registers are the fastest read and write storage
Register is word size in length stores 32-bit values
  Memory is accessed using pointers in registers
In assembly language the registers have predefined names starting with an r to differentiate them from memory addresses which are labels (address)
16 registers: from r0 to r15 (encoded: 0x0 – 0xf)
x
Registers
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
1- Byte
32-bit address
External memory
0x00000000
0xFFFFFFFF
Capacity:4 GBytes
CPU
CPU Memory Bus = Address + Data
arithmetic Logic Unit

## Slide 18: Using Arm-32 Registers
There are two basic groups of registers, general purpose and special use
General purpose registers can be used to contain up to 32-bits of data, but you must follow the rules for their use
  Rules specify how registers are to be used so software can communicate and share the use of registers (later slides)
Special purpose registers: dedicated hardware use (like r15 the pc) or special use when used with certain instructions (like r13 & r14)
r15/pc is the program counter that contains the address of an instruction being executed (not exactly … later)
r8
r9
r10
r4
r5
r6
r7
Preserved registers
Called functions can't change
r0
r1
r2
r3
Scratch Registers
First 4 Function Parameters
Function return value
Called functions can change
x
r15/pc
r13/sp
r14/lr
r11/fp
r12/ip
Special Use Registers
function call implementation & long branching
Special Use Registers
program counter

## Slide 19: Assembly and Machine Code
Machine Language (or code): Set of instructions the CPU executes are encoded in memory using patterns of ones and zeros (like binary numbers)
Assembly language is a symbolic version of the machine language
Each assembly statement (called an Instruction)
  Executes exactly one from a list of simple commands
  Instructions describe operations (e.g., =, +, -, *)
  Execution proceeds from low to high memory one instruction at a time unless there is a branch
One line of arm32 machine code contains one instruction in one word (32 bits)
x
0xFF…FF
0x00…00
32-bit address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment
1040c: e28db004 add fp, sp, 4
10410: e59f0010 ldr r0, [pc, 16]
10414: ebffffb3 bl 102e8 <printf>
10418: e3a00000 mov r0, 0
1041c: e24bd004 sub sp, fp, 4
Instruction Instruction (4-bytes)
Address contents Assembly Equivalent
Machine Code
high <- low bytes

## Slide 20: Anatomy of an Assembly instruction
Assembly language instructions specify an operation and the operands to the instruction (arguments of the operation)
Three basic types of operands
  Destination: where the result will be stored
  Source: where data is read from
  Immediate: an actual value like the 1 in y = x + 1
add r0, r1, r2
add r0, r1, 1
Operands (variables)
Source Operands
Destination Operand
Immediate Operand
x
operation

## Slide 21: Meaning of an Instruction
Operations are abbreviated int opcodes (1– 5 letters)
Assembly Instructions are specified with a very regular syntax
  Opcodes are followed by arguments
  Usually the destination argument is next, then one or more source arguments (this is not strictly the case, but it is generally true)
Why this order?
Analogy to C or Java
int r0, r1, r2;
r0 = r1 + r2; // c
x
r0 = r1 + r2
add r0, r1, r2 // assembly

## Slide 22: 32-Bit Arm - Registers
Almost all arithmetic, logic operations and data movement operations involve at least one register
As a result, Register addresses are directly encoded into 4-bit fields in machine instructions (see below)
x
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
registers
Arithmetic & Logic Unit (ALU)
All computations (add, subtract, etc.) are performed in the ALU

## Slide 23: Program Execution: A Series of Instructions
Instructions are retrieved sequentially from memory
Each instruction executes to completion before the next instruction is completed
Conceptually the pc (program counter) points at executing instruction
exceptions: loops, function calls, traps,..
add r0, r1, r1
add r0, r0, r0
add r0, r0, r0
sub r1, r0, r1
r0 = 4 r1 = 2
r0 = 1 r1 = 2
r0 = 8 r1 = 2
r0 = 16 r1 = 2
r0 = 16 r1 = 14
x
Memory Content in Text segment
initial values
Low memory
High memory
Register contents inside the CPU

## Slide 24: How to Access Memory?
31 | 0
Address of a location in memory | 
Consider a = b + c are operands are in memory
  Operation code: add Destination: a
  Operand 1: b Operand 2: c
Aarch32 Instructions are always word size: 32 bits wide
  Some bits must be used to specify the operation code
  Some bits must be used to specify the destination
  Some bits must be used to specify the operands
Address space is 32 bits wide so put a POINTER in a register
31 |  |  | 0 | 
Opcode
Destination
NOT ENOUGH BITS for FULL Addresses to be stored in the instruction
32 bits wide
x
Operand 1
Operand 2
0xFF…FF
0x00…00
32-bit Address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment

## Slide 25: 32-Bit Arm is a Load/Store Architecture
x
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
registers
1- Byte
32-bit address
memory
0x00000000
0xFFFFFFFF
Capacity:4 GBytes
Arithmetic & Logic Unit (ALU)
All computations (add, subtract, etc.) are performed in the ALU
Instruction operands and results are only in registers
Load:
(also called a Fill)
Copy the contents of a variable from memory into a register.
Store:
(also called a Spill)
Copy the contents of a register back into a variable in memory.

## Slide 26: Load/Store: Load
x
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
0x1004
0x4321
0x1
0x2
0x3
0x4
External memory
0x00001000
0x00001004
0x00001008
0x0000100c
0x00001010
// load store concept
int r3;
int x[2];
int *r1;
r1 = &x; // r1 contains x's address
r3 = *(r1); // read memory , load register 3
x[0]
x[1]
points at
reads memory
int x[2] = {0x4321, 0x0};
x[1] = x[0];

## Slide 27: Load/Store: Store
x
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
0x1004
0x4321
0x1
0x2
0x3
0x4
External memory
0x00001000
0x00001004
0x00001008
0x0000100c
0x00001010
x[0]
x[1]
r1 + 4
points at
writes memory
0x1
0x2
0x3
0x4
// load store concept
int r3;
int x[2];
int *r1;
r1 = &x; // r1 contains x's address
r3 = *(r1); // read memory , load register 3
r1 = r1 + 1;
*(r1) = r3; // store register 3 to memory
int x[2] = {0x4321, 0x0};
x[1] = x[0];

## Slide 28: Arm Register Summary
16 Named registers r0 – r15
The operands of almost all instructions are registers
To operate on a variable in memory do the following:
  Load the value(s) from memory into a register
  Execute the instruction
  Store the result back into memory (only if needed!)
Going to/from memory is expensive
  4X to 20X+ slower than accessing a register
Strategy: Keep variables in registers as much as possible
x

## Slide 29: AArch32 Instruction Categories
Data movement to/from memory
  Data Transfer Instructions between memory and registers
    Load, Store
Arithmetic and logic
  Data processing Instructions (registers only)
    Add, Subtract, Multiply, Shift, Rotate, …
Control Flow
  Compare, Test, If-then, Branch, function calls
Miscellaneous
  Traps (OS system calls), Breakpoints, wait for events, interrupt enable/disable, data memory barrier, data synchronization barrier
  Many others that we will not cover in the class
Arithmetic and logic
Data Movement
Control Flow
Miscellaneous
x

## Slide 30: First Look: Copying Values Between Registers - MOV
mov r0, r1
// Copies all 32 bits of the // value in register r1 into
// register r0
register r0
register r1
mov r0, 100
// Expands an 8-bit (imm8) value 100
// stored in the instruction
// into the register r0
register r0
100
x
Immediate "addressing"
register direct "addressing"

## Slide 31: mov – Copies Register Content between registers
mov r1, r5 // r1 = r5
mov r1, 1 // r1 = 1
mov r1, -4 // r1 = -4
constant (immediate value)
destination register
mov
Rd
source register
mov
Rd
Rm
destination register
rot4
imm8
mov Rd, constant // Rd = constant
mov Rd, Rm // Rd = Rm
machine code bit fields
x
Immediate "addressing"
register direct "addressing"
imm8 is 8 bits in size!
IMPACT: limited range of values
(-256) <= imm8 <= 255 + values from "rotating" bits - later

## Slide 32: First Look: Add/Sub Registers
add r0, r1, r2
// Adds r1 to r2 and
// stores the result // in r0
register r0
register r1
register r2
+
x
sub r0, r1, 100
// Perform r1 – 100 and
// stores the result in
// r0
register r0
register r1
100
-

## Slide 33: add/sub – Add or Subtract two integers
add r1, r2, r3 // r1 = r2 + r3
sub r1, r1, 1 // r1 = r1 – 1; or r1--
add r1, r2, 234 // r1 = r2 + 234
add Rd, Rn, constant // Rd = Rn + constant
sub Rd, Rn, constant // Rd = Rn - constant
add Rd, Rn, Rm // Rd = Rn + Rm
sub Rd, Rn, Rm // Rd = Rn - Rm
Operand 2 constant
destination
add/sub
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
add/sub
Rd
Rn
operand 1
Rm
x

## Slide 34: Writing a Sequence of Add & Subtract Instructions
You need to perform the following sequence of integer adds/subtracts
a = b + c + d - e;
Since ARM uses a three-operand instruction set, you can only operate on two operands at a time
So, you need to use one register as an accumulator and create a sequence of add instructions to build up the solution
a = b + c + d - e;
r0 = r1 + r2 + r3 – r4;
r0 = ((r1 + r2) + r3) – r4;
r0 = r1 + r2;
r0 = r0 + r3
r0 = r0 – r4
r0  a
r1  b
r2  c
r3  d
r4  e
a = (b + c) – 5;
r0 = (r1 + r2) – 5;
x
add r0, r1, r2
add r0, r0, r3
sub r0, r0, r4
add r0, r1, r2
sub r0, r0, 5

## Slide 35: Line Layout in an Arm Assembly Source
Assembly language source text files are line oriented (each ending in a '\n')
Each line represents a starting address in memory and does one of:
  Specifies the contents of memory for a variable (segments containing data)
  Specifies the contents of memory for an instruction (text segment)
  Assembler directives tell the assembler to do something (for example, change label scope, define a macro, etc.) that does not allocate memory
Each line is organized into up to four columns
  Not every column is used on each line
  Not every line will result in memory being allocated
label: operation operand(s) // comments
tab
white space
white space
x
column 1 column 2 column 3 column 4

## Slide 36: Labels in Arm Assembly - 1
Labels (optional); starts in column 1 (often on a line by itself ABOVE the "operation")
  Only put a label on a line when you need to associate a name (a global variable, a function name, a loop/ branch target, etc.) to that line's location in memory
  You then refer to the address by name in an instruction
Operation type 1: assembler directives (all start with a period e.g. .word )
Operation Type 2: assembly language instructions
Zero or more operands as required by the instruction or assembler directive
Comments: C and C++ style; also @ in the place of a C++ comment //
x
label: operation operand(s) // comment
// assembler directive below
cnt: .word 5 /* define a global int cnt = 5; */
/* instruction example below */
add r1 r2, r3 // add the values

## Slide 37: Labels in Arm Assembly - 2
Remember, a Label associates a name with memory location
Regular Label:
  Used with a Function name (label) or all static variables in any of the data segments
Local Label: Name starts with .L (local label prefix) only usable in the same file
  Targets for
    branches: if switch, goto, break, continue,
    loops: for, while, do-while
  Anonymous variables (the address of literal not the address of foo in the following)
    char *foo = "literal";
x
.Lmesg: .string "Hello CSE30! We Are CountinG UpPpER cASe letters!"
main:
push {fp, lr}
.Lwhile:
add r2, r2, 1 // increment char pointer
local label
Regular label
local label
label main is the starting address of the push instruction
label .Lmesg is the starting address for the ascii string
label .Lwhile is the starting address of the add instruction

## Slide 38: Unconditional Branching – Forces Execution to Continue at a Specified Label (goto)
b .Ldone // goto .Ldone
:
.Ldone:
add r0, EXIT_SUCCESS // set return value
Unconditional Branch instruction (branch to only local labels in CSE30)
b .Llabel
Causes an unconditional branch (aka goto) to the instruction with the address .Llabel
.Llabel is called a branch target label (the "target" of a branch instruction)
Be careful! do not to branch to a function label!
.Llabel: translates into an number offset being imm24 shifted left two bits (+/- 32 MB)
b
imm24
x
imm24 is Relative direction
from the branch instruction (in +/- instructions)

## Slide 39: Examples of of Unconditional Branching
Branches are used to change execution flow using labels as the branch target
In these example, .Lforward and .Lbackward are the branch target labels
Branch target labels are placed at the beginning of the line (or above it)
Caution: Backward branches should only used with loops!
b .Lforward
add r1, r2, 4
add r0, r6, 2
add r3, r7, 4
.Lforward:
sub r1, r2, 4
.Lbackward:
add r1, r2, 4
sub r1, r2, 4
add r4, r6, r7
b .Lbackward
// not reachable unless
// there is a label after the .b above
Backward Branch
(Infinite loop)
Unconditional Branch Forward
x
Not a practical example as this code is unreachable
Branch target (local label)

## Slide 40: Never Branch to the following instruction: It is not needed!
x
mov r2, 0
b .Lnext // do not do this, not needed
.Lnext:
add r1, r2, r3
mov r2, 0
add r1, r2, r3

## Slide 41: Anatomy of a Conditional Branch: If statement
Branch guard: determines when to execute the "condition true block" or the "condition false block"
In C, when the branch guard (condition test) evaluates non-zero you fall through to the condition true block, otherwise you branch to the condition false (else) block
Step 1: evaluate the branch guard(s) (involves one or more compares/tests)
Step 2: If branch guard evaluates to be false
  branch around the true block and execute the else block
  otherwise "fall through" and execute the true block
Block order in C is where the True Block appears above the False block
if (r0 == 5) {
/* condition block #1 */
/* branch to "here" */
} else {
/* condition block #2 */
/ * fall through to "here" */
}
// resume here
Branch condition
Test (branch guard)
r0 == 5
condition true block
condition else block

## Slide 42: cmp/cmm – Making Conditional Tests
cmp r1, 0 // r1 – 0 and sets flags on the result
cmp r1, r2 // r1 – r2 and sets flags on the result
cmp Rn, constant // Rn – constant; then sets condition flags
cmm Rn, constant // Rn + constant; then sets condition flags
cmp Rn, Rm // Rn – Rm; then sets condition flags
cmm Rn, Rm // Rn + Rm; then sets condition flags
Operand 2 constant
cmp/cmm
rot4
imm8
Rn
operand 1
Operand 2
cmp/cmm
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
The values stored in the registers Rn and Rm are not changed
The assembler will automatically substitute cmn for negative immediate values
x

## Slide 43: Quick Overview of the Condition Bits/Flags
The CSPR is a special register (like the other registers) in the CPU
The four bits at the left are called the Condition Code flags
  Summarize the result of a previous instruction
  Not all instruction will change the CC bits
Specifically, Condition Code flags are set by cmm/cmp (and others)
Example: cmp r4, r3
N (Negative) flag: Set to 1 when the result of r4 – r3 is negative, set to 0 otherwise
Z (Zero) flag: Set to 1 when the results of r4 – r3 is 0, set to 0 otherwise
C (Carry bit) flag: Set to 1 when r4 – r3 does not have a borrow, set to 0 otherwise
V flag (oVerflow): Set to 1 when r4 – r3 causes an overflow, set to 0 otherwise
N
Z
C
V
CPSR
31
30
29
28
5 0
Execution Mode
x

## Slide 44: Conditional Tests: Implementing ARM Branch guards
Branch instruction
bsuffix .Llabel
Bits in the condition field specify the conditions when the branch happens
If the condition evaluates to be true, next instruction executed is at .Llabel:
If the condition evaluates to be false, next instruction executed is immediately after the branch
Unconditional branch is when the condition is "always"
bsuffix
imm24
cond
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
BNE | Not equal | Z = 0
BGE | Signed ≥ ("Greater than or Equal") | N = V
BLT | Signed < ("Less Than") | N ≠ V
BGT | Signed > ("Greater Than") | Z = 0 && N = V
BLE | Signed ≤ ("Less than or Equal") | Z = 1 ¦¦ N ≠ V
BMI | Minus/negative | N = 1
BPL | Plus - positive or zero (non-negative) | N = 0
B | Branch Always (unconditional) | 
x
imm24 is Relative direction
from the branch instruction
(in +/- instructions)
Use a local label with branch instructions

## Slide 45: Branch and Loop Guard Strategy
How to implement a branch/loop guard in CSE30
Use a cmp/cmm instruction to set the condition bits
Follow the cmp/cmm with one or more variants of the conditional branch instruction
  Conditional branch instructions if evaluate to true (based on the flags set by the cmp) the next instruction will the one at the branch label
  Otherwise, execution falls through to the instruction that immediately follows the branch
You may have one or more conditional branches after a single cmp/cmm
cmp r0, 10
ble .Lendif
// True Block
.Lendif:
Branch guard
x

## Slide 46: Program Flow: Simple If statement, No Else
Realize that in ARM assembly you can only either "fall through" to the next instruction or branch to a specific instruction
Approach: adjust the conditional test then branch around the true block
Use a conditional test that specifies the inverse of the condition used in C
  This preserves C block order
C source Code | Incorrect Assembly | Correct Assembly
int r0; if (r0 > 10) { // True Block } | cmp r0, 10 bgt .Lendif // True Block .Lendif: | cmp r0, 10 ble .Lendif // True Block .Lendif:
x

## Slide 47: Branch Guard "Adjustment" Table Preserving C Block Order In Assembly
if (r0 compare 5)
/* condition true block */
/* then fall through */
}
Compare in C | "Inverse" Compare in C | Assembly using Inverse Compare
== | != | bne
!= | == | beq
> | <= | ble
>= | < | blt
< | >= | bge
<= | > | bgt
cmp r0, 5
inverse compare .Lelse
// condition true block
// then fall through
.Lendif:
x

## Slide 48: Arm Conditional Branching Simple IF no else
If statements in ARM
Step 1: make a conditional test using a cmp instruction
Step 2: if test evaluates to FALSE, branch around the condition true block with a one of the conditional branch instruction
x
cmp r0, 5
bne .Lendif
/* condition true block */
/* then fall through */
.Lendif:
/* branch around to this code */
If r0 == 5 false
then branch around the true block
int r0;
if (r0 == 5) {
/* condition true block */
/* then fall through */
}
/* branch around to this code */
If r0 == 5 true
then fall through to the true block
C If statement
ARM If statement

## Slide 49: If statement examples – Branch Around the True block!
int r0;
if (r0 == 5) {
r1 = r2++ + r3;
}
r3 = r2;
cmp r0, 5
bne .Lendif
add r1, r2, r3
add r2, r2, 1
.Lendif:
mov r3, r2
x
If r0 == 5 false
then branch around the true block
Fall through
int r0;
if (r0 <= 5) {
r1 = r2++;
}
r3 = r2;
cmp r0, 5
bgt .Lendif
mov r1, r2
add r2, r2, 1
.Lendif:
mov r3, r2
Fall through

## Slide 50: Branching Avoid: Spaghetti Code ("goto structure")
Do not use unnecessary branches
Optimize your use of "fall throughs"
For example: Do not make a conditional branch around an unconditional branch that immediately follows it
Do not do the following:
cmp r0, 0
beq .Lthen
b .Lendif
.Lthen:
add r1, r1, 1
.Lendif:
add r1, r1, 2
x
Do the following:
cmp r0, 0
bne .Lendif
// fall through
add r1, r1, 1
.Lendif:
add r1, r1, 2
Caution!
Two adjacent branches