## Slide 1
UCSD CSE 30
Keith Muller
Lecture - 13
Computer Organization and Systems Programming
Version 2.06

## Slide 3: Program Flow – Counting (For) Loop Version 1
mov r1, 0
.Lfor:
cmp r1, 10
bge .Lendfr
// block code
add r1, r1, 1
b .Lfor
.Lendfr:
A counting loop has three parts:
Pre-loop setup
Pre-test loop guard conditions
Post-loop update
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Post loop update
Pre loop setup
Pre-test loop guard

## Slide 4: Program Flow – Counting (For) Loop – Version 2
Alternative:
move Pre-test loop guard before the loop
Add post-test loop guard
  converts to do while
  removes an unconditional branch
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
mov r1, 0
cmp r1, 10
bge .Lendfr
.Ldo:
// block code
add r1, r1, 1
cmp r1, 10
blt .Ldo
.Lendfr:
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Pre-loop setup
Post loop update
Pre-test loop guard
Post-test loop guard

## Slide 5: Nested loops
Nest loop blocks as you would in C or Java
for (r3 = 0; r3 < 10; r3++) {
r0 = 0;
do {
r0 = r0 + r1++;
} while (r1 < 10);
// fall through
r2 = r2 + r1;
}
r5 = r0;
x
mov r3, 0
.Lfor:
cmp r3, 10 // loop guard
bge .Lendfor
mov r0, 0
.Ldo:
add r0, r0, r1
add r1, r1, 1
cmp r1, 10 // loop guard
blt .Ldo
// fall through
add r2, r2, r1
add r3, r3, 1 // loop iteration
b .Lfor
.Lendfor:
mov r5, r0

## Slide 6: Keep loops Properly Nested: Do not branch into the middle of a loop
It is hard to understand and debug loops when you branch into the middle of a loop
Keep loops proper nested
Do not do the following:
.Lloop1:
add r1, r1, 1
.Lloop2:
add r2, r2, 1
add r2, r1, r3
cmp r1, 10
blt .Lloop1
beq .Lend1
add r3, r3, 1
cmp r2, 20
ble .Lloop2
.Lend1:
x
Bad practice: branch into loop body

## Slide 7: What is a Bitwise Operation?
Bitwise operators are applied independently to each of the corresponding bit positions in each variable
Each bit position of the result depends only on bits in the same bit position within the operands
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0
x

## Slide 8: Bitwise (Bit to Bit) Operators in C
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
output = a | b;
| with 1 to set a bit to 1
| with 0 to let a bit through
a | ~a
0 | 1
1 | 0
output = ~a;
a | b | a ^ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
output = a ^ b; //EOR
^ with 1 will flip the bit
^ with 0 to let a bit through
a | b | a & b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
output = a & b;
& with 1 to let a bit through
& with 0 to set a bit to 0
0110
& 1100
----
0100
Bitwise
AND
0110
| 1100
----
1110
Bitwise
OR
0110
^ 1100
----
1010
Bitwise
EOR
~ 1100
----
0011
Bitwise
NOT
x

## Slide 9: Bitwise Not (vs Boolean Not)
a | ~a
0 | 1
1 | 0
in C
int output = ~a;
x
Boolean operators act on the entire value not the individual bits
Meaning | Operator | Operator | Meaning
Boolean NOT | !b | ~b | Bitwise NOT
 | Bitwise Not
number | 0101 1010 0101 1010 1111 0000 1001 0110
~number | 1010 0101 1010 0101 0000 1111 0110 1001
Type | Operation | result
bitwise | ~0x01 | 1111 1111 1111 1111 1111 1111 1111 1110
Boolean | !0x01 | 0000 0000 0000 0000 0000 0000 0000 0000
~ 1100
----
0011
Bitwise NOT

## Slide 10: MVN (not)
A bitwise NOT operation
mvn r0, r1
// Copies all 32 bits
// of the value held
// in register r1 into
// the register r0
// then does a bitwise NOT
register r0
register r1
mvn r0, 12
// Expands an imm8 value 0x0c
// stored in the instruction
// into a register then does
// a bitwise NOT
0xffff fff3
0x0c
x
~ 1100
----
0011
Bitwise NOT
register r0
0xfffffff3
0x 0c
imm8 expansion
0x0000000c
bitwise not

## Slide 11: mvn – Copies NOT (~)
constant (immediate value)
destination register
mvn
Rd
source register
mvn
Rd
Rm
destination register
bitwise NOT operation. Immediate (constant) version copies to 32-bit register, then does a bitwise NOT
mvn r1, 4 // x = ~4
mvn r1, r5 // x = ~y in C
mvn r1, 0 // x = -1
imm8 | extended imm8 | inverted imm8 | signed base 10
0x00 | 0x00 00 00 00 | 0xff ff ff ff | -1
0xff | 0x00 00 00 ff | 0xff ff ff 00 | -256
0xfffffffb
r1
0x4
invert the bits
0x00000004
copy into 32 bits zero extend
0xaaaaaaaa
0x55555555
r5
r1
rot4
imm8
~ 1100
----
0011
Bitwise NOT
x
mvn Rd, constant // Rd = constant
mvn Rd, Rm // Rd = Rm
0x0
0x11111111
r1

## Slide 12: Bitwise Instructions
<op> Rd, Rn, constant // Rd = Rn <op> constant
<op> Rd, constant // Rd = Rd <op> constant
<op> Rd, Rn, Rm // Rd = Rn <op> Rm
Operand 2 constant
destination
<op>
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
<op>
Rd
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
Bitwise <op> description | C Syntax | Arm <op> Syntax Op2: either register or constant value | Operation
Bitwise AND | a & b | and Rd, Rn, Op2 | Rd = Rn & Op2
Bitwise OR | a ¦ b | orr Rd, Rn, Op2 | Rd = Rn ¦ Op2
Exclusive OR | a ^ b | eor Rd, Rn, Op2 | Rd = Rn ^ Op2
Bitwise NOT | a = ~b | mvn Rd, Rn | Rd = ~Rn
x

## Slide 13: Bitwise versus C Boolean Operators
Boolean operators act on the entire value not the individual bits
bitwise & versus boolean &&
0x10 & 0x01 = 0x00 (bitwise)
0x10 && 0x01 = 0x01 (Boolean)
bitwise ~ versus boolean !
~0x01 = 0xfffffffe (bitwise)
!0x01 = 0x0 (Booelan)
Meaning | Operator |  | Operator | Meaning
Boolean AND | a && b |  | a & b | Bitwise AND
Boolean OR | a ¦¦ b |  | a ¦ b | Bitwise OR
Boolean NOT | !b |  | ~b | Bitwise NOT
x
Boolean Operators
Bitwise Operators

## Slide 14: The act (operation) of Masking
Bit masks access/modify specific bits in memory
Masking act of applying a mask to a value with a specific op:
orr: 0 passes bit unchanged, 1 sets bit to 1 (a = b | c; // in C)
eor: 0 passes bit unchanged, 1 inverts the bit (a = b ^ c; // in C)
and: 0 clears the bit, 1 passes bit unchanged (a = b & c; // in C)
x
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0

## Slide 15: Mask on
force bits to 1 "mask on" operation
  1 to set a bit to 1
  0 to let a bit through unchanged
orr r1, r2, r3
r1 = r2 | r3; // in C
x
Example: force lower 16 bits to 1
DATA: r2 0xab ab ab 77
orr
MASK: r3 0x00 00 ff ff
RSLT: r1 0xab ab ff ff
forces to a 1
unchanged
Example: force lower 8 bits to 1
DATA: r2 0xab ab ab 77
orr r1 r2, 0xff
r1 = r2 | 0xff; // in C
RSLT: r1 0xab ab ab ff

## Slide 16: Mask off
x
force bits to 0 "mask off" operation
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
r1 = r2 & r3; // in C
Example: force lower 8 bits to 0
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff ff ff 00
RSLT: r1 0xab ab ab 00
forces to a 0
unchanged
Example: force lower 8 bits to 0
DATA: r2 0xab ab ab 77
and r1 r2, 0xffffff00
r1 = r2 & 0xffffff00; // in C
RSLT: r1 0xab ab ab 00

## Slide 17: Extracting (Isolate) a Field of Bits with a mask
x
extract top 8 bits of r2 into r1
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff 00 00 00
RSLT: r1 0xab 00 00 00
forces to a 0
unchanged
extract top 8 bits of r2 into r1
DATA: r2 0xab ab ab 77
and r1, r2, 0xff000000
RSLT: r1 0xab 00 00 00
r1 = r2 & 0xff000000; // in C

## Slide 18: Finding if a bit is set
x
query the status of a bit "bit status" operation
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, 0x02
cmp r1, 0
beq .Lendif
// code for is set
.Lendif:
Example is bit 1 set
DATA: r2 0xab ab ab 77
and
MASK: 0x00 00 00 02 is bit 1 set?
RSLT: r1 0x00 00 00 02 != 0 if set
forces to a 0
unchanged
  unsigned int r1, r2;
  // code
  r1 = r2 & 0x02
  if (r1 != 0) {
  // code for is set
  }
  unsigned int r2;
  // code
  if ((r2 & 0x02) != 0) {
  // code for is set
  }

## Slide 19: Even/Odd
Even or odd, check LSB (same as mod %2)
check LSB (bit 0) if set then odd, else even
and r1, r2, 0x01
cmp r1, 0x01
bne .Lendif
// code for handling odd numbers
.Lendif:
x
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 01 (mod 2 even or odd)
RSLT: r1 0x00 00 00 01 (odd)
forces to a 0
unchanged
  unsigned int r2;
  // code
  if ((r2 & 0x01) != 0) {
  // code for handling odd numbers
  }

## Slide 20: MOD %<power of 2>
remainder (mod): num % d where num ≥ 0 and d = 2k
mask = 2k -1 so for mod 16, mask = 16 -1 = 15
and r1, r2, r3
x
Example: %2
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 01 (mod 2 even or odd)
RSLT: r1 0x00 00 00 01 (odd)
forces to a 0
unchanged
Example: Mod 16
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 0f (mod 16)
RSLT: r1 0x00 00 00 07
forces to a 0
unchanged

## Slide 21: Flipping bits: bit toggle Used in PA7/PA8
x
invert (flip) bits "bit toggle" operation
  1 will flip the bit
  0 to let a bit through
eor r1, r2, r3
Observation: When applied twice, it returns the original value (symmetric encoding)
With a mask of all 1's is a 1's compliment
Example: invert (flip) the lower 8-bits
DATA: r2 0xab ab ab 77
eor
MASK: r3 0x00 00 00 ff
RSLT: r1 0xab ab ab 88
inverts (flips)
unchanged
88: 1000 1000
DATA: r1 0xab ab ab 88
eor
MASK: r3 0x00 00 00 ff apply a 2nd time
RSLT: r1 0xab ab ab 77 original value!
inverts (flips)
77: 0111 0111
Example: flip the lower 8-bits
eor r1, r2, 0xff
unsigned int r1, r2;
r1 = r2 ^ 0xff;

## Slide 22: Unsigned Integers (positive numbers) with Fixed # of Bits
4 bits is = ONLY 16 distinct values
Modular (C operator: %) or clock math
  Numbers start at 0 and “wrap around” after 15 and go back to 0
Keep adding 1
wraps (clockwise)
  0000 -> 0001 … -> 1111 -> 0000
Keep subtracting 1
wraps (counter-clockwise)
  1111 -> 1110 … -> 0000 -> 1111
Addition and subtraction use normal "carry" and "borrow" rules, just operate in binary
x

## Slide 23: Problem: How to Encode Both Positive and Negative Integers
How do we represent the negative numbers within a fixed number of bits?
  Allocate some bit patterns to negative and others to positive numbers (and zero)
distinct bit patterns to encode positive and negative values
Unsigned values: 0 ... –1
Signed values: … –1 (dividing the range in ~ half including 0)
On a number line (below): 8-bit integers – signed and unsigned (e.g., char in C)
-
+
-1
Same “width” (same number of encodings), just shifted in value
-1
Unsigned
Signed
x
-1 comes from counting 0 as a "positive" number

## Slide 24: Two’s Complement: The MSB Has a Negative Weight
4-bit (w = 4) weight = = -23 = -8
  10102 unsigned: 1x23 + 0x22 + 1x21 + 0x20 = 10
  10102 two’s complement: -1x23 + 0x22 + 1x21 + 0x20 = -8 + 2 = –6
  -8 in two’s complement: 10002 = -23 + 0 = -8
  -1 in two’s complement: 11112 = -23 + (23 – 1) = -8 + 7 = -1
weight is ), all other bits: have positive weights )
. . .
b0
bn-1
bn-2
x

## Slide 25: 2's Complement Signed Integer Method
Positive numbers encoded same as unsigned numbers
All negative values have a one in the leftmost bit
All positive values have a zero in the leftmost bit
  This implies that 0 is a positive value
Only one zero
For n bits, Number range is) to - 1)
  Negative values “go 1 further” than the positive values
Example: the range for 8 bits: -128, -127, .. 0, .. 126, +127
Example the range for 32 bits: -2147483648 .. 0, .. +2147483647
Arithmetic is the same as with unsigned binary!
x

## Slide 26: Sign Extension (how type promotion works)
Sometimes you need to work with integers encoded with different number of bits
8 bits (char) -> (16 bits) short -> (32 bits) int
Sign extension increases the number of bits: -bit wide signed integer , EXPANDS to a wider n + -bit signed integer where both have the same value
Unsigned
Just add leading zeroes to the left side
Two’s Complement Signed:
If positive, add leading zeroes on the left
  Observe: Positive stay positive
If negative, add leading ones on the left
  Observe: Negative stays negative
• • •
• • •
• • •
• • •
n
original
copies of MSB
x

## Slide 27: Example: Two’s Complement Sign or bit Extension - 1
Adding 0's in front of a positive numbers does not change its value
7 = 0111
extend to
8 bits
00000111
Number is still 7
x
1 = 0001
extend to
8 bits
00000001
Number is still 1

## Slide 28: Example: Two’s Complement Sign or bit Extension -2
Adding 1's if front of a negative number does not change its value
7 = 0111
invert = 1000
add 1 + 1
-7 1001
7 = 00000111
invert = 11111000
add 1 + 1
-7 11111001
-7 = 1001
extend to
8 bits
11111001
x
1001 = -8 + 1 = -7
11111001 =
(-128 + 64 + 32 + 16 + 8) + 1 = -8 + 1 = -7

## Slide 29: Sign Extension in C: Type casts
Convert from smaller to larger integral data types
C and Java automatically performs sign extension
Example (on pi-cluster with 32-bit int)
x
#include <stdlib.h>
#include <stdio.h>
int main(void)
{
signed char c = -1;
signed int i = c;
unsigned char d = 1;
unsigned int j = d;
printf("c decimal = %hd\n", c);
printf("c = 0x%hhx\n", c);
printf("i decimal = %d\n", i);
printf("i = 0x%x\n", i);
printf("\nd decimal = %hd\n", d);
printf("d = 0x%hhx\n", d);
printf("j decimal = %d\n", j);
printf("j = 0x%x\n", j);
return EXIT_SUCCESS;
}
%./a.out
c decimal = -1
c = 0xff
i decimal = -1
i = 0xffffffff
d decimal = 1
d = 0x1
j decimal = 1
j = 0x1

## Slide 30: Different Type of Numbers each have a Fixed # of Bits Spanning one or more contiguous bytes of memory
x
C Data Type | AArch-32 contiguous Bytes
char (arm unsigned) | 1
short int | 2
unsigned short int | 2
int | 4
unsigned int | 4
long int | 4
long long int | 8
float | 4
double | 8
long double | 8
pointer * | 4
0
31
00000000
00000001
00000010
00000011
Word 32-bit integer uses 4 bytes
0
7
15
00000000
000000001
Half Word 16-bit integer uses 2 bytes
0
7
00000000
Byte 8-bit integer uses 1 byte
most significant bit (largest power of 2)
least significant bit (smallest power of 2)
most significant byte
least significant byte

## Slide 31: Byte Ordering of Numbers In Memory: Endianness
Two different ways to place multi-byte integers in a byte addressable memory
Big-endian: Most Significant Byte (“big end”) starts at the lowest (starting) address
Little-endian: Least Significant Byte (“little end”) starts at the lowest (starting) address
Example: 32-bit integer with 4-byte data
a1
b2
c3
d4
0x100
0x101
0x102
0x103
01
23
a1
b2
c3
d4
01
23
d4
c3
b2
a1
Big-Endian
Little-Endian
MSB
Most significant byte
LSB
Least significant byte
x
0x100
0x101
0x102
0x103

## Slide 32: Byte Ordering Example
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
int x = 12345;
// or x = 0x00003039; // show all 32 bits
39
30
00
00
IA32, ARM32 (little-endian)
30
39
00
00
(big-endian)
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
x

## Slide 33: Byte Addressable Memory Shown as 32-bit words
Observation
32-bit aligned addresses
rightmost 2 bits of the address are always 0
0x12345680
0x12345682
0x12345681
0x12345683
0x00
0x01
0x02
0x03
1 32-bit
(4 byte) word
0x12345684
0x12345686
0x12345687
0x12345685
0x04
0x05
0x06
0x07
1 byte Memory Content
One byte per row
Byte
Memory
Address
1 32-bit
(4 byte) word
Word Aligned address
Word Aligned address
x
0x04
0x05
0x06
0x07
0x00
0x01
0x02
0x03
LSByte
MSByte
0x12345680
0x12345681
0x12345682
0x12345683
Contents of Memory
One 32-bit (4 byte) word per row
0x12345680
0x12345684
Byte address
0x12345688
0x1234568c
Word
Memory
Address

## Slide 34: Using pointers to examine byte order (on pi-cluster)
#include <stdio.h>
#define SZ 2
int main()
{
unsigned int foo[SZ] = {0x11223344, 0xaabbccdd};
unsigned int *iptr = foo;
unsigned char *chptr = (unsigned char *)foo;
for (int i = SZ-1; i >= 0; i--)
printf("foo[%d]: %x\n", i, *(iptr + i));
for (int i = sizeof(foo)-1; i >= 0; i--)
printf("byte %d: %x\n", i, (unsigned int)*(chptr + i));
return 0;
}
kmuller@keithm-pi4:~$ ./a.out
foo[1]: aabbccdd
foo[0]: 11223344
byte 7: aa
byte 6: bb
byte 5: cc
byte 4: dd
byte 3: 11
byte 2: 22
byte 1: 33
byte 0: 44
0x12345680
0x12345682
0x12345681
0x12345683
0x44
0x33
0x22
0x11
0x12345684
0x12345686
0x12345687
0x12345685
0xdd
0xcc
0xbb
0xaa
x

## Slide 35: Shift and Rotate Instructions
Instruction | Syntax | Operation | Notes | Diagram
Logical Shift Left int x; or unsigned int x x << n; | lsl Rd, Rm, const5 lsl Rd, Rm, Rs | Rd  Rm << const5 Rd  Rm << Rs | Zero fills shift: 0 - 31 | 
Logical Shift Right unsigned int x; x >> n; | lsr Rd, Rm, const5 lsr Rd, Rm, Rs | Rd  Rm >> const5 Rd  Rm >> Rs | Zero fills shift: 1 – 32 | 
Arithmetic Shift Right int x; x >> n; | asr Rd, Rm, const5 asr Rd, Rm, Rs | Rd  Rm >> const5 Rd  Rm >> Rs | Sign extends shift: 1 - 32 | 
Rotate Right unsigned int x; x = (x>>n)¦(x<<(32-n)); | ror Rd, Rm, const5 ror Rd, Rm, Rs | Rd  Rm ror const5 Rd  Rm ror Rs | right rotate rot: 0 - 31 | 
operand 2 constant
destination
<inst>
Rd
const5
Rm
operand 1
Number of bit to shift or rotate: const 5 bits
operand 2
destination
<inst>
Rd
Rm
operand 1
Rs
Number of bit to shift or rotate: Rs
x

## Slide 36: Shift Operations in C
n is number of bits to shift a variable x of width w bits
Shifts by n < 0 or n ≥ w are undefined
Left shift (x << N) – Multiplies by
  Shift N bits left, Fill with 0s on right
In C: behavior of >> is determined by compiler
  gcc: it depends on data type of x (signed/unsigned)
Right shift (x >> N) - Divides by
  Logical shift (for unsigned variables)
    Shift N bits right, Fill with 0s on left
  Arithmetic shift (for signed variables) – Sign Extension
    Shift N bits right while Replicating the most significant bit on left
    Maintains sign of x
In Java: logical shift is >>> and arithmetic shift is >>
Left Shift
Right logical Shift
Right Arithmetic Shift
x

## Slide 37: Arithmetic Shift Right Example: Testing Sign
asr r2, r0, 31
r0 0xab ab ab 77 // bit 31 is a one
r2 0xff ff ff ff // see the sign extend
asr r2, r0, 31
cmp r2, -1
bne .Lendif
//code neg #
.Lendif:
Test for sign
-1 if r0 negative
x
int i;
//code
if ((i>>31) == -1) {
// code neg #
}

## Slide 38: Arithmetic Shift Right Example: Testing SIgn
asr r2, r0, 31
r0 0x7b ab ab 77 // bit 31 is a zero
r2 0x00 00 00 00 // see the sign extend
asr r2, r0, 31
cmp r2, 0
bne .Lendif
//code positive #
.Lendif:
Test for sign
0 if r0 positive
x
int i;
//code
if ((i>>31) == 0) {
// code pos #
}

## Slide 39: Logical Shift & Rotate Operations
lsr r2, r0, 8
r0 0xab ab ab 77
r2 0x00 ab ab ab
lsl r2, r0, 8
r0 0xab ab ab 77
r2 0xab ab 77 00
ror r2, r0, 8
r0 0xab ab ab 77
r2 0x77 ab ab ab
x

## Slide 40: Extracting/Isolating Unsigned Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsr r1, r1, 24
r1 = r1 >> 24;
unsigned zero-extension (all 0’s)
Extracted bit-field
r1
byte 0
byte 1
byte 3
byte 2
lsl r1, r0, 8
unsigned int r0,r1;
r1 = r0 << 8;
Next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
pushed bits to far right
Hint: Useful for PA7

## Slide 41: Extracting Signed Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsl r1, r0, 8
int r0,r1;
r1 = r0 << 8;
next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
asr r1, r1, 24
r1 = r1 >> 24;
signed extend (all 1’s)
Extracted
bit-field
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far right

## Slide 42: Inserting Bitfields – Inserting Source Field into Destination Field
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
r1
r0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Task: Insert source into destination
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
results in
orr r1, r1, r2
r1 = r1 | r2;
r1
r2
Approach
(1) isolate source field
(2) clear destination field
(3) Bitwise or together
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 43: Inserting Bitfields – Isolating the Source Field
r2
r0
x
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
isolate source field
lsl r2, r0, 24
lsr r2, r2, 8
r2 = r0 << 24;
r2 = r2 >> 8;
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r0
r2

## Slide 44: Inserting Bitfields – Clearing the Destination Field
x
lsl r1, r1, 8
r1 = r1 << 8;
r1
r3
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
r1
r1
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
clear the destination field
ror r1, r1, 24
r1=(r1>>24)|(r1<<8);
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ror r1, r1, 16
r1= (r1>>16)|(r1<<16);

## Slide 45: Inserting Bitfields – Combining Isolated Source and Cleared Destination
x
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
inserted field
orr r1, r1, r0
r1 = r1 | r0;
r1
r2
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
isolated source
r1
r1
field cleared in destination

## Slide 46: Masking Summary
Isolate a field: Use lsr, lsl, rot to get a field surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Select a field: Use and with a mask of one's surrounded by zero's to select the bits that have a 1 in the mask, all other bits will be set to zero
Clear a field: Use and with a mask of zero's surrounded by one's to select the bits that have a 1 in the mask, all other bits will be set to zero
1 1 1 1 1 1 1 1 | 0 0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
x
0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 | 0 0 0 0 0 0 0 0 0 0 0 0 0 0
selects this field when used with and
selection mask
clear a field mask
clears this field when used with and
lsl to get this edge into msb
lsr to get this edge into lsb
Insert a field: Use orr with fields surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Keep these bits | 0 0 0 0 0 0 0 0 | Keep these bits

## Slide 47: Reference For PA7/8: C Stream Functions Opening Files
FILE *fopen(char filename[], const char mode[]);
Opens a stream to the specified file in specified file access mode
  returns NULL on failure – always check the return value; make sure the open succeeded!
Mode is a string that describes the actions that can be performed on the stream:
''r’’ Open for reading.
The stream is positioned at the beginning of the file. Fail if the file does not exist.
''w’’ Open for writing.
The stream is positioned at the beginning of the file. Create the file if it does not exist.
''a’’ Open for writing.
The stream is positioned at the end of the file. Create the file if it does not exist.
Subsequent writes to the file will always be at current end of file.
An optional ''+'' following ''r'', ''w'', or ''a'' opens the file for both reading and writing
x

## Slide 48: Reference: C Stream Functions Closing Files and Usage
int fclose(FILE *stream);
  Closes the specified stream, forcing output to complete (eventually)
    returns EOF on failure (often ignored as no easy recovery other than a message)
Usage template for fopen() and fclose()
  Open a file with fopen() always checking the return value
  do i/o – keep calling stdio io routines
  close the file with fclose() when done with that I/O stream
x

## Slide 49: C Stream Functions Array/block read/write
  These do not process contents they simply transfer a fixed number of bytes to and from a buffer passed to them
  size_t fwrite(void *ptr, size_t size, size_t count, FILE *stream);
  Writes an array of count elements of size bytes from stream
  Updates the write file pointer forward by the number of bytes written
  returns number of elements written
  error is short element count or 0
  size_t fread(void *ptr, size_t size, size_t count, FILE *stream);
  Reads an array of count elements of size bytes from stream
  Updates the read file pointer forward by the number of bytes read
  returns number of elements read, EOF is a return of 0
  error is short element count or 0
I almost always set size to 1 to return bytes read/written
x

## Slide 50: C fread/fwrite Example - 1
#include <stdio.h>
#include <stdlib.h>
#include <errno.h>
#define BFSZ 8192 /* size of read */
int main(void)
{
unsigned char fbuf[BFSZ];
FILE *fin, *fout;
size_t readlen;
size_t bytes_copied = 0;
retval = EXIT_SUCCESS;
if (argc != 3){
fprintf(stderr, "%s requires two args\n", argv[0]);
return EXIT_FAILURE;
}
/* Open the input file for read */
if ((fin = fopen(argv[1], "r")) == NULL) {
fprintf(stderr,"fopen for read failed\n");
return EXIT_FAILURE;
}
/* Open the output file for write */
if ((fout = fopen(argv[2], "w") == NULL) {
fprintf(stderr, "fopen for write failed\n");
fclose(fin);
return EXIT_FAILURE;
}
x
To handle bytes moved
% ls –ls ZZZ
ls: ZZZ: No such file or directory
% ./a.out cp.c ZZZ
bytes copied: 1122
% ls -ls cp.c ZZZ
8 -rw-r--r-- 1 kmuller staff 1122 Jul 2 08:51 ZZZ
8 -rw-r--r-- 1 kmuller staff 1122 Jul 2 08:49 cp.c

## Slide 51: C fread/fwrite Example - 2
/* Read from the file, write to fout */
while ((readlen = fread(fbuf, 1, BUFSIZ, fin)) > 0) {
if (fwrite(fbuf, 1, readlen, fout) != readlen) {
fprintf(stderr, "write failed\n");
retval = EXIT_FAILURE;
break;
}
bytes_copied += readlen; //running sum bytes copied
}
if (retval == EXIT_FAILURE)
printf("Failure Copy did not complete only ");
printf("Bytes copied: %zu\n", bytes_copied);
fclose(fin);
fclose(fout);
return retval;
}
x
By using an element size of 1 with a char buffer, this is byte I/O
Capture the bytes read so you know how many bytes to write
unless the input file length is an exact multiple of BUFSIZ, last fread() will always read less than BUFSIZ which is why you write readln
readln
BUFSZ
Jargon: the last record is often called the "runt"

## Slide 52: Assembly Source File to Executable to Linux Memory
Local variables and function call overhead
code you write in the text segment
allocates space dynamically during execution by c runtime library code (text)
x
OS kernel [protected]
Stack
Heap
Static Data
Shared Libraries
Read Only Data
Read Only Text Segment
`
.bss
uninitialized static variables
.data
initialized static variables
.section .rodata
read-only literals
.text
assembly code
BSS
Sections in an Assembly Source file
File Header
Specify Hardware assembler generate the correct ARM version
file footer
.section .note.GNU-stack,…
.end
Text
Symbol table
Data
a.out executable
created by the assembler &
link editor
Header - Description

## Slide 53: Creating Segments, Definitions In Assembly Source
The following assembler directives indicate the start of a memory segment specification
  Remains in effect until the next segment directive is seen
x
.bss
    // start uninitialized static segment variables definitions
  // does not consume any space in the executable file
.data
// start initialized static segment variables definitions
.section .rodata
// start read-only data segment variables definitions
.text
// start read-only text segment (code)

## Slide 54: Assembly Source File Template
assembly programs end in .S
  That is a capital .S
  example: test.S
Always use gcc to assemble
  _start() and C runtime
File has a complete program
  gcc file.S
File has a partial program
  gcc –c file.S
Link files together
  gcc file.o cprog.o
// File Header
.arch armv6 // armv6 architecture instructions
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
// BSS Segment (only when you have initialized globals)
.bss
// Data Segment (only when you have uninitialized globals)
.data
// Read-Only Data (only when you have literals)
.section .rodata
// Text Segment – your code
.text
// Function Header .type main, %function // define main to be a function
.global main // export function name
main:
// function prologue // stack frame setup
// your code for this function here
// function epilogue //stack frame teardown
// function footer
.size main, (. – main)
// File Footer
.section .note.GNU-stack,"",%progbits // stack/data non-exec
.end
x

## Slide 55: Preview: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
r0, r1 = function(r0, r1, r2, r3) // 64-bit return – long long
Each parameter and return value is limited to data that can fit in 4 bytes or less
You receive up to the first four parameters in these four registers
You copy up to the first four parameters into these four registers before calling a function
For parameter values using more than 4 bytes, a pointer to the parameter is passed (we will cover this later)
You MUST ALWAYS assume that the called function will alter the contents of all four registers: r0-r3
  In terms of C runtime support, these registers contain the copies given to the called function
  C allows the copies to be changed in any way by the called function
Register | Function Call Use
r0 | 1st parameter
r1 | 2nd parameter
r2 | 3rd parameter
r3 | 4th parameter
Register | Function Return Value Use
r0 | 8, 16 or 32-bit result, 32-bit address or least-significant half of a 64-bit result
r1 | most-significant half of a 64-bit result
x

## Slide 56: Preview: Writing an ARM32 function
#include <stdlib.h>
#include <stdio.h>
int sum4(int, int, int, int);
int main()
{
int reslt;
reslt = sum4(1,2,3,4);
printf("%d\n", reslt);
return EXIT_SUCCESS;
}
#ifndef SUM4_H
#define SUM4_H
#ifndef __ASSEMBLER__
int sum4(int, int, int, int);
#else
.extern sum4
#endif
#endif
#include "sum4.h"
.arch armv6
.arm
.fpu vfp
.syntax unified
.global sum4
.type sum4, %function
.equ FP_OFF, 28
// r0 = sum4(r0, r1, r2, r3)
sum4:
push {r4-r9, fp, lr}
add fp, sp, FP_OFF
add r0, r0, r1
add r0, r0, r2
add r0, r0, r3
sub sp, fp, FP_OFF
pop {r4-r9, fp, lr}
bx lr
.size sum4, (. - sum4)
.section .note.GNU-stack,"",%progbits
.end
$ gcc -Wall -Wextra -c main.c
$ gcc -c sum4.S
$ gcc sum4.o main.o
$ ./a.out
10
two _

## Slide 57: Load/Store: Register Base Addressing
32-bit memory
register r0
register r1 (address)
ldr r0, [r1]
Copies a 32-bit word
from the memory location
whose address is contained
in r1 (r1 is a pointer)
into register r0
r1 is being used as a pointer to a location in memory
ldr requires the use of a pointer operand
str r0, [r1]
Copies all 32 bits of the value held in register r0 to the 32-bit memory location contained in register r1 (r1 pointer)
32-bit memory
register r0
register r1 (address)
r1 is being used as a pointer to a location in memory
str requires the use of a pointer operand
x

## Slide 58: LDR/STR – Base Register + Immediate Offset Addressing
ldr/str Rd, [Rn, +- imm12] // base register pointer + offset imm12 in bytes
-4095 <= imm12 <= 4095 (bytes)
ldr/str Rd, [Rn] // base register pointer + 0 offset (imm12 is 0)
Register Base Addressing:
  Pointer Address: Rn; source/destination data: Rd
  Unsigned pointer address in stored in the base register
Register Base + immediate offset Addressing:
  Pointer Address = register content + immediate offset
  Unsigned offset integer immediate value (bytes) is added or subtracted (U bit above says to add or subtract) from the pointer address in the base register
unsigned immediate offset
Rd – source/dest register
ldr/str
Rd
imm12
Rn
Rn – base register contains address (pointer)
U
+/- offset
x

## Slide 59: ldr/str Register Base and Register + Immediate Offset Addressing
Syntax | Address | Examples
ldr/str Rd, [Rn +/- constant] constant is in bytes | Rn + or – constant same | ldr r0, [r5,100] str r1, [r5, 0] str r1, [r5]
ldr/str
Rd
imm12
Rn
U
+ -
0 subtract
1 add
Memory Address
Instruction
Source for str
Destination for ldr
x

## Slide 60: Example Base Register Addressing Load – Modify – Store
x = x + 1;
ldr r0, [r1] // r0 = *r1 (read x)
add r0, r0, 1 // r0 = r0 + 1 (x++)
str r0, [r1] // *r1 = r0 write x
Memory assigned to x
register r0
register r1 (address)
+ 1
0b..0000100
Notice: word aligned!
(last two bits are 0's)
..00000000
..00000001
n-bit Memory
Address
binary
..00000010
..00000011
..00000100
..00000101
..00000110
..00000111
01010101
10101010
01010101
10101010
01010101
10101010
01010101
10101010
1 byte
contents
X starting address
x
x = x + 1
Where x is in memory
r1 is a pointer

## Slide 61: Loading and Storing: Variations List
Load and store have variations that move 8-bits, 16-bits and 32-bits
Load into a register with less than 32-bits will set the upper bits not filled from memory differently depending on which variation of the load instruction is used
Store will only select the lower 8-bit, lower 16-bits or all 32-bits of the register to copy to memory, register contents are not altered
Instruction | Meaning | Sign Extension | Memory Address Requirement
ldrsb | load signed byte | sign extension | none (any byte)
ldrb | load unsigned byte | zero fill (extension) | none (any byte)
ldrsh | load signed halfword | sign extension | halfword (2-byte aligned)
ldrh | load unsigned halfword | zero fill (extension) | halfword (2-byte aligned)
ldr | load word | --- | word (4-byte aligned)
strb | store low byte (bits 0-7) | --- | none (any byte)
strh | store halfword (bits 0-15) | --- | halfword (2-byte aligned)
str | store word (bits 0-31) | --- | word (4-byte aligned)
x

## Slide 62: Loading 32-bit Registers From Memory Variables < 32-Bits Wide
Unsigned
Zero-Extend: Add leading 0’s
example ldrb
Instructions that zero-extend:
ldrb, ldrh
0b 1110 0001
0x00
0x00
0x00
0xe1
memory
r0
Overwrite the upper three bytes with 0
Signed (2’s complement)
Sign-Extend: Replicate sign bit
example ldrsb
Instructions that sign-extend:
ldrsb, ldrsh
0xff
0xff
0xff
0xe1
memory
r0
Overwrite the upper three bytes with 1
0b 1110 0001
x

## Slide 63: Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrb r1, [r0]
r1
0
31
r1
Load a word
ldr r1, [r0]
observe the zero fill
x
0x0a
0x0b
0x0c
0x0d
0xe1
0xe3
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
0xe3
0xe1
0x00
0x00
0
31
r1
Load a halfword
ldrh r1, [r0]
0x00
0x00
0xe3
0xe1
observe the zero fill
0xe1

## Slide 64: Signed Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrsb r1, [r0]
r1
0
31
r1
Load a word (no change)
ldr r1, [r0]
observe the sign extend
x
0x0a
0x0b
0x0c
0x0d
1110 0001
1110 0011
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
1110 0011
1110 0001
0x00
0x00
0
31
r1
Load a halfword
ldrsh r1, [r0]
0x00
0x00
observe the sign extend
1110 0011
1110 0001
0xff
0xff
1110 0001
0xff
0xff
0xff

## Slide 65: Signed Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrsb r1, [r0]
r1
0
31
r1
Load a word (no change)
ldr r1, [r0]
observe the sign extend
x
0x0a
0x0b
0x0c
0x0d
0110 0001
0110 0011
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
0110 0011
0110 0001
0x00
0x00
0
31
r1
Load a halfword
ldrsh r1, [r0]
0x00
0x00
0110 0011
0110 0001
observe the sign extend
0110 0001

## Slide 66: Storing 32-bit Registers To Memory 8-bit, 16-bit, 32-bit
strb
0x00
0x00
0xe2
0xe1
memory
r0
0x??
0x??
0x??
0xe1
Not Changed
strh
0x00
0x00
0xe2
0xe1
memory
r0
0x??
0x??
0xe2
0xe1
Not Changed
x
str
0x04
0x03
0xe2
0xe1
memory
r0
0x04
0x03
0xe2
0xe1

## Slide 67: Store a Byte, Half-word, Word
0x20
0x00
0x00
0x00
initial value in r0
0
31
Store a byte
strb r1, [r0]
r1
0x87
0x65
0xe3
0xe1
0x11
0x22
0x33
0x20000000
0x20000001
0x20000002
0x20000003
observe other bytes NOT altered
Byte Address Byte
x
0x00
0xe1
0
31
r1
Store a halfword
strh r1, [r0]
0x87
0x65
0xe3
0xe1
0x22
0x33
0x20000000
0x20000001
0x20000002
0x20000003
Byte Address Byte
0x11
0x00
0xe1
0xe3
0
31
0x87
0x65
0xe3
0xe1
r1
Store a word
str r1, [r0]
0x20000000
0x20000001
0x20000002
0x20000003
Byte Address Byte
0x11
0x22
0x33
0x00
0xe1
0xe3
0x65
0x87