## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 2.05
Lecture – 20
Frontier Exascale
Final Exam Review

## Slide 3: Logistics
Monday 6/10/2024 11:30am - 2:30pm (Arrive at 11:20 AM if possible)
Two Rooms
PCYNH 109
PCYNH 122
Seating Chart (look it up before arriving)
See Piazza post or canvas

## Slide 4: Logistics
By appointment email: kmulller@ucsd.edu
Q&A zoom session as follows:
Friday: Jun 7, 2024 04:00 PM Pacific Time (US and Canada) https://ucsd.zoom.us/j/97367536447
Meeting ID: 973 6753 6447
Saturday Jun 8, 2024 03:00 PM Pacific Time (US and Canada)
https://ucsd.zoom.us/j/96404434647
Meeting ID: 964 0443 4647
Sunday Jun 9, 2024 03:00 PM Pacific Time (US and Canada)
https://ucsd.zoom.us/j/92978836290
Meeting ID: 929 7883 6290

## Slide 5
Asking me to Count the most dots…
WILL NOT Get Credit
Nice Job, Will get Credit

## Slide 6: Memory Triangle: Hardware Cost/Performance/Capacity Tiers
x
DIMM memory Module
PCI-E
ALU & Logic
Address
Data
Registers
Caches
Address
Data
CPU
~300 K Cycles
Largest Capacity
Slowest performance
Lowest Cost $/capacity
Assume each instruction takes 1 clock cycle
Clock cycle =~ time to access; larger is slower
Smallest Capacity
Highest Performance
Highest cost/capacity
Design Goal: best performance at the lowest (or specific) cost
Other goals: performance/energy (operating cost), expandability, high margin (price/cost)

## Slide 7: Variables in C
Global variables
  Defined at file scope (outside of a block)
  have static storage duration
  global variables defined without an initial value default to 0 (set prior to program execution start)
  global variables defined with an initial value are set at program start
Local (block scope, or automatic) variables (including function parameter variables)
  Defined at block scope (inside of a block)
  have automatic storage duration, with one exception (see below)
  block scope variables defined without an initial value have an unspecified initial value
  block scope variables defined with an initial are set each time by code when the block is entered
  All block scope variables become unspecified at block exit
Variable definitions preceded by the keyword static always have static storage duration including variables defined with block scope (when used global variables it restricts scope – later slides)
x
int global; // global with static storage duration, initial value = 0
int foo(void)
{
static int s; // "local" with static storage duration, initial value = 0
int x; // "local" with automatic storage duration
}

## Slide 8: Example: Block scope (local) static storage duration variables
x
#include <stdio.h>
#include <stdlib.h>
#define MAX 5
int foo(void)
{
static int s; //static storage duration, set to 0 at program start
return s += 1;
}
int main(void)
{
for (int i = 0; i < MAX; i++)
printf("%d ", foo());
printf("\n");
return EXIT_SUCCESS;
}
% ./a.out
1 2 3 4 5
%

## Slide 9: Conditional Statements (if, while, do...while, for)
C conditional test expressions: 0 (NULL) is FALSE, any non-0 value is TRUE
C comparison operators ( ==, !=, >, etc.) evaluate to either 0 (false) or 1 (true)
Legal in Java and in C:
Illegal in Java, but legal in C (often a typo!):
i = 0; if (i == 5) statement1; else statement2;
i = 0; if (i = 5) statement1; else statement2;
Assignment operators evaluate to
the value that is assigned, so….
Which statement is executed
after the if statement test?
Which statement is executed
after the if statement test?
x

## Slide 10: Program Flow – Short Circuit or Minimal Evaluation
In evaluation of conditional guard expressions, C uses what is called short circuit or minimal evaluation
Each expression argument is evaluated in sequence from left to right including any side effects (modified using parenthesis), before (optionally) evaluating the next expression argument
If after evaluating an argument, the value of the entire expression can be determined, then the remaining arguments are NOT evaluated (for performance)
x
if ((x == 5) || (y > 3)) // if x == 5 then y > 3 is not evaluated

## Slide 11: Program Flow – Short Circuit or Minimal Evaluation
x
if ((a != 0) && func(b)) // if a is 0, func(b) is not called
do_something();
// if (((x > 0) && (c == 'Q')) evaluates to non zero (true)
// then (b == 3) is not tested
while (((x > 0) && (c == 'Q')) || (b == 3)) { // c short circuit
x = x / 2;
if (x == 0) {
return 0;
}
}

## Slide 12: Address and Pointers
An address refers to a location in memory, the lowest or first byte in a contiguous sequence of bytes
A pointer is a variable whose contents (or value) can be properly used as an address
  The value in a pointer should be a valid address allocated to the process by the operating system
The variable x is at memory address 0x90001008
The variable pt is at memory location 0x90001000
The contents of pt is the address of x 0x90001008
00
00
00
77
(1 Byte)
90
00
01
08
0x90001000
0x90001001
0x90001002
0x90001003
0x90001004
0x90001005
0x90001006
0x90001007
0x90001008
0x90001009
0x9000100A
0x9000100B
0x9000100C
0x9000100D
0x9000100E
0x9000100F
32-bit address
(hex)
int x =
0x77; ------>
pt is a pointer to x------>
x

## Slide 13: Each use of a * operator results in one additional read : both sides
x
int c[] = {1, 2, 3};
int b = 4;
int *p;
p = c;
*(++p) = b;
1
b
4
c[2]
c[1]
c[0]
2
p
read address
write address (++)
write
4
p
1
2
read integer
write integer
0x108
b
read address
Address
0x110
0x10c
0x108
0x104
0x100
3
3
c[2]
c[1]
c[0]
read integer
2 reads and 2 writes
write address

## Slide 14: Double Indirection: Lside
x
int z = 2;
int y = 1;
int *w;
int *p;
int **d;
p = &z;
w = &y;
d = &p;
**d = *w;
0x108
p
1
z
2
read integer
write integer
read address
y
0x1c
w
read address
Address
0x10c
0x108
0x104
0x100
0x0fc
0x100
d
read address
w
2
y or *w
1
z or **d or *p
p or *d
read address
read address
read
write
d
read address

## Slide 15: Double Indirection: Rside
x
int z = 2;
int y = 1;
int *w;
int *p;
int **d;
p = &z;
w = &y;
d = &p;
**d = **d + *p;
w
2
y
1
z
p
read address
read address
read
d
read address
read
2 + 2
write Integer
0x108
p
1
z
2
read integer
write integer
read address
y
0x1c
w
read address
Address
0x10c
0x108
0x104
0x100
0x0fc
0x100
d
read address
2 + 2
Important Observation
**d on Lside is two reads
**d on Rside is three reads

## Slide 16: Variables in Memory: Size and Address
The number of contiguous bytes a variable uses is based on the type of the variable
  Different variable types require different numbers of contiguous bytes
Variable names map to a starting address in memory
Example Below: Variables all starting at address 0x80, each box is a byte
x
01010101
memory
char
80
Start
00000000
11111111
10101010
01010101
memory
int
4 bytes
80
82
81
83
Start
Size in bytes
memory
short int
2 bytes
80
10101010
81
01010101
Start
Size in bytes

## Slide 17: sizeof(): Variable Size (number of bytes) Operator
sizeof() operator returns a value of type size_t:
the number of bytes used to store a variable or variable type
  size_t size = sizeof(variable_type);
  or
  size_t size = sizeof(variable_name); // preferred!
The argument to sizeof() is often an expression:
size = sizeof(int * 10);
  reads as:
    number of bytes required to store 10 integers (an array of [10])
#include <stddef.h>
/* size_t type may vary by system but is always unsigned */
x

## Slide 18: Accessing Arrays Using Indexing
name[index] selects the index element of the array
  index should be unsigned
  Elements range from: 0 to count – 1 ( int x[count]; )
name[index] can be used as an assignment target or as a value in an expression
Array name (by itself with no [ ]) on the Rside evaluates to the address of the first element of the array
x
??
??
1 word
(int = 4 bytes)
9000
9004
9008
9012
9016
9020
high
address
low
address
b[0]
b[1]
b[2]
b[3]
b[4]
??
??
??
??
??
??
int a[2] = {1, 2};
a[0] = a[1];
int b[5];
int *p = b;
9000
p

## Slide 19: How many elements are in an array?
The number of elements of space allocated to an array (called element count) and indirectly the total size in bytes of an array is not stored anywhere!!!!!!
An array name is just the address of the first element in a block of contiguous memory
  So, an array does not know its own size!
??
??
??
??
??
??
??
??
??
??
??
??
??
??
1 word
(int = 4 bytes)
90000
90004
90008
90012
90016
90020
high
memory
address
b[0]
b[1]
b[2]
b[3]
b[4]
b[5]
int b[6];
x
#define SZ 6
int block[SZ]; // you specify the array has SZ elements
int indx; // use when SZ is defined
for (indx = 0; indx < SZ; indx++)
block[indx] = 0;

## Slide 20: Pointers and Arrays - 1
A few slides back we stated: Array name (by itself) on the Rside evaluates to the address of the first element of the array
Array indexing syntax ([ ]) an operator that performs pointer arithmetic
buf and &buf[0] on the Rside are equivalent, both evaluate to the address of the first array element
x
int buf[] = {2, 3, 5, 6, 11};
0x12345680
0x12345682
0x12345681
0x12345683
0x02
0x00
0x00
0x00
0x12345684
0x12345686
0x12345687
0x12345685
0x03
0x00
0x00
0x00
1 byte Memory Content
One byte per row
Byte
Memory
Address
p
p1
p2
int *p = buf; // or int *p = &buf[0];
int *p1 = &buf[1];
int *p2 = &buf[2];
int *p3 = &buf[3];

## Slide 21: C Strings - 1
C does not have a dedicated type for strings
Strings are an array of characters terminated by a sentinel termination character
'\0' is the Null termination character; has the value of zero (do not confuse with '0')
An array of chars contains a string only when it is terminated by a '\0'
Length of a string is the number of characters in it, not including the '\0'
Strings in C are not objects
  No embedded information about them, you just have a name and a memory location
  You cannot use + or += to concatenate strings in C
  For example, you must calculate string length using code at runtime looking for the sentinel
index | 0 | 1 | 2 | 3 | 4 | 5
char | 'H' | 'e' | 'l' | 'l' | 'o' | '\0'
length of the string: number of char (= 5)
length (size) of the array in number of char (= 6)
x

## Slide 22: Output Parameters (Mimics Call by Reference)
Passing a pointer parameter with the intent that the called function will use the address it to store values for use by the calling function, then pointer parameter is called an output parameter
To pass the address of a variable x use the address operator (&x) or the contents of a pointer variable that points at x, or the name of an array (the arrays address)
To be receive an address in the called function, define the corresponding parameter type to be a pointer (add *)
  It is common to describe this method as: "pass a pointer to x"
C is still using "pass by value"
  we pass the value of the address/pointer in a parameter copy
  The called routine uses the address to change a variable in the caller's scope
x
void inc(int *p);
int
main(void)
{
int x = 5;
inc(&x);
}
void
inc(int *p)
{
}

## Slide 23: Array Parameters: Call-By-Value or Call-By-Reference?
Type[] array parameter is automatically “promoted” to a pointer of type Type *, and a copy of the pointer is passed by value
Call-by-value pointer (callee can change the pointer parameter to point to something else!)
Acts like call-by-reference (called function can change the contents caller’s array)
void passa(int []);
int main(void)
{
int numbers[] = {9, 8, 1, 9, 5};
passa(numbers);
printf("numbers size:%lu\n", sizeof(numbers)); // 20
return EXIT_SUCCESS;
}
void passa(int a[])
{
printf("a size:%lu\n", sizeof(a)); // 4
return;
}
IMPORTANT:
See the size difference 20 in main() in passa() is 4 bytes (size of a pointer) on pi-cluster and 8 on ieng6
x
the name is the address, so this is
passing a pointer to the start of the array

## Slide 24: Arrays As Parameters, Approach 1: Pass the size
Two ways to pass array size
pass the count as an additional argument
add a sentinel element as the last element
int sumAll(int *a, int size);
int main(void)
{
int numb[] = {9, 8, 1, 9, 5};
int cnt = (int)(sizeof(numb)/sizeof(numb[0]));
printf("sum is: %d\n", sumAll(numb, cnt););
return EXIT_SUCCESS;
}
remember you can only use sizeof() to calculate element count where the array is defined
int sumAll(int *a, int size)
{
int sum = 0;
int *end;
end = a + size;
while (a < end)
sum += *a++;
return sum;
}
x
0x110
0x10c
0x108
0x104
0x100
1 word content
(int = 4 bytes)
9
8
1
9
5
0x??
0x??
end
a
0x100
0x114
numb
address
same as:
sum = sum + *a;
a++;

## Slide 25: Arrays As Parameters, Approach 2: Use a sentinel element
A sentinel is an element that contains a value that is not part of the normal data range
  Forms of 0 are often used (like with strings). Examples: '\0', NULL
int strlen(char *a); // returns number of chars in string, not counting \0
int main(void)
{
char buf[] = {'a', 'b', 'c', 'd', 'e', '\0'}; // or buf[] = "abcde";
printf("Number of chars is: %d\n", strlen(buf));
return EXIT_SUCCESS;
}
x
0x106
0x105
0x104
0x103
0x102
0x101
0x100
1 byte
'a'
'b'
'c'
'd'
'e'
'\0'
0x??
p
s
0x100
0x105
buf
address
/* Assumes parameter is a terminated string */
int strlen(char *s)
{
char *p = s;
if (p == NULL)
return 0;
while (*p != '\0')
p++;
return (p – s);
}

## Slide 26: Returning a Pointer To a Local Variable (Dangling Pointer)
There are many situations where a function will return a pointer, but a function must never return a pointer to a memory location that is no longer valid such as:
Address of a passed parameter copy as the caller may or will deallocate it after the call
Address of a local variable (automatic) that is invalid on function return
These errors are called a dangling pointer
int *bad_idea(int n)
{
return &n; // NEVER do this
}
n is a parameter with the scope of bad_idea
it is no longer valid after the function returns
a is an automatic (local) with a scope and lifetime within bad_idea2
a is no longer a valid location after the function returns
int *bad_idea2(int n)
{
int a = n * n; return &a; // NEVER do this
}
/*
* this is ok to do
* it is NOT a dangling
* pointer
*/
int *ok(int n)
{
static int a = n * n; return &a; // ok
}
x

## Slide 27: String Literals, Mutable and Immutable arrays - 1
mess1 is a mutable array (type is char [ ]) with enough space to hold the string + ’\0’
mess2 is a pointer to an immutable array with space to hold the string + ’\0’
mess3 is a pointer to a mutable array
char mess1[] = "Hello World";
*(mess1 + 5) = '\0'; // shortens string to "Hello"
char *mess2 = "Hello World"; // "Hello World" read only string literal
// mess2 is a pointer NOT an array!
*(mess2 + 1) = '\0'; // Not OK (bus error)
x
char *mess3 = (char []) {"Hello World"}; // mutable string
*(mess3 + 1) = '\0'; // ok
Hello World\0
mess1[ ]
Hello World\0
mess2
read only string literal
using the cast (char [ ]) makes it mutable
Hello World\0
mess3
mutable string

## Slide 28: main() Command line arguments: argc, argv
Arguments are passed to main() as a pointer to an array of pointers to char arrays (strings)(**argv)
Conceptually: % *argv[0] *argv[1] *argv[2] ….
argc is the number of VALID elements (they point at something)
*argv (argv[0]) is usually is the name of the executable file (% ./vim file.c)
argv[argc] or *(argv + argc) always contains a NULL (0) sentinel
argv elements point at mutable (fixed size) strings!
argv+0
argv+1
argv+2
argc
3
argv
x
% ./csv 2 3
argv+3
NULL
.
/
c
s
v
\0
2
\0
3
\0
argv[0][5]
argv[0][0]
argv[2][0]
argv[1][1]

## Slide 29: Accessing argv char at a time
argv is a pointer variable, whose contents can be changed
it is not an array name, which is just an address that cannot be changed
int main(int argc, char **argv)
{
char *pt;
(void)argc; // shut up the compiler
while ((pt = *argv++) != NULL) {
while (*pt != '\0')
putchar(*pt++);
putchar('\n');
}
return EXIT_SUCCESS;
}
x
argv+0
argv+1
argv+2
argc
3
argv
% ./csv 2 3
argv+3
NULL
.
/
c
s
v
\0
2
\0
3
\0
**(argv + 2)
*(*(argv + 2) + 0)
*(*(argv + 1) + 1)
*(*argv + 5)
*(*(argv + 0) + 5)
**argv
*(*(argv + 0) + 0)
**(argv + 1)
*(*(argv + 1) + 0)
*argv
*(argv + 0)
*(argv + 1)
*(argv + 2)

## Slide 30: Process Memory Under Linux
When your program is running it has been loaded into memory and is called a process
Stack segment: Stores Local variables
  Allocated and freed at function call entry & exit
Data segment + BSS: Stores Global and static variables
  Allocated/freed when the process starts/exits
  BSS - Static variables with an implicit initial value
  Static Data - Initialized with an explicit initial value
Heap segment: Stores dynamically-allocated variables
  Allocated with a function call
  Managed by the stdio library malloc() routines
Read Only Data: Stores immutable Literals
Text: Stores your code in machine language + libraries
0xFF…FF
0x00…00
per process address space
OS kernel [protected]
Stack
Heap
BSS
Read Only Data
Read Only Text Segment
Data
x

## Slide 31: The Heap Memory Segment
Heap: "pool" of memory that is available to a program
  Managed by C runtime library and linked to your code; not managed by the OS
Heap memory is dynamically "borrowed" or "allocated" by calling a library function
When heap memory is no longer needed, it is "returned" or deallocated for reuse
Heap memory has a lifetime from allocation until it is deallocated
  Lifetime is independent of the scope it is allocated in (it is like a static variable)
If too much memory has already been allocated, the library will attempt to borrow additional memory from the OS and will fail, returning a NULL
x
OS kernel [protected]
Stack
Heap
BSS
Read Only Data
Text
Data

## Slide 32: Heap Dynamic Memory Allocation Library Functions
#include <stdlib.h> | args | Clears memory at runtime
void *malloc(…) | size_t size | no
void *calloc(…) | size_t nmemb, size_t memsize | yes
void free(...) | void *ptr | no
void * means these library functions return a pointer to generic (untyped) memory
  Be careful with void * pointers and pointer math as void * points at untyped memory
  When assigned to a typed pointer, it "converts" it from a void * to the type of the pointer variable
size_t is an unsigned integer data type, the result of a sizeof() operator
please read: % man 3 malloc
x
int *ptr = malloc(sizeof(*ptr) * 100); // allocate an array of 100 ints

## Slide 33: Use of Malloc
void *malloc(size_t size)
  Returns a pointer to a contiguous block of size bytes of uninitialized memory from the heap
    The block is aligned to an 8-byte (arm32) or 16-byte (64-bit arm/intel) boundary
    returns NULL if allocation failed (also sets errno) always CHECK for NULL RETURN!
  Blocks returned on different calls to malloc() are not necessarily adjacent
  void * is implicitly cast into any pointer type on assignment to a pointer variable
char *bufptr;
/* ALWAYS CHECK THE RETURN VALUE FROM MALLOC!!!! */
if ((bufptr = malloc(cnt * sizeof(*bufptr))) == NULL) {
fprintf(stderr, "Unable to malloc memory");
return NULL;
}
// allocates a character array with 10 elements
x
?? | ?? | ?? | ?? | ?? | ?? | ?? | ?? | ?? | ??
bufptr

## Slide 34: Calloc()
void *calloc(size_t elementCnt, size_t elementSize)
calloc() variant of malloc() but zeros out every byte of memory during program execution before returning a pointer to it (so this has a runtime cost!)
  First parameter is the number of elements you would like to allocate space for
  Second parameter is the size of each element
Originally designed to allocate arrays but works for any memory allocation
  calloc() multiplies the two parameters together for the total size
calloc() is more expensive at runtime (uses both cpu and memory bandwidth) than malloc() because it must zero out memory it allocates at runtime
Use calloc() only when you need the buffer to be zero filled prior to FIRST use
// allocate 10-element array of pointers to char, zero filled
char **arr;
arr = calloc(10, sizeof(*arr));
if (arr == NULL) // handle the error
x
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
bufptr

## Slide 35: Using and Freeing Heap Memory
void free(void *p)
  Deallocates the whole block pointed to by p to the pool of available memory
  Freed memory is used in future allocations (expect the contents to change after freed)
  Pointer p must be the same address as originally returned by one of the heap allocation routines malloc(), calloc(), realloc()
  Pointer argument to free() is not changed by the call to free()
Defensive programming: set the pointer to NULL after passing it to free()
char *bufptr;
if ((bufptr = malloc(cnt * sizeof(*bufptr))) == NULL) {
fprintf(stderr, "Unable to malloc memory");
return NULL;
}
// other code
free(bufptr); // returns memory to the heap
bufptr = NULL; // set bufptr to NULL
x

## Slide 36: Mis-Use of Free() - 1
Call free()
  With the same address that you obtained with malloc() (or other allocators)
  It is NOT an error to pass free() a pointer to NULL
Freeing unallocated memory: Only call free() to free memory address that you obtain from one of the allocators (malloc(), calloc(), etc.)
char *bytes;
if ((bytes = malloc(1024 * sizeof(*bytes)) != NULL) {
/* some code */
free(bytes + 5); // Program aborts free(): invalid pointer
x
char *ptr = "cse30";
…
/* some code */
free(ptr); // Program aborts free(): invalid pointer

## Slide 37: Mis-Use of Free() - 2
Continuing to write to memory after you free() it is likely to corrupt the heap or return changed values
  Later calls to heap routines (malloc(), calloc(), strdup()) may fail or seg fault
Double Free: Freeing allocated memory more than once will cause your program to abort (terminate)
char *bytes;
if ((bytes = malloc(1024 * sizeof(*bytes)) != NULL) {
/* some code */
free(bytes);
strcpy(bytes, "cse30"); // INVALID! used after free
……
x
char *bytes;
if ((bytes = malloc(1024 * sizeof(*bytes)) != NULL) {
/* some code */
free(bytes);
free(bytes); // Program abort double free detected….
……

## Slide 38: More Dangling Pointers: Continuing to use "freed" memory
Review: Dangling pointer points to a memory location that is no longer "valid"
Really hard to debug as the use of the return pointers may not generate a seg fault
dangling_freed_heap() may cause the allocators (malloc()and friends) to seg fault when called later to allocate memory
  Why? Because it corrupts data structures the heap code uses to manage the memory pool (it often stores meta-data in the freed memory)
char *dangling_freed_heap(void)
{
char *buff = malloc(BLKSZ * sizeof(*buff));
…
free(buff); // memory pointed at buf may be reused
return buff; // but it is returned to the caller anyway - bad
}
x

## Slide 39: strdup(): Allocate Space and Copy a String
char *strdup(char *s);
strdup is a function that has a side effect of returning a null-terminated, heap-allocated string copy of the provided text
Alternative: malloc and copy the string with strncpy();
The caller is responsible for freeing this memory when no longer needed
H | e | l | l | o | \0
str
x
char *str = strdup("Hello");
*str = 'h'; // str points at a mutable string
free(str); // caller correctly frees up space allocated by strdup()
str = NULL;

## Slide 40: Heap Memory "Leaks"
A memory leak is when you allocate memory on the heap, but never free it
Best practice: free up memory you allocated when you no longer need it
  If you keep allocating memory, you may run out of memory in the heap!
Memory leaks may cause long running programs to fault when they exhaust OS memory limits
Valgrind is a tool for finding memory leaks (not pre-installed in all linux distributions though!)
void
leaky_memory (void)
{
char *buf = malloc(BLKSZ * sizeof(*bytes));
…
/* code that never calls free() to deallocates the memory */
return; // you lose the address in buf when leaving scope
}
x

## Slide 41: Introduction to Structs – An Aggregate Data Type
Structs are a collection (or aggregation) of values grouped under a single name
  Each variable in a struct is called a member (sometimes field is used)
  Each member is identified with a name
  Each member can be (and quite often are) different types, include other structs
  Like a Java class, but no associated methods or constructors with a struct
Structure definition does not define a variable instance, nor does it allocate memory:
  It creates a new variable type uniquely identified by its tagname:
  "struct tagname" includes the keyword struct and the tagname for this type
struct tagname {
type1 member1;
...
typeN memberN;
};
Easy to forget semicolon!
x
struct vehicle {
char *state;
char *plate;
char *make;
int year;
};

## Slide 42: Creating a Node & Inserting it at the Front of the List
struct node {
int year;
char *name;
struct node *next;
};
// create node; insert at front when passed head
struct node *
creatNode(int year, char *name, struct node *link)
{
struct node *ptr = malloc(sizeof(*ptr));
if (ptr != NULL) {
if ((ptr->name = strdup(name)) == NULL) {
free(ptr);
return NULL;
}
ptr->year = year;
ptr->next = link;
}
return ptr;
}
// calling function body
struct node *head = NULL; // insert at front
struct node *ptr;
if ((ptr = creatNode(2020, "Joe", head)) != NULL) {
head = ptr; // error handling not shown
}
if ((ptr = creatNode(1955, "Sam", head)) != NULL) {
head = ptr; // error handling not shown
}
head
x
head
2020
"Joe"
NULL
head
2020
"Joe"
NULL
1955
"Sam"
Never use head here!
you can lose your linked list
if creatNode() fails!

## Slide 43: Creating a Node & Inserting it at the End of the List
// create a node and insert at the end of the list
struct node *
insertEnd(int year, char *name, struct node *head)
{
struct node *ptr = head;
struct node *prev = NULL; // base case
struct node *new;
if ((new = creatNode(year, name, NULL)) == NULL)
return NULL;
while (ptr != NULL) {
prev = ptr;
ptr = ptr->next;
}
if (prev == NULL)
return new;
prev->next = new;
return head;
}
struct node *head = NULL; // insert at end
struct node *ptr;
if ((ptr = insertEnd(2020, "Joe", head)) != NULL)
head = ptr;
if ((ptr = insertEnd(1955, "Sam", head)) != NULL)
head = ptr;
x
head
head
2020
"Joe"
NULL
head
1955
"Sam"
NULL
2020
"Joe"

## Slide 44: "Dumping" the Linked List "walk the list from head to tail"
struct node *head;
struct node *ptr;
…
printf("\nDumping All Data\n");
ptr = head;
while (ptr != NULL) {
printf("year: %d name: %s\n", ptr->year, ptr->name);
ptr = ptr->next;
}
x
Dumping All Data
year: 1955 name: Sam
year: 2020 name: Joe
ptr
ptr
ptr
head
2020
"Joe"
NULL
1955
"Sam"
struct node {
int year;
char *name;
struct node *next;
};

## Slide 45: Allocating an empty Hash Table Good use for calloc() to initialize all entries with NULL
#define TBSZ 3
int main(void)
{
struct node *ptr;
struct node **tab; // pointer to hashtable
uint32_t index;
if ((tab = calloc(TBSZ, sizeof(*tab))) == NULL) {
fprintf(stderr,"Cannot allocate hash table\n");
return EXIT_FAILURE;
}
// continued on next slide
x
TABLESIZE = 3
tab[2]
tab[1]
tab[0]
tab

## Slide 46: 32-Bit Arm - Registers
Registers are memory located within the CPU
Registers are the fastest read and write storage
Register is word size in length stores 32-bit values
  Memory is accessed using pointers in registers
In assembly language, register "addresses" are specified using predefined names starting with an r to differentiate them from main memory addresses which are labels (address)
16 registers: from r0 to r15 (encoded: 0x0 – 0xf)
x
Registers
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
1- Byte
32-bit address
External memory
0x00000000
0xFFFFFFFF
Capacity:4 GBytes
CPU
CPU Memory Bus consists of two parts:
Address bus + Data bus
arithmetic Logic Unit

## Slide 47: Using Arm-32 Registers
There are two basic groups of registers, general purpose and special use
General purpose registers can be used to contain up to 32-bits of data, but you must follow the rules for their use
  Rules specify how registers are to be used so software can communicate and share the use of registers (later slides)
Special purpose registers: have a dedicated hardware use (r15 the pc) or special use when used with certain instructions (r13 & r14)
r15/pc is the program counter that contains the address of an instruction being executed (not exactly … later)
r8
r9
r10
r4
r5
r6
r7
Preserved registers
Called functions can't change
r0
r1
r2
r3
Scratch Registers
First 4 Function Parameters
Function return value
Called functions can change
x
r15/pc
r13/sp
r14/lr
r11/fp
r12/ip
Special Use Registers
function call implementation & long branching
Special Use Registers
program counter

## Slide 48: 32-Bit Arm - Registers
Almost all arithmetic, logic operations and data movement operations involve at least one register
As a result, Register addresses are directly encoded into 4-bit fields in machine instructions (see below)
x
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
registers
Arithmetic & Logic Unit (ALU)
All computations (add, subtract, etc.) are performed in the ALU

## Slide 49: How to Access Memory?
31 | 0
Address of a location in memory | 
Consider a = b + c are operands are in memory
  Operation code: add Destination: a
  Operand 1: b Operand 2: c
Aarch32 Instructions are always word size: 32 bits wide
  Some bits must be used to specify the operation code
  Some bits must be used to specify the destination
  Some bits must be used to specify the operands
Address space is 32 bits wide so put a POINTER in a register
31 |  |  | 0 | 
Opcode
Destination
NOT ENOUGH BITS for FULL Addresses to be stored in the instruction
32 bits wide
x
Operand 1
Operand 2
0xFF…FF
0x00…00
32-bit Address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment

## Slide 50: 32-Bit Arm is a Load/Store Architecture
x
4-bytes
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
4-bit address
Capacity: 16 Words
registers
1- Byte
32-bit address
memory
0x00000000
0xFFFFFFFF
Capacity:4 GBytes
Arithmetic & Logic Unit (ALU)
All computations (add, subtract, etc.) are performed in the ALU
Instruction operands and results are only in registers
Load:
(also called a Fill)
Copy the contents of a variable from memory into a register.
Store:
(also called a Spill)
Copy the contents of a register back into a variable in memory.

## Slide 51: mov – Copies Register Content between registers
mov r1, r5 // r1 = r5
mov r1, 1 // r1 = 1
mov r1, -4 // r1 = -4
constant (immediate value)
destination register
mov
Rd
source register
mov
Rd
Rm
destination register
rot4
imm8
mov Rd, constant // Rd = constant
mov Rd, Rm // Rd = Rm
machine code bit fields
x
Immediate "addressing"
register direct "addressing"
imm8 is 8 bits in size!
IMPACT: limited range of values
(-256) <= imm8 <= 255 + values from "rotating" bits - later

## Slide 52: add/sub – Add or Subtract two integers
add r1, r2, r3 // r1 = r2 + r3
sub r1, r1, 1 // r1 = r1 – 1; or r1--
add r1, r2, 234 // r1 = r2 + 234
add Rd, Rn, constant // Rd = Rn + constant
sub Rd, Rn, constant // Rd = Rn - constant
add Rd, Rn, Rm // Rd = Rn + Rm
sub Rd, Rn, Rm // Rd = Rn - Rm
Operand 2 constant
destination
add/sub
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
add/sub
Rd
Rn
operand 1
Rm
x

## Slide 53: Line Layout in an Arm Assembly Source
Assembly language source text files are line oriented (each ending in a '\n')
Each line represents a starting address in memory and does one of:
  Specifies the contents of memory for a variable (segments containing data)
  Specifies the contents of memory for an instruction (text segment)
  Assembler directives tell the assembler to do something (for example, change label scope, define a macro, etc.) that does not allocate memory
Each line is organized into up to four columns
  Not every column is used on each line
  Not every line will result in memory being allocated
label: operation operand(s) // comments
tab
white space
white space
x
column 1 column 2 column 3 column 4

## Slide 54: Labels in Arm Assembly - 2
Remember, a Label associates a name with memory location
Regular Label:
  Used with a Function name (label) or all static variables in any of the data segments
Local Label: Name starts with .L (local label prefix) only usable in the same file
  Targets for
    branches: if switch, goto, break, continue,
    loops: for, while, do-while
  Anonymous variables (the address of literal not the address of foo in the following)
    char *foo = "literal";
x
.Lmesg: .string "Hello CSE30! We Are CountinG UpPpER cASe letters!"
main:
push {fp, lr}
.Lwhile:
add r2, r2, 1 // increment char pointer
local label
Regular label
local label
label main is the starting address of the push instruction
label .Lmesg is the starting address for the ascii string
label .Lwhile is the starting address of the add instruction

## Slide 55: Unconditional Branching – Forces Execution to Continue at a Specified Label (goto)
b .Ldone // goto .Ldone
:
.Ldone:
add r0, EXIT_SUCCESS // set return value
Unconditional Branch instruction (branch to only local labels in CSE30)
b .Llabel
Causes an unconditional branch (aka goto) to the instruction with the address .Llabel
.Llabel is called a branch target label (the "target" of a branch instruction)
Be careful! do not to branch to a function label!
.Llabel: translates into an number offset being imm24 shifted left two bits (+/- 32 MB)
b
imm24
x
imm24 is Relative direction
from the branch instruction (in +/- instructions)

## Slide 56: Anatomy of a Conditional Branch: If statement
Branch guard: determines when to execute the "condition true block" or the "condition false block"
In C, when the branch guard (condition test) evaluates non-zero you fall through to the condition true block, otherwise you branch to the condition false (else) block
Step 1: evaluate the branch guard(s) (involves one or more compares/tests)
Step 2: If branch guard evaluates to be false
  branch around the true block and execute the else block
  otherwise "fall through" and execute the true block
Block order in C is where the True Block appears above the False block
if (r0 == 5) {
/* condition block #1 */
/* branch to "here" */
} else {
/* condition block #2 */
/ * fall through to "here" */
}
// resume here
Branch condition
Test (branch guard)
r0 == 5
condition true block
condition else block

## Slide 57: cmp/cmm – Making Conditional Tests
cmp r1, 0 // r1 – 0 and sets flags on the result
cmp r1, r2 // r1 – r2 and sets flags on the result
cmp Rn, constant // Rn – constant; then sets condition flags
cmm Rn, constant // Rn + constant; then sets condition flags
cmp Rn, Rm // Rn – Rm; then sets condition flags
cmm Rn, Rm // Rn + Rm; then sets condition flags
Operand 2 constant
cmp/cmm
rot4
imm8
Rn
operand 1
Operand 2
cmp/cmm
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
The values stored in the registers Rn and Rm are not changed
The assembler will automatically substitute cmn for negative immediate values
x

## Slide 58: Conditional Tests: Implementing ARM Branch guards
Branch instruction
bsuffix .Llabel
Bits in the condition field specify the conditions when the branch happens
If the condition evaluates to be true, next instruction executed is at .Llabel:
If the condition evaluates to be false, next instruction executed is immediately after the branch
Unconditional branch is when the condition is "always"
bsuffix
imm24
cond
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
BNE | Not equal | Z = 0
BGE | Signed ≥ ("Greater than or Equal") | N = V
BLT | Signed < ("Less Than") | N ≠ V
BGT | Signed > ("Greater Than") | Z = 0 && N = V
BLE | Signed ≤ ("Less than or Equal") | Z = 1 ¦¦ N ≠ V
BMI | Minus/negative | N = 1
BPL | Plus - positive or zero (non-negative) | N = 0
B | Branch Always (unconditional) | 
x
imm24 is Relative direction
from the branch instruction
(in +/- instructions)
Use a local label with branch instructions

## Slide 59: Program Flow: Simple If statement, No Else
Realize that in ARM assembly you can only either "fall through" to the next instruction or branch to a specific instruction
Approach: adjust the conditional test then branch around the true block
Use a conditional test that specifies the inverse of the condition used in C
  This preserves C block order
C source Code | Incorrect Assembly | Correct Assembly
int r0; if (r0 > 10) { // True Block } | cmp r0, 10 bgt .Lendif // True Block .Lendif: | cmp r0, 10 ble .Lendif // True Block .Lendif:
x

## Slide 60: Branch Guard "Adjustment" Table Preserving C Block Order In Assembly
if (r0 compare 5)
/* condition true block */
/* then fall through */
}
Compare in C | "Inverse" Compare in C | Assembly using Inverse Compare
== | != | bne
!= | == | beq
> | <= | ble
>= | < | blt
< | >= | bge
<= | > | bgt
cmp r0, 5
inverse compare .Lelse
// condition true block
// then fall through
.Lendif:
x

## Slide 61: Arm Conditional Branching Simple IF no else
If statements in ARM
Step 1: make a conditional test using a cmp instruction
Step 2: if test evaluates to FALSE, branch around the condition true block with a one of the conditional branch instruction
x
cmp r0, 5
bne .Lendif
/* condition true block */
/* then fall through */
.Lendif:
/* branch around to this code */
If r0 == 5 false
then branch around the true block
int r0;
if (r0 == 5) {
/* condition true block */
/* then fall through */
}
/* branch around to this code */
If r0 == 5 true
then fall through to the true block
C If statement
ARM If statement

## Slide 62: Program Flow: If with an Else
Approach:
adjust the conditional test to branch to the False Block
Fall through to the True Block
Bottom of the True Block unconditionally branches around the False block
C source Code | Assembly
int r0; if (r0 > 10) { // true block // branch always around the false block } else { // false block } | cmp r0, 10 ble .Lelse /fall through // true block b .Lendif .Lelse: // false block // fall through .Lendif:
x

## Slide 63: Review – Short Circuit or Minimal Evaluation
In evaluation of conditional guard expressions, C uses what is called short circuit or minimal evaluation
Each expression argument is evaluated in sequence from left to right including any side effects (modified using parenthesis), before (optionally) evaluating the next expression argument
If after evaluating an argument, the value of the entire expression can be determined, then the remaining arguments are NOT evaluated (for performance)
x
if ((x == 5) || (y > 3)) // if x == 5 then y > 3 is not evaluated
if ((a != 0) && func(b)) // if a is 0, func(b) is not called
// do something

## Slide 64: Program Flow – If statements && compound tests - 1
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
bne .Lendif
cmp r1, 3
ble .Lendif
mov r2, r5 // true block
// fall through
.Lendif:
mov r4, r3
If r0 == 5 false
then short circuit branch around the true block
x

## Slide 65: Program Flow – If statements && compound tests - 2
cmp r0, 5 // test 1
bne .Lelse
cmp r1, 3 // test 2
ble .Lelse
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse:
mov r5, r2 // false block
// fall through
.Lendif:
mov r4, r3
if r0 == 5 false
then short circuit branch to the false block
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
// branch around else
} else {
r5 = r2; False block */
/* fall through */
}
r4 = r3;
x
if r1 > 3 false
then branch to the false block
test1 test2

## Slide 66: Program Flow – If statements && compound tests - 3
cmp xx,xx // test 1
inverse test branch .Lelse
cmp xx, xx // test 2
inverse test branch .Lelse
// more tests
cmp xx, xx // test n
inverse test branch .Lelse
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse:
mov r5, r2 // false block
// fall through
.Lendif:
mov r4, r3
if (test1 && test2 & … & testn) {
// true block
// branch around else
} else {
// False block
/* fall through */
}
x
All compound && tests use an inverse test and if they evaluate to true branch to the false block

## Slide 67: Program Flow – If statements || compound tests - 1
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lendif
// fall through
.Lthen:
mov r2, r5 // true block
/* fall through */
.Lendif:
mov r4, r3
If r0 == 5 true, then branch to true block
if r1 > 3 false then branch around true block
x

## Slide 68: Program Flow – If statements || compound tests - 2
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lelse
// fall through
.Lthen:
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse
mov r5, r2 // false block
// fall through
.Lendif:
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* branch around else */
} else {
r5 = r2; // false block
/* fall through */
}
x
If r0 == 5 true, then branch to the true block
if r1 > 3 false then branch to false block

## Slide 69: Program Flow – If statements || compound tests - 3
cmp XX, XX // test 1
same test branch .Lthen
cmp XX, XX // test 2
same test branch .Lthen
// other tests
cmp XX, XX // test n
inverse test branch .Lelse
// fall through
.Lthen:
// true block
// branch around else
b .Lendif
.Lelse
// false block
// fall through
.Lendif:
if (test1 || test2 || .. || testn) {
// true block
/* branch around else */
} else {
// false block
/* fall through */
}
x
All compound || tests (except the last one) use the same test as C and if they evaluate to true branches to the true block
The last (leftmost) compound || test uses an inverse test and if it evaluates to true branches to false block

## Slide 70: Program Flow – Pre-test and Post-test Loop Guards
loop guard: code that must evaluate to true before the next iteration of the loop
If the loop guard test(s) evaluate to true, the body of the loop is executed again
pre-test loop guard is at the top of the loop
  If the test evaluates to true, execution falls through to the loop body
  if the test evaluates to false, execution branches around the loop body
post-test loop guard is at the bottom of the loop
  If the test evaluates to true, execution branches to the top of the loop
  If the test evaluates to false, execution falls through the instruction following the loop
x
while (i < 10) {
/* block */
i++;
}
pre-test
loop guard
loop control variable
zero or more iterations
do {
/* block */
i++;
} while (i < 10);
post-test
loop guard
one or more iterations

## Slide 71: Pre-Test Guards - While Loop
.Lwhile:
cmp r1, 10
bge .Lendw
// block
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
/* block */
r1++;
}
r2 = r1;
x
pre-test
loop guard
loop iteration
inverted test

## Slide 72: Pre-Test Guards - While Loop
x
.Lwhile:
cmp r1, 10
bge .Lendw
cmp r2, r1
beq .Lnext
// block
.Lnext:
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
if (r2 != r1) {
/* block */
}
r1++;
}
r2 = r1;
pre-test
loop guard
loop iteration
if stmt guard

## Slide 73: Post-Test Guards – Do While Loop
.Ldo:
// block
add r1, r1, 1
cmp r1, 10
blt .Ldo
mov r2, r1
do {
/* block */
r1++;
} while (r1 < 10);
r2 = r1;
x
loop iteration
post-test
loop guard
test is not inverted

## Slide 74: Post-Test Guards – Do While Loop
.Ldo:
cmp r2, r1
beq .Lnext
// block
.Lnext
add r1, r1, 1
cmp r1, 10
blt .Ldo
move r2, r1
x
do {
if (r2 != r1) {
/* block */
}
r1++;
} while (r1 < 10);
r2 = r1;
loop iteration
post-test
loop guard

## Slide 75: Program Flow – Counting (For) Loop Version 1
mov r1, 0
.Lfor:
cmp r1, 10
bge .Lendfr
// block code
add r1, r1, 1
b .Lfor
.Lendfr:
A counting loop has three parts:
Pre-loop setup
Pre-test loop guard conditions
Post-loop update
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Post loop update
Pre loop setup
Pre-test loop guard

## Slide 76: Program Flow – Counting (For) Loop – Version 2
Alternative:
move Pre-test loop guard before the loop
Add post-test loop guard
  converts to do while
  removes an unconditional branch
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
mov r1, 0
cmp r1, 10
bge .Lendfr
.Ldo:
// block code
add r1, r1, 1
cmp r1, 10
blt .Ldo
.Lendfr:
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Pre-loop setup
Post loop update
Pre-test loop guard
Post-test loop guard

## Slide 77: Nested loops
Nest loop blocks as you would in C or Java
for (r3 = 0; r3 < 10; r3++) {
r0 = 0;
do {
r0 = r0 + r1++;
} while (r1 < 10);
// fall through
r2 = r2 + r1;
}
r5 = r0;
x
mov r3, 0
.Lfor:
cmp r3, 10 // loop guard
bge .Lendfor
mov r0, 0
.Ldo:
add r0, r0, r1
add r1, r1, 1
cmp r1, 10 // loop guard
blt .Ldo
// fall through
add r2, r2, r1
add r3, r3, 1 // loop iteration
b .Lfor
.Lendfor:
mov r5, r0

## Slide 78: What is a Bitwise Operation?
Bitwise operators are applied independently to each of the corresponding bit positions in each variable
Each bit position of the result depends only on bits in the same bit position within the operands
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0
x

## Slide 79: Bitwise (Bit to Bit) Operators in C
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
output = a | b;
| with 1 to set a bit to 1
| with 0 to let a bit through
a | ~a
0 | 1
1 | 0
output = ~a;
a | b | a ^ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
output = a ^ b; //EOR
^ with 1 will flip the bit
^ with 0 to let a bit through
a | b | a & b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
output = a & b;
& with 1 to let a bit through
& with 0 to set a bit to 0
0110
& 1100
----
0100
Bitwise
AND
0110
| 1100
----
1110
Bitwise
OR
0110
^ 1100
----
1010
Bitwise
EOR
~ 1100
----
0011
Bitwise
NOT
x

## Slide 80: Bitwise Not (vs Boolean Not)
a | ~a
0 | 1
1 | 0
in C
int output = ~a;
x
Boolean operators act on the entire value not the individual bits
Meaning | Operator | Operator | Meaning
Boolean NOT | !b | ~b | Bitwise NOT
 | Bitwise Not
number | 0101 1010 0101 1010 1111 0000 1001 0110
~number | 1010 0101 1010 0101 0000 1111 0110 1001
Type | Operation | result
bitwise | ~0x01 | 1111 1111 1111 1111 1111 1111 1111 1110
Boolean | !0x01 | 0000 0000 0000 0000 0000 0000 0000 0000
~ 1100
----
0011
Bitwise NOT

## Slide 81: MVN (not)
A bitwise NOT operation
mvn r0, r1
// Copies all 32 bits
// of the value held
// in register r1 into
// the register r0
// then does a bitwise NOT
register r0
register r1
mvn r0, 12
// Expands an imm8 value 0x0c
// stored in the instruction
// into a register then does
// a bitwise NOT
0xffff fff3
0x0c
x
~ 1100
----
0011
Bitwise NOT
register r0
0xfffffff3
0x 0c
imm8 expansion
0x0000000c
bitwise not

## Slide 82: mvn – Copies NOT (~)
constant (immediate value)
destination register
mvn
Rd
source register
mvn
Rd
Rm
destination register
bitwise NOT operation. Immediate (constant) version copies to 32-bit register, then does a bitwise NOT
mvn r1, 4 // x = ~4
mvn r1, r5 // x = ~y in C
mvn r1, 0 // x = -1
imm8 | extended imm8 | inverted imm8 | signed base 10
0x00 | 0x00 00 00 00 | 0xff ff ff ff | -1
0xff | 0x00 00 00 ff | 0xff ff ff 00 | -256
0xfffffffb
r1
0x4
invert the bits
0x00000004
copy into 32 bits zero extend
0xaaaaaaaa
0x55555555
r5
r1
rot4
imm8
~ 1100
----
0011
Bitwise NOT
x
mvn Rd, constant // Rd = constant
mvn Rd, Rm // Rd = Rm
0x0
0xffffffff
r1

## Slide 83: Bitwise Instructions
<op> Rd, Rn, constant // Rd = Rn <op> constant
<op> Rd, Rn, Rm // Rd = Rn <op> Rm
Operand 2 constant
destination
<op>
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
<op>
Rd
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
Bitwise <op> description | C Syntax | Arm <op> Syntax Op2: either register or constant value | Operation
Bitwise AND | a & b | and Rd, Rn, Op2 | Rd = Rn & Op2
Bitwise OR | a ¦ b | orr Rd, Rn, Op2 | Rd = Rn ¦ Op2
Exclusive OR | a ^ b | eor Rd, Rn, Op2 | Rd = Rn ^ Op2
Bitwise NOT | a = ~b | mvn Rd, Rn | Rd = ~Rn
x

## Slide 84: Bitwise versus C Boolean Operators
Boolean operators act on the entire value not the individual bits
bitwise & versus Boolean &&
0x10 & 0x01 = 0x00 (bitwise)
0x10 && 0x01 = 0x01 (Boolean)
bitwise ~ versus Boolean !
~0x01 = 0xfffffffe (bitwise)
!0x01 = 0x0 (Boolean)
!0xff = 0x0 (Boolean)
Meaning | Operator |  | Operator | Meaning
Boolean AND | a && b |  | a & b | Bitwise AND
Boolean OR | a ¦¦ b |  | a ¦ b | Bitwise OR
Boolean NOT | !b |  | ~b | Bitwise NOT
x
Boolean Operators
Bitwise Operators

## Slide 85: The act (operation) of Masking
Bit masks access/modify specific bits in memory
Masking act of applying a mask to a value with a specific op:
orr: 0 passes bit unchanged, 1 sets bit to 1 (a = b | c; // in C)
eor: 0 passes bit unchanged, 1 inverts the bit (a = b ^ c; // in C)
and: 0 clears the bit, 1 passes bit unchanged (a = b & c; // in C)
x
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
 | <op> | <op> | <op> | <op> | <op> | <op> | <op> | <op>
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0

## Slide 86: Mask on
force bits to 1 "mask on" operation
  1 to set a bit to 1
  0 to let a bit through unchanged
orr r1, r2, r3
r1 = r2 | r3; // in C
x
Example: force lower 16 bits to 1
DATA: r2 0xab ab ab 77
orr
MASK: r3 0x00 00 ff ff
RSLT: r1 0xab ab ff ff
forces to a 1
unchanged
Example: force lower 8 bits to 1
DATA: r2 0xab ab ab 77
orr r1 r2, 0xff
r1 = r2 | 0xff; // in C
RSLT: r1 0xab ab ab ff

## Slide 87: Mask off
x
force bits to 0 "mask off" operation
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
r1 = r2 & r3; // in C
Example: force lower 8 bits to 0
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff ff ff 00
RSLT: r1 0xab ab ab 00
forces to a 0
unchanged
Example: force lower 8 bits to 0
DATA: r2 0xab ab ab 77
and r1 r2, 0xffffff00
r1 = r2 & 0xffffff00; // in C
RSLT: r1 0xab ab ab 00

## Slide 88: Extracting (Isolate) a Field of Bits with a mask
x
extract top 8 bits of r2 into r1
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, r3
DATA: r2 0xab ab ab 77
and
MASK: r3 0xff 00 00 00
RSLT: r1 0xab 00 00 00
forces to a 0
unchanged
extract top 8 bits of r2 into r1
DATA: r2 0xab ab ab 77
and r1, r2, 0xff000000
RSLT: r1 0xab 00 00 00
r1 = r2 & 0xff000000; // in C

## Slide 89: Finding if a bit is set
x
query the status of a bit "bit status" operation
  0 to set a bit to 0 ("clears the bit")
  1 to let a bit through unchanged
and r1, r2, 0x02
cmp r1, 0
beq .Lendif
// code for is set
.Lendif:
Example is bit 1 set
DATA: r2 0xab ab ab 77
and
MASK: 0x00 00 00 02 is bit 1 set?
RSLT: r1 0x00 00 00 02 != 0 if set
forces to a 0
unchanged
  unsigned int r1, r2;
  // code
  r1 = r2 & 0x02
  if (r1 != 0) {
  // code for is set
  }
  unsigned int r2;
  // code
  if ((r2 & 0x02) != 0) {
  // code for is set
  }

## Slide 90: Even/Odd
Even or odd, check LSB (same as mod %2)
check LSB (bit 0) if set then odd, else even
and r1, r2, 0x01
cmp r1, 0x01
bne .Lendif
// code for handling odd numbers
.Lendif:
x
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 01 (mod 2 even or odd)
RSLT: r1 0x00 00 00 01 (odd)
forces to a 0
unchanged
  unsigned int r2;
  // code
  if ((r2 & 0x01) != 0) {
  // code for handling odd numbers
  }

## Slide 91: MOD %<power of 2>
remainder (mod): num % d where num ≥ 0 and d = 2k
mask = 2k -1 so for mod 16, mask = 16 -1 = 15
and r1, r2, r3
x
Example: %2
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 01 (mod 2 even or odd)
RSLT: r1 0x00 00 00 01 (odd)
forces to a 0
unchanged
Example: Mod 16
DATA: r2 0xab ab ab 77
and
MASK: r3 0x00 00 00 0f (mod 16)
RSLT: r1 0x00 00 00 07
forces to a 0
unchanged

## Slide 92: Flipping bits: bit toggle Used in PA7/PA8
x
invert (flip) bits "bit toggle" operation
  1 will flip the bit
  0 to let a bit through
eor r1, r2, r3
Observation: When applied twice, it returns the original value (symmetric encoding)
With a mask of all 1's is a 1's compliment
Example: invert (flip) the lower 8-bits
DATA: r2 0xab ab ab 77
eor
MASK: r3 0x00 00 00 ff
RSLT: r1 0xab ab ab 88
inverts (flips)
unchanged
88: 1000 1000
DATA: r1 0xab ab ab 88
eor
MASK: r3 0x00 00 00 ff apply a 2nd time
RSLT: r1 0xab ab ab 77 original value!
inverts (flips)
77: 0111 0111
Example: flip the lower 8-bits
eor r1, r2, 0xff
unsigned int r1, r2;
r1 = r2 ^ 0xff;

## Slide 93: Unsigned Integers (positive numbers) with Fixed # of Bits
4 bits is = ONLY 16 distinct values
Modular (C operator: %) or clock math
  Numbers start at 0 and “wrap around” after 15 and go back to 0
Keep adding 1
wraps (clockwise)
  0000 -> 0001 … -> 1111 -> 0000
Keep subtracting 1
wraps (counter-clockwise)
  1111 -> 1110 … -> 0000 -> 1111
Addition and subtraction use normal "carry" and "borrow" rules, just operate in binary
x

## Slide 94: Problem: How to Encode Both Positive and Negative Integers
How do we represent the negative numbers within a fixed number of bits?
  Allocate some bit patterns to negative and others to positive numbers (and zero)
distinct bit patterns to encode positive and negative values
Unsigned values: 0 ... –1
Signed values: … –1 (dividing the range in ~ half including 0)
On a number line (below): 8-bit integers – signed and unsigned (e.g., char in C)
-
+
-1
Same “width” (same number of encodings), just shifted in value
-1
Unsigned
Signed
x
-1 comes from counting 0 as a "positive" number

## Slide 95: Two’s Complement: The MSB Has a Negative Weight
4-bit (w = 4) weight = = -23 = -8
  10102 unsigned: 1x23 + 0x22 + 1x21 + 0x20 = 10
  10102 two’s complement: -1x23 + 0x22 + 1x21 + 0x20 = -8 + 2 = –6
  -8 in two’s complement: 10002 = -23 + 0 = -8
  -1 in two’s complement: 11112 = -23 + (23 – 1) = -8 + 7 = -1
weight is ), all other bits: have positive weights )
. . .
b0
bn-1
bn-2
x

## Slide 96: 2's Complement Signed Integer Method
Positive numbers encoded same as unsigned numbers
All negative values have a one in the leftmost bit
All positive values have a zero in the leftmost bit
  This implies that 0 is a positive value
Only one zero
For n bits, Number range is) to - 1)
  Negative values “go 1 further” than the positive values
Example: the range for 8 bits: -128, -127, .. 0, .. 126, +127
Example the range for 32 bits: -2147483648 .. 0, .. +2147483647
Arithmetic is the same as with unsigned binary!
x

## Slide 97: Sign Extension (how type promotion works)
Sometimes you need to work with integers encoded with different number of bits
8 bits (char) -> (16 bits) short -> (32 bits) int
Sign extension increases the number of bits: -bit wide signed integer , EXPANDS to a wider n + -bit signed integer where both have the same value
Unsigned
Just add leading zeroes to the left side
Two’s Complement Signed:
If positive, add leading zeroes on the left
  Observe: Positive stay positive
If negative, add leading ones on the left
  Observe: Negative stays negative
• • •
• • •
• • •
• • •
n
original
copies of MSB
x

## Slide 98: Example: Two’s Complement Sign or bit Extension - 1
Adding 0's in front of a positive numbers does not change its value
7 = 0111
extend to
8 bits
00000111
Number is still 7
x
1 = 0001
extend to
8 bits
00000001
Number is still 1

## Slide 99: Example: Two’s Complement Sign or bit Extension -2
Adding 1's if front of a negative number does not change its value
7 = 0111
invert = 1000
add 1 + 1
-7 1001
7 = 00000111
invert = 11111000
add 1 + 1
-7 11111001
-7 = 1001
extend to
8 bits
11111001
x
1001 = -8 + 1 = -7
11111001 =
(-128 + 64 + 32 + 16 + 8) + 1 = -8 + 1 = -7

## Slide 100: Different Type of Numbers each have a Fixed # of Bits Spanning one or more contiguous bytes of memory
x
C Data Type | AArch-32 contiguous Bytes
char (arm unsigned) | 1
short int | 2
unsigned short int | 2
int | 4
unsigned int | 4
long int | 4
long long int | 8
float | 4
double | 8
long double | 8
pointer * | 4
0
31
00000000
00000001
00000010
00000011
Word 32-bit integer uses 4 bytes
0
7
15
00000000
000000001
Half Word 16-bit integer uses 2 bytes
0
7
00000000
Byte 8-bit integer uses 1 byte
most significant bit (largest power of 2)
least significant bit (smallest power of 2)
most significant byte
least significant byte

## Slide 101: Byte Ordering of Numbers In Memory: Endianness
Two different ways to place multi-byte integers in a byte addressable memory
Big-endian: Most Significant Byte (“big end”) starts at the lowest (starting) address
Little-endian: Least Significant Byte (“little end”) starts at the lowest (starting) address
Example: 32-bit integer with 4-byte data
a1
b2
c3
d4
0x100
0x101
0x102
0x103
01
23
a1
b2
c3
d4
01
23
d4
c3
b2
a1
Big-Endian
Little-Endian
MSB
Most significant byte
LSB
Least significant byte
x
0x100
0x101
0x102
0x103

## Slide 102: Byte Ordering Example
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
int x = 12345;
// or x = 0x00003039; // show all 32 bits
39
30
00
00
IA32, ARM32 (little-endian)
30
39
00
00
(big-endian)
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
x

## Slide 103: Byte Addressable Memory Shown as 32-bit words
Observation
32-bit aligned addresses
rightmost 2 bits of the address are always 0
0x12345680
0x12345682
0x12345681
0x12345683
0x00
0x01
0x02
0x03
1 32-bit
(4 byte) word
0x12345684
0x12345686
0x12345687
0x12345685
0x04
0x05
0x06
0x07
1 byte Memory Content
One byte per row
Byte
Memory
Address
1 32-bit
(4 byte) word
Word Aligned address
Word Aligned address
x
0x04
0x05
0x06
0x07
0x00
0x01
0x02
0x03
LSByte
MSByte
0x12345680
0x12345681
0x12345682
0x12345683
Contents of Memory
One 32-bit (4 byte) word per row
0x12345680
0x12345684
Byte address
0x12345688
0x1234568c
Word
Memory
Address

## Slide 104: Bit Shifting ARM and C Equivalents
Instruction | ARM | C | Diagram
Logical Shift Left 0 fills on right 0 <= n <= 32 bits | lsl Rd, Rm, n lsl Rd, Rm, Rs | int x; or unsigned int x x << n; | 
Logical Shift Right 0 fills on left 0 <= n <= 32 bits | lsr Rd, Rm, n lsr Rd, Rm, Rs | unsigned int x; x >> n; | 
Arithmetic Shift Right Sign extends on left 0 <= n <= 32 bits | asr Rd, Rm, n asr Rd, Rm, Rs | int x; x >> n; | 
Rotate Right 0 <= n <= 32 bits | ror Rd, Rm, n ror Rd, Rm, Rs | ror n in a 32-bit registers unsigned int x; x = (x >> n) ¦ (x << (32 - n)); | 
x
operand 2 constant
destination
<inst>
Rd
const5
Rm
operand 1
Number of bit to shift or rotate: const 5 bits
operand 2
destination
<inst>
Rd
Rm
operand 1
Rs
Number of bit to shift or rotate: Rs

## Slide 105: Shift Operations in C
n is number of bits to shift a variable x of width w bits
Shifts by n < 0 or n ≥ w are undefined
Left shift (x << N) – Multiplies by
  Shift N bits left, Fill with 0s on right
In C: behavior of >> is determined by compiler
  gcc: it depends on data type of x (signed/unsigned)
Right shift (x >> N) - Divides by
  Logical shift (for unsigned variables)
    Shift N bits right, Fill with 0s on left
  Arithmetic shift (for signed variables) – Sign Extension
    Shift N bits right while Replicating the most significant bit on left
    Maintains sign of x
In Java: logical shift is >>> and arithmetic shift is >>
Left Shift
Right logical Shift
Right Arithmetic Shift
x

## Slide 106: Logical Shift & Rotate Operations
lsr r2, r0, 8
r0 0xab ab ab 77
r2 0x00 ab ab ab
lsl r2, r0, 8
r0 0xab ab ab 77
r2 0xab ab 77 00
ror r2, r0, 8
r0 0xab ab ab 77
r2 0x77 ab ab ab
x

## Slide 107: Extracting/Isolating Unsigned Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsr r1, r1, 24
r1 = r1 >> 24;
unsigned zero-extension (all 0’s)
Extracted bit-field
r1
byte 0
byte 1
byte 3
byte 2
lsl r1, r0, 8
unsigned int r0,r1;
r1 = r0 << 8;
Next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
pushed bits to far right
Hint: Useful for PA7

## Slide 108: Extracting Signed Bitfields
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
next shift left = 8
r0
byte 0
byte 1
byte 3
byte 2
Move byte 2 in r0 to byte 0 in r1
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
lsl r1, r0, 8
int r0,r1;
r1 = r0 << 8;
next shift right = 24
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far left
asr r1, r1, 24
r1 = r1 >> 24;
signed extend (all 1’s)
Extracted
bit-field
r1
byte 0
byte 1
byte 3
byte 2
pushed bits to far right

## Slide 109: Inserting Bitfields – Inserting Source Field into Destination Field
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
r1
r0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Task: Insert source into destination
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
results in
orr r1, r1, r2
r1 = r1 | r2;
r1
r2
Approach
(1) isolate source field
(2) clear destination field
(3) Bitwise or together
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 110: Inserting Bitfields – Isolating the Source Field
r2
r0
x
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
isolate source field
lsl r2, r0, 24
lsr r2, r2, 8
r2 = r0 << 24;
r2 = r2 >> 8;
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r0
r2

## Slide 111: Inserting Bitfields – Clearing the Destination Field
x
lsl r1, r1, 8
r1 = r1 << 8;
r1
r3
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
r1
r1
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
clear the destination field
ror r1, r1, 24
r1=(r1>>24)|(r1<<8);
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ror r1, r1, 16
r1= (r1>>16)|(r1<<16);

## Slide 112: Inserting Bitfields – Combining Isolated Source and Cleared Destination
x
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
inserted field
orr r1, r1, r2
r1 = r1 | r2;
r1
r2
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
isolated source
r1
r1
field cleared in destination

## Slide 113: Assembly Source File to Executable to Linux Memory
Local variables and function call overhead
code you write in the text segment
allocates space dynamically during execution by c runtime library code (text)
x
OS kernel [protected]
Stack
Heap
Static Data
Shared Libraries
Read Only Data
Read Only Text Segment
`
.bss
uninitialized static variables
.data
initialized static variables
.section .rodata
read-only literals
.text
assembly code
BSS
Sections in an Assembly Source file
File Header
Specify Hardware assembler generate the correct ARM version
file footer
.section .note.GNU-stack,…
.end
Text
Symbol table
Data
a.out executable
created by the assembler &
link editor
Header - Description

## Slide 114: Creating Segments, Definitions In Assembly Source
The following assembler directives indicate the start of a memory segment specification
  Remains in effect until the next segment directive is seen
x
.bss
    // start uninitialized static segment variables definitions
  // does not consume any space in the executable file
.data
// start initialized static segment variables definitions
.section .rodata
// start read-only data segment variables definitions
.text
// start read-only text segment (code)

## Slide 115: Assembly Source File Template
assembly programs end in .S
  That is a capital .S
  example: test.S
Always use gcc to assemble
  _start() and C runtime
File has a complete program
  gcc file.S
File has a partial program
  gcc –c file.S
Link files together
  gcc file.o cprog.o
// File Header
.arch armv6 // armv6 architecture instructions
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
// BSS Segment (only when you have uninitialized globals)
.bss
// Data Segment (only when you have initialized globals)
.data
// Read-Only Data (only when you have literals)
.section .rodata
// Text Segment – your code
.text
// Function Header .type main, %function // define main to be a function
.global main // export function name
main:
// function prologue // stack frame setup
// your code for this function here
// function epilogue //stack frame teardown
// function footer
.size main, (. – main)
// File Footer
.section .note.GNU-stack,"",%progbits // stack/data non-exec
.end
x

## Slide 116: ARM Assembly Source File: Header and Footer
.syntax unified
  use the standard ARM assembly language syntax called Unified Assembler Language (UAL)
.section .note.GNU-stack,"",%progbits
  tells the linker to make the stack and all data segments not-executable (no instructions in those sections) – security measure
.end
  at the end of the source file, everything written after the .end is ignored
.arch armv6 // armv6 architecture
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
File Header
At the top of every ARM source file
.section .note.GNU-stack,"",%progbits // set stack/data non-exec
.end
// everything past the .end is ignored!
// Debugging notes etc
File Footer
At the bottom of every ARM source file
// Contents of the other memory segment include .text (your code)
x

## Slide 117: Assembler Directives: .equ and .equiv
.equ <symbol>, <expression>
  Defines and sets the value of a symbol to the evaluation of the expression
  Used for specifying constants, like a #define in C
  You can (re)set a symbol many times in the file, last one seen applies
  .equ BLKSZ, 10240 // buffer size in bytes
  // other lines
  .equ BLKSZ, 1024 // buffer size in bytes
.equ BLKSZ, 10240 // buffer size in bytes
.equ BUFCNT, 100*4 // buffer for 100 ints
.equ BLKSZ, STRSZ * 4 // redefine BLKSZ from here
x

## Slide 118: Example: Assembler Directive and Instructions
10 .equ NULL, 0
11 main:
12 3000 0310A0E1 mov r1, r3
13 .Lloop:
14 3004 043083E2 add r3, r3, 4
15 3008 001093E5 ldr r1, [r3]
16 300c 000051E3 cmp r1, NULL
17 3010 FBFFFF1A bne .Lloop
Instruction Memory Addresses (lowest 2-bits are always are 00)
Notice alignment and how addresses increase by 4 (32-bit instructions)
Regular label main
is associated with memory location 0x3000
Local label .Lloop
is associated with memory location 0x3004
assembler directive .equ does not allocate any memory (NULL = 0)
Memory Contents
Warning contents shown in "reverse" byte order: Lsb – Msb
output generated with
gcc -c -Wa,-ahlns space.S
partial output is shown
space.S
x

## Slide 119: Function Header and Footer Assembler Directives
.global function_name
  Exports the function name to other files. Required for main function, optional for others
.type name, %function
  The .type directive sets the type of a symbol/label name
  %function specifies that name is a function (name is the address of the first instruction)
equ FP_OFF, 4
  Used for basic stack frame setup; the number 4 will change – later slides
.size name, bytes
  The .size directive is used to set the size associated with a symbol
  Used by the linker to exclude unneeded code and/or data when creating an executable file
  It is also used by the debugger gdb
  bytes is best calculated as an expression: (period is the current address in a memory segment)
  .size name, (. – name)
.text
.global myfunc // make myfunc global for linking
.type myfunc, %function // define myfunc to be a function
.equ FP_OFF, 4 // fp offset in main stack frame
myfunc:
// function prologue, stack frame setup
    // your code
// function epilogue, stack frame teardown
.size myfunc, (. – myfunc)
function entry point
address of the first instruction in the function
Must not be a local label (does not start with .L)
Function Header
Function Footer
x

## Slide 120: Function Template
.text // start of the text segment
.global myfunc // make myfunc global for linking
.type myfunc, %function // define myfunc to be a function
.equ FP_OFF, 4 // fp offset in main stack frame
myfunc:
push {fp, lr} // push (save) fp and lr on stack
add fp, sp, FP_OFF // set fp for this function
    // your code
sub sp, fp, FP_OFF
pop {fp, lr} // pop (retore) fp and lr from stack
bx lr // return to caller
.size myfunc, (. – myfunc)
Function Prologue
creates stack frame
Function Epilogue
removes stack frame
x
Function header
Function footer
myfunc label is the address of the first instruction in myfunc (the push below)

## Slide 121: Preview: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
r0, r1 = function(r0, r1, r2, r3) // 64-bit return – long long
Each parameter and return value is limited to data that can fit in 4 bytes or less
You receive up to the first four parameters in these four registers
You copy up to the first four parameters into these four registers before calling a function
For parameter values using more than 4 bytes, a pointer to the parameter is passed (we will cover this later)
You MUST ALWAYS assume that the called function will alter the contents of all four registers: r0-r3
  In terms of C runtime support, these registers contain the copies given to the called function
  C allows the copies to be changed in any way by the called function
Register | Function Call Use
r0 | 1st parameter
r1 | 2nd parameter
r2 | 3rd parameter
r3 | 4th parameter
Register | Function Return Value Use
r0 | 8, 16 or 32-bit result, 32-bit address or least-significant half of a 64-bit result
r1 | most-significant half of a 64-bit result
x

## Slide 122: Assembler Directives: Label Scope Control (Normal Labels only)
.extern <label>
  Imports label (function name, symbol or a static variable name);
  An address associated with the label from another file can be used by code in this file
.global <label>
  Exports label (or symbol) to be visible outside the source file boundary (other assembly or c source)
  label is either a function name or a global variable name
  Only use with function names or static variables
Without .global, labels are usually local to the file from the point where they are defined
.extern printf
.extern fgets
.extern strcpy
.global fbuf
x

## Slide 123: Preview: Writing an ARM32 function
#include <stdlib.h>
#include <stdio.h>
#include "sum4.h"
int main()
{
int reslt;
reslt = sum4(1,2,3,4);
printf("%d\n", reslt);
return EXIT_SUCCESS;
}
#ifndef SUM4_H
#define SUM4_H
#ifndef __ASSEMBLER__
int sum4(int, int, int, int);
#else
.extern sum4
#endif
#endif
#include "sum4.h"
.arch armv6
.arm
.fpu vfp
.syntax unified
.global sum4
.type sum4, %function
.equ FP_OFF, 28
// r0 = sum4(r0, r1, r2, r3)
sum4:
push {r4-r9, fp, lr}
add fp, sp, FP_OFF
add r0, r0, r1
add r0, r0, r2
add r0, r0, r3
sub sp, fp, FP_OFF
pop {r4-r9, fp, lr}
bx lr
.size sum4, (. - sum4)
.section .note.GNU-stack,"",%progbits
.end
$ gcc -Wall -Wextra -c main.c
$ gcc -c sum4.S
$ gcc sum4.o main.o
$ ./a.out
10
We will cover this
when we do stack frames
We will cover this
when we do stack frames

## Slide 124: Load/Store: Register Base Addressing
32-bit memory
register r0
register r1 (address)
ldr r0, [r1]
Copies a 32-bit word
from the memory location
whose address is contained
in r1 (r1 is a pointer)
into register r0
r1 is being used as a pointer to a location in memory
ldr requires the use of a pointer operand
str r0, [r1]
Copies all 32 bits of the value held in register r0 to the 32-bit memory location contained in register r1 (r1 pointer)
32-bit memory
register r0
register r1 (address)
r1 is being used as a pointer to a location in memory
str requires the use of a pointer operand
x

## Slide 125: Example Base Register Addressing Load – Modify – Store
x = x + 1;
ldr r0, [r1] // r0 = *r1 (read x)
add r0, r0, 1 // r0 = r0 + 1 (x++)
str r0, [r1] // *r1 = r0 write x
Memory assigned to x
register r0
register r1 (address)
+ 1
0b..0000100
Notice: word aligned!
(last two bits are 0's)
..00000000
..00000001
n-bit Memory
Address
binary
..00000010
..00000011
..00000100
..00000101
..00000110
..00000111
01010101
10101010
01010101
10101010
01010101
10101010
01010101
10101010
1 byte
contents
X starting address
x
x = x + 1
Where x is in memory
r1 is a pointer

## Slide 126: Load/Store: Register Base Addressing + Immediate
32-bit memory
register r0
register r1 (address)
ldr r0, [r1, 4]
Copies a 32-bit word
from the memory location
whose address is contained
in r1 +4 (r1 is a pointer)
into register r0
str r0, [r1, 4]
Copies all 32 bits of the value held in register r0 to the 32-bit memory location contained in register r1+4 (r1 pointer)
32-bit memory
register r0
register r1 (address)
x
4
Immediate value in instruction
Immediate value in instruction
4

## Slide 127: LDR/STR – Base Register + Immediate Offset Addressing
Register Base Addressing:
  Pointer Address: Rn; source/destination data: Rd
  Unsigned pointer address in stored in the base register
Register Base + immediate offset Addressing:
  Pointer Address = register content + immediate offset -4095 <= imm12 <= 4095 (bytes)
  Unsigned offset integer immediate value (bytes) is added or subtracted (U bit above says to add or subtract) from the pointer address in the base register
  Often used to address struct members
    Address of struct is address of the first member and subsequent members are a fixed offset from the first based on their size of the preceding members
unsigned immediate offset
Rd – source/dest register
ldr/str
Rd
imm12
Rn
Rn – base register contains address (pointer)
U
+/- offset
x

## Slide 128: ldr/str Register Base + Immediate Offset Addressing
Syntax | Address | Examples
ldr/str Rd, [Rn, +/- constant] constant is in bytes ldr/str Rd, [Rn] | Rn + or – constant same | ldr r0, [r5,100] str r1, [r5, 0] str r1, [r5]
ldr/str
Rd
imm12
Rn
U
+ -
0 subtract
1 add
Memory Address
Instruction
Source for str
Destination for ldr
x
Add or subtract 12 bit binary
-4095 to +4095

## Slide 129: Loading and Storing: Variations List
Load and store have variations that move 8-bits, 16-bits and 32-bits
Load into a register with less than 32-bits will set the upper bits not filled from memory differently depending on which variation of the load instruction is used
Store will only select the lower 8-bit, lower 16-bits or all 32-bits of the register to copy to memory, register contents are not altered
Instruction | Meaning | Sign Extension | Memory Address Requirement
ldrsb | load signed byte | sign extension | none (any byte)
ldrb | load unsigned byte | zero fill (extension) | none (any byte)
ldrsh | load signed halfword | sign extension | halfword (2-byte aligned)
ldrh | load unsigned halfword | zero fill (extension) | halfword (2-byte aligned)
ldr | load word | --- | word (4-byte aligned)
strb | store low byte (bits 0-7) | --- | none (any byte)
strh | store halfword (bits 0-15) | --- | halfword (2-byte aligned)
str | store word (bits 0-31) | --- | word (4-byte aligned)
x

## Slide 130: Loading 32-bit Registers From Memory, 32-bit
x
ldr r1, [r0]
load unsigned byte
0x04
0x03
0x02
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
Memory
address

## Slide 131: Loading 32-bit Registers From Memory, 16-bit
x
ldrh r1, [r0]
load unsigned halfword
0x00
0x00
0x02
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x0201
positive number
Memory
address
0x00
0x00

## Slide 132: Loading 32-bit Registers From Memory, 16-bit
x
ldrsh r1, [r0]
load signed halfword
0x00
0x00
0x02
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x0201
positive number
Memory
address
0x00
0x00
0x02 = 0b00000010
No Sign extend

## Slide 133: Loading 32-bit Registers From Memory, 16-bit Signed
x
ldrsh r1, [r0]
load signed halfword
0xff
0xff
0x82
0x01
memory address
r1
0x04
0x03
0x82
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x8201
negative number
Sign extend
0x82 = 0b10000010
0xff
0xff

## Slide 134: Loading 32-bit Registers From Memory, 16-bit Unsigned
x
ldrh r1, [r0]
load unsigned halfword
0x00
0x00
0x82
0x01
memory address
r1
0x04
0x03
0x82
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x8201
positive number
0b10000010
0x00
0x00

## Slide 135: Loading 32-bit Registers From Memory, 8-bit
x
ldrb r1, [r0]
load unsigned byte
0x00
0x00
0x00
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x01
positive number
0x00
0x00
0x00

## Slide 136: Loading 32-bit Registers From Memory, 8-bit
x
ldrsb r1, [r0]
load signed byte
0x00
0x00
0x00
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x01
positive number
0x00
0x00
0x00
No Sign extend
0b00000001

## Slide 137: Loading 32-bit Registers From Memory, 8-bit Signed
x
ldrsb r1, [r0]
load signed byte
0xff
0xff
0xff
0x81
memory address
r1
0x04
0x03
0x02
0x81
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x81
negative number
Sign extend
0b10000001
0xff
0xff
0xff

## Slide 138: Loading 32-bit Registers From Memory, 8-bit Signed
x
ldrb r1, [r0]
load unsigned byte
0x00
0x00
0x00
0x81
memory address
r1
0x04
0x03
0x02
0x81
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x81
positive number
0x00
0x00
0x00

## Slide 139: Storing 32-bit Registers To Memory, 32-bit
x
str r1, [r0]
0x04
0x03
0x02
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0

## Slide 140: Storing 32-bit Registers To Memory, 16-bit
x
strh r1, [r0]
0x04
0x03
0x02
0x01
memory address
r1
0x??
0x??
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0

## Slide 141: Storing 32-bit Registers To Memory, 8-bit
x
strb r1, [r0]
0x04
0x03
0x02
0x01
memory address
r1
0x??
0x??
0x??
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0

## Slide 142: Storing 32-bit Registers To Memory, 8-bit – Storing different byte
x
strb r1, [r0]
0x00
0x04
0x03
0x02
memory address
r1
0x??
0x??
0x??
0x02
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x04
0x03
0x02
0x01
r2
lsr r1, r2, 8
0x00
We want store this byte to memory location 0x1000
you could also do a ror

## Slide 143: ldr/str practice - 1
r1 contains the Address of X (defined as int X) in memory; r1 points at X
r2 contains the Address of Y (defined as int *Y) in memory; r2 points at Y
write Y = &X;
str r1, [r2] // y  &x
address of y
0x0100c
r1
r2
X contents
x
??
Y contents
??
0x01008
0x0100c // this is y
0x01004 // this is x
0x01000
address of x
0x01004
??
0x01010
0x01004

## Slide 144: ldr/str practice - 2
r1 contains the Address of X (defined as int *X) in memory r1 points at X
r2 contains the Address of Y (defined as int Y) in memory; r2 points at Y
write Y = *X;
ldr r3, [r1] // r3  x (read 1)
ldr r0, [r3] // r0  *x (read 2)
str r0, [r2] // y  *x
x
address of y
0x0100c
r1
r2
X = 0x01010
??
Y contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
55
0x01010
55
?
r3
0x01010
r0
?
55

## Slide 145: using ldr/str: array copy
#include <stdio.h>
#include <stdlib.h>
#define SZ 6
void icpy(int *, int *, int);
int main(void)
{
int src[SZ] = {1, 2, 3, 4, 5, 6};
int dst[SZ];
icpy(src, dst, SZ);
for (int i = 0; i < SZ; i++)
printf("%d\n", *(dst + i));
return EXIT_SUCCESS;
}
x
void icpy(int *src, int *dst, int cnt)
{
int *end = src + cnt;
if (cnt <= 0)
return;
do {
*dst++ = *src++;
} while (src < end);
return;
}

## Slide 146: Base Register version
cmp r2, 0
ble .Ldone
lsl r2, r2, 2 //convert cnt to int size
add r3, r0, r2 // loop term pointer
.Ldo:
ldr r4, [r0] // load from src
str r4, [r1] // store to dest
add r0, r0, 4 // src++
add r1, r1, 4 // dst++
cmp r0, r3 // src < term pointer?
blt .Ldo
.Ldone:
.arch armv6
.arm
.fpu vfp
.syntax unified
.text
.global icpy
.type icpy, %function
.equ FP_OFF, 12
// r0 contains int *src
// r1 contains int *dst
// r2 contains int cnt
// r3 use as loop term pointer
// r4 use as temp
icpy:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
// see right ->
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size icpy, (. - icpy)
.end
x
loop guard
pre loop guard

## Slide 147: Load/Store: Register Base Addressing + Register Offset
32-bit memory
register r0
register r1 (address)
ldr r0, [r1, r4]
Copies a 32-bit word
from the memory location
whose address is contained
in r1 + r4 (r1 is a pointer) into register r0
str r0, [r1, r4]
Copies all 32 bits of the value held in register r0 to the 32-bit memory location contained in register r1+r4 (r1 pointer)
32-bit memory
register r0
register r1 (address)
x
R4 offset
R4 offset

## Slide 148: ldr/str Base Register + Register Offset Addressing
Syntax | Address | Examples
ldr/str Rd, [Rn +/- Rm ] | Rn + or – Rm | ldr r0, [r5, r4] str r1, [r5, r4]
ldr/str
Rd
Rn
U
+ -
0 -Rm
1 +Rm
Memory Address
Instruction
Source for str
Destination for ldr
Rm
x
Pointer Address = Base Register + Register Offset
  Unsigned offset integer in a register (bytes) is either added/subtracted from the pointer address in the base register

## Slide 149: ldr/str practice - 3
r1 contains Address of X (defined as int *X) in memory; r1 points at X
r2 contains Address of Y (defined as int Y[2]) in memory; r2 points at &(Y[0])
write *X = Y[1];
ldr r0, [r2, 4] // r0  y[1]
ldr r3, [r1] // r3  x
str r0, [r3] // *x  y[1]
x
address of y
0x0100c
r1
r2
X = 0x01000
??
Y[0] contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
Y[1] contents
0x01010
Y[1] contents
?
r3
r0
?
0x01000
Y[1] contents
+4

## Slide 150: ldr/str practice - 4
r1 contains Address of X (defined as int X[2]) in memory; r1 points at &(x[0])
r2 contains Address of Y (defined as int Y) in memory; r2 points at Y
r3 contains a 4
write Y = X[1];
ldr r0, [r1, r3] // r0  x[1]
str r0, [r2] // y  x[1]
x
address of y
0x0100c
r1
r2
??
x[0] contents
Y contents
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
x[1] contents
0x01010
x[1] contents
4
r3
r0
?
x[1] contents
+4

## Slide 151: Base Register + Register Offset Version
cmp r2, 0
ble .Ldone
lsl r2, r2, 2 //convert cnt to int size
mov r3, 0 // initialize counter
.Ldo:
ldr r4, [r0, r3] // load from src
str r4, [r1, r3] // store to dest
add r3, r3, 4 // counter++
cmp r3, r2 // count < r3
blt .Ldo
.Ldone:
.arch armv6
.arm
.fpu vfp
.syntax unified
.text
.global icpy
.type icpy, %function
.equ FP_OFF, 12
// r0 contains int *src
// r1 contains int *dst
// r2 contains int cnt
// r3 use as loop counter
// r4 use as temp
icpy:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
// see right ->
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size icpy, (. - cpy)
.end
x
loop guard
pre loop guard
one increment covers both arrays

## Slide 152: Base Register + Register Offset With chars
#include <stdio.h>
#include <stdlib.h>
#define SZ 6
void cpy(char *, char *, int);
int main(void)
{
char src[SZ] =
{'a', 'b', 'c', 'd', 'e', '\0'};
char dst[SZ];
cpy(src, dst, SZ);
printf("%s\n", dst);
return EXIT_SUCCESS;
}
x
cmp r2, 0
ble .Ldone
mov r3, 0 // initialize counter
.Ldo:
ldrb r4, [r0, r3] // load from src
strb r4, [r1, r3] // store to dest
add r3, r3, 1 // counter++
cmp r3, r2 // count < r3
blt .Ldo
.Ldone:

## Slide 153: Reference: Addressing Mode Summary for use in CSE30
index Type | Example | Description
Pre-index immediate | ldr r1, [r0] | r1  memory[r0] r0 is unchanged
Pre-index immediate | ldr r1, [r0, 4] | r1  memory[r0 + 4] r0 is unchanged
Pre-index immediate | str r1, [r0] | memory[r0]  r1 r0 is unchanged
Pre-index immediate | str r1, [r0, 4] | memory[r0 + 4]  r1 r0 is unchanged
Pre-index register | ldr r1, [r0, +-r2] | r1  memory[r0 +- r2] r0 is unchanged
Pre-index register | str r1, [r0, +-r2] | memory[r0 +- r2]  r1 r0 is unchanged
x

## Slide 154: Base Register Addressing + Offset register
int count(char *ptr, int len)
{
int cnt = 0;
int i;
for (i = 0; i < len; i++) {
if ((ptr[i] >= 'A') && (ptr[i] <= 'Z'))
cnt++;
}
return cnt;
}
#include <stdio.h>
#include <stdlib.h>
int count(char *, int);
int main(void)
{
char msg[] ="Hello CSE30! We Are CountinG UpPER cASe letters!";
printf("%d\n", count(msg, sizeof(msg)/sizeof(*msg)));
return EXIT_SUCCESS;
}
x

## Slide 155: Base Register + Offset register
count:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
mov r2, 0
cmp r1, 0
ble .Ldone
mov r3, 0
.Lfor:
cmp r3, r1
bge .Ldone
ldrb r4, [r0, r3]
cmp r4, 'A'
blt .Lendif
cmp r4, 'Z'
bgt .Lendif
add r2, r2, 1
.Lendif:
add r3, r3, 1
b .Lfor
.Ldone:
mov r0, r2
.arch armv6
.arm
.fpu vfp
.syntax unified
.text
.global count
.type count, %function
.equ FP_OFF, 12
// r0 contains char *ptr
// r1 contains int len
// r2 contains int cnt
// r3 contains int i
// r4 contains char
count:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
// see right ->
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size count, (. - count)
.end
x
loop guard
byte array
Also use ldrb here
offsets are 0,1,2,…

## Slide 156: What is the conceptual difference between .bss and .data?
All static variables that do not specify an initial value default to an initial value of 0 and are placed in .bss segment
To save file system space in the executable file (the a.out file) the assembler collapses these .bss variables to a location and size "table"
.data segment variables use the same space in the executable file as they have in memory
.section .rodata is handled the same as .data
Read Only Text Segment
BSS
Text
Symbol table
a.out executable
Header - Description
Static Data
Read Only Data
// these are .bss variables
int buf1[4096];
int buf2[4096];
// these are .data variables
int table[] = {1,2};
char string[] ="CSE30!!";
'\0'
'0'
'3'
'E'
'S'
'C'
Data
'!'
'!'
1
2
buf2 address size
buf1 address size
executable file
just big enough for address, size
same size as specified
Static Data
same size as a.out
buf2
BSS
expanded size
buf1
low main memory

## Slide 157: Variable Alignment In .data, .bss and .section .rodata
Use .align directive to force the assembler to align the address of the next variable defined after the .align
1
2 bytes
4 bytes
integer
short
char
x
4
bytes
1
Byte
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x0C
0x0D
0x0E
0x0F
Aligned Address
Hex
2
Bytes
0x00
0x02
0x04
0x06
0x08
0x0A
0x0C
0x0E
any address
addresses that end in 0b0
addresses that end in 0b00
0x00
0x04
0x08
0x0C
Aligned Address
Hex
Aligned Address
Hex
SIZE Alignment Requirements | Starting Address must end in | Align Directive
8-bit char -1 byte | 0b..0 or 0b..1 | 
16-bit int -2 bytes | 0b..0 | .align 1
32-bit int -4 bytes pointers, all arrays | 0b..00 | .align 2
.align 1
.align 2
no .align

## Slide 158: Defining Static Variables: Allocation and Initialization
Variable SIZE | Directive | .align | C static variable Definition | Assembler static variable Definition
8-bit char (1 byte) | .byte |  | char chx = 'A' char string[] = {'A','B','C', 0}; | chx: .byte 'A' string: .byte 'A','B',0x42,0
16-bit int (2 bytes) | .short | .align 1 | short length = 0x55aa; | length: .short 0x55aa
32-bit int (4 bytes) | .word .long | .align 2 | int dist = 5; int *distptr = &dist; unsigned int mask = 0xaa55; int array[] = {12,~0x1,0xCD,-1}; | dist: .word 5 distptr: .word dist mask: .word 0xaa55 array: .word 12,~0x1,0xCD,-3
string with '\0' | .string |  | char class[] = "cse30"; | class: .string "cse30"
x
Rule: Place the .align above the variable
.align 1
len: .short 0x55aa
Rule: use .align 2 before every array regardless of type
Rule: place variables with explicit initialized values in a .data segment
Rule: place variables with no explicit initiali value (default to 0) in .bss segment
Rule: place string literals in .section .rodata and use a local label (.Llabel:)

## Slide 159: Loading Static variables into a register
.text
// function header
main:
// load the address, then contents
// using r2
ldr r2, =x // int *r2 = &x
ldr r2, [r2] // r2 = *r2;
// &x was only needed once above
// Note: r2 was a pointer then an int
// no "type" checking in assembly!
// store the contents of r2
ldr r1, =y // int *r1 = &y
str r2, [r1] // *r1 = r2
x
.data
x: .word 200
load a static memory variable
  load the pointer to the memory
  read (load) from *pointer
Tell the assembler load the address (Lvalue) of a label into a register:
  ldr Rd, =Label // Rd = address
Tell the assembler load the contents into a register
ldr R0, [Rd] // Rd = address
Example to the right: y = x;
.bss
y: .space 4
store to a static memory variable
  load the pointer to the memory
  write (store) to *pointer

## Slide 160: Stack Segment: Support of Functions
The stack consists of a series of "stack frames" or "activation frames", one is created each time a function is called at runtime
Each frame represents a function that is currently being executed and has not yet completed (why activation frame)
A function’s stack "frame" goes away when the function returns
Specifically, a new stack frame is
  allocated (pushed on the stack) for each function call (contents are not implicitly zeroed)
  deallocated (popped from the stack) on function return
Stack frame contains:
  Local variables, parameters of function called
  Where to return to which caller when the function completes (the return address)
0xFF…FF
0x00…00
32-bit Address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment

## Slide 161: Stack types
A Stack Implements a last-in first-out (LIFO) protocol
Each time a function is called, a stack frame is activated
  space is allocated by moving the stack pointer
  push adds space, pop removes space
Stack growth direction
  Ascending stack: grows from low memory towards high memory (adding to the sp to allocate memory)
  Descending stack: grows from high memory towards low memory (subtracting from the sp to allocate memory)
Full versus empty stacks
  Empty stack: stack pointer (sp) points at the next word address after the last item pushed on the stack
  Full stack: stack pointer (sp) points at the last item pushed on the stack
ARM on Linux uses a full descending stack
Descending stack high memory
low memory
Ascending stack high memory
low memory
stack pointer
Empty descending stack high memory
low memory
stack pointer
Full descending stack high memory
low memory
x

## Slide 162: Ghost of Stack Frames Past…..
void ghost(int n)
{
int x;
int y;
printf("before ghost: %d %d\n", x, y);
x = 10*n;
y = 100*n;
printf("after ghost: %d %d\n", x, y);
return;
}
void wraith (void)
{
int a;
int b;
printf("wraith: %d %d\n", a, b);
return;
}
int main(void)
{
ghost(3);
wraith();
return EXIT_SUCCESS;
}
% ./a.out
before ghost: 0 66328
after ghost: 30 300
wraith: 30 300
%
See how wraith has the old values left over from the prior call to ghost
same stack frame variable layout
x

## Slide 163: Function Calls
Branch with Link (function call) instruction
bl label
Function call to the instruction with the address label (no local labels for functions)
  imm24 number of instructions from pc+8 (24-bits)
  label any function label in the current ﬁle, any function label that is deﬁned as .global in any ﬁle that it is linked to, any C function that is not static
Branch with Link Indirect (function call) instruction
blx Rm
Function call to the instruction whose address is stored in Rm (Rm is a function pointer)
bl and blx both save the address of the instruction immediately following the bl or blx instruction in register lr (link register is also known as r14)
The contents of the link register is the return address in the calling function
bl
imm24
x
main:
●
bl f1 f1:
● ●
(1) Branch to the instruction with the label f1
(2) copies the address of the instruction AFTER the bl in lr
blx
Rm

## Slide 164: Function Call Return
Branch & exchange (function return) instruction
bx lr // we will always use lr
Causes a branch to the instruction whose address is stored in register <lr>
  It copies lr to the PC
This is often used to implement a return from a function call (exactly like a C return) when the function is called using either bl label, or blx Rm
bx
Rn
main:
●
●
bl f1 f1: ●
● ●
● bx lr
●
Branch to the instruction whose address is stored in lr
x
Stores this address in lr
this is the address to resume at in the caller

## Slide 165: Understanding bl and bx - 1
int a(void)
{
return 0;
}
int main(void)
{
a();
a();
// not shown
x
But there is a problem we must address here – next slide
a:
103f4: mov r0, 0
103f8: bx lr
main:
103fc: bl 103f4 //a
10400: bl 103f4 //a
10404: mov r0, 0
lr:
10400
lr:
10404
lr:
10400
lr:
10404
Address in memory

## Slide 166: Understanding bl and bx - 2
int b(void)
{
return 0;
}
int a(void)
{
b();
return 0;
}
int main(void)
{
a();
a();
// not shown
x
b:
103f4: mov r0, 0
103f8: bx lr
a:
103fc: bl 103f4 <b>
10400: mov r0, 0
10404: bx lr
main:
10408: bl 103fc <a>
1040c: bl 103fc <a>
10410: mov r0, 0
lr:
1040c
lr:
10400
lr:
10400
lr:
10400
Uh No
Infinite loop!!!
Modifies the link register (lr), writing over main's return address Cannot return to main()
We need to preserve the lr!

## Slide 167: Understanding bl and blx - 3
int a(void)
{
return 0;
}
int (*func)() = a;
int main(void)
{
(*func)();
// not shown
.data
func:.word a // func initialized with address of a()
.text
.global a
.type a, %function
.equ FP_OFF, 4
a:
mov r0, 0
bx lr
.size a, (. - a)
.global main
.type main, %function
.equ FP_OFF, 4
main:
ldr r4, =func // load address of func in r4
ldr r4, [r4] // load contents of func in r4
blx r4 // we lose the lr for main!
// not shown
bx lr // infinite loop!
But this has the same infinite loop problem when main() returns!
x

## Slide 168: Preserving and Restoring Registers on the stack - 1
high memory
low memory
before
stack pointer
push{ }
after
stack pointer
pop{ }
after stack pointer
before stack
pointer
high memory
low memory
x
registers
registers
registers
registers
registers
registers
push (multiple register str to memory operation)
push (multiple register ldr from memory operation)
Operation | Pseudo Instruction |  | Operation
Push registers Function Entry | push | {reg list} | sp = sp – 4 × #registers Copy registers to mem[sp]
Pop registers Function Exit | pop | {reg list} | Copy mem[sp] to registers, sp = sp + 4 × #registers

## Slide 169: Preserving and Restoring Registers on the Stack - 2
{reg list} is a list of registers in numerically increasing order, left to right
push {r4-r10, fp, lr} // fp is r11, lr is r14
Registers cannot be:
  duplicated in the list
  listed out of increasing numeric order (left to right)
Register ranges can be specified {r4, r5, r8-r10, fp, lr}
Never! push/pop r12, r13, or r15
  the top two registers on the stack must always be fp, lr // ARM function spec – later slides
Operation | Pseudo Instruction |  | Operation
Push registers Function Entry | push | {reg list} | sp = sp – 4 × #registers Copy registers to mem[sp]
Pop registers Function Exit | pop | {reg list} | Copy mem[sp] to registers, sp = sp + 4 × #registers
x

## Slide 170: push: Multiple Register Save to the stack
push copies the contents of the {reg list} to stack segment memory
push subtracts (# of registers saved) * (4 bytes) from the sp to allocate space on the stack
  sp = sp – (# registers_saved * 4)
this must always be true: sp % 8 == 0
saved lr
saved fp
saved r8
saved r6
saved r4
saved r5
save registers
push {r4-r6, r8, fp, lr}
r8
r4
r5
lr
fp
r6
CPU registers to Save
copy
Registers are pushed on to the stack in order
right (high memory) to left (low memory)
If you have no stack variables (later slides) then always push an EVEN number of registers!
sp after push
allocated space
(# registers) * (4 bytes)
stack segment low memory
stack segment high memory
x
sp before push

## Slide 171: pop: Multiple Register Restore from the stack
pop copies the contents of stack segment memory to the {reg list}
pop adds: (# of registers restored) * (4 bytes) to sp to deallocate space on the stack
  sp = sp + (# registers restored * 4)
Remember: {reg list} must be the same in both the push and the corresponding pop
stack segment high memory
r8
r4
r5
saved lr
saved fp
saved r8
saved r6
saved r4
saved r5
lr
fp
r6
stack segment low memory
CPU registers
copy
Restored register contents
Registers are pop’d from the stack in order
left (low memory) to right (high memory)
restore registers
pop {r4-r6, r8, fp, lr}
sp after pop
deallocated space
(# registers) * (4 bytes)
x
sp before pop

## Slide 172: Registers: Rules For Use
Register | Function Call Use | Function Body Use | Save before use Restore before return
r0 | arg1 and return value | scratch registers | No
r1-r3 | arg2 to arg4 | scratch registers | No
r4-r10 | preserved registers | contents preserved across function calls | Yes
r11 / fp | stack frame pointer | Use to locate variables on the stack | Yes
r12 / ip | may used by assembler with large text file | can be used as a scratch if really needed | No
r13 / sp | stack pointer | stack space allocation | Yes
r14 / lr | link register | contains return address for function calls | Yes
r15 | Do not use | Do not use | No
x

## Slide 173: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
Each parameter and return value is limited to data that can fit in 4 bytes or less
Calling function:
  copy up to the first four parameters into these four registers before calling a function
  MUST assume that the called function will alter the contents of all four registers: r0-r3
  In terms of C runtime support, these registers contain the copies given to the called function
  C allows the copies to be changed in any way by the called function
Called function:
  you receive the first four parameters in these four registers (r0 – r3)
x
Register | Function Call Use | Function Body Use | Save before use Restore before return
r0 | arg1 and return value | scratch registers | No
r1-r3 | arg2 to arg4 | scratch registers | No

## Slide 174: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
For parameters, whose size is larger than 4 bytes, pass a pointer to the parameter (we will cover this later)
One arg value per register! – NO arrays across multiple registers
  chars, shorts and ints are directly stored
  Structs (not always), and arrays (always) are passed via a pointer
  Pointers passed as output parameters contain an address that points at the stack, BSS, data, or heap
x
Register | Function Call Use | Function Body Use | Save before use Restore before return
r0 | arg1 and return value | scratch registers | No
r1-r3 | arg2 to arg4 | scratch registers | No

## Slide 175: What it means to be a Temporary/argument register
  // main()
  // code not shown
  mov r0, 0
  mov r1, 1
  mov r2, 2
  mov r3, 3
  bl a
  // r0 = return value
  // r1-r3 values are unknown as a() has right to change them as it wants
int a(void)
{
// not shown
}
int main(void)
{
int r0 = 0;
int r1 = 1;
int r2 = 2;
int r3 = 3;
r0 = a();
// in C r1 and r3 would have the same values
// after the call

## Slide 176: Preserved Registers
Any value you have in a preserved register before a function call will still be there after the function returns (Contents are “preserved” across function calls)
If the function wants to use a preserved register it must:
  Save the value contained in the register at function entry
  Use the register in the body of the function
  Restore the original saved value to the register at function exit (before returning to the caller)
You use a preserved register when a function makes calls another function and you have:
  Local variables allocated to be in registers
  Parameters passed to you (in r0-r3) that you need to continue to use after calling another function
x
Register | Function Call Use | Function Body Use | Save before use Restore before return
r4-r10 | preserved registers | contents preserved across function calls | Yes
r11/fp | stack frame pointer | Use to locate variables on the stack | Yes
r13/sp | stack pointer | stack space allocation | Yes
r14/lr | link register | contains return address for function calls | Yes

## Slide 177: Minimum Stack Frame (Arm Arch32 Procedure Call Standards)
Minimal frame: allocating at function entry: push {fp, lr}
sp always points at top element in the stack (lowest byte address)
fp always points at the bottom element in the stack
  Bottom element is always the saved lr (contains the return address of caller)
  A saved copy of callers fp is always the next element below the lr
  fp will be used later when referencing stack variables
Minimal frame: deallocating at function exit: pop {fp, lr}
On function entry: sp must be 8-byte aligned (sp % 8 == 0)
x
low address
saved lr
callers fp
sp
fp
Minimum stack frame

## Slide 178: By following the saved fp, you can find each stack frame
How gdb finds stack frames
sp
fp
saved lr
callers fp
main()
lr to funcA()
funcA() fp
funcB()
lr to main()
main() fp
funcA()
sp
fp
x
Local Vars and outgoing args
saved lr
callers fp
main()
Local Vars and outgoing args
Local Vars and outgoing args

## Slide 179: Minimum Stack Frame (Arm Arch32 Procedure Call Standards)
main() calls funcA()
Function entry (Function Prologue):
  save lr and fp registers (push)
  set fp to top entry in stack
  allocate space for local vars – later slides
Function return (Function Epilogue):
  deallocate space for locals -later
  restores lr and fp registers (pop)
  Return To Caller
x
allocate stack space
SP = SP – "space"
grows "down"
lr to main()
main() fp
sp
fp
saved lr
callers fp
funcA()
main()
deallocate stack space
SP = SP + "space"
shrinks "up"
saved lr
callers fp
sp
fp
main()

## Slide 180: Function Prologue: Allocating the Stack Frame -1
callers fp
low memory
lr to caller
at function entry
x
fp
Function was just called this how the stack looks
The orange blocks are part of the caller's stack frame
Callers
Stack Frame
callers fp
low memory
lr to caller
sp
saved lr
callers fp
saved r5
saved r4
after
push {r4,r5,fp,lr}
sp
fp
using a push, save lr, fp and those preserved registers it wants to use on the stack
Called function
Stack Frame
Callers
Stack Frame
Prologue Step 1 of 3
callers fp
low memory
lr to caller
sp
saved lr
callers fp
saved r5
saved r4
Set FP
add fp, sp, FP_OFF
fp
move the fp to point at the saved lr as required by the Aarch32 spec
FP_OFF
Called function
Stack Frame
Callers
Stack Frame
Prologue Step 2 of 3
myfunc:
push {fp, lr} // push (save) fp and lr on stack
add fp, sp, FP_OFF // set fp for this function
add sp, sp, -FRMADD // allocate FRMADD bytes for local vars
    // by moving sp
Function Prologue

## Slide 181: Function Prologue: Allocating the Stack Frame - 2
callers fp
low memory
lr to caller
sp
Local Variables
Allocate Space for locals
add sp, sp, -FRMADD
saved lr
callers fp
saved r5
saved r4
FRMADD
x
Allocate Space for Local Variables
fp
FP_OFF
Space for local variables is allocated on the stack right below the lowest pushed register
Add memory to the stack frame for local variables by moving the sp towards low memory
The amount moved is the total size of all local variables in bytes plus memory alignment padding
FRMADD = total local var space (bytes) + padding
Allocate the space after the register push by
  add sp, sp, -FRMADD
fp (frame pointer) is used as a pointer (base register) to access all stack variables – later slides
Called function
Stack Frame
Callers
Stack Frame
Prologue Step 3 of 3
myfunc:
push {fp, lr} // push (save) fp and lr on stack
add fp, sp, FP_OFF // set fp for this function
add sp, sp, -FRMADD // allocate FRMADD bytes for local vars
    // by moving sp
Function Prologue

## Slide 182: Function Epilogue: Deallocating the Stack Frame - 1
callers fp
low memory
lr to caller
sp
Local Variables
Stack frame while during function body execution
saved lr
callers fp
saved r5
saved r4
FRMADD
fp
FP_OFF
Use fp as a pointer to find local variables on the stack
x
Stack Frame
callers fp
low memory
lr to caller
sp
Local Variables
Deallocate Space for locals
Put SP back so pop works
sub sp, fp, FP_OFF
saved lr
callers fp
saved r5
saved r4
Deallocated
stack space
Move SP back to where it was after the push in the prologue.
So, pop works properly (this also deallocates the local variables)
fp
FP_OFF
Stack Frame
Step 1
sub sp, fp, FP_OFF // deallocate local variables by moving sp
pop {fp, lr} // pop (restore) fp and lr from stack
bx lr // return to caller
function Epilogue

## Slide 183: Why You must move SP before POP in the Epilogue
callers fp
low memory
lr to caller
sp
Local Variables
Allocate Space for locals
add sp, sp, -FRMADD
saved lr
callers fp
saved r5
saved r4
FRMADD
fp
FP_OFF
callers fp
low memory
lr to caller
sp
saved lr
callers fp
saved r5
saved r4
after
push {r4,r5,fp,lr}
fp
callers fp
low memory
lr to caller
sp
Local Variables
If you do not move sp back!
You get a total mess
pop {r4, r5, fp, lr)
saved lr
callers fp
saved r5
saved r4
FRMADD
fp
FP_OFF
lr
fp
r5
r4
CPU registers
sub sp, fp, FP_OFF // deallocate local variables by moving sp
pop {fp, lr} // pop (restore) fp and lr from stack
bx lr // return to caller
function Epilogue
x

## Slide 184: Function Epilogue: Deallocating the Stack Frame
callers fp
low memory
lr to caller
sp
Local Variables
At function exit after
pop {r4,r5,fp,lr}
saved lr
callers fp
saved r5
saved r4
Deallocated
Eligible for reuse
out of scope
Use pop to restore the registers to the values they had at function entry
fp
x
Stack Frame
callers fp
low memory
lr to caller
sp
Local Variables
Deallocate Space for locals
Put SP back so pop works
sub sp, fp, FP_OFF
saved lr
callers fp
saved r5
saved r4
Deallocated
stack space
Move SP back to where it was after the push in the prologue.
So, pop works properly (this also deallocates the local variables)
fp
FP_OFF
Stack Frame
Step 1
Step 2
sub sp, fp, FP_OFF // deallocate local variables by moving sp
pop {fp, lr} // pop (restore) fp and lr from stack
bx lr // return to caller
function Epilogue

## Slide 185: How to Set FP
FP_OFF = (#regs saved - 1) * 4
low memory
4-byte words
sp
lr to caller
callers fp
saved r5
saved r4
after push {r4-r7,fp,lr}
add fp, sp, FP_OFF
fp = sp + 20 bytes
saved r7
saved r6
// other code etc .equ FP_OFF, 20
main:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF …….
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
# regs saved | FP_OFF in Bytes Distance from lr to lowest saved register
2 | 4
3 | 8
4 | 12
5 | 16
6 | 20
7 | 24
8 | 28
9 | 32
Function Prologue
always at top of function saves regs and sets fp
Function Epilogue
always at bottom of function restores regs including the sp
Function Stack Frame
FP_OFF:
Distance from lr to lowest saved register
Means Caution, odd number of saved regs!
If odd number pushed, make sure frame is 8-byte aligned (later)
this must always be true: sp % 8 == 0
x
grows down

## Slide 186: Reference Table: Global Variable access
.data
x: .data y //x = &y
.bss // from libc
stderr:.space 4 // FILE *
var | global variable address into r0 (lside) | global variable contents into r0 (rside) | contents of r0 into global variable
x | ldr r0, =x | ldr r0, =x ldr r0, [r0] | ldr r1, =x str r0, [r1]
*x | ldr r0, =x ldr r0, [r0] | ldr r0, =x ldr r0, [r0] ldr r0, [r0] | ldr r1, =x ldr r1, [r1] str r0, [r1]
**x | ldr r0, =x ldr r0, [r0] ldr r0, [r0] | ldr r0, =x ldr r0, [r0] ldr r0, [r0] ldr r0, [r0] | ldr r1, =x ldr r1, [r1] ldr r1, [r1] str r0, [r1]
stderr | ldr r0, =stderr | ldr r0, =stderr ldr r0, [r0] | <do not write unless you really know what you are doing>
.Lstr | ldr r0, =.Lstr | ldr r0, =.Lstr ldrb r0, [r0] | <read only>
.section .rodata
.Lstr: .string "HI\n"
stdin, stdout and stderr are global variables
x

## Slide 187: Passing global variables as a parameter: fprintf()
r0 = function(r0, r1, r2, r3)
fprintf(stderr, "arg2", arg3, arg4)
create a literal string for arg2 which tells fprintf() how to interpret the remaining arguments
stdin, stdout, stderr are all global variable and are part of libc
  these names are their lside (label names)
  get their contents and pass that to fprintf(), fread(), fwrite()
.extern fprintf //declare fprintf
.section .rodata // note the dots "."
.Lfst: .string "c=%d\n"
// part of the text segment below
mov r2, 2 // int a = 2;
mov r3, 3 // int b = 3;
add r2, r2, r3 // arg 3: int c = a + b;
ldr r0, =stderr // get stderr address
ldr r0, [r0] // arg 1: get stderr contents
ldr r1, =.Lfst // arg 2: =literal address
bl fprintf
#include <stdio.h>
#include <stdlib.h>
int
main(void)
{
int a = 2;
int b = 3;
int c;
c = a + b;
fprintf(stderr,"c=%d\n", c);
return EXIT_SUCCESS;
}
three passed args in this use of fprintf
x
We are going to put these variables in temporary registers
r0, r1, r2

## Slide 188: Putchar/getchar: The while loop
mov r4, 0 //count
bl getchar
cmp r0, EOF
beq .Ldone
.Lloop:
bl putchar
bl getchar
add r4, r4, 1
cmp r0, EOF
bne .Lloop
.Ldone:
mov r1, r4 //arg2
ldr r0, =.Lst //arg1
bl printf
#include <stdio.h>
#include <stdlib.h>
int
main(void)
{
int c;
int count = 0;
while ((c = getchar()) != EOF) {
putchar(c);
count++;
}
printf("Echo count: %d\n", count);
return EXIT_SUCCESS;
}
pre loop test with a call to getchar()
if it returns EOF in r0 we are done
File header and footers are not shown
echo the character read with getchar and then read another and increment count
initialize count
did getchar() return EOF if not loop
saw EOF, print count
x
address of string literal variable
.Lst: .string "Echo count: %d\n"

## Slide 189: Accessing Pointers (argv) in ARM assembly
.extern printf
.extern stderr
.section .rodata
.Lstr: .string "argv[%d] = %s\n"
.text
.global main // main(r0=argc, r1=argv)
.type main, %function
.equ FP_OFF, 20
main:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF
mov r7, r1 // save argv!
ldr r4, =stderr // get the address of stderr
ldr r4, [r4] // get the contents of stderr
ldr r5, =.Lstr // get the address of .Lstr
mov r6, 0 // set indx = 0;
// see next slide
.Ldone:
mov r0, 0
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
argc
**argv
Registers
argv[0]
./cipher
in/book
-b
-e
r7
r6
r5
r4
r3
r2
r1
r0
% ./cipher -e -b in/BOOK
argv[0] = ./cipher
argv[1] = -e
argv[2] = -b
argv[3] = in/BOOK
file * stderr
indx
"argv[%d] = %s\n"
fprintf(stderr, "argv[%d] = %s\n", indx, *argv);
argv[1]
argv[2]
argv[3]
NULL
need to save r1 as we are calling a function - fprintf
r0-r3 lost due to fprintf call
x

## Slide 190: Accessing Pointers (argv) in ARM assembly
.Lloop:
// fprintf(stderr, "argv[%d] = %s\n", indx, *argv)
ldr r3, [r7] // arg 4: *argv
cmp r3, 0 // check *argv == NULL
beq .Ldone // if so done
mov r2, r6 // arg 3: indx
mov r1, r5 // arg 2: "argv[%d] = %s\n"
mov r0, r4 // arg 1: stderr
bl fprintf
add r6, r6, 1 // indx++ for printing
add r7, r7, 4 // argv++ pointer
b .Lloop
.Ldone:
argc
**argv
Registers
argv[0]
./cipher
in/book
-b
-e
r7
r6
r5
r4
r3
r2
r1
r0
% ./cipher -e -b in/BOOK
argv[0] = ./cipher
argv[1] = -e
argv[2] = -b
argv[3] = in/BOOK
file * stderr
indx
"argv[%d] = %s\n"
argv[1]
argv[2]
argv[3]
NULL
observe the different increment sizes
r0-r3 lost due to fprintf call
x

## Slide 191: Allocating Space For Locals on the Stack
Space for local variables is allocated on the stack right below the lowest pushed register
  Move the sp towards low memory by the total size of all local variables in bytes plus padding
FRMADD = total local var space (bytes) + padding
Allocate the space after the register push by
  add sp, sp, -FRMADD
Requirement: on function entry, sp is always 8-byte aligned
  sp % 8 == 0
Padding (as required):
  Additional space between variables on the stack to meet memory alignment requirements
  Additional space so the frame size is evenly divisible by 8
fp (frame pointer) is used as a pointer (base register) to access all stack variables – later slides
sp
lr to caller
callers fp
fp
local
variables
sp = sp - local space
FP_OFF
x
saved register
saved register
FRMADD=
Local Space (bytes)
Total size % 8 == 0
grows down

## Slide 192: Local Variables on the stack
Add space on the stack for each local
  we will allocate space in same order the locals are listed the C function shown from high to low stack address
  gcc compiler allocates from low to high stack addresses
  Order does not matter for our use
int main(void)
{
int c;
int count = 0;
// rest of code
}
lr to caller
callers fp
saved r5
saved r4
after push {r4-r5,fp,lr}
add fp, sp, FP_OFF
fp
FRMADD = 8
count
sp after push
c
sp after
allocating locals
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 8
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
In this example we are allocating two variables on the stack
When writing assembly functions, in many situations you may choose allocate these to registers instead
x
// when FRMADD values fail to assemble
ldr r3, =-FRMADD
add sp, sp, r3

## Slide 193: Accessing Stack Variables: Introduction
To Access data stored in the stack
  use the ldr/str instructions
Use register fp with offset (distance in bytes) addressing (use either register offset or immediate offset)
No matter what address the stack frame is at, fp always points at saved lr, so you can find a local stack variable by using an offset address from the contents of fp
x
Variable | distance from fp | Read variable | Write Variable
int c | -16 | ldr r0, [fp, -16] | str r0, [fp, -16]
int count | -20 | ldr r0, [fp, -20] | str r0, [fp, -20]
low memory 4-byte words
lr to caller
callers fp
saved r5
saved r4
fp
count
c
sp
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 8
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
4
4
fp - 16
fp - 20
int main(void)
{
int c;
int count = 0;
// rest of code
}
Total frame size
24 bytes
8-byte aligned
FRMADD
FP_OFF
12
4

## Slide 194: Stack Frame Design – Local Variables
When writing an ARM equivalent for a C program, for CSE30 we will not re-arrange the order of the variables to optimize space (covered in the compiler course)
Arrays start at a 4-byte boundary (even arrays with only 1 element)
  Exception: double arrays [ ] start at an 8-byte boundary
  struct arrays are aligned to the requirements of largest member
Single chars (and shorts) can be grouped together in same 4-byte word (following the alignment for the short)
Padding may be required (see next slide)
x
A
B
C
D
E
0
pointer
int
a[0]
a[1]
1
2 bytes
pointers and integers
short
char
4 bytes
4
Rule: When the function is entered the stack is already 8-byte aligned
4
4
4
4

## Slide 195: Stack Variables: Padding
Variable padding – start arrays at 4-byte boundary and leave unused space at end (high side address) before the variable higher on the stack
Frame padding – add space below the last local variable to keep 8-byte alignment
x
lr to caller
callers fp
saved r5
saved r4
fp
sp
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 16
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
4
4
fp - 16
fp - 20
int main(void)
{
int c;
int count = 0;
char buf[] = "hi";
// rest of code
}
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
buf[2]
buf[1]
buf[0]
var pad
count
sp
buf
var pad
frame pad
count
c

## Slide 196: Accessing Stack Variables, the hard way
Calculating offsets is a lot of work to get it correct
It is also hard to debug
There is a better way!
x
Variable | distance from fp | Read variable | Write Variable
int c | 16 | ldr r0, [fp, -16] | str r0, [fp, -16]
int count | 20 | ldr r0, [fp, -20] | str r0, [fp, -20]
char buf[0] | 24 | ldrb r0, [fp, -24] | strb r0, [fp, -24]
char buf[1] | 23 | ldrb r0, [fp, -23] | strb r0, [fp, -23]
char buf[2] | 22 | ldrb r0, [fp, -22] | strb r0, [fp, -22]
lr to caller
callers fp
saved r5
saved r4
fp
sp
.text
.type main, %function
.global main
.equ FP_OFF, 12
.equ FRMADD, 16
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// but we are not done yet!
4
4
fp - 16
fp - 20
int main(void)
{
int c;
int count = 0;
char buf[] = "hi";
// rest of code
}
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
char buf[ ] by usage with ASCII chars we will use strb (or make it unsigned char)
count
c
buf[2]
buf[1]
buf[0]
var pad
fp - 24
fp - 23
fp - 22
fp - 21
increasing address

## Slide 197: Best Practice: Assembler Generated FP Distance Table
For each stack variable create a .equ symbol whose value is the distance in bytes from the FP after the prologue
After the last variable add a name PAD for the size of the frame padding (if any). if no padding, PAD will be set to the same value as the variable above it
The value of the symbol is an expression that calculates the distance from the FP based on the distance of the variable above it on the stack. The first variable will use SP_OFF as the starting distance
  .equ VAR, size_of var + variable_padding + previous_var_symbol // previous_var_symbol distance of the var above
Calculate the size of the local variable area that needs to be added to the sp in bytes
  FRMADD = distance PAD minus distance of the SP to the FP (FP_OFF) after the prologue push
x
lr to caller
callers fp
saved r5
saved r4
fp
sp
4
4
fp - 16
fp - 20
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
count
c
.type main, %function
.global main
.equ FP_OFF, 12
.equ C, 4 + FP_OFF
.equ COUNT, 4 + C
.equ BUF, 4 + COUNT
.equ PAD, 4 + BUF
.equ FRMADD, PAD – FP_OFF
// FRMADD = 28 - 12 = 16
variable size in bytes
Prior allocation distance
pushed reg fp distance
FP Distance Table one For each function

## Slide 198: Best Practice: Assembler Generated FP Distance Table
x
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int c | C | add r0, fp, -C | ldr r0, [fp, -C] | str r0, [fp, -C]
int count | COUNT | add r0, fp, -COUNT | ldr r0, [fp, -COUNT] | str r0, [fp, -COUNT]
char buf[0] | BUF | add r0, fp, -BUF | ldrb r0, [fp, -BUF] | strb r0, [fp, -BUF]
char buf[1] | BUF-1 | add r0, fp, -BUF+1 | ldrb r0, [fp, -BUF+1] | strb r0, [fp, -BUF+1]
char buf[2] | BUF-2 | add r0, fp, -BUF+2 | ldrb r0, [fp, -BUF+2] | strb r0, [fp, -BUF+2]
lr to caller
callers fp
saved r5
saved r4
fp
sp
.type main, %function
.global main
.equ FP_OFF, 12
.equ C, 4 + FP_OFF
.equ COUNT, 4 + C
.equ BUF, 4 + COUNT
.equ PAD, 4 + BUF
.equ FRMADD, PAD – FP_OFF
// FRMADD = 28 - 12 = 16
4
4
fp - 16
fp - 20
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
buf[2]
buf[1]
buf[0]
var pad
fp -BUF
fp –BUF+1
fp –BUF+2
fp –BUF+3
count
c
increasing address
FP Distance Table For each function

## Slide 199: Initializing and Accessing Stack variables
x
lr to caller
callers fp
saved r5
saved r4
fp
count
c
sp
4
4
fp - 16
fp - 20
Total frame size
32 bytes
8-byte aligned
buf
pad
frame pad
1 + 3
fp - 24
FRMADD
FP_OFF
4
12
4
./a.out
-136572160 0 hi
int main(int argc, char **argv)
{
int c;
int count = 0;
char buf[] = "hi";
printf("%d %d %s\n", c, count, buf);
// rest of code
pass stack address
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
add sp, sp, -FRMADD
// nothing to do for C
mov r2, 0
str r2, [fp, -COUNT]
strb r2, [fp, -BUF+2]
mov r2, 'h'
strb r2, [fp, -BUF]
mov r2, 'i'
strb r2, [fp, -BUF+1]
ldr r0, =.Lmess // arg1
ldr r1, [fp, -C] // arg2
ldr r2, [fp, -COUNT] // arg3
add r3, fp, -BUF // arg4
bl printf
passes address of a stack variable buf
passes contents of stack var C and COUNT
.section .rodata
.Lmess: .string "%d %d %s\n"
.extern printf
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int c | C | add r0, fp, -C | ldr r0, [fp, -C] | str r0, [fp, -C]
int count | COUNT | add r0, fp, -COUNT | ldr r0, [fp, -COUNT] | str r0, [fp, -COUNT]
char buf[0] | BUF | add r0, fp, -BUF | ldrb r0, [fp, -BUF] | strb r0, [fp, -BUF]
char buf[1] | BUF-1 | add r0, fp, -BUF+1 | ldrb r0, [fp, -BUF+1] | strb r0, [fp, -BUF+1]
char buf[2] | BUF-2 | add r0, fp, -BUF+2 | ldrb r0, [fp, -BUF+2] | strb r0, [fp, -BUF+2]

## Slide 200: Stack Frame Design Practice
Write the variables in C
Draw a picture of the stack frame
Write the code to generate the offsets
create the distance table to the variables
.equ FP_OFF, 12
.equ C, 1 + FP_OFF
.equ S, 3 + C
.equ B, 8 + S
.equ PTR, 4 + B
.equ PAD, 0 + PTR
.equ FRMADD, PAD – FP_OFF
// FRMADD = 28 - 12 = 16
void func(void)
{
signed char c;
signed short s;
unsigned char b[] = "Stack";
unsigned char *ptr = &b;
// rest of code
}
lr to caller
callers fp
saved r5
saved r4
12
4
s
var pad
C
1, 1+2
var pad
var pad
b[5]
b[4]
b[3]
b[2]
b[1]
b[0]
2 + 6
x
Variable | distance from fp | Address on Stack | Read variable | Write Variable
signed char c | C | add r0, fp, -C | ldrsb r0, [fp, -C] | strsb r0, [fp, -C]
signed short s | S | add r0, fp, -S | ldrsh r0, [fp, -S] | strsh r0, [fp, -S]
unsigned char b[0] | B | add r0, fp, -B | ldrb r0, [fp, -B] | strb r0, [fp, -B]
unsigned char *ptr | PTR | add r0, fp, -PTR | ldr r0, [fp, -PTR] | str r0, [fp, -PTR]
fp
*ptr
4
FRMADD = 16
fame PAD
0
sp
Total frame size
8-byte aligned
Alternative design
s
var pad
C
1+1,2
.equ FP_OFF, 12
.equ C, 2 + FP_OFF
.equ S, 2 + C
…

## Slide 201: Working with Pointers on the stack
int sum(int j, int k)
{
return j + k;
}
void testp(int j, int k, int (*func)(int, int), int *i)
{
*i = func(j,k);
return;
}
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
Output Parameters (like i) you pass a pointer to them, must be on the stack!

## Slide 202: Working with Pointers on the stack
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
.section .rodata
.Lmess: .string "%d\n"
.extern printf
.text
.global main
.type main, %function
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ FRMADD, PAD-FP_OFF
// FRMADD = 12 - 4 = 8
x
lr to caller
callers fp
4
4
i
4
(*pf)()
4
fp
sp
frame pad
0
FRMADD
Total frame size
8-byte aligned

## Slide 203: Working with Pointers on the stack
int main()
{
int i;
int (*pf)(int, int) = sum;
testp(1, 2, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
main:
push {fp, lr}
add fp, sp, FP_OFF
add sp, sp,-FRMADD
ldr r2, =sum // func address
str r2, [fp, -PF] // store in pf
mov r0, 1 // arg 1: 1
mov r1, 2 // arg 2: 2
ldr r2, [fp, -PF] // arg 3: (*pf)()
add r3, fp, -I // arg 4: &I
bl testp
ldr r0, =.Lmess // arg 1: "%d\n"
ldr r1, [fp, -I] // arg 2: I
bl printf
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
x
.section .rodata
.Lmess: .string "%d\n"
.extern printf
.text
.global main
.type main, %function
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ FRMADD, PAD-FP_OFF
// FRMADD = 12 - 4 = 8
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
lr to caller
callers fp
4
4
i
4
(*pf)()
4
fp
sp
frame pad
0
FRMADD
I is Output Parameter

## Slide 204: Working with Pointers on the stack
void
testp(int j, int k, int (*func)(int, int), int *i)
{
*i = func(j, k);
return;
}
.global testp
.type testp, %function
.equ FP_OFF, 12
testp:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
mov r4, r3 // save i
blx r2 // r0=func(r0,r1)
str r0, [r4] // *i =r0
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size testp, (. - testp)
r0,r1,r2 already set
x
lr to caller
callers fp
i
(*pf)()
fp
sp
frame pad
lr to main
main's fp
testp()
stack
main()
stack

## Slide 205: Working with Pointers on the stack
int
sum(int j, int k)
{
return j + k;
}
.global sum
.type sum, %function
.equ FP_OFF, 4
sum:
push {fp, lr}
add fp, sp, FP_OFF
add r0, r0, r1
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
.size sum, (. - sum)
x
lr to caller
callers fp
i
(*pf)()
frame pad
lr to main
main's fp
fp
sp
lr to testp
testp fp
testp()
stack
main()
stack
sum()
stack

## Slide 206: Passing More Than Four Arguments – At the point of Call
Approach: Increase stack frame size to include space for args# > 4
  Arg5 and above are in caller's stack frame at the bottom of the stack
Arg5 is always at the bottom (at sp), arg6 and greater are above it
One arg value per slot! – NO arrays across multiple slots
  chars, shorts and ints are directly stored
  Structs (not always), and arrays (always) are passed via a pointer
Output parameters contain an address that points at the stack, BSS, data, or heap
Prior to any function call (and obviously at the start of the called function):
  sp must point at arg5
  sp and therefore arg5 must be at an 8-byte boundary,
  Add padding to force arg5 alignment if needed is placed above the last argument the called function is expecting
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
x
arg 5
sp
lr to caller
callers fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
arg1 – arg4 Registers
fp
….
calling functions stack frame
Stack segment
high memory
saved regs
local
variables
PAD (if needed)
Outgoing arg space part of calling functions frame

## Slide 207: Passing More Than Four Arguments – At the point of Call
Called functions have the right to change stack args just like they can change the register args!
  Caller must always assume all args including ones on the stack are changed by the caller
Calling function prior to making the call you must
  Evaluate first four args: place the resulting values in r0-r3
  Evaluate Arg 5 and greater and place the resulting values on the stack
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
x
arg 5
sp
lr to caller
callers fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
arg1 – arg4 Registers
fp
….
calling functions stack frame
Stack segment
high memory
saved regs
local
variables
PAD (if needed)
Outgoing arg space part of calling functions frame

## Slide 208: Passing More Than Four Arguments – At the point of Call
Approach: Extend the stack frame to include enough space for stack arguments for the called function that has the greatest number of args
  Examine every function call in the body of a function
  Find the function call with greatest arg count, this determines space needed for outgoing args
  Add the greatest arg count space as needed to the frame layout
  Adjust PAD as required to keep the sp 8-byte aligned
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
x
arg 5
sp
lr to caller
callers fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
arg1 – arg4 Registers
fp
….
calling functions stack frame
Stack segment
high memory
saved regs
local
variables
PAD (if needed)
Outgoing arg space part of calling functions frame

## Slide 209: Calling Function Stack Frame: Pass ARG 5 and higher
oarg5
sp
oarg6
Frame PAD
lr to caller
callers fp
fp
Rules: At point of call
OARG5 must be pointed at by sp
SP must be 8-byte aligned at function call
x
Previous stack frame
.equ FP_OFF, 4
.equ CNT, 4 + FP_OFF // int cnt
.equ PAD, 4 + CNT // added as needed
.equ OARG6, 4 + PAD // 4 bytes
.equ OARG5, 4 + OARG6 // 4 bytes
.equ FRMADD OARG5 – FP_OFF
// FRMADD = 20 - 4 = 16
int cnt;
r0 = func(r0, r1, r2, r3, OARG5, OARG6);
cnt
4
FRMADD
Variable | distance from fp | Address on Stack | Read variable | Write Variable
int cnt | CNT | add r0, fp, -CNT | ldr r0, [fp, -CNT] | str r0, [fp, -CNT]
int oarg6 | OARG6 | add r0, fp, -OARG6 | ldr r0, [fp, -OARG6] | str r0, [fp, -OARG6]
int oarg5 | OARG5 | add r0, fp, -OARG5 | ldr r0, [fp, -OARG5] | str r0, [fp, -OARG5]
4
4
4
4
4
OARG5
OARG6
CNT
Total frame size
8-byte aligned

## Slide 210: Called Function: Retrieving Args From the Stack
At function start and before the push{} the sp is at an 8-byte boundary
Args > 4 in caller's stack frame and arg 5 always starts at fp+4
  Additional args are higher up the stack, with one “slot” every 4-bytes
This "algorithm" for finding args was designed to enable variable arg count functions like printf("conversion list", arg0, … argn);
No limit to the number of args (except running out of stack space)
r0 = func(r0, r1, r2, r3, ARG5, ARG6);
x
.equ ARGN, (N-4)*4 // where n must be > 4
oarg5
sp
oarg6
Frame PAD
lr to callers
callers fp
cnt
fp
Previous stack frame
lr to caller
callers fp
indx
c
fp-8
fp-12
fp+4
fp+8
Rule:
Called functions always access stack args using a positive offset to the fp
calling functions stack frame
called functions stack frame

## Slide 211: Called Function: Retrieving Args From the Stack
r0 = func(r0, r1, r2, r3, r4, ARG5, ARG6);
x
.equ FP_OFF, 4
.equ C, 4 + FP_OFF
.equ INDX, 4 + C
.equ PAD, 0 + INDX
.equ FRMADD, PAD – FP_OFF
// below are distances into the caller's stack frame
.equ ARG6, 8
.equ ARG5, 4
Variable or Argument | distance from fp | Address on Stack | Read variable | Write Variable
int arg6 | ARG6 | add r0, fp, ARG6 | ldr r0, [fp, ARG6] | str r0, [fp, ARG6]
int arg5 | ARG5 | add r0, fp, ARG5 | ldr r0, [fp, ARG5] | str r0, [fp, ARG5]
int c | C | add r0, fp, -C | ldr r0, [fp, -C] | str r0, [fp, -C]
int count | INDX | add r0, fp, -INDX | ldr r0, [fp, -INDX] | str r0, [fp, -INDX]
oarg5
sp
oarg6
Frame PAD
lr to caller
callers fp
cnt
fp
lr to callers
callers fp
indx
c
Rule:
Called functions always access stack args using a positive offset to the fp
calling functions stack frame
called functions stack frame
Observe the positive offsets
ARG5
ARG6
C
INDX
Frame PAD

## Slide 212: Example: Passing Stack Args, Calling Function
int sum(int j, int k)
{
return j + k;
}
void
testp(int j, int k, int l, int m, int (*func)(int, int), int *i)
{
*i = func(j,k) + func(l, m); // notice two func() calls
return;
}
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, 3, 4, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
arg1 arg2 arg3 arg4 arg5 arg6

## Slide 213: Example: Passing Stack Args, Calling Function
int main()
{
int i; // NOTICE: i must be on stack as you pass the address!
int (*pf)(int, int) = sum; // pf could be in a register
testp(1, 2, 3, 4, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ OARG6, 4 + PAD
.equ OARG5 4 + OARG6
.equ FRMADD, OARG5 - FP_OFF
// FRMADD = 20 - 4 = 16
oarg5
sp
oarg6
fp
FRMADD = 16
4
4
lr to caller
callers fp
i
4
(*pf)()
4
frame pad
0
4
4
Main() stack
Variable or Argument | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
int oarg6 | OARG6 | add r0, fp, -OARG6 | ldr r0, [fp, -OARG6] | str r0, [fp, -OARG6]
int oarg5 | OARG5 | add r0, fp, -OARG5 | ldr r0, [fp, -OARG5] | str r0, [fp, -OARG5]
Total frame size
8-byte aligned

## Slide 214: Example: Passing Stack Args, Calling Function
main:
push {fp, lr}
add fp, sp, FP_OFF
add sp, sp,-FRMADD
ldr r0, =sum // get func address
str r0, [fp, -PF] // store sum in var pf
add r0, fp, -I // get address of I
str r0, [fp,-OARG6] // arg 6: store address of I
ldr r0, [fp, -PF] // get PF from stack
str r0, [fp,-OARG5] // arg 5: store sum() address
mov r0, 1 // arg 1: 1
mov r1, 2 // arg 2: 2
mov r2, 3 // arg 3: 3
mov r3, 4 // arg 4: 4
bl testp
ldr r0, =.Lmess // arg 1: "%d\n"
ldr r1, [fp, -I] // arg 2: i
bl printf
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
int main()
{
int i;
int (*pf)(int, int) = sum;
testp(1, 2, 3, 4, pf, &i);
printf("%d\n", i);
return EXIT_SUCCESS;
}
x
Variable or Argument | distance from fp | Address on Stack | Read variable | Write Variable
int i | I | add r0, fp, -I | ldr r0, [fp, -I] | str r0, [fp, -I]
int (*pf)() | PF | add r0, fp, -PF | ldr r0, [fp, -PF] | str r0, [fp, -PF]
int oarg6 | OARG6 | add r0, fp, -OARG6 | ldr r0, [fp, -OARG6] | str r0, [fp, -OARG6]
int oarg5 | OARG5 | add r0, fp, -OARG5 | ldr r0, [fp, -OARG5] | str r0, [fp, -OARG5]
.section .rodata
.Lmess: .string "%d\n"
// other stuff not shown
.equ FP_OFF, 4
.equ I, 4 + FP_OFF
.equ PF, 4 + I
.equ PAD, 0 + PF
.equ OARG6, 4 + PAD
.equ OARG5 4 + OARG6
.equ FRMADD, OARG5 - FP_OFF
// FRMADD = 20 - 4 = 16
oarg5
sp
oarg6
fp
FRMADD = 16
4
4
lr to caller
callers fp
i
4
(*pf)()
4
frame pad
0
4
4
Total frame size
8-byte aligned

## Slide 215: Example: Passing Stack Args, Called Function
void
testp(int j, int k, int l, int m, int (*func)(int, int), int *i)
{
*i = func(j, k) + func(l, m);
return;
}
x
oarg5
sp
oarg6
fp
4
4
lr to caller
callers fp
i
(*pf)()
frame pad
testp()
stack
lr to main
main's fp
Argument | distance | Address on Stack | Read variable | Write Variable
int *i | ARG6 | add r0, fp, ARG6 | ldr r0, [fp, ARG6] | str r0, [fp, ARG6]
int (*pf)() | ARG5 | add r0, fp, ARG5 | ldr r0, [fp, ARG5] | str r0, [fp, ARG5]
.equ FP_OFF, 20
.equ ARG6, 8
.equ ARG5, 4
testp:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF
mov r4, r2 // save l
mov r5, r3 // save m
ldr r6, [fp, ARG5] // load func
ldr r7, [fp, ARG6] // load i
blx r6 // r0 = func(j, k)
mov r1, r5 // arg 2 saved m
mov r5, r0 // save func return value
mov r0, r4 // arg 1 saved l
blx r6 // r0 = func(l, m)
add r0, r0, r5 // func(l,m) + func(j,k)
str r0, [r7] // store sum to *i
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
main()
stack
arg1 arg2 arg3 arg4 arg5 arg6
short circuit: make this call first