## Slide 1
UCSD CSE 30
Keith Muller
Lecture - 15
Computer Organization and Systems Programming
Version 2.09
Colossus MkII - 1944

## Slide 3: Masking Summary - 1
Isolate a field: Use lsr, lsl to get a field surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Select a field: Use and with a mask of one's surrounded by zeros to select the bits that have a 1 in the mask, all other bits will be set to zero
Clear a field: Use and with a mask of zero's surrounded by ones to select the bits that have a 1 in the mask, all other bits will be set to zero
x
0 0 0 0 0 0 0 0 | 0 0 0 0 0 0 0 0 | 0 0 0 0 0 0 0 0 | 0 0 1 1 1 1 0 0
selects this field when used with and
selection mask 0x3c
clear a field mask 0xffffffc3
clears this field when used with and
lsl this edge to bit 31 (left edge)
then lsr to move back
lsr this edge to bit 0 (right edge)
then lsl to move back
1 1 1 1 1 1 1 1 | 1 1 1 1 1 1 1 1 | 1 1 1 1 1 1 1 1 | 1 1 0 0 0 0 1 1

## Slide 4: Masking Summary - 2
Isolate a field: Use and to get a field surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 | 0 0 0 0 0 0 0 0
x
Insert a field: Use orr with fields surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Keep these bits | 0 0 0 0 0 0 0 0 | Keep these bits
selection mask 0x00ff0000
rotate a field: Use ror to move a field without changing other bits
Keep these bits | source | Keep these bits
Keep these bits | Keep these bits | source

## Slide 5: Assembly Source File to Executable to Linux Memory
Local variables and function call overhead
code you write in the text segment
allocates space dynamically during execution by c runtime library code (text)
x
OS kernel [protected]
Stack
Heap
Static Data
Shared Libraries
Read Only Data
Read Only Text Segment
`
.bss
uninitialized static variables
.data
initialized static variables
.section .rodata
read-only literals
.text
assembly code
BSS
Sections in an Assembly Source file
File Header
Specify Hardware assembler generate the correct ARM version
file footer
.section .note.GNU-stack,…
.end
Text
Symbol table
Data
a.out executable
created by the assembler &
link editor
Header - Description

## Slide 6: Assembly Source File Template
assembly programs end in .S
  That is a capital .S
  example: test.S
Always use gcc to assemble
  _start() and C runtime
File has a complete program
  gcc file.S
File has a partial program
  gcc –c file.S
Link files together
  gcc file.o cprog.o
// File Header
.arch armv6 // armv6 architecture instructions
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
// BSS Segment (only when you have uninitialized globals)
.bss
// Data Segment (only when you have initialized globals)
.data
// Read-Only Data (only when you have literals)
.section .rodata
// Text Segment – your code
.text
// Function Header .type main, %function // define main to be a function
.global main // export function name
main:
// function prologue // stack frame setup
// your code for this function here
// function epilogue //stack frame teardown
// function footer
.size main, (. – main)
// File Footer
.section .note.GNU-stack,"",%progbits // stack/data non-exec
.end
x

## Slide 7: Assembler Directives: .equ and .equiv
.equ <symbol>, <expression>
  Defines and sets the value of a symbol to the evaluation of the expression
  Used for specifying constants, like a #define in C
  You can (re)set a symbol many times in the file, last one seen applies
  .equ BLKSZ, 10240 // buffer size in bytes
  // other lines
  .equ BLKSZ, 1024 // buffer size in bytes
.equ BLKSZ, 10240 // buffer size in bytes
.equ BUFCNT, 100*4 // buffer for 100 ints
.equ BLKSZ, STRSZ * 4 // redefine BLKSZ from here
x

## Slide 8: Function Template
.text // start of the text segment
.global myfunc // make myfunc global for linking
.type myfunc, %function // define myfunc to be a function
.equ FP_OFF, 4 // fp offset in main stack frame
myfunc:
push {fp, lr} // push (save) fp and lr on stack
add fp, sp, FP_OFF // set fp for this function
    // your code
sub sp, fp, FP_OFF
pop {fp, lr} // pop (retore) fp and lr from stack
bx lr // return to caller
.size myfunc, (. – myfunc)
Function Prologue
creates stack frame
Function Epilogue
removes stack frame
x
Function header
Function footer
myfunc label is the address of the first instruction in myfunc (the push below)

## Slide 9: Preview: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
r0, r1 = function(r0, r1, r2, r3) // 64-bit return – long long
Each parameter and return value is limited to data that can fit in 4 bytes or less
You receive up to the first four parameters in these four registers
You copy up to the first four parameters into these four registers before calling a function
For parameter values using more than 4 bytes, a pointer to the parameter is passed (we will cover this later)
You MUST ALWAYS assume that the called function will alter the contents of all four registers: r0-r3
  In terms of C runtime support, these registers contain the copies given to the called function
  C allows the copies to be changed in any way by the called function
Register | Function Call Use
r0 | 1st parameter
r1 | 2nd parameter
r2 | 3rd parameter
r3 | 4th parameter
Register | Function Return Value Use
r0 | 8, 16 or 32-bit result, 32-bit address or least-significant half of a 64-bit result
r1 | most-significant half of a 64-bit result
x

## Slide 10: Preview: Writing an ARM32 function
#include <stdlib.h>
#include <stdio.h>
#include "sum4.h"
int main()
{
int reslt;
reslt = sum4(1,2,3,4);
printf("%d\n", reslt);
return EXIT_SUCCESS;
}
#ifndef SUM4_H
#define SUM4_H
#ifndef __ASSEMBLER__
int sum4(int, int, int, int);
#else
.extern sum4
#endif
#endif
#include "sum4.h"
.arch armv6
.arm
.fpu vfp
.syntax unified
.global sum4
.type sum4, %function
.equ FP_OFF, 28
// r0 = sum4(r0, r1, r2, r3)
sum4:
push {r4-r9, fp, lr}
add fp, sp, FP_OFF
add r0, r0, r1
add r0, r0, r2
add r0, r0, r3
sub sp, fp, FP_OFF
pop {r4-r9, fp, lr}
bx lr
.size sum4, (. - sum4)
.section .note.GNU-stack,"",%progbits
.end
$ gcc -Wall -Wextra -c main.c
$ gcc -c sum4.S
$ gcc sum4.o main.o
$ ./a.out
10
We will cover this
when we do stack frames
We will cover this
when we do stack frames

## Slide 11: Load/Store: Register Base Addressing
32-bit memory
register r0
register r1 (address)
ldr r0, [r1]
Copies a 32-bit word
from the memory location
whose address is contained
in r1 (r1 is a pointer)
into register r0
r1 is being used as a pointer to a location in memory
ldr requires the use of a pointer operand
str r0, [r1]
Copies all 32 bits of the value held in register r0 to the 32-bit memory location contained in register r1 (r1 pointer)
32-bit memory
register r0
register r1 (address)
r1 is being used as a pointer to a location in memory
str requires the use of a pointer operand
x

## Slide 12: Example Base Register Addressing Load – Modify – Store
x = x + 1;
ldr r0, [r1] // r0 = *r1 (read x)
add r0, r0, 1 // r0 = r0 + 1 (x++)
str r0, [r1] // *r1 = r0 write x
Memory assigned to x
register r0
register r1 (address)
+ 1
0b..0000100
Notice: word aligned!
(last two bits are 0's)
..00000000
..00000001
n-bit Memory
Address
binary
..00000010
..00000011
..00000100
..00000101
..00000110
..00000111
01010101
10101010
01010101
10101010
01010101
10101010
01010101
10101010
1 byte
contents
X starting address
x
x = x + 1
Where x is in memory
r1 is a pointer

## Slide 13: Load/Store: Register Base Addressing + Immediate
32-bit memory
register r0
register r1 (address)
ldr r0, [r1, 4]
Copies a 32-bit word
from the memory location
whose address is contained
in r1 +4 (r1 is a pointer)
into register r0
str r0, [r1, 4]
Copies all 32 bits of the value held in register r0 to the 32-bit memory location contained in register r1+4 (r1 pointer)
32-bit memory
register r0
register r1 (address)
x
4
Immediate value in instruction
Immediate value in instruction
4

## Slide 14: LDR/STR – Base Register + Immediate Offset Addressing
Register Base Addressing:
  Pointer Address: Rn; source/destination data: Rd
  Unsigned pointer address in stored in the base register
Register Base + immediate offset Addressing:
  Pointer Address = register content + immediate offset -4095 <= imm12 <= 4095 (bytes)
  Unsigned offset integer immediate value (bytes) is added or subtracted (U bit above says to add or subtract) from the pointer address in the base register
  Often used to address struct members
    Address of struct is address of the first member and subsequent members are a fixed offset from the first based on their size of the preceding members
unsigned immediate offset
Rd – source/dest register
ldr/str
Rd
imm12
Rn
Rn – base register contains address (pointer)
U
+/- offset
x

## Slide 15: ldr/str Register Base + Immediate Offset Addressing
Syntax | Address | Examples
ldr/str Rd, [Rn, +/- constant] constant is in bytes ldr/str Rd, [Rn] | Rn + or – constant same | ldr r0, [r5,100] str r1, [r5, 0] str r1, [r5]
ldr/str
Rd
imm12
Rn
U
+ -
0 subtract
1 add
Memory Address
Instruction
Source for str
Destination for ldr
x
Add or subtract 12 bit binary
-4095 to +4095

## Slide 16: Loading and Storing: Variations List
Load and store have variations that move 8-bits, 16-bits and 32-bits
Load into a register with less than 32-bits will set the upper bits not filled from memory differently depending on which variation of the load instruction is used
Store will only select the lower 8-bit, lower 16-bits or all 32-bits of the register to copy to memory, register contents are not altered
Instruction | Meaning | Sign Extension | Memory Address Requirement
ldrsb | load signed byte | sign extension | none (any byte)
ldrb | load unsigned byte | zero fill (extension) | none (any byte)
ldrsh | load signed halfword | sign extension | halfword (2-byte aligned)
ldrh | load unsigned halfword | zero fill (extension) | halfword (2-byte aligned)
ldr | load word | --- | word (4-byte aligned)
strb | store low byte (bits 0-7) | --- | none (any byte)
strh | store halfword (bits 0-15) | --- | halfword (2-byte aligned)
str | store word (bits 0-31) | --- | word (4-byte aligned)
x

## Slide 17: Loading 32-bit Registers From Memory, 32-bit
x
ldr r1, [r0]
load unsigned byte
0x04
0x03
0x02
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
Memory
address

## Slide 18: Loading 32-bit Registers From Memory, 16-bit
x
ldrh r1, [r0]
load unsigned halfword
0x00
0x00
0x02
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x0201
positive number
Memory
address
0x00
0x00

## Slide 19: Loading 32-bit Registers From Memory, 16-bit
x
ldrsh r1, [r0]
load signed halfword
0x00
0x00
0x02
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x0201
positive number
Memory
address
0x00
0x00
0x02 = 0b00000010
No Sign extend

## Slide 20: Loading 32-bit Registers From Memory, 16-bit Signed
x
ldrsh r1, [r0]
load signed halfword
0xff
0xff
0x82
0x01
memory address
r1
0x04
0x03
0x82
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x8201
negative number
Sign extend
0x82 = 0b10000010
0xff
0xff

## Slide 21: Loading 32-bit Registers From Memory, 16-bit Unsigned
x
ldrh r1, [r0]
load unsigned halfword
0x00
0x00
0x82
0x01
memory address
r1
0x04
0x03
0x82
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x8201
positive number
0b10000010
0x00
0x00

## Slide 22: Loading 32-bit Registers From Memory, 8-bit
x
ldrb r1, [r0]
load unsigned byte
0x00
0x00
0x00
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x01
positive number
0x00
0x00
0x00

## Slide 23: Loading 32-bit Registers From Memory, 8-bit
x
ldrsb r1, [r0]
load signed byte
0x00
0x00
0x00
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x01
positive number
0x00
0x00
0x00
No Sign extend
0b00000001

## Slide 24: Loading 32-bit Registers From Memory, 8-bit Signed
x
ldrsb r1, [r0]
load signed byte
0xff
0xff
0xff
0x81
memory address
r1
0x04
0x03
0x02
0x81
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x81
negative number
Sign extend
0b10000001
0xff
0xff
0xff

## Slide 25: Loading 32-bit Registers From Memory, 8-bit Signed
x
ldrb r1, [r0]
load unsigned byte
0x00
0x00
0x00
0x81
memory address
r1
0x04
0x03
0x02
0x81
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x81
positive number
0x00
0x00
0x00

## Slide 26: Storing 32-bit Registers To Memory, 32-bit
x
str r1, [r0]
0x04
0x03
0x02
0x01
memory address
r1
0x04
0x03
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0

## Slide 27: Storing 32-bit Registers To Memory, 16-bit
x
strh r1, [r0]
0x04
0x03
0x02
0x01
memory address
r1
0x??
0x??
0x02
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0

## Slide 28: Storing 32-bit Registers To Memory, 8-bit
x
strb r1, [r0]
0x04
0x03
0x02
0x01
memory address
r1
0x??
0x??
0x??
0x01
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0

## Slide 29: Storing 32-bit Registers To Memory, 8-bit – Storing different byte
x
strb r1, [r0]
0x00
0x04
0x03
0x02
memory address
r1
0x??
0x??
0x??
0x02
0x00
0x00
0x10
0x00
0x00001000
0x00001001
0x00001002
0x00001003
0x??
0x??
r0
0x04
0x03
0x02
0x01
r2
lsr r1, r2, 8
0x00
We want store this byte to memory location 0x1000
you could also do a ror

## Slide 30: ldr/str practice - 1
r1 contains the Address of X (defined as int X) in memory; r1 points at X
r2 contains the Address of Y (defined as int *Y) in memory; r2 points at Y
write Y = &X;
str r1, [r2] // y  &x
address of y
0x0100c
r1
r2
X contents
x
??
Y contents
??
0x01008
0x0100c // this is y
0x01004 // this is x
0x01000
address of x
0x01004
??
0x01010
0x01004

## Slide 31: ldr/str practice - 2
r1 contains the Address of X (defined as int *X) in memory r1 points at X
r2 contains the Address of Y (defined as int Y) in memory; r2 points at Y
write Y = *X;
ldr r3, [r1] // r3  x (read 1)
ldr r0, [r3] // r0  *x (read 2)
str r0, [r2] // y  *x
x
address of y
0x0100c
r1
r2
X = 0x01010
??
Y contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
55
0x01010
55
?
r3
0x01010
r0
?
55

## Slide 32: using ldr/str: array copy
#include <stdio.h>
#include <stdlib.h>
#define SZ 6
void icpy(int *, int *, int);
int main(void)
{
int src[SZ] = {1, 2, 3, 4, 5, 6};
int dst[SZ];
icpy(src, dst, SZ);
for (int i = 0; i < SZ; i++)
printf("%d\n", *(dst + i));
return EXIT_SUCCESS;
}
x
void icpy(int *src, int *dst, int cnt)
{
int *end = src + end;
if (cnt <= 0)
return;
do {
*dst++ = *src++;
} while (src < end);
return;
}

## Slide 33: Base Register version
cmp r2, 0
ble .Ldone
lsl r2, r2, 2 //convert cnt to int size
add r3, r0, r2 // loop term pointer
.Ldo:
ldr r4, [r0] // load from src
str r4, [r1] // store to dest
add r0, r0, 4 // src++
add r1, r1, 4 // dst++
cmp r0, r3 // src < term pointer?
blt .Ldo
.Ldone:
.arch armv6
.arm
.fpu vfp
.syntax unified
.text
.global icpy
.type icpy, %function
.equ FP_OFF, 12
// r0 contains int *src
// r1 contains int *dst
// r2 contains int cnt
// r3 use as loop term pointer
// r4 use as temp
icpy:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
// see right ->
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size icpy, (. - icpy)
.end
x
loop guard
pre loop guard

## Slide 34: Load/Store: Register Base Addressing + Register Offset
32-bit memory
register r0
register r1 (address)
ldr r0, [r1, r4]
Copies a 32-bit word
from the memory location
whose address is contained
in r1 + r4 (r1 is a pointer) into register r0
str r0, [r1, r4]
Copies all 32 bits of the value held in register r0 to the 32-bit memory location contained in register r1+r4 (r1 pointer)
32-bit memory
register r0
register r1 (address)
x
R4 offset
R4 offset

## Slide 35: ldr/str Base Register + Register Offset Addressing
Syntax | Address | Examples
ldr/str Rd, [Rn +/- Rm ] | Rn + or – Rm | ldr r0, [r5, r4] str r1, [r5, r4]
ldr/str
Rd
Rn
U
+ -
0 subtract
1 add
Memory Address
Instruction
Source for str
Destination for ldr
Rm
x
Pointer Address = Base Register + Register Offset
  Unsigned offset integer in a register (bytes) is either added/subtracted from the pointer address in the base register

## Slide 36: ldr/str practice - 3
r1 contains Address of X (defined as int *X) in memory; r1 points at X
r2 contains Address of Y (defined as int Y[2]) in memory; r2 points at &(Y[0])
write *X = Y[1];
ldr r0, [r2, 4] // r0  y[1]
ldr r3, [r1] // r3  x
str r0, [r3] // *x  y[1]
x
address of y
0x0100c
r1
r2
X = 0x01000
??
Y[0] contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
Y[1] contents
0x01010
Y[1] contents
?
r3
r0
?
0x01000
Y[1] contents
+4

## Slide 37: ldr/str practice - 4
r1 contains Address of X (defined as int X[2]) in memory; r1 points at &(x[0])
r2 contains Address of Y (defined as int Y) in memory; r2 points at Y
r3 contains a 4
write Y = X[1];
ldr r0, [r1, r3] // r0  x[1]
str r0, [r2] // y  x[1]
x
address of y
0x0100c
r1
r2
??
x[0] contents
Y contents
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
x[1] contents
0x01010
x[1] contents
4
r3
r0
?
x[1] contents
+4

## Slide 38: Base Register + Register Offset Version
cmp r2, 0
ble .Ldone
lsl r2, r2, 2 //convert cnt to int size
mov r3, 0 // initialize counter
.Ldo:
ldr r4, [r0, r3] // load from src
str r4, [r1, r3] // store to dest
add r3, r3, 4 // counter++
cmp r3, r2 // count < r3
blt .Ldo
.Ldone:
.arch armv6
.arm
.fpu vfp
.syntax unified
.text
.global icpy
.type icpy, %function
.equ FP_OFF, 12
// r0 contains int *src
// r1 contains int *dst
// r2 contains int cnt
// r3 use as loop counter
// r4 use as temp
icpy:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
// see right ->
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size icpy, (. - cpy)
.end
x
loop guard
pre loop guard
one increment covers both arrays

## Slide 39: Base Register + Register Offset With chars
#include <stdio.h>
#include <stdlib.h>
#define SZ 6
void cpy(char *, char *, int);
int main(void)
{
char src[SZ] =
{'a', 'b', 'c', 'd', 'e', '\0'};
char dst[SZ];
cpy(src, dst, SZ);
printf("%s\n", dst);
return EXIT_SUCCESS;
}
x
cmp r2, 0
ble .Ldone
mov r3, 0 // initialize counter
.Ldo:
ldrb r4, [r0, r3] // load from src
strb r4, [r1, r3] // store to dest
add r3, r3, 1 // counter++
cmp r3, r2 // count < r3
blt .Ldo
.Ldone:

## Slide 40: Reference: Addressing Mode Summary for use in CSE30
index Type | Example | Description
Pre-index immediate | ldr r1, [r0] | r1  memory[r0] r0 is unchanged
Pre-index immediate | ldr r1, [r0, 4] | r1  memory[r0 + 4] r0 is unchanged
Pre-index immediate | str r1, [r0] | memory[r0]  r1 r0 is unchanged
Pre-index immediate | str r1, [r0, 4] | memory[r0 + 4]  r1 r0 is unchanged
Pre-index register | ldr r1, [r0, +-r2] | r1  memory[r0 +- r2] r0 is unchanged
Pre-index register | str r1, [r0, +-r2] | memory[r0 +- r2]  r1 r0 is unchanged
x

## Slide 41: Base Register Addressing + Offset register
int count(char *ptr, int len)
{
int cnt = 0;
int i;
for (i = 0; i < len; i++) {
if ((ptr[i] >= 'A') && (ptr[i] <= 'Z'))
cnt++;
}
return cnt;
}
#include <stdio.h>
#include <stdlib.h>
int count(char *, int);
int main(void)
{
char msg[] ="Hello CSE30! We Are CountinG UpPER cASe letters!";
printf("%d\n", count(msg, sizeof(msg)/sizeof(*msg)));
return EXIT_SUCCESS;
}
x

## Slide 42: Base Register + Offset register
count:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
mov r2, 0
cmp r1, 0
ble .Ldone
mov r3, 0
.Lfor:
cmp r3, r1
bge .Ldone
ldrb r4, [r0, r3]
cmp r4, 'A'
blt .Lendif
cmp r4, 'Z'
bgt .Lendif
add r2, r2, 1
.Lendif:
add r3, r3, 1
b .Lfor
.Ldone:
mov r0, r2
.arch armv6
.arm
.fpu vfp
.syntax unified
.text
.global count
.type count, %function
.equ FP_OFF, 12
// r0 contains char *ptr
// r1 contains int len
// r2 contains int cnt
// r3 contains int i
// r4 contains char
count:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
// see right ->
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size count, (. - count)
.end
x
loop guard
byte array
Also use ldrb here
offsets are 0,1,2,…

## Slide 43: Variable Alignment In Memory and Performance
Accessing address aligned memory on many systems based on data type has the best performance (due to hardware implementation)
1
2 bytes
4 bytes
integer
short
char
x
4
bytes
1
Byte
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x0C
0x0D
0x0E
0x0F
Aligned Address
Hex
2
Bytes
0x00
0x02
0x04
0x06
0x08
0x0A
0x0C
0x0E
any address
addresses that end in 0b0
addresses that end in 0b00
0x00
0x04
0x08
0x0C
Aligned Address
Hex
Aligned Address
Hex

## Slide 44: Defining Static Variables: Allocation and Initialization
Variable SIZE | Directive | .align | C static variable Definition | Assembler static variable Definition
8-bit char (1 byte) | .byte |  | char chx = 'A' char string[] = {'A','B','C', 0}; | chx: .byte 'A' string: .byte 'A','B',0x42,0
16-bit int (2 bytes) | .short | .align 1 | short length = 0x55aa; | length: .short 0x55aa
32-bit int (4 bytes) | .word .long | .align 2 | int dist = 5; int *distptr = &dist; unsigned int mask = 0xaa55aa55; int array[] = {12,~0x1,0xCD,-1}; | dist: .word 5 distptr: .word dist mask: .word 0xff array: .word 12,~0x1,0xCD,-3
string with '\0' | .string |  | char class[] = "cse30"; | class: .string "cse30"
x
SIZE | Address ends in | Align
8-bit char -1 byte | 0b..0 or 0b..1 | 
16-bit int -2 bytes | 0b..0 | .align 1
32-bit int -4 bytes and all arrays | 0b..00 | .align 2
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x00
0x02
0x04
0x06
0x00
0x04
Rule: Place the align above the variable
.align 1
len: .short 0x55aa

## Slide 45: Defining Static Variables: Allocation and Initialization
.data
chx: .byte 'A'
.align 2
cnt: .word 4
int num; //4 bytes
int *ptr = &num; //4 bytes
char *lit = "456"; //4 bytes,"456" string literal
char msg[] = "123"; //4 bytes – array
.bss
.align 2
num: .word 0
.data
.align 2
ptr: .word num
.align 2
lit: .word .Lmsg
.align 2
msg: .string "123"
.section .rodata
.Lmsg: .string "456"
initializes a pointer
read-only string literal
Sets alignment for next variable
<chx>: 12028 00000041
<cnt>: 12029 00000004
<chx>: 12028 00000041
<cnt>: 1202c 00000004
.data
chx: .byte 'A'
cnt: .word 4
x
See cnt is not word aligned
See cnt is word aligned

## Slide 46: Defining Static Array Variables
.space size, fill
Allocates size bytes, each of which contain the value fill
Both size and fill are absolute expressions
If the comma and fill are omitted, fill is assumed to be zero
.bss section: Must be used without a specified fill
.bss
int_buf: .space 400 // convert 100 to 400 bytes
.align 2
char_buf: .space 100
.data
array: .word 1, 2, 3, 4, 5
.align 2
one_buf: .space 100, 1 // 100 bytes each byte filled with 1
x
Label: .size_directive expression, … expression
In C: int int_buf[100];
int array[] = {1, 2, 3, 4, 5};
char buffer[100];

## Slide 47: Loading Static variablesinto a register
.text
// function header
main:
// load the address, then contents
// using r2
ldr r2, =x // int *r2 = &x
ldr r2, [r2] // r2 = *r2;
// &x was only needed once above
// Note: r2 was a pointer then an int
// no "type" checking in assembly!
// store the contents of r2
ldr r1, =y // int *r1 = &y
str r2, [r1] // *r1 = r2
…
x
.data
x: .word 200
two step to load a memory variable
  load the pointer to the memory
  read (load) from *pointer
Tell the assembler load the address (Lvalue) of a label into a register:
  ldr/str Rd, =Label // Rd = address
Example to the right: y = x;
.bss
y: .space 4
two steps store to a memory variable
  load the pointer to the memory
  write (store) to *pointer

## Slide 48: Loading large constants into a register: Error: invalid constant (3ff) after fixup
In data processing instructions, the field imm8 + rotate 4 bits is too small to store store the immediate value, how do you get larger immediate values into a register?
Answer: use ldr instruction with the constant as an operand: =constant
Assembler creates a literal table entry with the constant
mov r0, 1023
xxx.s:24: Error: invalid constant (3ff) after fixup
ldr r0, =1023
fails
replacement
mov
Rd
rot4
imm8
x
ldr Rd, =constant // =constant
ldr r1, =0x2468abcd // loads the constant 0x246abcd into r1

## Slide 49: Reference: LDR/STR – Register To/From Memory Copy
ldr/str Rd, [Rn, +- imm12] // base register pointer + offset imm12 in bytes
-4095 <= imm12 <= 4095 (bytes)
ldr/str Rd, [Rn] // base register pointer + 0 (imm12 is 0)
ldr/str Rd, [Rn, +- Rm] // base register pointer +- offset register
offset constant
Rd – destination register
ldr/str
Rd
imm12
Rn
Rn – base register contains address
U
+/- offset
Offset/index Register
Rd – destination register
ldr/str
Rd
Rn
Rn – base register contain address
Rm
U
+/- offset
ldr r1, =var_x // r1 = &var_x
str r1, =mylabel+4 // *(mylabel+4) = r1
ldr r1, =0x246abcd // load an immediate into r1
ldr r1, [r3] // y = *r3 (4 bytes)
str r1, [r0] // *r0 = r1
ldr r1, [r3, -4] // y = *(r3 – 4) (4 bytes)
str r1, [r0, r2] // *(r0 + r2) = r1
x

## Slide 50: Stack types
A Stack Implements a last-in first-out (LIFO) protocol
Each time a function is called, a stack frame is activated
  space is allocated by moving the stack pointer
  push adds space, pop removes space
Stack growth direction
  Ascending stack: grows from low memory towards high memory (adding to the sp to allocate memory)
  Descending stack: grows from high memory towards low memory (subtracting from the sp to allocate memory)
Full versus empty stacks
  Empty stack: stack pointer (sp) points at the next word address after the last item pushed on the stack
  Full stack: stack pointer (sp) points at the last item pushed on the stack
ARM on Linux uses a full descending stack
Descending stack high memory
low memory
Ascending stack high memory
low memory
stack pointer
Empty descending stack high memory
low memory
stack pointer
Full descending stack high memory
low memory
x

## Slide 51: Arm: Stack Operation
Stack is expandable and grows downward from high memory address towards low memory address
Stack pointer (sp) always points at the top of stack
  contains the starting address of the top element
New items are pushed (added) onto the top of the stack by subtracting from the stack pointer the size of the element and then writing the element
Existing items are popped (removed) from the top of the stack by adding to the stack pointer the size of the element (leaving the old contents unchanged)
0x00010000
0x00010004
0x00010008
0x0001000c
0x00010010
0x00010014
0x00010018
0x0001001c
0x00010020
0x00010024
0x00010028
0x0001002c
0x00010030
0x00010034
contents
High Word address
top of stack
push (sp - element size) & write
pop (sp + element size)
0x100
0x101
0x102
eligible for reuse
x
allocated

## Slide 52: Function Calls, Parameters and Locals: Requirements
  int
  main(int argc, char *argv[])
  {
  int x, z = 4;
  x = a(z);
  z = b(z);
  return EXIT_SUCCESS;
  }
  int
  a(int n)
  {
  int i = 0;
  if (n == 1)
  i = b(n);
  return i;
  }
  int
  b(int m)
  {
  return m+1;
  /* the return cannot be done with a branch */
  }
Since b() is called both by main and a() how does the return m+1 statement in b() know where to return to? (Obviously, it cannot be a branch)
Where are the parameters (args) to a function stored so the function has a copy that it can alter?
Where is the return value from a function call stored?
How are Automatic variables lifetime and scope implemented?
  When you enter a variables scope: memory is allocated for the variables
  When you leave a variable scope: memory lifetime is ended (memory can be reused -- deallocated) – contents are no longer valid
x

## Slide 53: Stack Segment: Support of Functions
The stack consists of a series of "stack frames" or "activation frames", one is created each time a function is called at runtime
Each frame represents a function that is currently being executed and has not yet completed (why activation frame)
A function’s stack "frame" goes away when the function returns
Specifically, a new stack frame is
  allocated (pushed on the stack) for each function call (contents are not implicitly zeroed)
  deallocated (popped from the stack) on function return
Stack frame contains:
  Local variables, parameters of function called
  Where to return to which caller when the function completes (the return address)
0xFF…FF
0x00…00
32-bit Address space
OS kernel [protected]
Stack
Heap
Static Data (+BSS)
Shared Libraries
Read Only Data
Read Only Text Segment

## Slide 55: ARM Assembly Source File: Header and Footer
.syntax unified
  use the standard ARM assembly language syntax called Unified Assembler Language (UAL)
.section .note.GNU-stack,"",%progbits
  tells the linker to make the stack and all data segments not-executable (no instructions in those sections) – security measure
.end
  at the end of the source file, everything written after the .end is ignored
.arch armv6 // armv6 architecture
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
File Header
At the top of every ARM source file
.section .note.GNU-stack,"",%progbits // set stack/data non-exec
.end
// everything past the .end is ignored!
// Debugging notes etc
File Footer
At the bottom of every ARM source file
// Contents of the other memory segment include .text (your code)
x

## Slide 56: Function Header and Footer Assembler Directives
.global function_name
  Exports the function name to other files. Required for main function, optional for others
.type name, %function
  The .type directive sets the type of a symbol/label name
  %function specifies that name is a function (name is the address of the first instruction)
equ FP_OFF, 4
  Used for basic stack frame setup; the number 4 will change – later slides
.size name, bytes
  The .size directive is used to set the size associated with a symbol
  Used by the linker to exclude unneeded code and/or data when creating an executable file
  It is also used by the debugger gdb
  bytes is best calculated as an expression: (period is the current address in a memory segment)
  .size name, (. – name)
.text
.global myfunc // make myfunc global for linking
.type myfunc, %function // define myfunc to be a function
.equ FP_OFF, 4 // fp offset in main stack frame
myfunc:
// function prologue, stack frame setup
    // your code
// function epilogue, stack frame teardown
.size myfunc, (. – myfunc)
function entry point
address of the first instruction in the function
Must not be a local label (does not start with .L)
Function Header
Function Footer
x

## Slide 57: Example: Assembler Directive and Instructions
10 .equ NULL, 0
11 main:
12 3000 0310A0E1 mov r1, r3
13 .Lloop:
14 3004 043083E2 add r3, r3, 4
15 3008 001093E5 ldr r1, [r3]
16 300c 000051E3 cmp r1, NULL
17 3010 FBFFFF1A bne .Lloop
Instruction Memory Addresses (lowest 2-bits are always are 00)
Notice alignment and how addresses increase by 4 (32-bit instructions)
Regular label main
is associated with memory location 0x3000
Local label .Lloop
is associated with memory location 0x3004
assembler directive .equ does not allocate any memory (NULL = 0)
Memory Contents
Warning contents shown in "reverse" byte order: Lsb – Msb
output generated with
gcc -c -Wa,-ahlns space.S
partial output is shown
space.S
x

## Slide 58: Preview: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
r0, r1 = function(r0, r1, r2, r3) // 64-bit return – long long
Each parameter and return value is limited to data that can fit in 4 bytes or less
You receive up to the first four parameters in these four registers
You copy up to the first four parameters into these four registers before calling a function
For parameter values using more than 4 bytes, a pointer to the parameter is passed (we will cover this later)
You MUST ALWAYS assume that the called function will alter the contents of all four registers: r0-r3
  In terms of C runtime support, these registers contain the copies given to the called function
  C allows the copies to be changed in any way by the called function
Register | Function Call Use
r0 | 1st parameter
r1 | 2nd parameter
r2 | 3rd parameter
r3 | 4th parameter
Register | Function Return Value Use
r0 | 8, 16 or 32-bit result, 32-bit address or least-significant half of a 64-bit result
r1 | most-significant half of a 64-bit result
x

## Slide 59: Assembler Directives: Label Scope Control (Normal Labels only)
.extern <label>
  Imports label (function name, symbol or a static variable name);
  An address associated with the label from another file can be used by code in this file
.global <label>
  Exports label (or symbol) to be visible outside the source file boundary (other assembly or c source)
  label is either a function name or a global variable name
  Only use with function names or static variables
Without .global, labels are usually local to the file from the point where they are defined
.extern printf
.extern fgets
.extern strcpy
.global fbuf
x

## Slide 60: Variable Alignment In Memory and Performance
Accessing address aligned memory on many systems based on data type has the best performance (due to hardware implementation)
1
2 bytes
4 bytes
integer
short
char
x
4
bytes
1
Byte
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x0C
0x0D
0x0E
0x0F
Aligned Address
Hex
2
Bytes
0x00
0x02
0x04
0x06
0x08
0x0A
0x0C
0x0E
any address
addresses that end in 0b0
addresses that end in 0b00
0x00
0x04
0x08
0x0C
Aligned Address
Hex
Aligned Address
Hex

## Slide 61: LDR/STR – Base Register + Immediate Offset Addressing
Register Base Addressing:
  Pointer Address: Rn; source/destination data: Rd
  Unsigned pointer address in stored in the base register
Register Base + immediate offset Addressing:
  Pointer Address = register content + immediate offset -4095 <= imm12 <= 4095 (bytes)
  Unsigned offset integer immediate value (bytes) is added or subtracted (U bit above says to add or subtract) from the pointer address in the base register
unsigned immediate offset
Rd – source/dest register
ldr/str
Rd
imm12
Rn
Rn – base register contains address (pointer)
U
+/- offset
x

## Slide 62: Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrb r1, [r0]
r1
0
31
r1
Load a word
ldr r1, [r0]
observe the zero fill
x
0x0a
0x0b
0x0c
0x0d
0xe1
0xe3
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
0xe3
0xe1
0x00
0x00
0
31
r1
Load a halfword
ldrh r1, [r0]
0x00
0x00
0xe3
0xe1
observe the zero fill
0xe1

## Slide 63: Signed Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrsb r1, [r0]
r1
0
31
r1
Load a word (no change)
ldr r1, [r0]
observe the sign extend
x
0x0a
0x0b
0x0c
0x0d
1110 0001
1110 0011
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
1110 0011
1110 0001
0x00
0x00
0
31
r1
Load a halfword
ldrsh r1, [r0]
0x00
0x00
observe the sign extend
1110 0011
1110 0001
0xff
0xff
1110 0001
0xff
0xff
0xff

## Slide 64: Signed Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrsb r1, [r0]
r1
0
31
r1
Load a word (no change)
ldr r1, [r0]
observe the sign extend
x
0x0a
0x0b
0x0c
0x0d
0110 0001
0110 0011
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
0110 0011
0110 0001
0x00
0x00
0
31
r1
Load a halfword
ldrsh r1, [r0]
0x00
0x00
0110 0011
0110 0001
observe the sign extend
0110 0001

## Slide 65: Store a Byte, Half-word, Word
0x20
0x00
0x00
0x00
initial value in r0
0
31
Store a byte
strb r1, [r0]
r1
0x87
0x65
0xe3
0xe1
0x11
0x22
0x33
0x20000000
0x20000001
0x20000002
0x20000003
observe other bytes NOT altered
Byte Address Byte
x
0x00
0xe1
0
31
r1
Store a halfword
strh r1, [r0]
0x87
0x65
0xe3
0xe1
0x22
0x33
0x20000000
0x20000001
0x20000002
0x20000003
Byte Address Byte
0x11
0x00
0xe1
0xe3
0
31
0x87
0x65
0xe3
0xe1
r1
Store a word
str r1, [r0]
0x20000000
0x20000001
0x20000002
0x20000003
Byte Address Byte
0x11
0x22
0x33
0x00
0xe1
0xe3
0x65
0x87

## Slide 66: ldr/str practice - 1
r1 contains the Address of X (defined as int X) in memory; r1 points at X
r2 contains the Address of Y (defined as int *Y) in memory; r2 points at Y
write Y = &X;
str r1, [r2] // y  &x
address of y
0x0100c
r1
r2
X contents
x
??
Y contents
??
0x01008
0x0100c // this is y
0x01004 // this is x
0x01000
address of x
0x01004
??
0x01010
0x01004

## Slide 67: ldr/str practice - 2
r1 contains the Address of X (defined as int *X) in memory r1 points at X
r2 contains the Address of Y (defined as int Y) in memory; r2 points at Y
write Y = *X;
ldr r3, [r1] // r3  x (read 1)
ldr r0, [r3] // r0  *x (read 2)
str r0, [r2] // y  *x
x
address of y
0x0100c
r1
r2
X = 0x01010
??
Y contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
55
0x01010
55
?
r3
0x01010
r0
?
55