## Slide 1
UCSD CSE 30
Keith Muller
Lecture - 12
Computer Organization and Systems Programming
Version 2.03
Cray XMP-1982

## Slide 3: Line Layout in an Arm Assembly Source
Assembly language source text files are line oriented (each ending in a '\n')
Each line represents a starting address in memory and does one of:
  Specifies the contents of memory for a variable (segments containing data)
  Specifies the contents of memory for an instruction (text segment)
  Assembler directives tell the assembler to do something (for example, change label scope, define a macro, etc.) that does not allocate memory
Each line is organized into up to four columns
  Not every column is used on each line
  Not every line will result in memory being allocated
label: operation operand(s) // comments
tab
white space
white space
x
column 1 column 2 column 3 column 4

## Slide 4: Labels in Arm Assembly - 1
Labels (optional); starts in column 1 (often on a line by itself ABOVE the "operation")
  Only put a label on a line when you need to associate a name (a global variable, a function name, a loop/ branch target, etc.) to that line's location in memory
  You then refer to the address by name in an instruction
Operation type 1: assembler directives (all start with a period e.g. .word )
Operation Type 2: assembly language instructions
Zero or more operands as required by the instruction or assembler directive
Comments: C and C++ style; also @ in the place of a C++ comment //
x
label: operation operand(s) // comment
// assembler directive below
cnt: .word 5 /* define a global int cnt = 5; */
/* instruction example below */
add r1 r2, r3 // add the values

## Slide 5: Labels in Arm Assembly - 2
Remember, a Label associates a name with memory location
Regular Label:
  Used with a Function name (label) or all static variables in any of the data segments
Local Label: Name starts with .L (local label prefix) only usable in the same file
  Targets for
    branches: if switch, goto, break, continue,
    loops: for, while, do-while
  Anonymous variables (the address of literal not the address of foo in the following)
    char *foo = "literal";
x
.Lmesg: .string "Hello CSE30! We Are CountinG UpPpER cASe letters!"
main:
push {fp, lr}
.Lwhile:
add r2, r2, 1 // increment char pointer
local label
Regular label
local label
label main is the starting address of the push instruction
label .Lmesg is the starting address for the ascii string
label .Lwhile is the starting address of the add instruction

## Slide 6: Unconditional Branching – Forces Execution to Continue at a Specified Label (goto)
b .Ldone // goto .Ldone
:
.Ldone:
add r0, EXIT_SUCCESS // set return value
Unconditional Branch instruction (branch to only local labels in CSE30)
b .Llabel
Causes an unconditional branch (aka goto) to the instruction with the address .Llabel
.Llabel is called a branch target label (the "target" of a branch instruction)
Be careful! do not to branch to a function label!
.Llabel: translates into an number offset being imm24 shifted left two bits (+/- 32 MB)
b
imm24
x
imm24 is Relative direction
from the branch instruction (in +/- instructions)

## Slide 7: Examples of of Unconditional Branching
Branches are used to change execution flow using labels as the branch target
In these example, .Lforward and .Lbackward are the branch target labels
Branch target labels are placed at the beginning of the line (or above it)
Caution: Backward branches should only used with loops!
b .Lforward
add r1, r2, 4
add r0, r6, 2
add r3, r7, 4
.Lforward:
sub r1, r2, 4
.Lbackward:
add r1, r2, 4
sub r1, r2, 4
add r4, r6, r7
b .Lbackward
// not reachable unless
// there is a label after the .b above
Backward Branch
(Infinite loop)
Unconditional Branch Forward
x
Not a practical example as this code is unreachable
Branch target (local label)

## Slide 8: Never Branch to the following instruction: It is not needed!
x
mov r2, 0
b .Lnext // do not do this, not needed
.Lnext:
add r1, r2, r3
mov r2, 0
add r1, r2, r3

## Slide 9: Anatomy of a Conditional Branch: If statement
Branch guard: determines when to execute the "condition true block" or the "condition false block"
In C, when the branch guard (condition test) evaluates non-zero you fall through to the condition true block, otherwise you branch to the condition false (else) block
Step 1: evaluate the branch guard(s) (involves one or more compares/tests)
Step 2: If branch guard evaluates to be false
  branch around the true block and execute the else block
  otherwise "fall through" and execute the true block
Block order in C is where the True Block appears above the False block
if (r0 == 5) {
/* condition block #1 */
/* branch to "here" */
} else {
/* condition block #2 */
/ * fall through to "here" */
}
// resume here
Branch condition
Test (branch guard)
r0 == 5
condition true block
condition else block

## Slide 10: cmp/cmm – Making Conditional Tests
cmp r1, 0 // r1 – 0 and sets flags on the result
cmp r1, r2 // r1 – r2 and sets flags on the result
cmp Rn, constant // Rn – constant; then sets condition flags
cmm Rn, constant // Rn + constant; then sets condition flags
cmp Rn, Rm // Rn – Rm; then sets condition flags
cmm Rn, Rm // Rn + Rm; then sets condition flags
Operand 2 constant
cmp/cmm
rot4
imm8
Rn
operand 1
Operand 2
cmp/cmm
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
The values stored in the registers Rn and Rm are not changed
The assembler will automatically substitute cmn for negative immediate values
x

## Slide 11: Quick Overview of the Condition Bits/Flags
The CSPR is a special register (like the other registers) in the CPU
The four bits at the left are called the Condition Code flags
  Summarize the result of a previous instruction
  Not all instruction will change the CC bits
Specifically, Condition Code flags are set by cmm/cmp (and others)
Example: cmp r4, r3
N (Negative) flag: Set to 1 when the result of r4 – r3 is negative, set to 0 otherwise
Z (Zero) flag: Set to 1 when the results of r4 – r3 is 0, set to 0 otherwise
C (Carry bit) flag: Set to 1 when r4 – r3 does not have a borrow, set to 0 otherwise
V flag (oVerflow): Set to 1 when r4 – r3 causes an overflow, set to 0 otherwise
N
Z
C
V
CPSR
31
30
29
28
5 0
Execution Mode
x

## Slide 12: Conditional Tests: Implementing ARM Branch guards
Branch instruction
bsuffix .Llabel
Bits in the condition field specify the conditions when the branch happens
If the condition evaluates to be true, next instruction executed is at .Llabel:
If the condition evaluates to be false, next instruction executed is immediately after the branch
Unconditional branch is when the condition is "always"
bsuffix
imm24
cond
Condition | Meaning | Flag Checked
BEQ | Equal | Z = 1
BNE | Not equal | Z = 0
BGE | Signed ≥ ("Greater than or Equal") | N = V
BLT | Signed < ("Less Than") | N ≠ V
BGT | Signed > ("Greater Than") | Z = 0 && N = V
BLE | Signed ≤ ("Less than or Equal") | Z = 1 ¦¦ N ≠ V
BMI | Minus/negative | N = 1
BPL | Plus - positive or zero (non-negative) | N = 0
B | Branch Always (unconditional) | 
x
imm24 is Relative direction
from the branch instruction
(in +/- instructions)
Use a local label with branch instructions

## Slide 13: Branch and Loop Guard Strategy
How to implement a branch/loop guard in CSE30
Use a cmp/cmm instruction to set the condition bits
Follow the cmp/cmm with one or more variants of the conditional branch instruction
  Conditional branch instructions if evaluate to true (based on the flags set by the cmp) the next instruction will the one at the branch label
  Otherwise, execution falls through to the instruction that immediately follows the branch
You may have one or more conditional branches after a single cmp/cmm
cmp r0, 10
ble .Lendif
// True Block
.Lendif:
Branch guard
x

## Slide 14: Program Flow: Simple If statement, No Else
Realize that in ARM assembly you can only either "fall through" to the next instruction or branch to a specific instruction
Approach: adjust the conditional test then branch around the true block
Use a conditional test that specifies the inverse of the condition used in C
  This preserves C block order
C source Code | Incorrect Assembly | Correct Assembly
int r0; if (r0 > 10) { // True Block } | cmp r0, 10 bgt .Lendif // True Block .Lendif: | cmp r0, 10 ble .Lendif // True Block .Lendif:
x

## Slide 15: Branch Guard "Adjustment" Table Preserving C Block Order In Assembly
if (r0 compare 5)
/* condition true block */
/* then fall through */
}
Compare in C | "Inverse" Compare in C | Assembly using Inverse Compare
== | != | bne
!= | == | beq
> | <= | ble
>= | < | blt
< | >= | bge
<= | > | bgt
cmp r0, 5
inverse compare .Lelse
// condition true block
// then fall through
.Lendif:
x

## Slide 16: Arm Conditional Branching Simple IF no else
If statements in ARM
Step 1: make a conditional test using a cmp instruction
Step 2: if test evaluates to FALSE, branch around the condition true block with a one of the conditional branch instruction
x
cmp r0, 5
bne .Lendif
/* condition true block */
/* then fall through */
.Lendif:
/* branch around to this code */
If r0 == 5 false
then branch around the true block
int r0;
if (r0 == 5) {
/* condition true block */
/* then fall through */
}
/* branch around to this code */
If r0 == 5 true
then fall through to the true block
C If statement
ARM If statement

## Slide 17: If statement examples – Branch Around the True block!
int r0;
if (r0 == 5) {
r1 = r2++ + r3;
}
r3 = r2;
cmp r0, 5
bne .Lendif
add r1, r2, r3
add r2, r2, 1
.Lendif:
mov r3, r2
x
If r0 == 5 false
then branch around the true block
Fall through
int r0;
if (r0 <= 5) {
r1 = r2++;
}
r3 = r2;
cmp r0, 5
bgt .Lendif
mov r1, r2
add r2, r2, 1
.Lendif:
mov r3, r2
Fall through

## Slide 18: Branching Avoid: Spaghetti Code ("goto structure")
Do not use unnecessary branches
Optimize your use of "fall throughs"
For example: Do not make a conditional branch around an unconditional branch that immediately follows it
Do not do the following:
cmp r0, 0
beq .Lthen
b .Lendif
.Lthen:
add r1, r1, 1
.Lendif:
add r1, r1, 2
x
Do the following:
cmp r0, 0
bne .Lendif
// fall through
add r1, r1, 1
.Lendif:
add r1, r1, 2
Caution!
Two adjacent branches

## Slide 19: Program Flow: If with an Else
Approach:
adjust the conditional test to branch to the False Block
Fall through to the True Block
Bottom of the True Block unconditionally branches around the False block
C source Code | Assembly
int r0; if (r0 > 10) { // true block // branch always around the false block } else { // false block } | cmp r0, 10 ble .Lelse /fall through // true block b .Lendif .Lelse: // false block // fall through .Lendif:
x

## Slide 20: If with an Else Examples
if (r0 == 5) {
/* cond. true block */
/* branch around false */
} else {
/* condition false block */
/* fall through */
}
r1 = 4;
If r0 == 5 false
then branch to false block
x
cmp r0, 5
bne .Lelse
// Fall through
// cond. true block
/*
* Now branch around the
* condition false block
*/
b .Lendif
.Lelse
// condition false block
// fall through
.Lendif:
mov r1, 4
If r0 == 5 false
then branch to false block

## Slide 21: If with an Else Examples
…
if (r0 < r1) {
r2 = 1;
// branch around else
} else {
r2 = 0;
/* fall through */
}
r4 = r2 + r4;
  cmp r0, r1
  bge .Lelse
  mov r2, 1
  b .Lendif
.Lelse:
mov r2, 0
/* fall through */
.Lendif:
add r4, r2, r4
x
If r0 < r1 false
then branch to false block
Branch condition
Test (branch guard)
condition true block
condition false block

## Slide 22: If statement – C Block Reordering
if (r0 != 5) {
/* condition block #2 */
} else {
/* condition block #1 */
/* fall through */
}
Block order: (the order the blocks appear in C code) can be changed by inverting the conditional test, swapping the order of the true and false blocks
if (r0 == 5) {
/* condition block #1 */
} else {
/* condition block #2 */
/ * fall through */
}
x
Branch condition
Test (branch guard)
condition true block
condition false block
condition true block
condition false block
Branch condition
Test (branch guard)

## Slide 23: Preserving the same branch guard test
if (r0 < r1) {
// true block
r2 = 1;
// now branch around else
} else {
// false block
r2 = 0;
/* fall through */
}
r4 = r2 + r4;
x
  cmp r0, r1
  blt .Lelse
  // false block
mov r2, 0
  b .Lendif // around else
.Lelse:
  // true block
  mov r2, 1
/* fall through */
.Lendif:
add r4, r2, r4
Swap the order of true and false blocks
Same branch guard test

## Slide 24: Switch Statement
switch (r0) {
case 1:
// block 1
break;
case 2:
// block 2
break;
default:
// default 3
break;
}
x
cmp r0, 1
beq .Lblk1
cmp r0, 2
beq .Lblk2
// fall through
// default 3
b .Lendsw // break
.Lblk1:
// block 1
b .Lendsw // break
.Lblk2:
// block 2
// fall through
// NO b .Lendsw
.Lendsw:
Branch block

## Slide 25: Bad Style: Branching Upwards (When Not a loop)
Do not Branch "Upwards" unless it is part of a loop (later slides)
If you cannot easily write the equivalent C code for your assembly code, you may have code that is harder to read than it should be
Action: adjust your assembly code to have a similar structure as an equivalent version written in C
  mov r3, r4
  b .Llabel2
.Llabel1:
mov r2, 0
b .Llabel3
.Llabel2:
add r4, r3, r2
b .Llable1
.Llabel3:
add r4, r2, r4
x
Upwards
branch
Do not do this
  mov r3, r4
  add r4, r3, r2
mov r2, 0
add r4, r2, r4
Do this

## Slide 26: Review – Short Circuit or Minimal Evaluation
In evaluation of conditional guard expressions, C uses what is called short circuit or minimal evaluation
Each expression argument is evaluated in sequence from left to right including any side effects (modified using parenthesis), before (optionally) evaluating the next expression argument
If after evaluating an argument, the value of the entire expression can be determined, then the remaining arguments are NOT evaluated (for performance)
x
if ((x == 5) || (y > 3)) // if x == 5 then y > 3 is not evaluated
if ((a != 0) && func(b)) // if a is 0, func(b) is not called
// do something

## Slide 27: Program Flow – If statements && compound tests - 1
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
bne .Lendif
cmp r1, 3
ble .Lendif
mov r2, r5 // true block
// fall through
.Lendif:
mov r4, r3
If r0 == 5 false
then short circuit branch around the true block
x

## Slide 28: Program Flow – If statements && compound tests - 2
cmp r0, 5 // test 1
bne .Lelse
cmp r1, 3 // test 2
ble .Lelse
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse:
mov r5, r2 // false block
// fall through
.Lendif:
mov r4, r3
if r0 == 5 false
then short circuit branch to the false block
if ((r0 == 5) && (r1 > 3)) {
r2 = r5; // true block
// branch around else
} else {
r5 = r2; False block */
/* fall through */
}
r4 = r3;
x
if r1 > 3 false
then branch to the false block
test1 test2

## Slide 29: Program Flow – If statements || compound tests - 1
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* fall through */
}
r4 = r3;
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lendif
// fall through
.Lthen:
mov r2, r5 // true block
/* fall through */
.Lendif:
mov r4, r3
If r0 == 5 true, then branch to true block
if r1 > 3 false then branch around true block
x

## Slide 30: Program Flow – If statements || compound tests - 2
cmp r0, 5
beq .Lthen
cmp r1, 3
ble .Lelse
// fall through
.Lthen:
mov r2, r5 // true block
// branch around else
b .Lendif
.Lelse
mov r5, r2 // false block
// fall through
.Lendif:
if ((r0 == 5) || (r1 > 3)) {
r2 = r5; // true block
/* branch around else */
} else {
r5 = r2; // false block
/* fall through */
}
x
If r0 == 5 true, then branch to the true block
if r1 > 3 false then branch to false block

## Slide 31: Program Flow – Pre-test and Post-test Loop Guards
loop guard: code that must evaluate to true before the next iteration of the loop
If the loop guard test(s) evaluate to true, the body of the loop is executed again
pre-test loop guard is at the top of the loop
  If the test evaluates to true, execution falls through to the loop body
  if the test evaluates to false, execution branches around the loop body
post-test loop guard is at the bottom of the loop
  If the test evaluates to true, execution branches to the top of the loop
  If the test evaluates to false, execution falls through the instruction following the loop
x
while (i < 10) {
/* block */
i++;
}
pre-test
loop guard
loop control variable
zero or more iterations
do {
/* block */
i++;
} while (i < 10);
post-test
loop guard
one or more iterations

## Slide 32: Pre-Test Guards - While Loop
.Lwhile:
cmp r1, 10
bge .Lendw
// block
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
/* block */
r1++;
}
r2 = r1;
x
pre-test
loop guard
loop iteration
inverted test

## Slide 33: Pre-Test Guards - While Loop
x
.Lwhile:
cmp r1, 10
bge .Lendw
cmp r2, r1
beq .Lnext
// block
.Lnext:
add r1, r1, 1
b .Lwhile
.Lendw:
mov r2, r1
while (r1 < 10) {
if (r2 != r1) {
/* block */
}
r1++;
}
r2 = r1;
pre-test
loop guard
loop iteration
if stmt guard

## Slide 34: Post-Test Guards – Do While Loop
.Ldo:
// block
add r1, r1, 1
cmp r1, 10
blt .Ldo
mov r2, r1
do {
/* block */
r1++;
} while (r1 < 10);
r2 = r1;
x
loop iteration
post-test
loop guard
test is not inverted

## Slide 35: Post-Test Guards – Do While Loop
.Ldo:
cmp r2, r1
beq .Lnext
// block
.Lnext
add r1, r1, 1
cmp r1, 10
blt .Ldo
move r2, r1
x
do {
if (r2 != r1) {
/* block */
}
r1++;
} while (r1 < 10);
r2 = r1;
loop iteration
post-test
loop guard

## Slide 36: Program Flow – Counting (For) Loop Version 1
mov r1, 0
.Lfor:
cmp r1, 10
bge .Lendfr
// block code
add r1, r1, 1
b .Lfor
.Lendfr:
A counting loop has three parts:
Pre-loop setup
Pre-test loop guard conditions
Post-loop update
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Post loop update
Pre loop setup
Pre-test loop guard

## Slide 37: Program Flow – Counting (For) Loop – Version 2
Alternative:
move Pre-test loop guard before the loop
Add post-test loop guard
  converts to do while
  removes an unconditional branch
for (r1 = 0; r1 < 10; r1++) {
/* block */
}
mov r1, 0
cmp r1, 10
bge .Lendfr
.Ldo:
// block code
add r1, r1, 1
cmp r1, 10
blt .Ldo
.Lendfr:
Pre loop setup
Pre-test
Loop guard
Post loop update
x
Pre-loop setup
Post loop update
Pre-test loop guard
Post-test loop guard

## Slide 38: Nested loops
Nest loop blocks as you would in C or Java
for (r3 = 0; r3 < 10; r3++) {
r0 = 0;
do {
r0 = r0 + r1++;
} while (r1 < 10);
// fall through
r2 = r2 + r1;
}
r5 = r0;
x
mov r3, 0
.Lfor:
cmp r3, 10 // loop guard
bge .Lendfor
mov r0, 0
.Ldo:
add r0, r0, r1
add r1, r1, 1
cmp r1, 10 // loop guard
blt .Ldo
// fall through
add r2, r2, r1
add r3, r3, 1 // loop iteration
b .Lfor
.Lendfor:
mov r5, r0

## Slide 39: Keep loops Properly Nested: Do not branch into the middle of a loop
It is hard to understand and debug loops when you branch into the middle of a loop
Keep loops proper nested
Do not do the following:
.Lloop1:
add r1, r1, 1
.Lloop2:
add r2, r2, 1
add r2, r1, r3
cmp r1, 10
blt .Lloop1
beq .Lend1
add r3, r3, 1
cmp r2, 20
ble .Lloop2
.Lend1:
x
Bad practice: branch into loop body