## Slide 1
UCSD CSE 30
Keith Muller
Lecture - 14
Computer Organization and Systems Programming
Version 2.11

## Slide 3: Using pointers to examine byte order (on pi-cluster)
#include <stdio.h>
#include <stdlib.h>
#define SZ 2
int main()
{
unsigned int foo[SZ] = {0x11223344, 0xaabbccdd};
unsigned char *chptr = (unsigned char *)foo;
// print from MSB to LSB – high to low memory)
for (int i = sizeof(foo)-1; i >= 0; i--)
printf("byte %d: %x\n", i, *(chptr + i));
return EXIT_SUCCESS;
}
$ ./a.out
byte 7: aa
byte 6: bb
byte 5: cc
byte 4: dd
byte 3: 11
byte 2: 22
byte 1: 33
byte 0: 44
0x12345680
0x12345682
0x12345681
0x12345683
0x44
0x33
0x22
0x11
0x12345684
0x12345686
0x12345687
0x12345685
0xdd
0xcc
0xbb
0xaa
x
a1
b2
c3
d4
01
23
d4
c3
b2
a1
Little-Endian
MSB
Most significant byte
LSB
Least significant byte
0x100
0x101
0x102
0x103

## Slide 4: mvn – Copies NOT (~)
constant (immediate value)
destination register
mvn
Rd
source register
mvn
Rd
Rm
destination register
bitwise NOT operation. Immediate (constant) version copies to 32-bit register, then does a bitwise NOT
mvn r1, 4 // x = ~4
mvn r1, r5 // x = ~y in C
mvn r1, 0 // x = -1
imm8 | extended imm8 | inverted imm8 | signed base 10
0x00 | 0x00 00 00 00 | 0xff ff ff ff | -1
0xff | 0x00 00 00 ff | 0xff ff ff 00 | -256
0xfffffffb
r1
0x4
invert the bits
0x00000004
copy into 32 bits zero extend
0xaaaaaaaa
0x55555555
r5
r1
rot4
imm8
~ 1100
----
0011
Bitwise NOT
x
mvn Rd, constant // Rd = constant
mvn Rd, Rm // Rd = Rm
0x0
0xffffffff
r1

## Slide 5: Bitwise Instructions
<op> Rd, Rn, constant // Rd = Rn <op> constant
<op> Rd, Rn, Rm // Rd = Rn <op> Rm
Operand 2 constant
destination
<op>
Rd
rot4
imm8
Rn
operand 1
Operand 2
destination
<op>
Rd
Rn
operand 1
Rm
Bytes: 0 <= imm8 <= 255 + values from "rotating" rot 4 bits
Bitwise <op> description | C Syntax | Arm <op> Syntax Op2: either register or constant value | Operation
Bitwise AND | a & b | and Rd, Rn, Op2 | Rd = Rn & Op2
Bitwise OR | a ¦ b | orr Rd, Rn, Op2 | Rd = Rn ¦ Op2
Exclusive OR | a ^ b | eor Rd, Rn, Op2 | Rd = Rn ^ Op2
Bitwise NOT | a = ~b | mvn Rd, Rn | Rd = ~Rn
x

## Slide 6: Inserting Bitfields – Inserting Source Field into Destination Field
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
r1
r0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
x
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Task: Insert source into destination
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
results in
orr r1, r1, r2
r1 = r1 | r2;
r1
r2
Approach
(1) isolate source field
(2) clear destination field
(3) Bitwise or together
a | b | a ¦ b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 7: Inserting Bitfields – Isolating the Source Field
r2
r0
x
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
isolate source field
lsl r2, r0, 24
lsr r2, r2, 8
r2 = r0 << 24;
r2 = r2 >> 8;
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  |  | 0
other bits |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r0
r2

## Slide 8: Inserting Bitfields – Clearing the Destination Field
x
lsl r1, r1, 8
r1 = r1 << 8;
r1
r3
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
r1
r1
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1
clear the destination field
ror r1, r1, 24
r1=(r1>>24)|(r1<<8);
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ror r1, r1, 16
r1= (r1>>16)|(r1<<16);

## Slide 9: Inserting Bitfields – Combining Isolated Source and Cleared Destination
x
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
inserted field
orr r1, r1, r2
r1 = r1 | r2;
r1
r2
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
all zero's |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | all zero's |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 16 | 1 5 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | all zeros |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
isolated source
r1
r1
field cleared in destination

## Slide 10: Example: Swapping bits7,6 with bits 1,0
x
r0
r1
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
r0
source
r1
r2
and r1, r0, 0x3 (0b11)
(optional bits 31-8 == 0)
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
r0
r0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
lsl r1, r1, 6
lsr r2, r0, 6
and r0, r0, 0x3c
(0b 0011 1100)
orr r0, r0, r2
orr r0, r0, r1

## Slide 11: Masking Summary
Isolate a field: Use lsr, lsl, rot to get a field surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Select a field: Use and with a mask of one's surrounded by zero's to select the bits that have a 1 in the mask, all other bits will be set to zero
Clear a field: Use and with a mask of zero's surrounded by one's to select the bits that have a 1 in the mask, all other bits will be set to zero
1 1 1 1 1 1 1 1 | 0 0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
x
0 0 0 0 0 0 0 0 | 1 1 1 1 1 1 1 1 1 | 0 0 0 0 0 0 0 0 0 0 0 0 0 0
selects this field when used with and
selection mask
clear a field mask
clears this field when used with and
lsl to get this edge into msb
lsr to get this edge into lsb
Insert a field: Use orr with fields surrounded by zeros
0 0 0 0 0 0 0 0 | source | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
Keep these bits | 0 0 0 0 0 0 0 0 | Keep these bits

## Slide 12: Reference For PA7/8: C Stream Functions Opening Files
FILE *fopen(char filename[], const char mode[]);
Opens a stream to the specified file in specified file access mode
  returns NULL on failure – always check the return value; make sure the open succeeded!
Mode is a string that describes the actions that can be performed on the stream:
''r’’ Open for reading.
The stream is positioned at the beginning of the file. Fail if the file does not exist.
''w’’ Open for writing.
The stream is positioned at the beginning of the file. Create the file if it does not exist.
''a’’ Open for writing.
The stream is positioned at the end of the file. Create the file if it does not exist.
Subsequent writes to the file will always be at current end of file.
An optional ''+'' following ''r'', ''w'', or ''a'' opens the file for both reading and writing
x

## Slide 13: Reference: C Stream Functions Closing Files and Usage
int fclose(FILE *stream);
  Closes the specified stream, forcing output to complete (eventually)
    returns EOF on failure (often ignored as no easy recovery other than a message)
Usage template for fopen() and fclose()
  Open a file with fopen() always checking the return value
  do i/o – keep calling stdio io routines
  close the file with fclose() when done with that I/O stream
x

## Slide 14: C Stream Functions Array/block read/write
  These do not process contents they simply transfer a fixed number of bytes to and from a buffer passed to them
  size_t fwrite(void *ptr, size_t size, size_t count, FILE *stream);
  Writes an array of count elements of size bytes from stream
  Updates the write file pointer forward by the number of bytes written
  returns number of elements written
  error is short element count or 0
  size_t fread(void *ptr, size_t size, size_t count, FILE *stream);
  Reads an array of count elements of size bytes from stream
  Updates the read file pointer forward by the number of bytes read
  returns number of elements read, EOF is a return of 0
  error is short element count or 0
I almost always set size to 1 to return bytes read/written
x

## Slide 15: C fread() and fwrite()
#define BUFSZ 128
int copy(FILE *infp, FILE *outfp) {
unsigned char buf[BUFSZ];
size_t cnt;
while ((cnt = fread(buf, 1, BUFSZ, infp)) > 0) {
fprintf(stderr, "bytes: %u\n", cnt);
if (fwrite(buf, 1, cnt, outfp) != cnt)
return -1;
}
return 0;
}
x
element size of 1 with a char buffer is byte I/O
Capture bytes read so you know how many bytes to write
unless the input file length is an exact multiple of BUFSIZ, last fread() will always read less than BUFSIZ which is why you write cnt
cnt
BUFSZ
Jargon: the last record is often called the "runt"
  size_t
  fread(void *ptr, size_t size, size_t count, FILE *stream)
  Reads an array of count elements of size bytes from stream
  size_t
  fwrite(void *ptr, size_t size, size_t count, FILE *stream
  Writes an array of count elements of size bytes to stream
% ls –l a
4 -rw-r--r-- 1 kmuller 1104 May 15 09:45 a
% ./a.out a b
bytes: 128
bytes: 128
bytes: 128
bytes: 128
bytes: 128
bytes: 128
bytes: 128
bytes: 128
bytes: 80
128 * 8 + 80 = 1104

## Slide 16: Using fopen() and fclose()
int main(int argc, char **argv)
{
FILE *infp;
FILE *outfp;
int reslt;
if (argc != 3) {
fprintf(stderr, "%s requires two args\n", argv[0]);
return EXIT_FAILURE;
}
// Open the input file for read
if ((infp = fopen(*(argv+1), "r")) == NULL) {
fprintf(stderr,"fopen for read failed\n");
return EXIT_FAILURE;
}
// Open the output file for write
if ((outfp = fopen(*(argv+2), "w")) == NULL) {
fprintf(stderr, "fopen for write failed\n");
fclose(infp);
return EXIT_FAILURE;
}
reslt = copy(infp, outfp);
fclose(infp);
fclose(outfp);
if (reslt != 0) {
fprintf(stderr, "copy %s to %s failed\n", *(argv+1), *(argv+2));
return EXIT_FAILURE;
}
return EXIT_SUCCESS;
}
x

## Slide 17: Assembly Source File to Executable to Linux Memory
Local variables and function call overhead
code you write in the text segment
allocates space dynamically during execution by c runtime library code (text)
x
OS kernel [protected]
Stack
Heap
Static Data
Shared Libraries
Read Only Data
Read Only Text Segment
`
.bss
uninitialized static variables
.data
initialized static variables
.section .rodata
read-only literals
.text
assembly code
BSS
Sections in an Assembly Source file
File Header
Specify Hardware assembler generate the correct ARM version
file footer
.section .note.GNU-stack,…
.end
Text
Symbol table
Data
a.out executable
created by the assembler &
link editor
Header - Description

## Slide 18: Creating Segments, Definitions In Assembly Source
The following assembler directives indicate the start of a memory segment specification
  Remains in effect until the next segment directive is seen
x
.bss
    // start uninitialized static segment variables definitions
  // does not consume any space in the executable file
.data
// start initialized static segment variables definitions
.section .rodata
// start read-only data segment variables definitions
.text
// start read-only text segment (code)

## Slide 19: Assembly Source File Template
assembly programs end in .S
  That is a capital .S
  example: test.S
Always use gcc to assemble
  _start() and C runtime
File has a complete program
  gcc file.S
File has a partial program
  gcc –c file.S
Link files together
  gcc file.o cprog.o
// File Header
.arch armv6 // armv6 architecture instructions
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
// BSS Segment (only when you have initialized globals)
.bss
// Data Segment (only when you have uninitialized globals)
.data
// Read-Only Data (only when you have literals)
.section .rodata
// Text Segment – your code
.text
// Function Header .type main, %function // define main to be a function
.global main // export function name
main:
// function prologue // stack frame setup
// your code for this function here
// function epilogue //stack frame teardown
// function footer
.size main, (. – main)
// File Footer
.section .note.GNU-stack,"",%progbits // stack/data non-exec
.end
x

## Slide 20: ARM Assembly Source File: Header and Footer
.syntax unified
  use the standard ARM assembly language syntax called Unified Assembler Language (UAL)
.section .note.GNU-stack,"",%progbits
  tells the linker to make the stack and all data segments not-executable (no instructions in those sections) – security measure
.end
  at the end of the source file, everything written after the .end is ignored
.arch armv6 // armv6 architecture
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
File Header
At the top of every ARM source file
.section .note.GNU-stack,"",%progbits // set stack/data non-exec
.end
// everything past the .end is ignored!
// Debugging notes etc
File Footer
At the bottom of every ARM source file
// Contents of the other memory segment include .text (your code)
x

## Slide 21: Assembler Directives: .equ and .equiv
.equ <symbol>, <expression>
  Defines and sets the value of a symbol to the evaluation of the expression
  Used for specifying constants, like a #define in C
  You can (re)set a symbol many times in the file, last one seen applies
  .equ BLKSZ, 10240 // buffer size in bytes
  // other lines
  .equ BLKSZ, 1024 // buffer size in bytes
.equ BLKSZ, 10240 // buffer size in bytes
.equ BUFCNT, 100*4 // buffer for 100 ints
.equ BLKSZ, STRSZ * 4 // redefine BLKSZ from here
x

## Slide 22: Example: Assembler Directive and Instructions
10 .equ NULL, 0
11 main:
12 3000 0310A0E1 mov r1, r3
13 .Lloop:
14 3004 043083E2 add r3, r3, 4
15 3008 001093E5 ldr r1, [r3]
16 300c 000051E3 cmp r1, NULL
17 3010 FBFFFF1A bne .Lloop
Instruction Memory Addresses (lowest 2-bits are always are 00)
Notice alignment and how addresses increase by 4 (32-bit instructions)
Regular label main
is associated with memory location 0x3000
Local label .Lloop
is associated with memory location 0x3004
assembler directive .equ does not allocate any memory (NULL = 0)
Memory Contents
Warning contents shown in "reverse" byte order: Lsb – Msb
output generated with
gcc -c -Wa,-ahlns space.S
partial output is shown
space.S
x

## Slide 23: Function Header and Footer Assembler Directives
.global function_name
  Exports the function name to other files. Required for main function, optional for others
.type name, %function
  The .type directive sets the type of a symbol/label name
  %function specifies that name is a function (name is the address of the first instruction)
equ FP_OFF, 4
  Used for basic stack frame setup; the number 4 will change – later slides
.size name, bytes
  The .size directive is used to set the size associated with a symbol
  Used by the linker to exclude unneeded code and/or data when creating an executable file
  It is also used by the debugger gdb
  bytes is best calculated as an expression: (period is the current address in a memory segment)
  .size name, (. – name)
.text
.global myfunc // make myfunc global for linking
.type myfunc, %function // define myfunc to be a function
.equ FP_OFF, 4 // fp offset in main stack frame
myfunc:
// function prologue, stack frame setup
    // your code
// function epilogue, stack frame teardown
.size myfunc, (. – myfunc)
function entry point
address of the first instruction in the function
Must not be a local label (does not start with .L)
Function Header
Function Footer
x

## Slide 24: Function Prologue and Epilogue: Stack Frame Management Minimum Sized stack frame shown
.text
.global myfunc // make myfunc global for linking
.type myfunc, %function // define myfunc to be a function
.equ FP_OFF, 4 // fp offset in main stack frame
myfunc:
// function prologue, stack frame setup – (later slides)
push {fp, lr}
add fp, sp, FP_OFF
    // your code
// function epilogue, stack frame teardown, return - (later slides)
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
.size myfunc, (. – myfunc)
Function Prologue
Function Epilogue
x

## Slide 25: Preview: Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
r0, r1 = function(r0, r1, r2, r3) // 64-bit return – long long
Each parameter and return value is limited to data that can fit in 4 bytes or less
You receive up to the first four parameters in these four registers
You copy up to the first four parameters into these four registers before calling a function
For parameter values using more than 4 bytes, a pointer to the parameter is passed (we will cover this later)
You MUST ALWAYS assume that the called function will alter the contents of all four registers: r0-r3
  In terms of C runtime support, these registers contain the copies given to the called function
  C allows the copies to be changed in any way by the called function
Register | Function Call Use
r0 | 1st parameter
r1 | 2nd parameter
r2 | 3rd parameter
r3 | 4th parameter
Register | Function Return Value Use
r0 | 8, 16 or 32-bit result, 32-bit address or least-significant half of a 64-bit result
r1 | most-significant half of a 64-bit result
x

## Slide 26: Assembler Directives: Label Scope Control (Normal Labels only)
.extern <label>
  Imports label (function name, symbol or a static variable name);
  An address associated with the label from another file can be used by code in this file
.global <label>
  Exports label (or symbol) to be visible outside the source file boundary (other assembly or c source)
  label is either a function name or a global variable name
  Only use with function names or static variables
Without .global, labels are usually local to the file from the point where they are defined
.extern printf
.extern fgets
.extern strcpy
.global fbuf
x

## Slide 27: Preview: Writing an ARM32 function
#include <stdlib.h>
#include <stdio.h>
#include "sum4.h"
int main()
{
int reslt;
reslt = sum4(1,2,3,4);
printf("%d\n", reslt);
return EXIT_SUCCESS;
}
#ifndef SUM4_H
#define SUM4_H
#ifndef __ASSEMBLER__
int sum4(int, int, int, int);
#else
.extern sum4
#endif
#endif
#include "sum4.h"
.arch armv6
.arm
.fpu vfp
.syntax unified
.global sum4
.type sum4, %function
.equ FP_OFF, 28
// r0 = sum4(r0, r1, r2, r3)
sum4:
push {r4-r9, fp, lr}
add fp, sp, FP_OFF
add r0, r0, r1
add r0, r0, r2
add r0, r0, r3
sub sp, fp, FP_OFF
pop {r4-r9, fp, lr}
bx lr
.size sum4, (. - sum4)
.section .note.GNU-stack,"",%progbits
.end
$ gcc -Wall -Wextra -c main.c
$ gcc -c sum4.S
$ gcc sum4.o main.o
$ ./a.out
10

## Slide 28: Variable Alignment In Memory and Performance
Accessing address aligned memory on many systems based on data type has the best performance (due to hardware implementation)
1
2 bytes
4 bytes
integer
short
char
x
4
bytes
1
Byte
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x0C
0x0D
0x0E
0x0F
Aligned Address
Hex
2
Bytes
0x00
0x02
0x04
0x06
0x08
0x0A
0x0C
0x0E
any address
addresses that end in 0b0
addresses that end in 0b00
0x00
0x04
0x08
0x0C
Aligned Address
Hex
Aligned Address
Hex

## Slide 29: Load/Store: Register Base Addressing
32-bit memory
register r0
register r1 (address)
ldr r0, [r1]
Copies a 32-bit word
from the memory location
whose address is contained
in r1 (r1 is a pointer)
into register r0
r1 is being used as a pointer to a location in memory
ldr requires the use of a pointer operand
str r0, [r1]
Copies all 32 bits of the value held in register r0 to the 32-bit memory location contained in register r1 (r1 pointer)
32-bit memory
register r0
register r1 (address)
r1 is being used as a pointer to a location in memory
str requires the use of a pointer operand
x

## Slide 30: LDR/STR – Base Register + Immediate Offset Addressing
Register Base Addressing:
  Pointer Address: Rn; source/destination data: Rd
  Unsigned pointer address in stored in the base register
Register Base + immediate offset Addressing:
  Pointer Address = register content + immediate offset -4095 <= imm12 <= 4095 (bytes)
  Unsigned offset integer immediate value (bytes) is added or subtracted (U bit above says to add or subtract) from the pointer address in the base register
unsigned immediate offset
Rd – source/dest register
ldr/str
Rd
imm12
Rn
Rn – base register contains address (pointer)
U
+/- offset
x

## Slide 31: ldr/str Register Base + Immediate Offset Addressing
Syntax | Address | Examples
ldr/str Rd, [Rn, +/- constant] constant is in bytes ldr/str Rd, [Rn] | Rn + or – constant same | ldr r0, [r5,100] str r1, [r5, 0] str r1, [r5]
ldr/str
Rd
imm12
Rn
U
+ -
0 subtract
1 add
Memory Address
Instruction
Source for str
Destination for ldr
x

## Slide 32: Example Base Register Addressing Load – Modify – Store
x = x + 1;
ldr r0, [r1] // r0 = *r1 (read x)
add r0, r0, 1 // r0 = r0 + 1 (x++)
str r0, [r1] // *r1 = r0 write x
Memory assigned to x
register r0
register r1 (address)
+ 1
0b..0000100
Notice: word aligned!
(last two bits are 0's)
..00000000
..00000001
n-bit Memory
Address
binary
..00000010
..00000011
..00000100
..00000101
..00000110
..00000111
01010101
10101010
01010101
10101010
01010101
10101010
01010101
10101010
1 byte
contents
X starting address
x
x = x + 1
Where x is in memory
r1 is a pointer

## Slide 33: Loading and Storing: Variations List
Load and store have variations that move 8-bits, 16-bits and 32-bits
Load into a register with less than 32-bits will set the upper bits not filled from memory differently depending on which variation of the load instruction is used
Store will only select the lower 8-bit, lower 16-bits or all 32-bits of the register to copy to memory, register contents are not altered
Instruction | Meaning | Sign Extension | Memory Address Requirement
ldrsb | load signed byte | sign extension | none (any byte)
ldrb | load unsigned byte | zero fill (extension) | none (any byte)
ldrsh | load signed halfword | sign extension | halfword (2-byte aligned)
ldrh | load unsigned halfword | zero fill (extension) | halfword (2-byte aligned)
ldr | load word | --- | word (4-byte aligned)
strb | store low byte (bits 0-7) | --- | none (any byte)
strh | store halfword (bits 0-15) | --- | halfword (2-byte aligned)
str | store word (bits 0-31) | --- | word (4-byte aligned)
x

## Slide 34: Loading 32-bit Registers From Memory Variables < 32-Bits Wide
Unsigned
Zero-Extend: Add leading 0’s
example ldrb
Instructions that zero-extend:
ldrb, ldrh
0b 1110 0001
0x00
0x00
0x00
0xe1
memory
r0
Overwrite the upper three bytes with 0
Signed (2’s complement)
Sign-Extend: Replicate sign bit
example ldrsb
Instructions that sign-extend:
ldrsb, ldrsh
0xff
0xff
0xff
0xe1
memory
r0
Overwrite the upper three bytes with 1
0b 1110 0001
x

## Slide 35: Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrb r1, [r0]
r1
0
31
r1
Load a word
ldr r1, [r0]
observe the zero fill
x
0x0a
0x0b
0x0c
0x0d
0xe1
0xe3
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
0xe3
0xe1
0x00
0x00
0
31
r1
Load a halfword
ldrh r1, [r0]
0x00
0x00
0xe3
0xe1
observe the zero fill
0xe1

## Slide 36: Signed Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrsb r1, [r0]
r1
0
31
r1
Load a word (no change)
ldr r1, [r0]
observe the sign extend
x
0x0a
0x0b
0x0c
0x0d
1110 0001
1110 0011
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
1110 0011
1110 0001
0x00
0x00
0
31
r1
Load a halfword
ldrsh r1, [r0]
0x00
0x00
observe the sign extend
1110 0011
1110 0001
0xff
0xff
1110 0001
0xff
0xff
0xff

## Slide 37: Signed Load a Byte, Half-word, Word
0x00
0x00
0x00
0x00
0
31
Load a byte
ldrsb r1, [r0]
r1
0
31
r1
Load a word (no change)
ldr r1, [r0]
observe the sign extend
x
0x0a
0x0b
0x0c
0x0d
0110 0001
0110 0011
0x65
0x87
0x00
0x00
0x00
0x10
r0
0001 0000
0001 0001
0001 0010
0001 0011
0001 0000
Byte Address Byte
.align 2 word aligned
0x87
0x65
0110 0011
0110 0001
0x00
0x00
0
31
r1
Load a halfword
ldrsh r1, [r0]
0x00
0x00
0110 0011
0110 0001
observe the sign extend
0110 0001

## Slide 38: Storing 32-bit Registers To Memory 8-bit, 16-bit, 32-bit
strb
0x00
0x00
0xe2
0xe1
memory
r0
0x??
0x??
0x??
0xe1
Not Changed
strh
0x00
0x00
0xe2
0xe1
memory
r0
0x??
0x??
0xe2
0xe1
Not Changed
x
str
0x04
0x03
0xe2
0xe1
memory
r0
0x04
0x03
0xe2
0xe1

## Slide 39: Store a Byte, Half-word, Word
0x20
0x00
0x00
0x00
initial value in r0
0
31
Store a byte
strb r1, [r0]
r1
0x87
0x65
0xe3
0xe1
0x11
0x22
0x33
0x20000000
0x20000001
0x20000002
0x20000003
observe other bytes NOT altered
Byte Address Byte
x
0x00
0xe1
0
31
r1
Store a halfword
strh r1, [r0]
0x87
0x65
0xe3
0xe1
0x22
0x33
0x20000000
0x20000001
0x20000002
0x20000003
Byte Address Byte
0x11
0x00
0xe1
0xe3
0
31
0x87
0x65
0xe3
0xe1
r1
Store a word
str r1, [r0]
0x20000000
0x20000001
0x20000002
0x20000003
Byte Address Byte
0x11
0x22
0x33
0x00
0xe1
0xe3
0x65
0x87

## Slide 40: ldr/str practice - 1
r1 contains the Address of X (defined as int X) in memory; r1 points at X
r2 contains the Address of Y (defined as int *Y) in memory; r2 points at Y
write Y = &X;
str r1, [r2] // y  &x
address of y
0x0100c
r1
r2
X contents
x
??
Y contents
??
0x01008
0x0100c // this is y
0x01004 // this is x
0x01000
address of x
0x01004
??
0x01010
0x01004

## Slide 41: ldr/str practice - 2
r1 contains the Address of X (defined as int *X) in memory r1 points at X
r2 contains the Address of Y (defined as int Y) in memory; r2 points at Y
write Y = *X;
ldr r3, [r1] // r3  x (read 1)
ldr r0, [r3] // r0  *x (read 2)
str r0, [r2] // y  *x
x
address of y
0x0100c
r1
r2
X = 0x01010
??
Y contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
55
0x01010
55
?
r3
0x01010
r0
?
55

## Slide 42: using ldr/str: array copy
#include <stdio.h>
#include <stdlib.h>
#define SZ 6
void icpy(int *, int *, int);
int main(void)
{
int src[SZ] = {1, 2, 3, 4, 5, 6};
int dst[SZ];
icpy(src, dst, SZ);
for (int i = 0; i < SZ; i++)
printf("%d\n", *(dst + i));
return EXIT_SUCCESS;
}
x
void icpy(int *src, int *dst, int cnt)
{
for (int i = 0; i < cnt; i++)
*dst++ = *src++;
return;
}

## Slide 43: Base Register version
cmp r2, 0
ble .Ldone
lsl r2, r2, 2 //convert cnt to int size
add r3, r0, r2 // loop term pointer
.Ldo:
ldr r4, [r0] // load from src
str r4, [r1] // store to dest
add r0, r0, 4 // src++
add r1, r1, 4 // dst++
cmp r0, r3 // src < term pointer?
blt .Ldo
.Ldone:
.arch armv6
.arm
.fpu vfp
.syntax unified
.text
.global icpy
.type icpy, %function
.equ FP_OFF, 12
// r0 contains int *src
// r1 contains int *dst
// r2 contains int cnt
// r3 use as loop term pointer
// r4 use as temp
icpy:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
// see right ->
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size icpy, (. - icpy)
.end
x
loop guard
pre loop guard

## Slide 44: ldr/str practice - 3
r1 contains Address of X (defined as int *X) in memory; r1 points at X
r2 contains Address of Y (defined as int Y[2]) in memory; r2 points at &(Y[0])
write *X = Y[1];
ldr r0, [r2, 4] // r0  y[1]
ldr r3, [r1] // r3  x
str r0, [r3] // *x  y[1]
x
address of y
0x0100c
r1
r2
X = 0x01000
??
Y[0] contents
??
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
Y[1] contents
0x01010
Y[1] contents
?
r3
r0
?
0x01000
Y[1] contents
+4

## Slide 45: ldr/str Base Register + Register Offset Addressing
Syntax | Address | Examples
ldr/str Rd, [Rn +/- Rm ] | Rn + or – Rm | ldr r0, [r5, r4] str r1, [r5, r4]
ldr/str
Rd
Rn
U
+ -
0 subtract
1 add
Memory Address
Instruction
Source for str
Destination for ldr
Rm
x
Pointer Address = Base Register + Register Offset
  Unsigned offset integer in a register (bytes) is either added/subtracted from the pointer address in the base register

## Slide 46: ldr/str practice - 4
r1 contains Address of X (defined as int X[2]) in memory; r1 points at &(x[0])
r2 contains Address of Y (defined as int Y) in memory; r2 points at Y
r3 contains a 4
write Y = X[1];
ldr r0, [r1, r3] // r0  x[1]
str r0, [r2] // y  x[1]
x
address of y
0x0100c
r1
r2
??
x[0] contents
Y contents
0x01008
0x0100c
0x01004
0x01000
address of x
0x01004
x[1] contents
0x01010
x[1] contents
4
r3
r0
?
x[1] contents
+4

## Slide 47: Base Register + Register Offset Version
cmp r2, 0
ble .Ldone
lsl r2, r2, 2 //convert cnt to int size
mov r3, 0 // initialize counter
.Ldo:
ldr r4, [r0, r3] // load from src
str r4, [r1, r3] // store to dest
add r3, r3, 4 // counter++
cmp r3, r2 // count < r3
blt .Ldo
.Ldone:
.arch armv6
.arm
.fpu vfp
.syntax unified
.text
.global icpy
.type icpy, %function
.equ FP_OFF, 12
// r0 contains int *src
// r1 contains int *dst
// r2 contains int cnt
// r3 use as loop counter
// r4 use as temp
icpy:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
// see right ->
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size icpy, (. - cpy)
.end
x
loop guard
pre loop guard
one increment covers both arrays

## Slide 48: Base Register + Register Offset With chars
#include <stdio.h>
#include <stdlib.h>
#define SZ 6
void cpy(char *, char *, int);
int main(void)
{
char src[SZ] =
{'a', 'b', 'c', 'd', 'e', '\0'};
char dst[SZ];
cpy(src, dst, SZ);
printf("%s\n", dst);
return EXIT_SUCCESS;
}
x
cmp r2, 0
ble .Ldone
mov r3, 0 // initialize counter
.Ldo:
ldrb r4, [r0, r3] // load from src
strb r4, [r1, r3] // store to dest
add r3, r3, 1 // counter++
cmp r3, r2 // count < r3
blt .Ldo
.Ldone:

## Slide 49: Reference: Addressing Mode Summary for use in CSE30
index Type | Example | Description
Pre-index immediate | ldr r1, [r0] | r1  memory[r0] r0 is unchanged
Pre-index immediate | ldr r1, [r0, 4] | r1  memory[r0 + 4] r0 is unchanged
Pre-index immediate | str r1, [r0] | memory[r0]  r1 r0 is unchanged
Pre-index immediate | str r1, [r0, 4] | memory[r0 + 4]  r1 r0 is unchanged
Pre-index register | ldr r1, [r0, +-r2] | r1  memory[r0 +- r2] r0 is unchanged
Pre-index register | str r1, [r0, +-r2] | memory[r0 +- r2]  r1 r0 is unchanged
x

## Slide 50: Base Register Addressing + Offset register
int count(char *ptr, int len)
{
int cnt = 0;
int i;
for (i = 0; i < len; i++) {
if ((ptr[i] >= 'A') && (ptr[i] <= 'Z'))
cnt++;
}
return cnt;
}
#include <stdio.h>
#include <stdlib.h>
int count(char *, int);
int main(void)
{
char msg[] ="Hello CSE30! We Are CountinG UpPER cASe letters!";
printf("%d\n", count(msg, sizeof(msg)/sizeof(*msg)));
return EXIT_SUCCESS;
}
x

## Slide 51: Base Register + Offset register
count:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
mov r2, 0
cmp r1, 0
ble .Ldone
mov r3, 0
.Lfor:
cmp r3, r1
bge .Ldone
ldrb r4, [r0, r3]
cmp r4, 'A'
blt .Lendif
cmp r4, 'Z'
bgt .Lendif
add r2, r2, 1
.Lendif:
add r3, r3, 1
b .Lfor
.Ldone:
mov r0, r2
.arch armv6
.arm
.fpu vfp
.syntax unified
.text
.global count
.type count, %function
.equ FP_OFF, 12
// r0 contains char *ptr
// r1 contains int len
// r2 contains int cnt
// r3 contains int i
// r4 contains char
count:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
// see right ->
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size count, (. - count)
.end
x
loop guard
byte array
Also use ldrb here
offsets are 0,1,2,…